Source	CANADA NEWSWIRE
Date	02/27/2019
Time	04:04:00 AM

Company	 Osino Resources Corp.
Title	Osino Resources Announces Three New Gold Anomalies and Provides
Exploration Update on Its Otjikoto East Project, Namibia





    CDNX Symbol: OSI











Press Release




" BC-Osino-Gold-Anomalies   02-27 1165
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Osino Resources Announces Three New Gold Anomalies and Provides
Exploration Update on Its Otjikoto East Project, Namibia@

VANCOUVER, Feb. 27, 2019 /CNW/ - Osino Resources Corp. (TSXV: OSI)
("Osino" or "the Company"), is pleased to announce the delineation of three
new gold anomalies and ongoing exploration progress at its Otjikoto East
Project ("Otjikoto East") in northern Namibia. Otjikoto East is comprised of
three contiguous licenses covering a total area of 1538km2. It includes 120km
of prospective strike length of the Otjikoto host stratigraphy, directly east
and along strike from B2Gold Corp's producing Otjikoto Gold Mine.
Exceptional progress has been made at Otjikoto East since the last press
release dated October 2, 2018. Osino acquired these licenses in 2017 and
exploration activities to date have included systematic regional mapping and
surface geochemical sampling, augmented by a high-resolution magnetic and
radiometric survey. Approximately 60% of the strike length of prospective
stratigraphy has now been covered by surface geochemical sampling and five
coherent gold anomalies have been discovered by Osino to date.
Figure 1: Otjikoto East: Gold Anomalies and Geological Interpretation
from Airborne Magnetics
The Fairview anomaly is particularly exciting as two gold-bearing veins
were also found within this sand covered area 30km east of the Otjikoto mine.
Despite this ground being under continuous licence for the last 30 years, this
is the first new gold occurrence in the Otavi area since the discovery of
Otjikoto in 1999.
Airborne Magnetic and Radiometric Survey
A geological interpretation was carried out using the detailed
geophysical information collected during the high-resolution magnetic and
radiometric survey flown by Osino in May 2018. Otjikoto East has very limited
outcrop and the interpreted geology is essential to prioritize and direct
activities on the ground. Exploration is focused on large-scale, fertile
structures and prospective stratigraphy, which includes the area sampled to
date as well as the area which will be covered during H1 2019 (indicated by
red polygons on Figure 1).
Gold Anomalies Discovered to Date
<<

--  Fairview - A multipoint gold anomaly in sand adjacent to an interpreted
dome structure. Subsequent pitting and rock chip sampling of limited
quartz veins produced two positive assays of 1.16 and 0.90g/t gold,
along with anomalous silver and copper.
--  Omagonde - A low-level gold and silver anomaly within calcrete in the
northwest corner of the farm.
--  Gaidaus - An east-west striking gold anomaly in calcrete, along an
interpreted thrust fault between schists and marbles. The historical
Okurusu occurrence listed in the previous press release is a small
copper - gold gossan adjacent to the Gaidaus anomaly.
--  Omahona Fold - A large-scale, low-grade gold anomaly in soils along the
folded contact between schists and marbles.
--  Waldorf South - Several gold anomalies in sand overlying marble layers
within schist, adjacent to major structure (Otjohorongo Lineament)
<>>
Future Work Program
Osino's exploration program at Otjikoto East for the next 6-12 months
consists of the following phases:
<<

--  H1 2019 - Calcrete and sand sampling of remaining priority areas.
Follow-up sampling over anomalies to delineate Rotary Air Blast (RAB)
drill targets.
--  H2 2019 - Testing of geochemical anomalies by pitting and RAB drilling
to obtain bedrock samples
--  H2 2019/H1 2020 - Testing of bedrock anomalies using conventional
reverse circulation and core drilling
<>>
Geological Setting
Osino is exploring for gold in the Northern and Northern Central Zones of
the Neoproterozoic Damara Belt, targeting gold mineralisation that broadly
fits the orogenic gold model. Much of the historical exploration for gold in
Namibia did not take an orogenic approach and although the project area was
previously held by several other exploration companies, very little grassroots
exploration was carried out.
A large part of Otjikoto East is covered by calcrete (caliche) which is
often also covered by wind-blown sand, disqualifying the use of conventional
soil sampling. The Company has pioneered the use of calcrete as a sample
medium in Namibia and proven its effectiveness on the Karibib Gold Project
(refer to press release dated January 17, 2019).
Calcrete is a hardened, calcium-rich layer in, or on top of, a soil which
is formed as a result of climatic fluctuations in arid and semiarid regions.
Calcite is dissolved in groundwater and, under drying conditions, is
precipitated as the water evaporates at the surface. Rainwater saturated with
carbon dioxide acts as an acid and dissolves calcite and then redeposits it on
the surfaces of the soil particles; as the spaces between soil particles are
filled, an impermeable crust is formed. This crust can vary from less than 1m
to more than 50m thick.
Quality Assurance
All Osino sample assay results have been independently monitored through
a quality assurance / quality control ("QA/QC") program including the
insertion of blind standards, blanks and field duplicate samples. QA/QC
samples make up 10% of all samples submitted. Calcrete and sand (anthill)
samples are prepared at Intertek, Johannesburg, South Africa. Samples are
dried, crushed to ~10mm and pulverised (300g up to 1.2kg). A split of 120g is
shipped to the Intertek Analysis laboratory in Perth, Australia. Samples (10g)
are leached in cyanide for 24 hours and analyzed for gold using ICP-MS with an
ultra-low detection limit of 0.01ppb. Additional elements analyzed are Ag, Cu
and As. Conventional soil samples are field-sieved (-212 micron) and prepared
at ALS Global in Swakopmund, Namibia. The samples are pulverised to 85%
passing 75 microns. Samples are shipped to ALS Global Laboratory in Vancouver,
Canada. Gold analysis is by 25g Aqua Regia Digest and ICP-MS finish with a
lower detection limit of 1ppb. 50-element analysis is by ICP-MS.
Qualified Person
David Underwood, a Chartered Professional Geologist (SACNASP) and a
Qualified Person for the purposes of National Instrument 43-101 Standards of
Disclosure for Mineral Projects for the Karibib Gold Project, has reviewed,
verified and approved the contents of this news release.
About Osino Resources
Osino Resources Corp. (TSXV: OSI) is a Canadian company, focused on the
acquisition and development of gold projects in Namibia. Osino's Namibian
interests comprise 20 exclusive exploration licenses located within the
central and northern zones of Namibia's prospective Damara belt, mostly in
proximity to and along strike of the producing Navachab and Otjikoto Gold
Mines. Osino is currently focusing its efforts on developing the Karibib Gold
Project and defining new exploration targets in the Otjikoto East area and on
our other licenses. The Karibib Gold Project is located approximately 130 km
north-west of Namibia's capital city Windhoek. By virtue of its location, the
projects benefit significantly from Namibia's well-established infrastructure
with paved highways, railway, power and water in close proximity. Namibia is
mining-friendly and lauded as one of the continent's most politically and
socially stable jurisdictions. Osino continues to evaluate new ground with a
view to expanding its Namibian portfolio.
Further details are available on the Company's website at
https://osinoresources.com/
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this press release.
SOURCE Osino Resources Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/February2019/27/c7332.html

-0-                           02/27/2019
/For further information: Osino Resources Corp., Heye Daun: CEO, Tel: +27
(21) 418 2525, hdaun(at)osinoresources.com; Julia Becker: Investor Relations
Manager, Tel: +1 (604) 785 0850, jbecker(at)osinoresources.com/
(OSI.)

CO:  Osino Resources Corp.
ST:  British Columbia
IN:  MIN MNG PRM FIN
SU:

-30-