Source	CANADA NEWSWIRE
Date	02/19/2020
Time	11:17:58 AM

Company	 Abraplata Resource Corp.
Title	AbraPlata Intercepts 14 Metres of 6.40 g/t Gold & 197 g/t Silver and
Identifies High-Grade Copper Zone with Intercept of 15 Metres of 5.1%
Copper, 2.35 g/t Gold & 658 g/t Silver





    CDNX Symbol: ABRA











Press Release




" BC-AbraPlata-GoldGrade   02-19 1935
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention co.431799:
^AbraPlata Intercepts 14 Metres of 6.40 g/t Gold & 197 g/t Silver and
Identifies High-Grade Copper Zone with Intercept of 15 Metres of 5.1%
Copper, 2.35 g/t Gold & 658 g/t Silver@

TORONTO, Feb. 19, 2020 /CNW/ - AbraPlata Resource Corp. (TSX.V:ABRA;
OTCPK: ABBRF) ("AbraPlata" or the "Company") is pleased to announce
significant high-grade assay results from the third diamond drill hole, DDH
20-001, completed at the Oculto deposit, located on its wholly-owned
Diablillos project in Salta province, Argentina. In addition to intercepting
high-grade gold and silver mineralisation, DDH 20-001 intercepted high-grade
copper mineralisation in the vertical continuation of a hydrothermal breccia
beneath the current gold and silver resources at Oculto (see Table 2).
Hole DDH 20-001 was drilled to a depth of 359 metres to test for the
vertical continuation of the Main Breccia below the existing mineral resources
(Figures 1 and 2). DDH 20-001 intersected 14 metres grading 6.40 g/t gold with
197 g/t silver from 261 metres, which is interpreted to be part of the
high-grade gold zone at the unconfirmity contact between the volcanics and
basement. Immediately underneath this gold-rich interval, drilling intersected
15 metres of sulphide mineralisation grading 5.10% copper, 2.35 g/t gold and
658 g/t silver including 4 metres grading 10.28% copper, 6.44 g/t gold and
1,476 g/t silver (see Table 1).
Table 1 - DDH 20-001 Drill Result Highlights:
From     To

Type          Interval       Silver        Gold     AgEq(1)        Copper
(m)      (m)                         (m)            g/t           g/t
g/t

%



146     160
Oxides                    14           133         0.10         117


165     191
Oxides                    26           264         0.03         220


261     290
Mixed                     29           430         4.30         630           
2.77


Including      261     275          Transition             14           
197         6.40         574           2.53


and        275     290          Sulphides              15           658         
2.35         691           5.10
Note:  True widths are estimated to
be 80% of the interval widths.




(1)              Silver Equivalent ("AgEq")
excludes copper and is
calculated based on a gold
to silver ratio of 75:1
and assumes average LoM
recoveries of 86% Au and
82% Ag from the 2018 PEA.
For example, AgEq (equal sign) (Ag
grade (x) 82%) + (Au grade x
75 (x) 86%).

The highlight copper, silver, and gold intercepts are shown on cross
sections in Figures 2, 4 and 5, respectively. A summary table of the full
assay results, including copper, from the three holes drill holes completed to
date is set out in Annex I.
John Miniotis, President and CEO of AbraPlata, commented, "Drilling
results at Oculto continue to exceed expectations and further demonstrate the
continuity of high-grade mineralisation within and outside the current mineral
resource. Most importantly, results continue to validate our geological
interpretation and have increased our confidence in multiple high potential
targets, which we expect to drill-test over the coming months."
"We have now intersected the highest grade copper mineralisation ever
observed at Oculto which we believe may be the upper part of an intrusive
system that was the mineralizing engine for the overlying high sulphidation
epithermal silver-gold system and has not been tested at depth. This
represents a major new exploration target at the Oculto project," said David
O'Connor, Chief Geologist at AbraPlata.
Figure 1 - Plan Map of Oculto Zone with 2019/2020 Drill Holes
Figure 2 - Cross-Section (Looking East) with Highlight Copper Intercepts
in Hole DDH 20-001
Copper Mineralisation at Oculto
DDH 20-001 intersected significant intervals of higher grade copper
mineralisation than have ever been encountered in the +450 drill holes
(approx. 88,000 metres) of historic drilling on the Diablillos project. A
number of holes from previous drill campaigns did intersect substantial copper
sulphide mineralisation at depth, but exploration was focused on oxide
mineralisation and drilling was typically stopped even if in sulphide
mineralisation. Highlights of historical copper intercepts are shown in Figure
5 below.
Figure 3 - Long Section Showing Some Historical Copper Intercepts at
Oculto (looking north)
The copper sulphide mineralisation in DDH 20-001 from 275 to 290 metres
is associated with siliceous breccias that cut basement rocks beneath the
andesitic volcanics that are the main host of epithermal silver and gold oxide
mineralisation. Massive to disseminated sulphide mineralisation in this
interval is described as chalcopyrite, possibly bornite, with minor enargite
and with associated galena in places.
While some historical copper intercepts at Oculto are associated with
elevated levels of arsenic, the high-grade copper intercept in the Main
Breccia intercepted by DDH 20-001 had low levels of arsenic (i.e., As (equal 
sign)
0.037%). Mineralogical studies are ongoing to confirm the copper bearing
phases and identify the gold and silver association. Metallurgical testing as
appropriate will follow.
Next Steps
Given the positive results from the three initial holes drilled to date,
the Company is reviewing and interpreting the new information and historical
drill results in order to select the next batch of drill targets.
The initial drill results to date support our belief that the Oculto
deposit, despite its already large Indicated silver-gold resource, has
excellent potential for expansion of the resource. High-grade results over
broad widths reinforce our view that Oculto might ultimately be better suited
to bulk underground mining targeting high grade cyanide leachable zones, which
could require substantially less initial capex than an open pit mine. Besides
the potential for additional near surface silver-gold oxide mineralisation,
the identification of high grade gold-silver-copper sulphides beneath the
current silver-gold oxide resource also opens up new exploration
opportunities, both at Oculto and in general on the Diablillos property.
Figure 4 - Cross-Section (Looking East) with Highlight Silver Intercepts
in Hole DDH 20-001
Figure 5 - Cross-Section (Looking East) with Highlight Gold Intercepts in
Hole DDH 20-001
About Diablillos
The 80 km2 Diablillos property is located in the Argentine Puna region -
the southern extension of the Altiplano of southern Peru, Bolivia, and
northern Chile - and was acquired from SSR Mining Inc. by the Company in 2016.
There are several known mineral zones on the Diablillos property, with the
Oculto zone being the most advanced with approximately 85,000 metres drilled
in 306 RC and diamond drill holes. Oculto is a high-sulphidation epithermal
silver-gold deposit derived from remnant hot springs activity following
Tertiarty-age local magmatic and volcanic activity. Comparatively nearby
examples of high sulphidation epithermal deposits include: El Indio, Chile;
Veladero, Argentina; and Pascua Lama, on the Chile-Argentine border.
Table 2 - 2018 Mineral Resource Estimate for the Oculto Deposit,
Diablillos Project
Category Tonnage   Ag     Au

Contained Ag

Contained Au

(000 t) (g/t)  (g/t)

(000 oz Ag)

(000 oz Au)

---

Indicated           26,900   93.0    0.85              80,300                   
732

---

Inferred             1,000   46.8    0.89               
1,505                    29

---
Effective August 31, 2017. Full details of
the Mineral Resources are available in a
Company news release dated March 2, 2018.
For additional information please see
Technical Report on the Diablillos Project,
Salta Province, Argentina, dated April 16,
2018, completed by Roscoe Postle Associates
Inc, and available on www.SEDAR.com.

QA/QC and Core Sampling Protocols
AbraPlata applies industry standard exploration methodologies and
techniques, and all drill core samples are collected under the supervision of
the Company's geologists in accordance with industry practices. Drill core is
transported from the drill platform to the logging facility where drill data
is compared and verified with the core in the trays. Thereafter, it is logged,
photographed, and split by diamond saw prior to being sampled. Samples are
then bagged, and quality control materials are inserted at regular intervals;
these include blanks and certified reference materials as well as duplicate
core samples which are collected in order to measure sample representivity.
Groups of samples are then placed in large bags which are sealed with numbered
tags in order to maintain a chain-of-custody during the transport of the
samples from the project site to the laboratory.
All samples are received by the SGS offices in Salta who then dispatch
the samples to the SGS preparation facility in San Juan. From there, the
prepared samples are sent to the SGS laboratory in Lima, Peru where they are
analyzed. All samples are analyzed using a multi-element technique consisting
of a four acid digestion followed by ICP/AES detection, and gold is analyzed
by 50g Fire Assay with an AAS finish. Silver results greater than 100g/t are
reanalyzed using four acid digestion with an ore grade AAS finish.
Qualified Persons
David O'Connor P.Geo., Chief Geologist for AbraPlata, is the qualified
person as defined by National Instrument 43-101 Standards of Disclosure for
Mineral Projects, has reviewed and approved the scientific and technical
information in this news release.

ANNEX 1 - Drill Result Summary of Holes DDH 19-001, DDH 19-002 and DDH
20-001.
Note: Drill Holes DDH 19-001 and DDH 19-002 values of gold and silver
were previously reported.
Drill Hole                From       To      Intercept       Thickness    Ag 
(g/t)     Au (g/t)      Cu (%)
(m)       (m)       (m)             (m)

---

DDH 19-001

---

166.0     231.0            65.0            54.20          105          0.20



including     201.0     204.0             3.0             2.50          
346          0.30

---

302.0     312.0            10.0              8.0           10          
0.08        0.86



326.0     327.0             1.0             0.83           48          
0.93        1.76



353.0     354.0             1.0             0.83           15          
6.93        0.54





DDH 19-002

---

56.0      78.0            22.0            18.33           17          2.74



including                 57.0      60.0             3.0             
2.50          104          2.91

---

137.5     155.0            17.5            14.58          604          0.10



180.0     200.0            20.0            16.67          140          0.03



242.0     257.0            15.0            12.50          286         10.42



including     250.0     257.0             7.0             5.83          
202         20.64

---

367.0     376.0             9.0             4.50           49          
7.31        1.28



including     371.0     376.0             5.0             2.50           
17         11.27        1.48

---

369.0     400.0            31.0            25.00           25          
2.27        1.30



438.0     450.0            12.0             6.00           24          
0.47        1.60





DDH 20-001

---

146       160            14.0            11.20          133          0.10



165       191            26.0            20.80          264          0.03



261       290            29.0            23.20          430          
4.30        2.77



including       261       275            14.0            11.20          
197          6.40        2.53

---

including       278       282            15.0            12.00          
658          2.35        5.10

---

Collar Data
Hole
Number            UTM Coordinates             Elevation        Azimuth     
Dip         Depth

---

DDH
19-001
X 720293
Y 7199273           4315 0         -60
380 m

---

DDH
19-002
X 720295
Y 7199404           4300 0         -60
464 m

---

DDH
20-001
X 720197
Y 7199235           4267 0         -60
359 m

---

About AbraPlata
AbraPlata is a mineral exploration company with a diversified portfolio
of silver-gold and copper exploration projects in Argentina and Chile. The
Company is focused on advancing its 100%-owned Diablillos silver-gold project
in the mining-friendly Salta province of Argentina, which is well-advanced,
with more than US$35 million spent historically on exploration with drilling
ongoing and an initial open pit PEA completed in 2018. The Company is led by
an experienced management team and has long-term supportive shareholders
including Altius Minerals and SSR Mining. In addition, AbraPlata owns theArcas 
project in Chile where Rio Tinto has an option to earn up to a 75%
interest by funding up to US$25 million in exploration. AbraPlata is listed on
the TSX-V under the symbol "ABRA".
Cautionary Statements
This news release includes certain "forward-looking statements" under
applicable Canadian securities legislation. Forward-looking statements are
necessarily based upon a number of estimates and assumptions that, while
considered reasonable, are subject to known and unknown risks, uncertainties,
and other factors which may cause the actual results and future events to
differ materially from those expressed or implied by such forward-looking
statements. All statements that address future plans, activities, events or
developments that the Company believes, expects or anticipates will or may
occur are forward-looking information. There can be no assurance that such
statements will prove to be accurate, as actual results and future events
could differ materially from those anticipated in such statements.
Accordingly, readers should not place undue reliance on forward-looking
statements. The Company disclaims any intention or obligation to update or
revise any forward-looking statements, whether as a result of new information,
future events or otherwise, except as required by law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
SOURCE AbraPlata Resource Corp.



View original content to download multimedia:
http://www.newswire.ca/en/releases/archive/February2020/19/c3289.html

-0-                           02/19/2020
/For further information: please visit the AbraPlata Resource website at
www.abraplata.com or contact: John Miniotis, President & CEO,
john(at)abraplata.com, Tel: +1 416-306-8334/
(ABRA. ABBRF)

CO:  AbraPlata Resource Corp.
ST:  Ontario
IN:  MIN PRM MNG OTC
SU:

-30-