Source	Marketwire
Date	07/26/2007
Time	04:31:14 AM

Company	 NEVADA COPPER CORP.
Title	Nevada Copper-Intersects 51.6 Meters of 2.54% Copper





    CDNX Symbol: NCU











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: Nevada Copper Corp.

TSX VENTURE SYMBOL: NCU
FRANKFURT SYMBOL: ZYT

July 26, 2007

Nevada Copper-Intersects 51.6 Meters of 2.54% Copper


VANCOUVER, BRITISH COLUMBIA--(Marketwire - July 26, 2007) - Nevada Copper Corp. 
(TSX VENTURE:NCU)(FRANKFURT:ZYT) ("Nevada Copper") is pleased to announce 
additional high grade copper results from on-going drilling at its 100% owned 
Pumpkin Hollow Copper Development Property located in Nevada. Drilling 
continues to demonstrate the continuity of mineralization, in addition to 
expanding the significant copper resources of both the East and North deposits.

NC07-14 drilled as an infill hole in the East Deposit was located 50 meters 
(165 ft) from the nearest mineralized intercept and encountered several high 
grade copper zones. The largest of these zones intersected 51.6 meters (169.2 
ft) averaging 2.54% copper, 0.181 g/t gold, 5.8 g/t silver, and 29.5% iron. 
NC07-14 offset the mineralization in nearby KM-20 (33.8 meters averaging 3.31% 
copper and 8.5 meters averaging 3.89% copper).

NC07-15 drilled in the open pittable North Deposit, was designed to infill an 
area where drilling was wide spaced and assay data was lacking. The drill hole 
established good continuity and encountered several large zones of open pit 
grade mineralization. The two largest zones in NC07-15 intersected 30.5 meters 
(100 ft) averaging 0.99% copper and 35.0 meters (115 ft) averaging 0.87% copper.

A plan map and cross sections for the deposits are available at 
www.nevadacopper.com. Drill results announced here represent true thicknesses.

/T/

EAST DEPOSIT - Assays greater than 1% Cu

------------------------------------------------------------------------
Drill Hole   From      To  Length  Length  Copper    Gold  Silver   Iron
#              (m)     (m)     (m)    (ft)     (%)   (g/t)   (g/t)    (%)
------------------------------------------------------------------------
NC07-14     518.1     519     0.9     3.1    1.86   0.049     3.7   19.3
------------------------------------------------------------------------
525.3   528.8     3.5    11.5    1.50   0.088     3.1   22.5
------------------------------------------------------------------------
577.2   628.8    51.6   169.2    2.54   0.181     5.8   29.5
------------------------------------------------------------------------
Including   577.2   612.6    35.4   116.2    3.08   0.230     7.4   23.7
------------------------------------------------------------------------
Including   619.7   623.5     3.8    12.2    2.82   0.102     3.8   23.6
------------------------------------------------------------------------


NORTH DEPOSIT - Assays greater than 0.3% Cu

-----------------------------------------------------------------
Drill Hole   From      To  Length  Length  Copper    Gold  Silver
#              (m)     (m)     (m)    (ft)     (%)   (g/t)   (g/t)
-----------------------------------------------------------------
NC07-15     173.7   204.2    30.5     100    0.99   0.061     3.3
-----------------------------------------------------------------
217.9   234.7    16.8      55    0.52   0.042     1.5
-----------------------------------------------------------------
242.3   251.5     9.2      30    0.34   0.013     0.9
-----------------------------------------------------------------
304.8   339.8    35.0     115    0.87   0.096     3.4
-----------------------------------------------------------------
Including   313.0   327.9    14.9      49    1.37   0.161     5.5
-----------------------------------------------------------------


E-2 DEPOSIT - Assays greater than 1.0% Cu

-----------------------------------------------------------------
Drill Hole   From      To  Length  Length  Copper    Gold  Silver
#              (m)     (m)     (m)    (ft)     (%)   (g/t)   (g/t)
-----------------------------------------------------------------
NC07-16      No mineralization greater than 1.0% Cu Intersected
-----------------------------------------------------------------

/T/

Hole NC07-16 was drilled along the eastern edge of the E-2 deposit and bounded 
mineralization.

Over 18,000 meters of drilling is planned in the recently expanded program. To 
date 33 holes have been drilled for a total of 17,000 meters. Of the holes 
drilled, results from 22 have been released to date. Future drilling results 
will be released as they become available.

About Nevada Copper

Nevada Copper is a well financed emerging copper company, responsibly 
developing the Pumpkin Hollow copper-iron property located in Western Nevada. 
In June 2006, a National Instrument 43-101 compliant resource estimate for the 
advanced-stage Pumpkin Hollow property was completed, as previously announced: 
At a 0.2% copper cutoff grade, the measured and indicated copper resource is 
2.7 billion pounds of copper, contained in 312 million tons grading 0.44% 
copper and 12.3% iron. An additional inferred copper resource of 3.4 billion 
pounds of copper is contained in 454 million tons grading 0.37% copper and 8.2% 
iron.

Within these large resources is a significant high grade copper resource. Using 
a 0.75% copper cutoff grade, the measured and indicated resources contain 700 
million pounds of copper in 25 million tons of material grading 1.45% copper 
and, in addition, the inferred resource contains 500 million pounds of copper 
within 17 million tons grading 1.5% copper. Over half of this high grade copper 
mineralization is contained in the East and E-2 deposits.

Nevada Copper has embarked on a systematic fast-track program to develop its 
advanced stage Pumpkin Hollow Property into Nevada's next copper mine. 
Concurrent with the resource delineation drilling program, metallurgical, 
geotechnical, hydrological and environmental baseline data is being processed. 
The current drilling program will support an updated resource estimate and 
economic feasibility study scheduled to commence in late 2007.

The Pumpkin Hollow project is under the supervision of Gregory French, CPG 
#10708, a Qualified Person as defined in Canadian National Instrument 43-101, 
who is responsible for the preparation of the technical information in this 
news release. All assaying and whole rock geochemistry is processed at the 
American Assay Laboratories (AAL) in Reno, Nevada. Samples are delivered from 
the project core logging facility to AAL by Nevada Copper or AAL personnel. A 
Quality Assurance and Quality Control Assay Protocol have been implemented 
whereby blanks and standards are inserted into the assay stream and check 
samples are sent to Chemex-Reno and Inspectorate-Reno laboratories.

Nevada Copper has 35.5 million shares outstanding and is well financed with no 
debt. For additional information about Nevada Copper please visit our website 
at www.nevadacopper.com.

NEVADA COPPER CORP.

Giulio T. Bonifacio, President & CEO

This news release includes certain statements that may be deemed 
"forward-looking statements". All statements in this release, other than 
statements of historical facts, including the likelihood of commercial mining 
and possible future financings are forward-looking statements. Although the 
Company believes the expectations expressed in such forward-looking statements 
are based on reasonable assumptions, such statements are not guarantees of 
future performance and actual results or developments may differ materially 
from those in the forward-looking statements. Factors that could cause actual 
results to differ materially from those in forward-looking statements include 
unsuccessful exploration results, changes in metals prices, changes in the 
availability of funding for mineral exploration, unanticipated changes in key 
management personnel and general economic conditions. Mining is an inherently 
risky business. Accordingly the actual events may differ materially from those 
projected in the forward-looking statements. For more information on the 
Company and the risks and challenges of its business, investors should review 
the Company's annual filings that are available at www.sedar.com.

- 30 -

CONTACT INFO:

Longview Capital Partners Incorporated
Eugene Toffolo
(604) 681-5755 or Toll Free: 1-877-687-5755

or

Nevada Copper Corp.
Susan L. Wilson
Corporate Communications
(604) 688-7508
Fax: (604) 681-0122
Email: info@nevadacopper.com
Website: www.nevadacopper.com

The TSX Venture Exchange has neither approved nor disapproved of the contents 
of this news release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS