Source	Marketwire
Date	07/03/2014
Time	06:03:35 AM

Company	 HIGHLAND COPPER COMPANY INC.
Title	Highland Provides Exploration Update from the White Pine North Project, 
Michigan





    CDNX Symbol: HI











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Highland Copper Company Inc.

TSX VENTURE SYMBOL: HI

July 3, 2014

Highland Provides Exploration Update from the White Pine North Project, Michigan


LONGUEUIL, QUEBEC--(Marketwired - July 3, 2014) - Highland Copper Company Inc. 
(TSX VENTURE:HI) ("Highland" or the "Company") is pleased to report the results 
from an initial exploration program conducted at the White Pine North Project 
located in the Upper Peninsula of Michigan, an area which has historically been 
one of the most important copper producing regions in the United States. Figure 
1 shows the projects in which Highland has an interest.

Highland has recently completed the interim closing of the acquisition of the 
White Pine copper project from Copper Range Company ("CRC"). The production at 
the former White Pine mine from 1952 to 1995 was 198,070,985 short tons 
averaging 1.14% copper, for approximately 4.5 billion pounds of copper. Mining 
ceased at White Pine in 1995 due largely to depressed copper prices, although 
significant amounts of mineralization remained, particularly to the north of 
the former mine ("White Pine North"). In 1995, CRC completed an estimate of 
resources at White Pine North based on 526 diamond drill holes. Highland's 
exploration efforts are focused on that area, with the objective of completing 
a National Instrument 43-101 compliant resource estimate in 2014.

White Pine North: Results from the 2014 Phase 1 In-Fill Drilling Program

During March and April 2014, Highland completed nine diamond drill holes 
totaling 8,853 meters using HQ core size at White Pine North (Figure 2). Three 
holes were cased for re-entry during the winter of 2015 because of spring 
melting. Highland also completed eleven wedges from eight holes to obtain 
approximately 435 kg of mineralized samples for metallurgical testing. Nine of 
the 12 holes were drilled vertically and core recoveries averaged over 99 
percent. Highland had designed its 2014 winter drilling program both to in-fill 
the historical drill grid and to expand the historical mineral resource area. 
The results from this first phase in-fill drilling program are consistent with 
results from previous CRC drill programs and confirmed copper- silver 
mineralization from adjacent historical drill holes.

Analytical results for the mineralized zones from the 2014 drilling program are 
summarized in Table 1.

Table 1.   Drill hole intersections from the White Pine North Project

/T/


True
Mineralized      From        To   Length  Thickness     Cu     Ag
Hole#             Unit       (m)       (m)      (m)        (m)      %    ppm

WP528      Upper Shale   603.125   604.940     1.82       1.82   1.01    5.7
Parting Shale   607.405   609.690     2.29       2.29   1.31   30.1

WP531      Upper Shale   547.033   548.895     1.86       1.86   1.18    7.2
Parting Shale   550.516   552.370     1.85       1.85   1.22   72.3

WP532      Upper Shale   866.085   868.385     2.30       2.30   1.05    5.9
Parting Shale   870.445   872.235     1.79       1.79   0.88   10.0

WP533      Upper Shale   901.015   902.980     1.97       1.97   1.04    7.3
Parting Shale   905.137   906.950     1.81       1.81   1.37   17.9

WP534      Upper Shale   791.560   793.975     2.42       2.09   1.30   8.12
Parting Shale   796.660   799.420     2.76       2.39   0.99   7.67

WP535      Upper Shale   179.565   180.875     1.31       1.31   1.11    8.5
Parting Shale   183.595   185.540     1.94       1.94   1.17   34.5

WP536      Upper Shale   928.370   929.705     1.34       1.34   0.88   3.90
Parting Shale   931.840   934.475     2.63       2.63   1.03  13.31

WP537      Upper Shale   328.640   329.690     1.05       1.05   0.90    6.1
Parting Shale   333.035   335.080     2.04       2.04   0.89    7.8

WP538      Upper Shale   813.010   814.776     1.77       1.77   0.68   4.34
Parting Shale   817.770   819.585     1.82       1.82   1.10   2.20

WP539      Upper Shale   991.485   993.655     2.17       2.06   0.23   3.65
Parting Shale   996.035   999.380     3.35       3.18   1.21  13.16

WP540      Upper Shale   886.897   888.365     1.47       1.46   1.31   9.68
Parting Shale   890.620   892.488     1.87       1.85   1.10  25.71

WP541      Upper Shale   876.330   877.770     1.44       1.43   1.16   9.09
Parting Shale   880.345   882.195     1.85       1.84   1.14  29.07

/T/

"Parting Shale" is an assemblage of five mineralized stratigraphic units at the 
base of the Nonesuch Formation. The Upper Shale consists of a similar 
assemblage of four mineralized units about 1.2 meters above the Parting Shale.

Activation Laboratories in Thunder Bay, Ontario, Canada (IOS 17025 
accreditation), assayed all samples using an ICP method tailored for the 
project samples, followed by a metallic procedure for samples containing at 
least 0.1% Cu. Highland applied industry standard QA/QC protocols to all steps 
of the drilling program.

White Pine North: Validation of Historical Drilling Data

In January 2014, Highland initiated an analytical program to validate 
historical assay results from 51 diamond drill holes completed by CRC in the 
White Pine North deposit. Thirty-six of these holes were drilled between 1958 
and 1980 with both BQ and AQ core, while the other 15 holes were drilled in 
1994 and 1995 with NQ core.

Highland's validation program used a 1/4 cut of the original whole core from 
883 historic sample intervals. This resampling duplicated the exact interval 
previously sampled and assayed in the historical programs. The remaining 1/4 of 
the original core was retained as reference material. The validation analytical 
technique used both a screen metallic assay method and a 2.5-gram digestion ICP 
assay method to determine total copper and results from both methods were in 
good agreement. The location of the validated historical drill holes is shown 
on Figure 2.

The results from this validation program are shown graphically on Figure 3. 
Highland considers the correlation between the historical and validation assays 
to be excellent, showing no bias between the two groups of assays. Highland 
plans to use the sample values from the original program for a future resource 
estimate at White Pine North.

Plans Going Forward

Highland plans to complete a second phase drilling program by boring ten drill 
holes totaling approximately 6,100 m, during the summer and fall of 2014. These 
drill holes will focus on the higher-grade central portion of the deposit.

Highland has retained G Mining Services Inc. to carry out a number of technical 
studies including metallurgy, infrastructure requirements and mining methods 
that are intended to be used in a future prefeasibility study. The Company has 
also retained the services of Golder Associates to initiate hydrological 
studies of the area overlaying the White Pine North deposit.

Qualified Person

The technical information contained in this news release has been approved by 
Carlos Bertoni, P.Geo. Highland's Project Manager. Mr. Bertoni is a qualified 
person as defined in NI 43-101.

ABOUT HIGHLAND

Highland Copper Company Inc. is a Canadian exploration company focused on 
exploring and developing copper projects in the Upper Peninsula of Michigan, 
U.S.A. For more information about the White Pine project refer to the 
"Technical Report on the White Pine Copper Property, White Pine, Michigan, USA" 
dated as of February 10, 2014 and filed on SEDAR (www.sedar.com) on April 3, 
2014. Highland has approximately $3.2 million in cash at June 30, 2014 and has 
96,966,745 issued and outstanding common shares listed on the TSXV under the 
symbol 'HI'. Additional information about Highland is available on the 
Company's website at www.highlandcopper.com and on SEDAR at www.sedar.com.

CAUTIONARY STATEMENT

Certain statements contained in this press release constitute forward looking 
information under the provisions of Canadian securities laws. Such statements 
include without limitation: the Company's plans and objectives to complete a 
current mineral resource and expand the historical estimate at White Pine 
North; statements about completing studies for a prefeasibility studies; the 
long-term potential of Highland's project; and other statements and information 
regarding anticipated results regarding the Company's operations and 
exploration. Such statements reflect the Company's views as at the date of this 
press release and are subject to certain risks, uncertainties and assumptions, 
and undue reliance should not be placed on such statements. Actual results may 
be materially different from those currently anticipated. Many factors, known 
and unknown could cause the actual results to be materially different from 
those expressed or implied by such forward looking statements. Such risks 
include, but are not limited to: the Company being unable to satisfy the 
remaining conditions to complete the final closing of the White Pine 
acquisition; further drilling will be required to confirm and expand the 
historical estimate as a current mineral resource, and there is no certainty 
that this can be accomplished; the availability of additional funds to complete 
the Company's planned exploration and development programs; mining risks; risks 
associated with governmental and environmental regulation and obtaining all the 
necessary permits for the development of the project; and risks associated with 
global economic growth. The Company does not intend, and does not assume any 
obligation, to update these forward-looking statements and information, except 
as required by law. Accordingly, readers are advised not to place undue 
reliance on forward-looking statements.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Figure 1, Figure 2 and Figure 3 are available at this address : 
http://media3.marketwire.com/docs/955650e_Figures.pdf

- 30 -

CONTACT INFO:

David Fennell, Executive Chairman
+1.450.677.2455

or

James Crombie, Interim President
+1.450.677.2455
info@highlandcopper.com
www.highlandcopper.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=489362139