Source	CANADA NEWSWIRE
Date	07/03/2014
Time	09:06:58 AM

Company	 Golden Band Resources Inc.
Title	Golden Band Reports Assay Results From Spring 2014 Decade Gold Mine
Drilling





    CDNX Symbol: GBN











Press Release	




" BC-GoldenBand-AssayRslts   07-03 1100
News release via Canada NewsWire, Calgary 403-269-7605 -ME-

Attention Business  Editors:
^Golden Band Reports Assay Results From Spring 2014 Decade Gold Mine
Drilling@

GBN: TSX Venture Exchange
SASKATOON, July 3, 2014 /CNW/ - Golden Band Resources Inc. (GBN:TSXV)
announced today the assay results from the drilling program completed in May,
2014 on the Company's 100%-owned Decade gold deposit located in the La Ronge
Gold Belt of Saskatchewan (see previous news releases of January 29, 2014 and
March 11, 2008). The following table summarizes the assay highlights.
Table 1: Decade Gold Deposit Assay Data - Results 2014 Spring Drilling
Program Summary of Aggregated Uncut Gold Results

_____________________________________________________________________
|         | Azimuth |  Dip    |Drillhole|From | To  |Downhole| Assay  |
|Drillhole|(degrees)|(degrees)|  Depth  | (m) | (m) |Interval|(g/t Au)|
|         |         |         |   (m)   |     |     |  (m)   |        |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-44-14 |   148.7 |   -44.9 |   46.65 |21.00|25.00|   4.00 |   0.51 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |   45.73 |24.00|28.00|   4.00 |   2.43 |
|DC-45-14 |   145.3 |   -45.1 |_________|_____|_____|________|________|
|         |         |         |includes |25.00|26.00|   1.00 |   4.05 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |   44.82 |17.60|23.00|   5.40 |  23.77 |
|DC-46-14 |   140.8 |   -44.7 |_________|_____|_____|________|________|
|         |         |         |Includes |17.60|19.10|   1.50 |  81.96 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |   44.82 |15.00|22.00|   7.00 |   0.56 |
|DC-47-14 |   139.1 |   -43.9 |_________|_____|_____|________|________|
|         |         |         |Includes |18.00|19.00|   1.00 |   1.41 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-48-14 |   146.6 |   -44.2 |   48.78 |18.00|22.00|   4.00 |   1.56 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-49-14 |   147.3 |   -43.4 |   69.21 |41.00|47.00|   6.00 |   0.36 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |   69.21 |43.50|46.00|   2.50 |   0.61 |
|DC-50-14 |   147.6 |   -44.1 |_________|_____|_____|________|________|
|         |         |         |         |61.75|63.50|   1.75 |   1.00 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-51-14 |   148.9 |   -46.5 |   38.41 |24.90|26.50|   1.60 |   0.39 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-52-14 |   145.9 |   -45.1 |   41.77 |   No Significant Intervals  |
|_________|_________|_________|_________|_____________________________|
|DC-53-14 |   148.0 |   -45.1 |   41.77 |14.60|21.30|   6.70 |   0.21 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |   57.01 |46.10|49.50|   3.40 |  18.96 |
|DC-54-14 |   147.2 |   -44.5 |_________|_____|_____|________|________|
|         |         |         |Includes |46.10|47.00|   0.90 |  65.24 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |         |59.00|61.00|   2.00 |   0.52 |
|         |         |         |         |_____|_____|________|________|
|         |         |         |         |61.50|62.20|   0.70 |   2.33 |
|         |         |         |         |_____|_____|________|________|
|DC-55-14 |   145.4 |   -50.7 |  113.72 |69.00|70.00|   1.00 |   1.03 |
|         |         |         |         |_____|_____|________|________|
|         |         |         |         |70.90|72.70|   1.80 |   1.04 |
|         |         |         |         |_____|_____|________|________|
|         |         |         |         |88.20|90.50|   2.30 |   0.61 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-56-14 |   148.7 |   -46.8 |  111.89 |84.50|87.00|   2.50 |   1.29 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-57-14 |   147.5 |   -48.9 |   96.65 |66.50|67.70|   1.20 |   1.84 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-58-14 |   329.3 |   -48.4 |   78.35 |60.80|63.50|   2.70 |   0.34 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-59-14 |   329.5 |   -48.6 |   78.35 |49.90|50.70|   0.80 |   7.17 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |   87.50 |53.90|56.70|   2.80 |   2.62 |
|DC-60-14 |   328.7 |   -49.1 |_________|_____|_____|________|________|
|         |         |         |Includes |54.90|55.90|   1.00 |   7.07 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-61-14 |   329.6 |   -49.1 |   90.55 |60.00|61.70|   1.70 |   1.67 |
|_________|_________|_________|_________|_____|_____|________|________|
|DC-62-14 |   328.9 |   -50.9 |   99.70 |   No Significant Intervals  |
|_________|_________|_________|_________|_____________________________|
|         |         |         |         |56.00|58.00|   2.00 |   0.50 |
|DC-63-14 |   331.3 |   -48.1 |  105.79 |_____|_____|________|________|
|         |         |         |         |75.00|78.00|   3.00 |   0.50 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |         |23.40|23.70|   0.30 |   3.69 |
|         |         |         |   99.70 |_____|_____|________|________|
|DC-64-14 |   331.1 |   -46.3 |         |83.30|87.70|   4.40 |  13.34 |
|         |         |         |_________|_____|_____|________|________|
|         |         |         |Includes |84.50|85.50|   1.00 |  44.42 |
|_________|_________|_________|_________|_____|_____|________|________|
|         |         |         |         |76.70|78.70|   2.00 |   0.49 |
|DC-65-14 |   327.8 |   -47.0 |   90.55 |_____|_____|________|________|
|         |         |         |         |79.70|81.70|   2.00 |   0.38 |
|_________|_________|_________|_________|_____|_____|________|________|

The spring 2014 drilling program at the former Decade mine consisted of
22 diamond drillholes (NQ-diameter) totalling 1,600.93 m. Drillhole spacing
were typically 12.5 m apart, with the objective to test for:
1. The existence of a southwest zone down-plunge for an earlier high
grade drill hole intersect,
2. The possible existence of higher grade mineralization down plunge
of the mine workings,
3. The possible existence of higher grade mineralization to the
northeast of the mine workings,
4. The possible existence of a new zone to the far northeast of the
existing mine workings.
Golden Band is encouraged by these initial results which indicate that
additional higher-grade, near-surface gold occurrences exist than what were
previously indicated and that these gold zones could potentially be available
for near-term production as part of the Company's plans to re-start gold
production using its Jolu mill.
The former Decade mine workings are only 275 metres from the Company's
Jolu gold mill, and 600 metres from the former Jolu gold mine, all 100%-owned
by Golden Band. The Decade area was discovered in 1944 and saw limited
underground operations in the 1970's and 1990's. The deepest portion of the
existing development is approximately 50 m below surface and certain portions
of the gold mineralization were drill tested in the 1990's to about 100-150 m
below surface.
QA/QC A total of 831 samples were analyzed at Golden Bands' on-site
laboratory; 77 samples were re-assayed as duplicates, 58 sample standards and
blanks were routinely inserted into the sample stream and 61 samples were
assayed via the "Total Pulp Metallics" method. An additional 55 samples were
selected from the mineralized intervals and were sent to TSL Laboratories in
Saskatoon, Saskatchewan, which is an ISO/IEC accredited facility, as an
independent check of samples that occur within the significantly mineralized
zone (the results from these independent checks on assay results are pending).
Frank Hrdy, P.Geo., (APEGS) Consulting Geologist, has acted as the
Qualified Person as defined in National Instrument 43-101 for this disclosure
and has reviewed and approved the scientific and technical information
contained in this release.
About Golden Band Resources Inc. Golden Band Resources Inc. is a gold
producer operating in the La Ronge gold belt in northern Saskatchewan and is
listed on the TSX Venture Exchange in Canada under the symbol GBN. Commercial
production was declared on April 1, 2011. The Company has recently suspended
mining operations ( see news release of June 30, 2014) but has been actively
exploring the La Ronge Gold Belt since 1994 and has assembled a land package
of 870 km2, including 13 known gold deposits and five former producing mines,
being Jolu, Decade, Star Lake, EP and Komis.
On behalf of the Board of Directors of Golden Band Resources Inc.,
"Paul Saxton" Paul Saxton, CEO
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Caution Regarding Forward-Looking Information and Statements: This news
release includes certain forward-looking statements or information. All
statements other than statements of historical fact included in this release,
including, without limitation, statements regarding the future exploration
plans, restructuring of operations, estimates of production, costs of
production, the sufficiency and availability of capital and financing and
other future plans, objectives or expectations of Golden Band Resources Inc.
(Company) are forward-looking statements that involve various risks and
uncertainties. There can be no assurance that such statements will prove to be
accurate and actual results and future events could differ materially from
those anticipated in such statements. Important factors that could cause
actual results to differ materially from the Company's plans or expectations
include risks relating to the actual results of operations, current
exploration activities, fluctuating gold prices, possibility of equipment
breakdowns and delays, cost overruns, general economic, market or business
conditions, regulatory changes, timeliness of government or regulatory
approvals and other risks detailed herein and from time to time in the filings
made by the Company. The Company makes all reasonable efforts to update its
corporate information on a timely basis.
The TSX Venture Exchange has not reviewed and does not accept
responsibility for the adequacy or accuracy of this release.
SOURCE Golden Band Resources Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2014/03/c9578.html

-0-                           07/03/2014
/For further information:
Investor Relations: 604-682-6852  Email: info(at)goldenbandresources.com
Web: www.goldenbandresources.com
/
(GBN. GBRIF)

CO:  Golden Band Resources Inc.
ST:  Saskatchewan
IN:  MNG OTC
SU:  DSC

-30-