Source	Filing Services Canada
Date	07/03/2014
Time	08:03:08 AM

Company	 TOSCA MINING CORP.
Title	Tosca Announces Drilling Results from Carol Copper Project





    CDNX Symbol: TSQ











Press Release	




SOURCE: Filing Services Canada
Date: 07/03/2014
Time: 11:03:00

Company: TOSCA MINING CORP.
Title:Tosca Announces Drilling Results from Carol Copper Project (TSQ - TSXV) 
TSXV SYMBOL: TSQ


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Tosca Mining Corp.
TSXV SYMBOL: TSQ
Thursday, July 03, 2014 - 11:03 AM

Original Source Location: 
http://fscwire.com/newsrelease/tosca-announces-drilling-results-carol-copper-pro
ject

Tosca Announces Drilling Results from Carol Copper Project


Vancouver, British Columbia (FSCwire) - Tosca Mining Corp (TSQ-TSX-V, 
TSMNF:OTCBB, TQ4:FSE), announces that it has received analytical results from 
core samples obtained from a recently completed drill program on its Carol 
Copper project, located in Sonora, Mexico.



Six drill holes, totaling of 577 metres, were drilled to investigate the 
continuity and extent of skarn mineralization encountered in surface trenches 
and outcrop. Drilling tested a target area measuring 875 metres in length.



All holes encountered moderately to strongly altered skarn zones. The Company 
is in the process of correlating surface data with the drill results.



A total of 400 samples (including blanks and standards) were sent for analysis 
with core samples ranging in length from 0.5 to 2 metres. Values received 
ranged from trace to 0.288 g/t gold, trace to 9.2 g/t silver, trace to 2.39% 
copper, trace to 0.10 % lead and trace to 1.06 % zinc.



In general, mineralization is localized over narrow widths. The widest 
intervals encountered in core were from hole 5, which intersected 0.98 % zinc 
over 2 metres from 6 to 8 metres depth and 0.29 % copper over 3 metres from 26 
to 29 metres depth.



Fracture controlled mineralization combined with geochemistry indicates that 
the skarn formation was subjected to significant leaching and subsequent 
remobilization that has resulted in the copper/silver/gold/lead/zinc 
mineralization being concentrated in a zone at or near surface. The controls on 
the location of the higher grade mineralization intersected in the trenches 
remains to be fully understood.



About the Carol Copper Project



The Carol Copper project covers over 750 hectares and is located in southern 
Sonora State, Mexico. It is approximately five km northeast of the producing 
Piedras Verdes copper mine, Mexicos third largest. Tosca has the right to 
acquire a 100 percent interest in the Carol project under an option agreement 
further described in its Oc. 14, 2013, news release.



Ian Foreman, P.Geo., president of Alta Vista Ventures and independent to Tosca, 
is the Qualified Person, as defined by NI 43-101, for the Carol Project and is 
responsible for the technical information in this news release.



Samples from Carol were prepared and analyzed by IPL Inspectorate in their 
facilities in Mexico and Vancouver, respectively. Samples generally consisted 
of 1-3 kg of material. Gold, silver, copper, lead and zinc were analyzed as 
part of a multi-element ICP package using an aqua regia digestion. Over limit 
samples with greater than 1% Cu, Pb and Zn were re-analyzed using ore grade 
detection limits.



On behalf of the Board of Directors,



"Ron Shenton"



Ron Shenton
President & CEO
Tosca Mining Corp.




Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.


Statements in this press release, other than purely historical information, 
including statements relating to the Company's future plans and objectives or 
expected results, may include forward-looking statements. Forward-looking 
statements are based on numerous assumptions and are subject to all of the 
risks and uncertainties inherent in resource exploration and development. As a 
result, actual results may vary materially from those described in the 
forward-looking statements.







To view this press release as a PDF file, click onto the following link:
http://www.fscwire.com/sites/default/files/news_release_pdf/tosca07032014.pdf
Source: Tosca Mining Corp. (TSX Venture:TSQ, FWB:TQ4) 
http://www.toscamining.com/s/Home.asp

Maximum News Dissemination by FSCwire. http://www.fscwire.com
Copyright - (C)2014  Filing Services Canada Inc.