Source	CANADA NEWSWIRE
Date	07/03/2014
Time	08:13:39 AM

Company	 Midnight Sun Mining Corp.
Title	Midnight Sun Drills 14.2 Metres Grading 5.71% Copper at Solwezi





    CDNX Symbol: MMA











Press Release	




" BC-MidnightSun-Drilling   07-03 1100
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Midnight Sun Drills 14.2 Metres Grading 5.71% Copper at Solwezi@

VANCOUVER, July 3, 2014 /CNW/ - Midnight Sun Mining Corp. (the "Company"
or "Midnight Sun") (TSX-V: MMA) announces the results for the recently
completed core drilling program on the Solwezi copper property in northwest
Zambia. The drill program was undertaken in April and May 2014 and consisted
of 739 metres HQ core drilled in 12 holes.
Highlights of significant, near surface copper mineralization include the
following:
--  5.71% copper over 14.2 metres, including 9.58% copper over 7.2
metres in drill hole SLZ-DD-14-010;
--  5.08% copper over 8.0 metres in drill hole SLZ-DD-14-005; and
--  6.27% copper over 4.5 metres in drill hole SLZ-DD-14-001.
Note: The above reported lengths are intercept lengths and not estimated
true widths
The recent drill program targeted an area of the Solwezi property located
approximately 10km southwest of the Kansanshi mine, the largest copper mine in
Africa, which is operated by First Quantum Minerals (FQM-T). This program was
designed to expand the area of high grade copper mineralization and locate
primary copper mineralization.
"These results continue to confirm the presence of high grade, near
surface, oxide copper mineralization in this location," commented Bob
Sibthorpe, President and CEO. "The Company is actively reviewing the
information provided by these latest results to further delineate the
geological model and design a follow up exploration program to expand the
known mineralized areas and identify the source of this high grade copper."
Copper mineralization is mainly in the form of malachite, a mineral
comprised of 57.48% copper and often associated with acid leaching operations.
An image highlighting the area targeted by this core drill program, tables
listing full information on all drilling to date, including reverse
circulation ("RC") drilling, and location maps are available on the Company's
website at www.midnightsunmining.com.
The following table summarizes the assay results of the recently
completed 12 drill holes:

___________________________________________________________________
|Hole (number sign)       |From (m)|To (m)|Interval (m)|True width(x) 
(m)|Copper %|
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-001|  13.50 |18.00 |      4.50  |        3.60   |   6.27 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-002|   0.00 |13.00 |     13.00  |       10.40   |   0.06 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-003|  10.00 |19.95 |      9.95  |        7.96   |   0.50 |
|_____________|________|______|____________|_______________|________|
|and          |  29.40 |37.00 |      7.60  |        6.08   |   0.46 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-004|  17.35 |17.75 |      0.40  |        0.32   |   1.40 |
|_____________|________|______|____________|_______________|________|
|and          |  43.00 |43.90 |      0.90  |        0.72   |   0.51 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-005|  21.70 |29.70 |      8.00  |        6.40   |   5.08 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-006|   14.0 | 24.0 |      10.0  |         8.0   |   0.08 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-007|   8.00 |13.90 |      5.90  |        4.70   |   1.15 |
|_____________|________|______|____________|_______________|________|
|and          |  17.50 |48.00 |     30.50  |       24.40   |   0.55 |
|_____________|________|______|____________|_______________|________|
|including    |  33.50 |37.50 |      4.00  |        3.20   |   3.17 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD14--008|   6.00 |12.50 |      6.50  |        5.20   |   0.49 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-009|  12.00 |23.60 |     11.60  |        9.28   |   0.34 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-010|  12.00 |26.20 |     14.20  |       11.36   |   5.71 |
|_____________|________|______|____________|_______________|________|
|including    |  12.00 |19.20 |      7.20  |        5.76   |   9.58 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-011|  24.00 |26.60 |      2.60  |        2.08   |   0.26 |
|_____________|________|______|____________|_______________|________|
|SLZ-DD-14-012|  10.00 |26.00 |     16.00  |       12.80   |   0.29 |
|_____________|________|______|____________|_______________|________|
(x) True widths are estimated to be between 75-85% of reported intervals
for all core holes and were estimated by cross sectional analysis.
All drilling was carried out by Layne Drilling Zambia and assaying was
performed by Genalysis Laboratory Services, an accredited lab located in
Australia. Minor silver values were associated with the higher grade copper
samples.
The Company's technical report, dated July 27, 2013 on the Solwezi
property entitled "Technical Report on the Geology and Exploration Summary of
the Solwezi Group of Prospecting Licences," prepared in accordance with
National Instrument 43-101, is available on the company's website, as well as
on SEDAR at www.sedar.com.
Qualified Control/Quality Assurance: Samples obtained during core
drilling were transported directly to Genalysis Laboratories in Chingola,
Zambia by Midnight Sun personnel for sample preparation. Samples were sorted,
dried, crushed, and pulped before being sent to Perth, Australia for final
chemical analysis using ICP-MS methods. All samples returning >20,000 ppm Cu
were automatically re-checked by Genalysis. Genalysis is a fully accredited
Laboratory and sample duplicates, standards and blanks were inserted by
Genalysis and verified by the qualified person. All assays received from the
2013 reverse circulation drill program in excess of 2% copper were tested for
acid solubility and these generally exceeded 95% acid soluble copper.
Qualified Person: Warren Robb, P.Geo, a Qualified Person under NI 43-101,
has reviewed and approved the technical data and contents of this release.
About Midnight Sun: Midnight Sun is a mineral exploration company with an
African focus. The Company has entered into a definitive agreement to option a
60% interest in the Solwezi Licences in Zambia. This option agreement is a
part of an ongoing strategic alliance with Kam Chuen Resource Holdings Ltd.
Kam Chuen holds an exclusive prospecting license portfolio of over 150
exploration permits covering over 100,000 km2 in five African countries. Kam
Chuen has agreed to provide Midnight Sun full access to its property
portfolio, as well as first right of refusal regarding the optioning of any of
Kam Chuen's exploration licenses, and in exchange, Midnight Sun has agreed to
offer Kam Chuen technical expertise in the management and selection of
properties.
ON BEHALF OF THE BOARD
Robert Sibthorpe B.Sc.(Geology), M.B.A. President & CEO
NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS
THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS NEWS RELEASE.
This news release includes certain statements that may be deemed
"forward-looking statements." All statements in this release, other than
statements of historical facts, are forward-looking statements. Although the
Company believes the expectations expressed in such forward-looking statements
are based on reasonable assumptions, such statements are not guarantees of
future performance and actual results or developments may differ materially
from those in the forward-looking statements. Factors that could cause actual
results to differ materially from those in forward-looking statements include,
changes in market conditions, unsuccessful exploration results, changes in the
price of gold, unanticipated changes in key management personnel and general
economic conditions. Mining exploration and development is an inherently risky
business. Accordingly, the actual events may differ materially from those
projected in the forward-looking statements. This list is not exhaustive of
the factors that may affect any of the Company's forward-looking statements.
These and other factors should be considered carefully and readers should not
place undue reliance on the Company's forward-looking statements. The Company
does not undertake to update any forward-looking statement that may be made
from time to time by the Company or on its behalf, except in accordance with
applicable securities laws.
SOURCE Midnight Sun Mining Corp.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2014/03/c9614.html

Image with caption: "Midnight Sun Mining Corp. (CNW Group/Midnight Sun Mining
Corp.)". Image available at:
http://photos.newswire.ca/images/20140703_C9614_PHOTO_EN_41944.jpg

-0-                           07/03/2014
/For further information:

Al Fabbro Director Tel: 604-351-8850
/
(MMA.)

CO:  Midnight Sun Mining Corp.
ST:  British Columbia
IN:  MNG
SU:  DSC

-30-