Source	Marketwire
Date	07/08/2014
Time	04:00:29 AM

Company	 SAMA RESOURCES INC./RESSOURCES SAMA INC.
Title	Sama Resources Announces Up to 92.9% Graphite Concentrate Purity on 
Initial Metallurgical Testing at the Lola Graphite Deposit, Republic of Guinea, 
West Africa





    CDNX Symbol: SME











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Sama Resources Inc.

TSX VENTURE SYMBOL: SME

July 8, 2014

Sama Resources Announces Up to 92.9% Graphite Concentrate Purity on Initial 
Metallurgical Testing at the Lola Graphite Deposit, Republic of Guinea, West 
Africa


MONTREAL, QUEBEC--(Marketwired - July 8, 2014) - Sama Resources Inc./Ressources 
Sama Inc. ("Sama" or the "Company") (TSX VENTURE:SME) is pleased to announce 
that the first metallurgical test performed at Activation Laboratories Ltd., 
Thunder Bay, Canada ("ActLab") has returned high quality Graphite concentrate 
with up to 96% graphite recovery. This metallurgical test is the first of a 
series of proposed laboratory tests in order to define the grade and recovery 
of the final graphite concentrate.

The maiden test was performed on the two prominent mineralised facies of the 
deposit: the oxide material (first 20 meters ("m") from surface of totally to 
partially weathered material (saprolite)) and the underlying non-oxide material 
(below 20m).

The maiden metallurgical batch test on the oxide material returned a recovery 
to rougher concentrate of 96% of graphite flakes, producing a final table 
graphite concentrate having 60% of jumbo and large size flakes showing 92.9% 
and 90% graphite content respectively. Table 1 summarizes the findings.

Furthermore, the obtained concentrate was analysed for a series of elements to 
check for any possible contaminants, the assay data in Table 2 shows that the 
concentrates contained very low levels of minor elements.

"We are pleased with these impressive results from the initial test. It is a 
clear indication of the very high potential of the Lola Graphite 
mineralization," commented Dr. Marc-Antoine Audet, President and CEO of Sama. 
"A series of additional tests are planned in order to refine and further 
improve the already excellent recovery and grade of the graphite concentrate," 
Dr. Audet added.

Sama will continue to define and develop the Lola Graphite project on its own, 
however it is currently pursuing discussions for a partnership with known 
graphite developers and producers in order to accelerate the path to production.

Sama has launched a 4,000m drilling program designed to establish the mineral 
resources within the oxide material with its two 100% owned Jacro drill rigs.

/T/


Table 1: Metallurgical results of the maiden test at ActLab
on the oxide and non-oxide mineralised material at the
Lola Graphite deposit.

-----------------------------------------------------------
Oxide material
-----------------------------------------------------------
Flake Size          Distribution %    Graphite Content, %Cg
-----------------------------------------------------------
+50 mesh (jumbo)             29.2%                    92.9%
-----------------------------------------------------------
+80 mesh (large)             30.8%                    90.0%
-----------------------------------------------------------
+150 mesh                    17.9%                    80.4%
-----------------------------------------------------------
-150 mesh                    22.2%                    71.0%
-----------------------------------------------------------

-----------------------------------------------------------
Non-Oxide material
-----------------------------------------------------------
Flake Size          Distribution %     Graphite Content %Cg
-----------------------------------------------------------
+50 mesh (jumbo)             20.4%                    89.4%
-----------------------------------------------------------
+80 mesh (large)             25.6%                    84.7%
-----------------------------------------------------------
+150 mesh                    22.7%                    76.0%
-----------------------------------------------------------
-150 mesh                    31.3%                    73.9%
-----------------------------------------------------------


Table 2: Trace element analysis of the produced table graphite concentrate:
ppm: part per million


----------------------------------------------------------------------------
Element
Material/        Chromium Cobalt Copper Lead Molybdenum Nickel Vanadium Zinc
Fraction              ppm    ppm    ppm  ppm        ppm    ppm      ppm  ppm
----------------------------------------------------------------------------
Oxide material
----------------
+50 mesh (Jumbo)       20    6.4     52 2.54       1.63   10.5      2.7   11
+80 mesh (large)       32    9.8     81    4       2.97   17.9      1.6   17
+150 mesh              49   12.3    118 6.24       4.33   32.4        8   24
-150 mesh              62   13.8    140 7.25       6.05   40.4      1.3   27
Non-oxide
material
----------------
+50 mesh (Jumbo)       69   5.28     77 9.11       16.6   55.2     46.2   74
+80 mesh (large)       85   15.2    125 8.64         44   88.5      4.9  114
+150 mesh              76   19.3    218 17.7        126    106     22.4  127
-150 mesh              60     21    596 22.9        198    122       11  153

----------------------------------------------------------------------------

/T/

The Graphite Project is 100% owned by Sama Resources Guinea SARL, a fully owned 
subsidiary of the Company. The Graphite Project is located near the town of 
Lola in eastern Guinea and within 50 km from the border with Cote d'Ivoire.

Additional details for the Lola Graphite project can be viewed in the Sama's 
updated compilation at: 
http://www.samaresources.com/i/pdf/Sama_Corporate_Presentation.pdf

The technical information in this release has been reviewed and approved by Dr. 
Marc-Antoine Audet, P.Geo and President and CEO of Sama and by Dr. Phillip 
Mackey, P.Eng., a metallurgical consultant, both acting as qualified persons as 
defined by NI 43-101 Standards of Disclosure for Mineral Projects.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements Certain of the statements made and information 
contained herein are "forward-looking statements" within the meaning of 
Canadian securities legislation or "forward-looking information" within the 
meaning of the Ontario Securities Act and the Securities Act (British 
Columbia).  This includes statements concerning the Company's plans at its 
mineral properties, which involve known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company, or industry results, to vary or be materially different from 
any future results, performance or achievements expressed or implied by such 
forward-looking statements or forward-looking information. Information 
regarding drilling results may also be deemed to be forward-looking statements 
or forward-looking information in that they reflect a prediction of what may be 
found to be present when and if a project is actually developed.

Forward-looking statements and forward-looking information are subject to a 
variety of risks and uncertainties which could cause actual events or results 
to differ from those reflected in the forward-looking statements or 
forward-looking information, including, without limitation, the availability of 
financing for activities, risks and uncertainties relating to the 
interpretation of drill results and the estimation of mineral resources and 
reserves, the geology, grade and continuity of mineral deposits, the 
possibility that future exploration, development or mining results will not be 
consistent with the Company's expectations, metal price fluctuations, 
environmental and regulatory requirements, availability of permits, escalating 
costs of remediation and mitigation, risk of title loss, the effects of 
accidents, equipment breakdowns, labour disputes or other unanticipated 
difficulties with or interruptions in exploration or development, the potential 
for delays in exploration or development activities, the inherent uncertainty 
of cost estimates and the potential for unexpected costs and expenses, 
commodity price fluctuations, currency fluctuations, expectations and beliefs 
of management and other risks and uncertainties.

In addition, forward-looking statements and forward-looking information are 
based on various assumptions. Should one or more of these risks and 
uncertainties materialize, or should underlying assumptions prove incorrect, 
actual results may vary materially from those described in forward-looking 
information or forward-looking statements. Accordingly, readers are advised not 
to place undue reliance on forward-looking statements or forward-looking 
information. Except as required under applicable securities legislation, the 
Company undertakes no obligation to publicly update or revise forward-looking 
statements or forward-looking information, whether as a result of new 
information, future events or otherwise.

- 30 -

CONTACT INFO:

Sama Resources Inc./Ressources Sama Inc.
Dr. Marc-Antoine Audet
President and CEO
(514) 726-4158

or

Sama Resources Inc./Ressources Sama Inc.
Mr. Matt Johnston
(604) 443-3835 or Toll Free: 1 (877) 792-6688, Ext. 4
www.samaresources.com

INDUSTRY: Financial Services - Venture Capital, Manufacturing and Production - 
Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=489671457


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Sama Resources Inc.

TSX VENTURE SYMBOL: SME

July 8, 2014

Sama Resources Announces Up to 92.9% Graphite Concentrate Purity on Initial 
Metallurgical Testing at the Lola Graphite Deposit, Republic of Guinea, West 
Africa


MONTREAL, QUEBEC--(Marketwired - July 8, 2014) - Sama Resources Inc./Ressources 
Sama Inc. ("Sama" or the "Company") (TSX VENTURE:SME) is pleased to announce 
that the first metallurgical test performed at Activation Laboratories Ltd., 
Thunder Bay, Canada ("ActLab") has returned high quality Graphite concentrate 
with up to 96% graphite recovery. This metallurgical test is the first of a 
series of proposed laboratory tests in order to define the grade and recovery 
of the final graphite concentrate.

The maiden test was performed on the two prominent mineralised facies of the 
deposit: the oxide material (first 20 meters ("m") from surface of totally to 
partially weathered material (saprolite)) and the underlying non-oxide material 
(below 20m).

The maiden metallurgical batch test on the oxide material returned a recovery 
to rougher concentrate of 96% of graphite flakes, producing a final table 
graphite concentrate having 60% of jumbo and large size flakes showing 92.9% 
and 90% graphite content respectively. Table 1 summarizes the findings.

Furthermore, the obtained concentrate was analysed for a series of elements to 
check for any possible contaminants, the assay data in Table 2 shows that the 
concentrates contained very low levels of minor elements.

"We are pleased with these impressive results from the initial test. It is a 
clear indication of the very high potential of the Lola Graphite 
mineralization," commented Dr. Marc-Antoine Audet, President and CEO of Sama. 
"A series of additional tests are planned in order to refine and further 
improve the already excellent recovery and grade of the graphite concentrate," 
Dr. Audet added.

Sama will continue to define and develop the Lola Graphite project on its own, 
however it is currently pursuing discussions for a partnership with known 
graphite developers and producers in order to accelerate the path to production.

Sama has launched a 4,000m drilling program designed to establish the mineral 
resources within the oxide material with its two 100% owned Jacro drill rigs.

/T/


Table 1: Metallurgical results of the maiden test at ActLab
on the oxide and non-oxide mineralised material at the
Lola Graphite deposit.

-----------------------------------------------------------
Oxide material
-----------------------------------------------------------
Flake Size          Distribution %    Graphite Content, %Cg
-----------------------------------------------------------
+50 mesh (jumbo)             29.2%                    92.9%
-----------------------------------------------------------
+80 mesh (large)             30.8%                    90.0%
-----------------------------------------------------------
+150 mesh                    17.9%                    80.4%
-----------------------------------------------------------
-150 mesh                    22.2%                    71.0%
-----------------------------------------------------------

-----------------------------------------------------------
Non-Oxide material
-----------------------------------------------------------
Flake Size          Distribution %     Graphite Content %Cg
-----------------------------------------------------------
+50 mesh (jumbo)             20.4%                    89.4%
-----------------------------------------------------------
+80 mesh (large)             25.6%                    84.7%
-----------------------------------------------------------
+150 mesh                    22.7%                    76.0%
-----------------------------------------------------------
-150 mesh                    31.3%                    73.9%
-----------------------------------------------------------


Table 2: Trace element analysis of the produced table graphite concentrate:
ppm: part per million


----------------------------------------------------------------------------
Element
Material/        Chromium Cobalt Copper Lead Molybdenum Nickel Vanadium Zinc
Fraction              ppm    ppm    ppm  ppm        ppm    ppm      ppm  ppm
----------------------------------------------------------------------------
Oxide material
----------------
+50 mesh (Jumbo)       20    6.4     52 2.54       1.63   10.5      2.7   11
+80 mesh (large)       32    9.8     81    4       2.97   17.9      1.6   17
+150 mesh              49   12.3    118 6.24       4.33   32.4        8   24
-150 mesh              62   13.8    140 7.25       6.05   40.4      1.3   27
Non-oxide
material
----------------
+50 mesh (Jumbo)       69   5.28     77 9.11       16.6   55.2     46.2   74
+80 mesh (large)       85   15.2    125 8.64         44   88.5      4.9  114
+150 mesh              76   19.3    218 17.7        126    106     22.4  127
-150 mesh              60     21    596 22.9        198    122       11  153

----------------------------------------------------------------------------

/T/

The Graphite Project is 100% owned by Sama Resources Guinea SARL, a fully owned 
subsidiary of the Company. The Graphite Project is located near the town of 
Lola in eastern Guinea and within 50 km from the border with Cote d'Ivoire.

Additional details for the Lola Graphite project can be viewed in the Sama's 
updated compilation at: 
http://www.samaresources.com/i/pdf/Sama_Corporate_Presentation.pdf

The technical information in this release has been reviewed and approved by Dr. 
Marc-Antoine Audet, P.Geo and President and CEO of Sama and by Dr. Phillip 
Mackey, P.Eng., a metallurgical consultant, both acting as qualified persons as 
defined by NI 43-101 Standards of Disclosure for Mineral Projects.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Forward-Looking Statements Certain of the statements made and information 
contained herein are "forward-looking statements" within the meaning of 
Canadian securities legislation or "forward-looking information" within the 
meaning of the Ontario Securities Act and the Securities Act (British 
Columbia).  This includes statements concerning the Company's plans at its 
mineral properties, which involve known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company, or industry results, to vary or be materially different from 
any future results, performance or achievements expressed or implied by such 
forward-looking statements or forward-looking information. Information 
regarding drilling results may also be deemed to be forward-looking statements 
or forward-looking information in that they reflect a prediction of what may be 
found to be present when and if a project is actually developed.

Forward-looking statements and forward-looking information are subject to a 
variety of risks and uncertainties which could cause actual events or results 
to differ from those reflected in the forward-looking statements or 
forward-looking information, including, without limitation, the availability of 
financing for activities, risks and uncertainties relating to the 
interpretation of drill results and the estimation of mineral resources and 
reserves, the geology, grade and continuity of mineral deposits, the 
possibility that future exploration, development or mining results will not be 
consistent with the Company's expectations, metal price fluctuations, 
environmental and regulatory requirements, availability of permits, escalating 
costs of remediation and mitigation, risk of title loss, the effects of 
accidents, equipment breakdowns, labour disputes or other unanticipated 
difficulties with or interruptions in exploration or development, the potential 
for delays in exploration or development activities, the inherent uncertainty 
of cost estimates and the potential for unexpected costs and expenses, 
commodity price fluctuations, currency fluctuations, expectations and beliefs 
of management and other risks and uncertainties.

In addition, forward-looking statements and forward-looking information are 
based on various assumptions. Should one or more of these risks and 
uncertainties materialize, or should underlying assumptions prove incorrect, 
actual results may vary materially from those described in forward-looking 
information or forward-looking statements. Accordingly, readers are advised not 
to place undue reliance on forward-looking statements or forward-looking 
information. Except as required under applicable securities legislation, the 
Company undertakes no obligation to publicly update or revise forward-looking 
statements or forward-looking information, whether as a result of new 
information, future events or otherwise.

- 30 -

CONTACT INFO:

Sama Resources Inc./Ressources Sama Inc.
Dr. Marc-Antoine Audet
President and CEO
(514) 726-4158

or

Sama Resources Inc./Ressources Sama Inc.
Mr. Matt Johnston
(604) 443-3835 or Toll Free: 1 (877) 792-6688, Ext. 4
www.samaresources.com

INDUSTRY: Financial Services - Venture Capital, Manufacturing and Production - 
Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=489671457