Source	MARKET NEWS
Date	07/08/2014
Time	05:55:47 AM

Company	 Sama Resources Inc./Ressources Sama Inc.
Title	Up To 92.9% 
Graphite Concentrate Purity On Initi





    CDNX Symbol: SME











Press Release	





SAMA RESOURCES INC ("SME-V")
- Up To 92.9% Graphite Concentrate Purity On Initial Metallurgical
- Testing At The Lola Graphite Deposit, Republic Of Guinea, West
- Africa

Sama Resources Inc./Ressources Sama Inc.("Sama" or the "Company")
is pleased to announce that the first metallurgical test performed at
Activation Laboratories Ltd., Thunder Bay, Canada ("ActLab") has
returned high quality Graphite concentrate with up to 96% graphite
recovery. This metallurgical test is the first of a series of proposed
laboratory tests in order to define the grade and recovery of the final
graphite concentrate.

The maiden test was performed on the two prominent mineralised
facies of the deposit: the oxide material (first 20 meters ("m") from
surface of totally to partially weathered material (saprolite)) and the
underlying non-oxide material (below 20m).

The maiden metallurgical batch test on the oxide material returned
a recovery to rougher concentrate of 96% of graphite flakes, producing
a final table graphite concentrate having 60% of jumbo and large size
flakes showing 92.9% and 90% graphite content respectively. Table 1
summarizes the findings.

Furthermore, the obtained concentrate was analysed for a series of
elements to check for any possible contaminants, the assay data in
Table 2 shows that the concentrates contained very low levels of minor
elements.

"We are pleased with these impressive results from the initial
test. It is a clear indication of the very high potential of the Lola
Graphite mineralization," commented Dr. Marc-Antoine Audet, President
and CEO of Sama. "A series of additional tests are planned in order to
refine and further improve the already excellent recovery and grade of
the graphite concentrate," Dr. Audet added.

Sama will continue to define and develop the Lola Graphite project
on its own, however it is currently pursuing discussions for a
partnership with known graphite developers and producers in order to
accelerate the path to production.

Sama has launched a 4,000m drilling program designed to establish
the mineral resources within the oxide material with its two 100% owned
Jacro drill rigs.

//st
Table 1: Metallurgical
results of the maiden
test at ActLab on
the oxide & non-oxide
mineralised material
at the Lola Graphite
deposit.

Oxide material
Flake Size                 Distribution %  Graphite Content, %Cg
+50 mesh (jumbo)                    29.2%                  92.9%
+80 mesh (large)                    30.8%                  90.0%
+150 mesh                           17.9%                  80.4%
-150 mesh                           22.2%                  71.0%

Non-Oxide material
Flake Size                 Distribution %   Graphite Content %Cg
+50 mesh (jumbo)                    20.4%                  89.4%
+80 mesh (large)                    25.6%                  84.7%
+150 mesh                           22.7%                  76.0%
-150 mesh                           31.3%                  73.9%
//et

//st
Table 2: Trace element
analysis of the produced
table graphite concentrate:
ppm: part per million

Element
Material/
Fraction
Chromium Cobalt Copper Lead Molybdenum Nickel Vanadium Zinc
ppm    ppm    ppm  ppm        ppm    ppm      ppm  ppm
Oxide material
+50 mesh
(Jumbo)    20   6.4      52 2.54       1.63   10.5      2.7   11
+80 mesh
(large)    32   9.8      81    4       2.97   17.9      1.6   17
+150 mesh   49  12.3     118 6.24       4.33   32.4        8   24
-150 mesh   62  13.8     140 7.25       6.05   40.4      1.3   27
Non-oxide material
+50 mesh
(Jumbo)    69  5.28      77 9.11       16.6   55.2     46.2   74
+80 mesh
(large)    85  15.2     125 8.64         44   88.5      4.9  114
+150 mesh   76  19.3     218 17.7        126    106     22.4  127
-150 mesh   60    21     596 22.9        198    122       11  153
//et

The Graphite Project is 100% owned by Sama Resources Guinea SARL, a
fully owned subsidiary of the Company. The Graphite Project is located
near the town of Lola in eastern Guinea and within 50 km from the
border with Cote d'Ivoire.

Additional details for the Lola Graphite project can be viewed in
the Sama's updated compilation at:
http://www.samaresources.com/i/pdf/Sama_Corporate_Presentation.pdf

The technical information in this release has been reviewed and
approved by Dr. Marc-Antoine Audet, P.Geo and President and CEO of Sama
and by Dr. Phillip Mackey, P.Eng., a metallurgical consultant, both
acting as qualified persons as defined by NI 43-101 Standards of
Disclosure for Mineral Projects.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Forward-Looking Statements Certain of the statements made and
information contained herein are "forward-looking statements" within
the meaning of Canadian securities legislation or "forward-looking
information" within the meaning of the Ontario Securities Act and the
Securities Act (British Columbia).  This includes statements concerning
the Company's plans at its mineral properties, which involve known and
unknown risks, uncertainties and other factors which may cause the
actual results, performance or achievements of the Company, or industry
results, to vary or be materially different from any future results,
performance or achievements expressed or implied by such
forward-looking statements or forward-looking information. Information
regarding drilling results may also be deemed to be forward-looking
statements or forward-looking information in that they reflect a
prediction of what may be found to be present when and if a project is
actually developed.

Forward-looking statements and forward-looking information are
subject to a variety of risks and uncertainties which could cause
actual events or results to differ from those reflected in the
forward-looking statements or forward-looking information, including,
without limitation, the availability of financing for activities, risks
and uncertainties relating to the interpretation of drill results and
the estimation of mineral resources and reserves, the geology, grade
and continuity of mineral deposits, the possibility that future
exploration, development or mining results will not be consistent with
the Company's expectations, metal price fluctuations, environmental and
regulatory requirements, availability of permits, escalating costs of
remediation and mitigation, risk of title loss, the effects of
accidents, equipment breakdowns, labour disputes or other unanticipated
difficulties with or interruptions in exploration or development, the
potential for delays in exploration or development activities, the
inherent uncertainty of cost estimates and the potential for unexpected
costs and expenses, commodity price fluctuations, currency
fluctuations, expectations and beliefs of management and other risks
and uncertainties.

In addition, forward-looking statements and forward-looking
information are based on various assumptions. Should one or more of
these risks and uncertainties materialize, or should underlying
assumptions prove incorrect, actual results may vary materially from
those described in forward-looking information or forward-looking
statements. Accordingly, readers are advised not to place undue
reliance on forward-looking statements or forward-looking information.
Except as required under applicable securities legislation, the Company
undertakes no obligation to publicly update or revise forward-looking
statements or forward-looking information, whether as a result of new
information, future events or otherwise.

TEL:   (514) 726-4158  Dr. Marc-Antoine Audet, President and CEO

































































TEL:   (604) 443-3835  Mr. Matt Johnston
TSX Venture closing price for SME-V
Date: 2014/07/07
Closing Price: 0.30

TEL: 1 (877) 792-6688 Ext 4
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1418800015TS11418800704-05543120140708