Source	Marketwire
Date	07/09/2014
Time	05:45:10 AM

Company	 TASMAN METALS LTD.
Title	Tasman Precipitates Heavy Rare Earth Element Concentrate and Provides 
Flowsheet Development Update for Norra Karr Project, Sweden





    CDNX Symbol: TSM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Tasman Metals Ltd.

TSX VENTURE SYMBOL: TSM
FRANKFURT SYMBOL: T61
NYSE MKT SYMBOL: TAS

July 9, 2014

Tasman Precipitates Heavy Rare Earth Element Concentrate and Provides Flowsheet 
Development Update for Norra Karr Project, Sweden


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 9, 2014) - Tasman Metals Ltd. 
("Tasman" or the "Company") (TSX VENTURE:TSM)(FRANKFURT:T61)(NYSE MKT:TAS). Mr 
Mark Saxon, President & CEO, is pleased to announce the precipitation of a 
heavy rare earth element (REE) rich concentrate as part of the 
hydrometallurgical testwork program underway on the 100%-owned Norra Karr heavy 
REE project in Sweden. Preparation of this concentrate is the final step in 
defining the Norra Karr flowsheet, and marks a significant milestone in the 
Company's metallurgical programs. An update on recent beneficiation progress is 
also provided.

Beneficiation and hydrometallurgy testwork has been completed by various 
internationally recognized laboratories and delivered data of a quality 
suitable for the Norra Karr Pre-Feasibility Study (PFS) which remains in 
progress.

Norra Karr is one of the most significant heavy REE deposits in the world, with 
a simple and predictable REE mineralogy. Previous testwork has shown that the 
only REE-bearing mineral with significant abundance at Norra Karr is the 
zirconosilicate eudialyte. Eudialyte is weakly magnetic (paramagnetic) and 
dissolves rapidly in weak acid at low temperature. This simplicity has allowed 
for an uncomplicated flowsheet to be developed, that can be achieved with 
standard mining/processing equipment and widely available chemicals.

Highlights

/T/

--  Crushing and grinding characteristics of the Norra Karr mineralized
material are now well known. A grind size of 60 micron has been chosen
which provides adequate liberation of the REE-bearing mineral
(eudialyte) that can easily be achieved through standard commercial
equipment;
--  Extensive testwork and optimization of single-stage magnetic separation
has been completed by equipment manufacturer Metso Minerals and
metallurgical laboratories of the Geological Survey of Finland (GTK).
This optimization has increased REE recovery in beneficiation to in
excess of 86% in less than 35% of the original mass, such that flotation
is no longer deemed necessary as was envisaged under the Norra Karr
Preliminary Economic Assessment (PEA) published June 2013. Magnetic
separation shall use standard commercial equipment and does not require
process chemicals;
--  Extensive hydrometallurgical research has been completed by ANSTO
Minerals which has tested/optimized a process of sulphuric acid
leaching, leach solution purification, REE solvent extraction and
precipitation of an REE-concentrate. Sulphuric acid was chosen due to
its relatively low cost, and its widespread availability in Sweden. A
railway line which passes only 25km from Norra Karr already transports
bulk sulphuric acid;
--  Under the hydrometallurgical process developed, leaching is undertaken
at ambient temperature and pressure. High temperature roasting is not
required to dissolve eudialyte;
--  The improved magnetic separation has significantly reduced the amount of
sulphuric acid-consuming gangue minerals within the eudialyte-rich
mineral concentrate. As a result, sulphuric acid consumption per tonne
of ore has fallen to 85 kg/tonne from the 150 kg/tonne envisaged in the
PEA;
--  A heavy REE enriched oxalate has been precipitated by ANSTO during
continuous testing with a grade of approximately 45% REE. The high value
heavy REE dysprosium (Dy) contributes 4.8% of the REE content. This
oxalate can be easily calcined to a high grade REE-oxide (REO) subject
to customer requirements;
--  Despite Norra Karr being a high-grade zirconium (Zr) and hafnium (Hf)
deposit, under the metallurgical process being modeled for the PFS, the
recovery of Zr is not being considered. Zr shall pass with Hf and
niobium (Nb) to a by-product that shall be stockpiled for potential
future recovery;

/T/

"Tasman staff and their consultants have worked hard to optimize the processing 
conditions for the Norra Karr deposit for our Pre-Feasibility Study" said Mark 
Saxon, Tasman's President and CEO. "We have extensively tested our 
metallurgical process and have achieved the significant milestone of 
precipitating an attractive high purity heavy REE product. Eudialyte was once 
believed to be a difficult mineral to process, but due to the excellent work by 
Tasman's team, robust process pathways are now available. We congratulate our 
team on the milestones they have achieved and are proud to have taken the 
project from discovery to this significant milestone."

With the guidance of Tasman's PFS consultants, samples used in testwork were 
carefully chosen from drill core to be representative of the Norra Karr 
deposit, both in grade and ore type distribution. A 5 tonne sample was 
homogenized then crushed and ground to the target P80 size at a facility in 
Germany. This bulk sample has a total rare earth oxide (TREO) grade of 0.61% 
and has provided a consistent material source for all testing. Where possible, 
registered REE standards have been inserted to ensure assay quality, and mass 
balance calculations have consistently been completed to confirm results.

Magnetic Separation Tests

Due to the paramagnetic nature of eudialyte, magnetic separation has been the 
focus for beneficiation research. Following multi-laboratory testing of 
magnetic separation equipment, the Metso Minerals continuous HGMS was chosen as 
most promising for optimization. Metso has worked with the metallurgical 
division of the Geological Survey of Finland (GTK) to undertake both batch and 
continuous testing under a wide range of operating parameters (flow velocity, 
magnetic field strength, load density, grind size). The optimum operating 
conditions have been determined, which have been applied repeatedly under 
continuous tests, the results being both stable and predictable.

Recovery in single pass magnetic separation consistently exceeded 86% recovery 
in 35% of the original mass. Size-by-size assaying and Mineral Liberation 
Analysis (MLA) has demonstrated that approximately 70% of the 14% REE lost to 
the tailings stream is in the fine grained (below 20 micron) fraction, which 
should be recoverable by a combination of hydrocyclone separation to recover 
the fine particles and small volume magnetic separation scavenging step.

Mineralogy of the mineral concentrate from the HGMS is comprised predominantly 
of the paramagnetic minerals eudialyte (16.0%) and aegirine (56.9%), with minor 
contribution of the felsic minerals feldspar (11.1%), nepheline (6.0%) and 
zeolite (4.9%). The very low content of nepheline and zeolite in this mineral 
concentrate is significant, as both minerals are soluble in sulphuric acid and 
therefore increase acid consumption.

Hydrometallurgy Tests

ANSTO Minerals in Australia were engaged by Tasman in 2013 to optimize and 
finalize the Norra Karr hydrometallurgical flowsheet that had been initiated by 
other parties. ANSTO are an acknowledged world leader in REE hydrometallurgy, 
and were chosen due to their experience in similar projects. Work was initiated 
on a poorer quality mineral concentrate, but moved to the higher quality 
material described above in 2014.

ANSTO's work has defined a stable and repeatable hydrometallurgical process 
that has been applied in continuous operation through to precipitation of an 
REE oxalate. ANSTO's extensive experience with silica management has allowed 
for any process-related issues to be quickly resolved.

In previous testwork, various acids were trialed, each giving certain process 
benefits. ANSTO has used only sulphuric acid for leaching due to its low cost, 
and widespread availability in Sweden. A railway line which passes only 25km 
from Norra Karr already transports bulk sulphuric acid that is produced in 
copper smelting in Sweden and Finland.

Due to the improved mineral concentrate and ANSTO's superior process control, 
sulphuric acid consumption (including residual acid) in leaching has been 
reduced to 85 kg per tonne of ore. This is a very significant reduction, as PEA 
financial modeling indicates sulphuric acid is the single largest processing 
cost.

Following leaching, purification of the leach solution via chemical and pH 
control was completed to remove various impurities including silica, iron and 
manganese. The concentration of REE's in solution was increased using 
conventional solvent extraction, which were then precipitated in oxalate form 
through the addition of oxalic acid. The composition of this REE-oxalate is 
provided in Table 1 below. This oxalate is strongly enriched in the high value 
heavy REE's, which contribute 44% of the material.

The recovery of REE's achieved in the hydrometallurgy stage (leaching to 
precipitation) is approximately 90%, with heavy REE (not including yttrium) 
recovery consistently exceeding light REE recovery.

"The results described above come at an important stage of the development of 
Norra Karr, and will be incorporated into the PFS models" said Mark Saxon, 
Tasman's President and CEO. "Norra Karr is unusual in its heavy REE enrichment, 
and furthermore has the unique advantage of lying within a first world 
mining-friendly country with easy access to road, rail, power, process 
chemicals, skilled labor and the large European market."

/T/

----------------------------------------------------------------------------
Element    Weight % REE in Oxalate Solid   REO as % of TREO
----------------------------------------------------------------------------
La                    4.94                     10.7           LIGHT REE
--------------------------------------------------------------
Ce                   10.75                     23.2
--------------------------------------------------------------
Pr                    1.46                     3.1
--------------------------------------------------------------
Nd                    6.76                     14.5
--------------------------------------------------------------
Sm                    1.65                     3.5
----------------------------------------------------------------------------
Eu                    0.27                     0.6            HEAVY REE
--------------------------------------------------------------
Gd                    1.66                     3.5
--------------------------------------------------------------
Tb                    0.35                     0.7
--------------------------------------------------------------
Dy                    2.19                     4.6
--------------------------------------------------------------
Ho                    0.49                     1.0
--------------------------------------------------------------
Er                    1.29                     2.7
--------------------------------------------------------------
Tm                    0.18                     0.4
--------------------------------------------------------------
Yb                    1.14                     2.4
--------------------------------------------------------------
Lu                    0.15                     0.3
--------------------------------------------------------------
Y                   12.21                     28.6
----------------------------------------------------------------------------
Total REE               45.48                    100 %
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Light REE %                                        55.1
----------------------------------------------------------------------------
Heavy REE %                                        44.9
----------------------------------------------------------------------------
Table 1: Composition of REE-oxalate precipitated by ANSTO Minerals from
Norra Karr project, with REO relative abundance (when converted to oxide)

/T/

Norra Karr lies 15km NNE of the township of Granna and 300km SW of the capital 
Stockholm in mixed forestry and farming land, and is secured to Tasman with a 
25-year Mining Lease. The short time taken from discovery to Mining Lease 
granting demonstrates the efficiency and advantage of operating in a 
jurisdiction with a strong and transparent Mining Act and a long term 
association with resource industries. The project is proximal to road, rail, 
power and operating ports, plus skilled personnel, minimizing the need for 
offsite infrastructure to be built by the Company.

Tasman's Qualified Person, Mr. Mark Saxon, President and Chief Executive 
Officer of Tasman and a Fellow of the Australasian Institute of Mining and 
Metallurgy and Member of the Australian Institute of Geoscientists, has 
reviewed and verified the contents of this news release.

About Tasman Metals Ltd.

Tasman is a Canadian mineral development company focused on critical metals 
including Rare Earth Elements (REE's) and tungsten (W) in Scandinavia. Tasman 
is listed on the TSX Venture Exchange under the symbol "TSM" and the NYSE-MKT 
under the symbol "TAS". REE and tungsten demand is increasing, due to the 
metals' unique properties that make them essential for high technology and 
industry. Since over 95% of REE and 80% of tungsten supply is sourced from 
China, the European Commission promotes policy to develop domestic supply of 
critical metals to ensure the security of industry. Tasman receives research 
funding from the European Commission.

Tasman's exploration portfolio is uniquely placed, with the capacity to deliver 
strategic metals from politically stable, mining friendly jurisdictions with 
developed infrastructure and skills. The Company's Norra Karr and Olserum 
projects in Sweden are two of the most significant known heavy REE resources in 
the world, enriched in dysprosium, yttrium, terbium and neodymium. The Company 
is now focused on the safe, sustainable and responsible development of its 
Scandinavian mineral portfolio.

On behalf of the Board,

Mark Saxon, President & CEO
The TSX Venture Exchange nor its Regulation Services Provider (as that term is 
defined in the policies of the TSX Venture Exchange), the NYSE - MKT nor the 
Frankfurt Stock Exchange accepts responsibility for the adequacy or accuracy of 
this news release.

Cautionary Note to U.S. Investors Concerning Mineral Resources and Reserves. In 
this news release, the definition of "mineral resources" is that used by the 
Canadian securities administrators and conforms to the definition utilized by 
CIM in the "CIM Standards on Mineral Resources and Reserves - Definitions and 
Guidelines" adopted on August 20, 2000 and amended December 11, 2005.

The standards employed in estimating the mineral resources referenced in this 
news release differ significantly from the requirements of the United States 
Securities and Exchange Commission (the "SEC") and the resource information 
reported may not be comparable to similar information reported by United States 
companies. The term "resources" does not equate to "reserves" and normally may 
not be included in documents filed with the SEC. "Resources" are sometimes 
referred to as "mineralization" or "mineral deposits." While the terms "mineral 
resource", "measured mineral resource", "indicated mineral resource" and 
"inferred mineral resource" are recognized and required by Canadian 
regulations, they are not defined terms under standards in the United States 
and normally are not permitted to be used in reports and registration 
statements filed with the SEC. The terms "mineral reserve," "proven mineral 
reserve" and "probable mineral reserve" are Canadian mining terms as defined in 
accordance with National Instrument 43-101 - Standards of Disclosure for 
Mineral Projects ("NI 43-101") and the CIM - CIM Definition Standards on 
Mineral Resources and Mineral Reserves, adopted by the CIM Council, as may be 
amended from time to time by the CIM. These definitions differ from the 
definitions in the United States Securities and Exchange Commission Industry 
Guide 7 ("SEC Industry Guide 7") under the Securities Act of 1933. Under 
Canadian rules, estimates of inferred mineral resources may not form the basis 
of feasibility or prefeasibility studies, except in rare cases. Disclosure of 
"contained ounces" in a resource is permitted disclosure under Canadian 
regulations; however, the SEC normally only permits issuers to report 
mineralization that does not constitute "reserves" by SEC standards as in place 
tonnage and grade without reference to unit measures.

The estimation of measured, indicated and inferred mineral resources involves 
greater uncertainty as to their existence and economic feasibility than the 
estimation of proven and probable reserves. U.S. investors are cautioned (i) 
not to assume that measured or indicated resources will be converted into 
reserves and (ii) not to assume that estimates of inferred mineral resources 
exist, are economically or legally minable, or will be upgraded into measured 
or indicated mineral resources. It cannot be assumed that the Company will 
identify any viable mineral resources on its properties or that any mineral 
reserves, if any, can be recovered profitably, if at all. As such, information 
contained in this news release and the documents incorporated by reference 
herein concerning descriptions of mineralization and resources under Canadian 
standards may not be comparable to similar information made public by United 
States companies in SEC filings.

Cautionary Statements. Certain statements found in this release may constitute 
forward-looking statements as defined in the U.S. Private Securities Litigation 
Reform Act of 1995. Forward-looking statements reflect the speaker's current 
views with respect to future events and financial performance and include any 
statement that does not directly relate to a current or historical fact. Such 
statements reflect the current risks, uncertainties and assumptions related to 
certain factors including, without limitations, competitive factors, general 
economic conditions, customer relations, uncertainties related to the 
availability and costs of financing, unexpected geological conditions, success 
of future development initiatives, imprecision in resource estimates, ability 
to obtain necessary permits and approvals, relationships with vendors and 
strategic partners, the interest rate environment, governmental regulation and 
supervision, seasonality, technological change, changes in industry practices, 
changes in world metal markets, changes in equity markets, environmental and 
safety risks, and one-time events. Should any one or more of these risks or 
uncertainties materialize, or should any underlying assumptions prove 
incorrect, actual results may vary materially from those described herein. 
Forward-looking statements cannot be guaranteed and actual results may vary 
materially due to the uncertainties and risks, known and unknown, associated 
with such statements. Shareholders and other readers should not place undue 
reliance on "forward-looking statements," as such statements speak only as of 
the date of this release.

- 30 -

CONTACT INFO:

Investor Information
Tasman Metals Ltd.
Jim Powell, V.P. - Corporate Development
+ 1 (647) 478 8952
jpowell@tasmanmetals.com

or

Tasman Metals Ltd.
Mariana Bermudez
+1 (604) 685 9316
info@tasmanmetals.com
www.tasmanmetals.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=489844537