Source	Marketwire
Date	07/09/2014
Time	05:50:07 AM

Company	 COLOMBIAN MINES CORPORATION
Title	Colombian Mines Drills High Grade Mineralization to 25.85 g/T Gold 
Equivalent in First Hole from Sabana Blanca Adit





    CDNX Symbol: CMJ











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Colombian Mines Corporation

TSX VENTURE SYMBOL: CMJ
FRANKFURT SYMBOL: X6C

July 9, 2014

Colombian Mines Drills High Grade Mineralization to 25.85 g/T Gold Equivalent 
in First Hole from Sabana Blanca Adit


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 9, 2014) - Colombian Mines 
Corporation (TSX VENTURE:CMJ)(FRANKFURT:X6C) ("Colombian Mines" or the 
"Company") is pleased to announce that drill hole 1360-01 intersected a high 
grade mineralized interval averaging 13.01 grams of gold per metric tonne (g/T 
Au), 24.60 grams silver per metric tonne (g/T Ag), 7.10.% copper (Cu) and 1.70% 
zinc (Zn) with  a combined gold equivalent grade (g/T AuEq) of 25.85 grams per 
metric tonne within a larger 31.8 meter interval averaging 2.75 g/T AuEq. Table 
1 below, summarizes salient intercepts in hole 1360-01.

Table 1. Summary Drill Intercepts Sabana Blanca Creek Outcrop Area

/T/

----------------------------------------------------------------------------
----------------------------------------------------------------------------
Intercept
Hole               From    To     Length     Au     Ag     Cu     Zn   AuEq
(m)    (m)        (m)    g/T    g/T      %      %  (g/T)
----------------------------------------------------------------------------
----------------------------------------------------------------------------
1360-01               0   31.8       31.8   1.56   4.22   0.59   0.32   2.75
----------------------------------------------------------------------------
including             0   18.4       18.4   2.25   6.03   1.01   0.46   4.23
----------------------------------------------------------------------------
including           4.3    9.5        5.2   4.39   7.01   1.67   0.56   7.51
----------------------------------------------------------------------------
including           4.3    5.3        1.0  13.01  24.60   7.10   1.70  25.85
----------------------------------------------------------------------------
----------------------------------------------------------------------------
(i)Note: Gold Equivalent values were calculated using the following, Gold
$40.99 / gram, Silver $0.63 / gram, Copper $3.04 / pound, Zinc $0.96 / pound
and full recovery of the metal value.

/T/

Discussion and Results

Hole 1360-01 is the first hole drilled from the Sabana Blanca Adit and 
intersected disseminated, semi-massive and massive mineralization comprised of 
chalcopyrite, sphalerite, pyrite and pyrrhotite as disseminated to massive 
sulfide zones in a gangue of multi-phased crystalline quartz hosted by the same 
metamorphosed volcanic rocks known to host the Sabana Blanca Zone elsewhere.

Hole 1360-01 provided an excellent test of a portion of the mineralized zone 
and corresponds very well with the Company's underground channel sampling, but 
did not cross the entire mineralized zone due to limitations of underground 
access at this point. As discussed in the Company's previous release, drilling 
from the 1360 meter level, the Sabana Blanca Adit elevation, provides access to 
drill test high grade targets the Company has not been able to test with 
surface based drilling.

These highly successful results confirm the value of drilling from the Sabana 
Blanca Adit and the Company looks forward to completing additional holes from 
the adit in the near future.

Notes and Comments

All drill intercepts reported herein are drilled intercept length. Insufficient 
drilling has been done in this drill area to reasonably determine the geometry 
and estimate true width of the above intercepts.

Gold equivalency calculations are included to more clearly present the 
approximate value of the high grade polymetallic mineralization at El Dovio and 
assume; 100% recovery, metal prices of Gold; $1275.00 per troy ounce ($40.99 / 
gram), Silver; $19.75 per troy ounce ($0.63 / gram), Copper; $3.04 / pound and 
Zinc; $0.96 / pound. One troy ounce contains approximately 31.1 grams and one 
percent equals approximately 22 pounds per metric tonne.

About El Dovio: The Company's 100% owned El Dovio project covers gold rich, 
high grade poly metallic mineralization where the Company owns 100% of both the 
surface and mineral rights covering the entire zone of mineralization and 
surrounding areas. Outcropping mineralization and drilling to date indicate the 
main Sabana Blanca zone is a feeder or "stringer zone" that may have a strike 
length of one (1) kilometer or more that is beneath a sedimentary horizon 
highly prospective for the development of Volcanogenic Massive Sulfide ("VMS") 
type deposits. Recent drilling in the Brazo 1 zone intersected bedded sulfide 
mineralization indicative of a VMS horizon that is interpreted to overlie the 
Sabana Blanca zone.

Preliminary metallurgical flotation studies on material from the Sabana Blanca 
adit resulted in recoveries of 96.4% of the contained gold, 97.8% of copper, 
91.1% of silver and 96.8% of zinc from a bulk sample with a calculated head 
grade of 5.3 g/T Au, 4.7 grams g/T Ag, 0.86% Cu and 1.12% Zn as announced in 
the Company's press release dated April 24, 2012 reported.

Sample Collection - Quality Control - Quality Assurance

The Company's samples are collected in accordance with accepted industry best 
practices. Core is transported from the site to the Company's core facility in 
Medellin, Colombia by Company personnel. After being logged, photographed, 
diamond saw cut and sampled, samples are delivered the SGS's Medellin 
laboratory for preparation and analyses, (ISO9001:2000). Gold is analyzed by 
fire assay with an ICP/AES finish. Silver and base metal analyses were 
determined with ICP/AES techniques. The Company maintains and continuously 
monitors its rigid QC-QA through insertion of a series of blank, duplicate, 
certified standard samples at a rate of 1:30 or higher into the sample stream.

Mr. Robert G. Carrington, P.Geo., a Qualified Person as defined by National 
Instrument 43-101 and President of the Company, has reviewed and verified the 
technical information in this news release.

About Colombian Mines Corporation: Colombian Mines Corporation is an aggressive 
exploration and development stage company and a "first mover" in Colombia. 
Developing shareholder value through exploration and development of key 
projects, the Company is also one of Colombia's leading "prospect generators". 
Additional information is available on our website at www.colombianmines.com.

Robert G. Carrington

President & CEO

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this release.

Forward-Looking Statement:

Some of the statements in this news release contain forward-looking information 
that involves inherent risk and uncertainty affecting the business of Colombian 
Mines Corporation. Actual results may differ materially from those currently 
anticipated in such statements.

- 30 -

CONTACT INFO:

Colombian Mines Corporation
Sharon Hebgin
Corporate Communications
(604) 649-9195 - Canada, (760) 668-7211 - United States
shebgin@colombianmines.com

or

Colombian Mines Corporation
Dave Cross
Chief Financial Officer and Corporate Secretary
(604) 669-0868
dcross@crossdavis.com
www.colombianmines.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=489812968