Source	MARKET NEWS
Date	07/10/2014
Time	06:40:33 AM

Company	 Columbus Gold Corporation
Title	Eastside 
Project In Nevada Yields 95% Gold Recov





    CDNX Symbol: CGT











Press Release	





COLUMBUS GOLD CORP ("CGT-V;CBGDF-0")
- Eastside Project In Nevada Yields 95% Gold Recoveries From
- Metallurgical Testing

Columbus Gold Corporation ("Columbus Gold") (CGT) is pleased to
report the results of initial metallurgical tests on gold and silver
mineralization at its Eastside gold project in Esmeralda County,
Nevada.

Fourteen samples of rotary drill cuttings were selected for the
initial metallurgical tests using 92 hour, cyanide-leach, bottle roll
tests. Testwork was performed by Kappes, Cassiday, and Associates (KCA)
in Reno, Nevada. The samples were selected to represent a wide range of
gold and silver grade, differing depths below the surface, differing
areas of the deposit, and differing oxidation.

One split of each of the fourteen samples was ground to 80%
passing 200 mesh. The average recovery from cyanide leaching of this
ground material was 95% for gold and 52% for silver. The gold
recoveries ranged from 85% to 99% and the silver recoveries ranged from
27% to 79%. The entire KCA report is available for review at the
following link: www.columbusgoldcorp.com/i/nr/2014-07-10-report.pdf.

Almost all gold mineralization drilled at Eastside is oxidized
with the exception of only one deep intercept in Hole ES-32 which was
unoxidized and sulfide-bearing, but is amenable to leaching with
cyanide as shown by the KCA leach results of the sample taken from the
965-970 ft (294-296 meters) deep intercept in vertical hole ES-32. The
gold recovery from this unoxidized sample was 95% and the silver
recovery was 79%.

In addition a second split of each of the 14 drill samples was
processed "as is", or exactly as collected at the drill, with no
grinding or crushing. These samples varied greatly from sample to
sample in the amount of coarse and fine material present. The largest
fragments of solid rock ranged up to 3/4 of an inch (19 mm) in size. On
the other hand, some of the samples had little rock above 1/2 inch in
size (12 mm). A visual estimate of the amount of coarse versus fine
material in each sample, and the maximum fragment sizes present, is
contained in the KCA report linked above.

The recoveries from the 14 "as is" samples by cyanide leaching for
92 hours averaged 57% for gold and 18% for silver. The range of
recoveries from the "as is" samples was extreme, ranging from 20% to
85% for gold, and from 6% to 52% for silver. The wide range in results
does not seem to be due to grade, depth, oxidation, or alteration type,
but rather to the variation in the amount of coarse material in the
samples. Further testing is in progress, beginning with screen analysis
of raw samples.

The purpose of metallurgical tests on "as is" materials is to
begin to understand if Eastside gold mineralization might be processed
by heap leach techniques, although it is impossible to predict actual
recoveries from such preliminary testing. Much larger samples, usually
obtained by core drilling, and metallurgical testing of that core,
including column leach tests, will be necessary before one can more
accurately predict heap leach recoveries and properly evaluate
crushing. Columbus management believes that these results are
sufficiently encouraging to proceed with further testing. Core drilling
is planned as part of the next drilling program currently being
permitted.

Andy Wallace is a Certified Professional Geologist (CPG) with the
American Institute of Professional Geologists and is the Qualified
Person under NI 43-101 who has reviewed and approved the technical
content of this press release. Mr. Wallace is a director of Columbus
Gold and the principal of Cordilleran Exploration Company (Cordex),
which is conducting exploration and project generation activities for
Columbus Gold on an exclusive basis.

ON BEHALF OF THE BOARD,
Robert F. Giustra, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This release contains forward-looking information and statements,
as defined by law including without limitation Canadian securities laws
and the "safe harbor" provisions of the US Private Securities
Litigation Reform Act of 1995 ("forward-looking statements"),
respecting drilling, testing, sampling, metallurgical studies,
potential mining methods, permitting, the apparent reason for a wide
range of recoveries and Columbus Gold's general exploration plans.
Forward-looking statements involve risks, uncertainties and other
factors that may cause actual results to be materially different from
those expressed or implied by the forward-looking statements, including
without limitation the ability to acquire necessary permits and other
authorizations; environmental compliance; cost increases; availability
of qualified workers and drill equipment; competition for mining
properties; risks associated with exploration projects, mineral reserve
and resource estimates (including the risk of assumption and
methodology errors); dependence on third parties for services;
non-performance by contractual counterparties; title risks; and general
business and economic conditions. Forward-looking statements are based
on a number of assumptions that may prove to be incorrect, including
without limitation assumptions about: general business and economic
conditions; the timing and receipt of required approvals; availability
of financing; power prices; ability to procure equipment and supplies
including without limitation drill rigs; and ongoing relations with
employees, partners and joint venturers. The foregoing list is not
exhaustive Columbus Gold undertakes no obligation to update any of the
foregoing except as required by law.


TEL:  604-634-0970  Columbus Gold Corporation
TSX Venture closing price for CGT-V
Date: 2014/07/09
Closing Price: 0.48

TEL:  1-888-818-1364
FAX:  (604) 634-0971
EMAIL:  info@columbusgroup.com
INTERNET:  www.columbusgroup.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1419000018TS11419001009-06390920140710