Source	Marketwire
Date	07/10/2014
Time	06:00:15 AM

Company	 COLUMBUS GOLD CORPORATION
Title	Columbus Gold's Eastside Project in Nevada Yields 95% Gold Recoveries from 
Metallurgical Testing





    CDNX Symbol: CGT











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Columbus Gold Corporation

TSX VENTURE SYMBOL: CGT

July 10, 2014

Columbus Gold's Eastside Project in Nevada Yields 95% Gold Recoveries from 
Metallurgical Testing


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 10, 2014) - Columbus Gold 
Corporation (TSX VENTURE:CGT) ("Columbus Gold") (CGT) is pleased to report the 
results of initial metallurgical tests on gold and silver mineralization at its 
Eastside gold project in Esmeralda County, Nevada.

Fourteen samples of rotary drill cuttings were selected for the initial 
metallurgical tests using 92 hour, cyanide-leach, bottle roll tests. Testwork 
was performed by Kappes, Cassiday, and Associates (KCA) in Reno, Nevada. The 
samples were selected to represent a wide range of gold and silver grade, 
differing depths below the surface, differing areas of the deposit, and 
differing oxidation.

One split of each of the fourteen samples was ground to 80% passing 200 mesh. 
The average recovery from cyanide leaching of this ground material was 95% for 
gold and 52% for silver. The gold recoveries ranged from 85% to 99% and the 
silver recoveries ranged from 27% to 79%. The entire KCA report is available 
for review at the following link: 
www.columbusgoldcorp.com/i/nr/2014-07-10-report.pdf.

Almost all gold mineralization drilled at Eastside is oxidized with the 
exception of only one deep intercept in Hole ES-32 which was unoxidized and 
sulfide-bearing, but is amenable to leaching with cyanide as shown by the KCA 
leach results of the sample taken from the 965-970 ft (294-296 meters) deep 
intercept in vertical hole ES-32. The gold recovery from this unoxidized sample 
was 95% and the silver recovery was 79%.

In addition a second split of each of the 14 drill samples was processed "as 
is", or exactly as collected at the drill, with no grinding or crushing. These 
samples varied greatly from sample to sample in the amount of coarse and fine 
material present. The largest fragments of solid rock ranged up to 3/4 of an 
inch (19 mm) in size. On the other hand, some of the samples had little rock 
above 1/2 inch in size (12 mm). A visual estimate of the amount of coarse 
versus fine material in each sample, and the maximum fragment sizes present, is 
contained in the KCA report linked above.

The recoveries from the 14 "as is" samples by cyanide leaching for 92 hours 
averaged 57% for gold and 18% for silver. The range of recoveries from the "as 
is" samples was extreme, ranging from 20% to 85% for gold, and from 6% to 52% 
for silver. The wide range in results does not seem to be due to grade, depth, 
oxidation, or alteration type, but rather to the variation in the amount of 
coarse material in the samples. Further testing is in progress, beginning with 
screen analysis of raw samples.

The purpose of metallurgical tests on "as is" materials is to begin to 
understand if Eastside gold mineralization might be processed by heap leach 
techniques, although it is impossible to predict actual recoveries from such 
preliminary testing. Much larger samples, usually obtained by core drilling, 
and metallurgical testing of that core, including column leach tests, will be 
necessary before one can more accurately predict heap leach recoveries and 
properly evaluate crushing. Columbus management believes that these results are 
sufficiently encouraging to proceed with further testing. Core drilling is 
planned as part of the next drilling program currently being permitted.

Andy Wallace is a Certified Professional Geologist (CPG) with the American 
Institute of Professional Geologists and is the Qualified Person under NI 
43-101 who has reviewed and approved the technical content of this press 
release. Mr. Wallace is a director of Columbus Gold and the principal of 
Cordilleran Exploration Company (Cordex), which is conducting exploration and 
project generation activities for Columbus Gold on an exclusive basis.

ON BEHALF OF THE BOARD,

Robert F. Giustra, Chairman & CEO

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This release contains forward-looking information and statements, as defined by 
law including without limitation Canadian securities laws and the "safe harbor" 
provisions of the US Private Securities Litigation Reform Act of 1995 
("forward-looking statements"), respecting drilling, testing, sampling, 
metallurgical studies, potential mining methods, permitting, the apparent 
reason for a wide range of recoveries and Columbus Gold's general exploration 
plans. Forward-looking statements involve risks, uncertainties and other 
factors that may cause actual results to be materially different from those 
expressed or implied by the forward-looking statements, including without 
limitation the ability to acquire necessary permits and other authorizations; 
environmental compliance; cost increases; availability of qualified workers and 
drill equipment; competition for mining properties; risks associated with 
exploration projects, mineral reserve and resource estimates (including the 
risk of assumption and methodology errors); dependence on third parties for 
services; non-performance by contractual counterparties; title risks; and 
general business and economic conditions. Forward-looking statements are based 
on a number of assumptions that may prove to be incorrect, including without 
limitation assumptions about: general business and economic conditions; the 
timing and receipt of required approvals; availability of financing; power 
prices; ability to procure equipment and supplies including without limitation 
drill rigs; and ongoing relations with employees, partners and joint venturers. 
The foregoing list is not exhaustive Columbus Gold undertakes no obligation to 
update any of the foregoing except as required by law.

- 30 -

CONTACT INFO:

Columbus Gold Corporation
Investor Relations
604-634-0970 or Toll Free: 1-888-818-1364
Fax: (604) 634-0971
info@columbusgroup.com
www.columbusgroup.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=489992949