Source	Marketwire
Date	07/03/2014
Time	12:13:04 PM

Company	 BEARING RESOURCES LTD.
Title	Bearing Provides Drill Results From Pedro Gold Project, Mexico





    CDNX Symbol: BRZ











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Bearing Resources Ltd.

TSX VENTURE SYMBOL: BRZ

July 3, 2014

Bearing Provides Drill Results From Pedro Gold Project, Mexico


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 3, 2014) - Bearing Resources 
Ltd. ("Bearing", or the "Company") (TSX VENTURE:BRZ) has received the drill 
results from Newmont de Mexico, S.A. de C.V ("Newmont"), a wholly owned 
subsidiary of Newmont Mining Corporation, from its recently completed drill 
program on Bearing's 100% owned Pedro property in Durango Mexico. Newmont 
terminated the option agreement on Pedro with an effective date of July 11, 
2014.

The drill program comprised 11 drill holes totalling 1,744 metres of which two 
holes (409 metres) were cored and the remaining drilled by reverse circulation. 
Areas tested included the HP breccia prospect and its northern extension; a 
distance of some three kilometres. The best results were encountered in hole 
LP-013-R that returned a core length of 10.5 metres grading 0.51 grams per 
tonne gold from silicified conglomerate of the Ahuichila Formation. Details of 
the recent drilling are presented below. Drill intervals reported are hole 
lengths and true thickness for hole LP-013-R is estimated to be close to the 
reported core length. Collar locations are presented at the end of this 
release. Results for all other holes were low to barren.

/T/


Table 1: Significant Intersections (Suffix R-
reverse circulation, D- core)

--------------------------------------------------
From        To    Length        Au
Hole             (m)       (m)       (m)     (g/T)
--------------------------------------------------
LP-007-R         4.5      16.5     12.00      0.23
--------------------------------------------------
LP-008-R        33.0      37.5      4.50      0.35
--------------------------------------------------
LP-010-R        31.5      37.5      6.00      0.21
--------------------------------------------------
LP-011-D         4.0       9.6      5.55      0.59
--------------------------------------------------
LP-013-R        51.0      61.5     10.50      0.51
--------------------------------------------------
LP-017-R       144.0     201.0     57.00      0.07
--------------------------------------------------

/T/

The HP Breccia prospect is defined by a gold soil anomaly (greater than 40 ppb 
gold) extending over a 1,800 metre x 600 metre area that coincides with exposed 
silicified conglomerate of the Ahuichila Formation. Drill results from this 
area (holes 7 through 15) in large part reflect the results from surface 
sampling. Gold is mostly associated with the Ahuichila conglomerate with no 
values being present within the underlying Caracol Formation. No source or 
feeder system for this stratabound gold has been identified. The northern 
extension of the HP breccia prospect located 2 kilometres to the north is 
underlain by volcanic rocks and Aurora Formation limestone and was tested by 
holes 16 and 17. The Aurora Formation is weakly mineralised throughout with 
hole 17 returning 57 metres averaging 70 ppb gold. The Company will continue to 
compile all results received from Newmont including surface geochemistry, 
geophysics and drilling. Additional targets on this large property have yet to 
be tested and the property remains in good standing.

QA/QC:

Drill samples and analytical data for the Pedro project were collected under 
the supervision of Newmont, using industry standard quality assurance/quality 
control protocols. Core holes began as HQ and were terminated as NQ. For 
reverse circulation drilling dry sampling was used for approx. 75% or more of 
drill samples. Dry sampling used a standard rotary cyclone capture with all 
drill cuttings passing through a 1/8th cut Gilson splitter before bagging for 
assay. Wet sampling methods were used in intervals with excessive ground water. 
A multi-stage sampling process was used for these samples including: 
rig-mounted rotary wet splitter making a 1/8th to 1/16th sample split depending 
on water quantity, sample bags within stainless steel baskets to catch all 
material and fluid passing through rotary wet splitter, flocculent was added to 
sample bags during and after sample collection to retain all solid materials. 
Wet samples were allowed to dry on-site to a semi-solid consistency. Samples 
were transported to ALS-Chemex's preparation lab in Zacatecas and gold was 
analyzed by fire assay and AAS from a 30 g nominal sample weight in ALS 
Chemex's analytical facilities in Vancouver, Canada.

/T/


Table 2: Drill Hole Locations (WGS84 Z13) (Suffix R- reverse circulation, D-
core)

----------------------------------------------------------------------------
Elev.                     Length
Area    Hole ID      Area  Easting Northing   (m) Azimuth Inclination    (m)
----------------------------------------------------------------------------
Pedro  LP-007-R     Pedro   584814  2854778  1643       0          90  106.5
----------------------------------------------------------------------------
Pedro  LP-008-R     Pedro   584759  2854708  1656       0          90  120.0
----------------------------------------------------------------------------
Pedro  LP-009-R     Pedro   584672  2854697  1615       0          90   70.5
----------------------------------------------------------------------------
Pedro  LP-010-R     Pedro   585007  2854820  1615       0          90  100.5
----------------------------------------------------------------------------
Pedro  LP-011-D     Pedro   585126  2854655  1608      60          70  207.4
----------------------------------------------------------------------------
Pedro  LP-012-R     Pedro   585093  2854855  1610       0          90  211.5
----------------------------------------------------------------------------
Pedro  LP-013-R     Pedro   585183  2854895  1605       0          90  121.5
----------------------------------------------------------------------------
Pedro  LP-014-R     Pedro   584795  2854951  1616      30          60  201.0
----------------------------------------------------------------------------
Pedro  LP-015-R     Pedro   584904  2855215  1593     210          60  202.5
----------------------------------------------------------------------------
Pedro  LP-016-D     Pedro   583400  2857321  1571     215          60  201.3
Norte
----------------------------------------------------------------------------
Pedro  LP-017-R     Pedro   583558  2857046  1582     230          60  201.0
Norte
----------------------------------------------------------------------------

/T/

Other Matters:

The Company is currently renegotiating its option on the Flume Gold project.

Robert Cameron, P.Geo., President and CEO who is a qualified person within the 
context of National Instrument 43-101, has read and takes responsibility for 
this news release.

About Bearing Resources

Bearing is a Canadian based precious and base metal exploration company with 
projects located in British Columbia, the Yukon and Mexico. In Mexico the 
Company owns the Pedro epithermal gold project while in British Columbia the 
Company has discovered a gold-bearing skarn system on its October Dome 
property. The Company's Mount Polley project is located in near Imperial Metals 
Corporation's ("Imperial") Mt. Polley copper-gold mine and includes a 
production royalty on the Boundary property. The Company also holds interests 
in projects in the Yukon including the Flume Project in the White Gold District.

BEARING RESOURCES LTD.

Robert Cameron, President & CEO

This news release includes certain "forward-looking statements" under 
applicable Canadian securities legislation. Such forward-looking statements or 
information, including but not limited to, those with respect to future 
exploration programs and venture arrangements involve known and unknown risks, 
uncertainties, and other factors which may cause the actual results, 
performance or achievements of Bearing to be materially different from any 
future results, performance or achievements expressed or implied by such 
forward-looking statements or information. Such factors include, among others, 
the actual prices of commodities, the factual results of current exploration, 
development and mining activities, changes in project parameters as plans 
continue to be evaluated, as well as those factors disclosed in documents filed 
from time to time with the securities regulators in the applicable Provinces of 
British Columbia and Alberta. Neither TSX Venture Exchange nor its Regulation 
Services Provider (as that term is defined in the policies of the TSX Venture 
Exchange) accepts responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Bearing Resources Ltd.
Robert Cameron
(604) 682-5546
rcameron@bearingresources.ca
www.bearingresources.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=489422477