Source	MARKET NEWS
Date	07/23/2014
Time	07:30:31 AM

Company	 Durango Resources Inc.
Title	Discovers 
Significant Gold Mineralization At Dec





    CDNX Symbol: DGO











Press Release	





DURANGO RESOURCES INC. ("DGO-V")
- Discovers Significant Gold Mineralization At Decouverte

Durango Resources Inc. (the "Company" or "Durango") is pleased to
report the assay / analytical results for its recently completed
exploration program on the Decouverte (Discovery) property in northern
Quebec. The results show gold values associated with quartz veining
along the contact zone between a pegmatitic granite and mafic volcanics
in the northeastern portion of the 5,600 ha property.

In June, Durango carried out follow up exploration from 2012 soil
samples and also conducted prospecting in the unexplored Target 2 area
located in the northeast part of the property where a cluster of medium
intensity anomalies 4km long and 2km wide are located. The program
included geological reconnaissance, grab and chip/channel sampling of
outcrops and float, soil geochemistry on alteration zones and
geochemical and geophysical anomalies which had been defined by Durango
from 2011 to 2013.

The new Target 2 area not previously noted or sampled lies along
the contact between an intrusive, pegmatitic, granite body and the host
mafic volcanics (basalts) lies along a recently constructed woods road,
was evaluated with five quartz vein (QV) samples and a number of both
basalt and pegmatite samples from outcrop. Two of the QV samples,
approximately 40 metres apart, gave values of 7.6 g/T and 6.24 g/T Au.
The first sample was a channel sample over 1m from a 5 cm quartz vein
in the basalts consisting of both quartz and basalt. The second sample
was a channel sample over 0.6 m of grey quartz up to 6 cm wide,
crosscutting the contact between the basalt and granite. No sulphides
were seen although limonite (Fe oxide) was noted in both samples. Both
samples gave anomalous values in Te (11.7, 59.6 ppm) and Bi (384, 371
ppm) possibly indicating that the gold may be associated with bismuth
tellurides. The other samples from the area, two from the host rocks
and the other from an area of quartz veining in the granites, gave
background to weakly anomalous (up to 26 ppb Au in the basalt) values.
Widespread quartz veining was noted extending for over 100 metres in
each direction along the contact, although these veins were not
sampled. Further exploration is required to evaluate this new area of
gold mineralization which is readily accessible on existing roads.

Chip / channel rock samples, both outcrop and float of gossanized
(Fe oxide), mineralized / altered zones which carried strong pyrite and
minor arsenopyrite (NR - June 26, 2014) in the central part of the
property, gave one anomalous value in gold of 119 ppb (in a float
boulder) with some base metal enrichment in the zones: highest - Cu -
387 ppm with a number ) 100 ppm; Zn - 1560 ppm (with Cd 4.7 ppm); Pb -
190 ppm (3 )100 ppm) with no correlation noted between Cu,Pb,Zn. Three
tungsten (W) values ) 100 ppm, were noted with two associated with
quartz veining (459, 5180 ppm) and one (134 ppm) associated with
basalt. Soils, which were taken in one small area in the southwest part
of the claims, gave no significant values in base or precious metals
(high of 6 ppb Au) although Ba values may be somewhat elevated () 500
ppm).

Marcy Kiesman, CEO, stated, "I am excited by the gold values along
the Hamburger Hill contact zone. This new gold discovery is located in
an area not previously sampled along a woods road, making it easily
accessible for further exploration. The discovery lies in Fugro
airborne magnetic anomaly Target Area 2 with the contact paralleling
the road for over two kilometres. Un-sampled quartz veining was noted
along the contact in the area of the discovery and 500 m further along
the road. Durango personnel will be returning to Decouverte to sample
all veins along the contact zone to further evaluate this new gold
discovery."
The technical information in this news release has been reviewed
and approved by Peter Dimmell, P.Geo., (NL, ON, QC), a "Qualified
Person" as defined in National Instrument 43-101.

About Decouverte

The Decouverte (Discovery) property is located 100km north of
Chibougamau, Quebec in the Frotet - Evans greenstone belt. Durango
carried out a helicopter borne DIGHEM EM/magnetic airborne geophysical
survey on the property in 2011 (NR Nov 24, 2011) and soil geochemistry
and prospecting covered target areas identified in the airborne survey
in 2013.

The geological setting is mainly mafic volcanics
(basalts/andesites) cut by granitic units. Strong alteration including
silicification and iron carbonate is noted. Significant soil values
included 174 ppb Au, 0.66 ppm Ag, 150 ppm Ni, 200 ppm Cu and 240 ppm
Ba. The property benefits from very favorable infrastructure including
road accessibility (within 10km of Route du Nord and a myriad of
logging roads), and a power line which bisects the property.

About Durango

Durango is a natural resources company engaged in the acquisition
and exploration of mineral properties. The Company has a 100% interest
in the Decouverte and Trove gold properties in the Abitibi of Quebec,
the McGillivray property in British Columbia, the Albany Spurs graphite
property in northeastern Ontario and the Buckshot graphite property
near the Miller Graphite mine in Quebec.

For further information on Durango, please refer to its SEDAR
profile at www.sedar.com.

Marcy Kiesman, Chief Executive Officer

Telephone: 604.428.2900

Facsimile: 888.266.3983

Email: durangoresourcesinc@gmail.com

Website: www.durangoresourcesinc.com

Forward-Looking Statements

This document may contain or refer to forward-looking information
based on current expectations, including, but not limited to timing of
mineral resource estimates, obtaining financing, future exploration or
project development programs and the impact on the Company of these
events. Forward-looking information is subject to significant risks and
uncertainties, as actual results may differ materially from forecasted
results. Forward-looking information is provided as of the date hereof
and we assume no responsibility to update or revise them to reflect new
events or circumstances. For a detailed list of risks and
uncertainties, as it relates to Durango, please refer to the Company's
Prospectus filed with SEDAR.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for DGO-V
Date: 2014/07/22
Closing Price: 0.09

TEL:  604.428.2900   DURANGO RESOURCES INC.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1420300017TS11420301206-07294920140723