Source	CANADA NEWSWIRE
Date	07/14/2014
Time	02:16:46 PM

Company	 Mundoro Capital Inc.
Title	Mundoro Provides Update on Serbia Drilling and Announces Closing of
Acquisition of New Copper Gold License





    CDNX Symbol: MUN











Press Release	




" BC-MundoroSerbiaDrilling   07-14 1600
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Mundoro Provides Update on Serbia Drilling and Announces Closing of
Acquisition of New Copper Gold License@

VANCOUVER, July 14, 2014 /CNW/ - Mundoro Capital Inc. (TSXV:MUN,
www.mundoro.com) ("Mundoro" or the "Company") is pleased to announce an update
on the Tiva Rosh drilling program in Serbia as well as the closing of the
acquisition of the Chuprene Exploration Permit ("Chuprene"), located in
northwestern Bulgaria approximately 65km southeast of Bor in the Timok
Complex.
Serbia Drilling Program Update
Mundoro recently began drilling on its Tilva Rosh prospect in Serbia on
June 28, 2014. The Tilva Rosh prospect was outlined by a gold-in-soil anomaly
of 600m by 150m which was confirmed with follow up trenching in Q4-2013 and
Q2-2014.
The Company is drill testing depth extension of the outcropping
epithermal gold mineralization with six diamond drill holes each with a depth
of approximately 150m (see Figure 1 - Tilva Rosh Drill Plan and Progress). The
Company has completed the first three holes concentrating on the area of the
previously reported trenching results, which returned 12m of 30.39 g/tonne
gold and 171.27 g/tonne silver (see press release dated October 21, 2013).
The drill core has intersected the hydrothermal breccia hosting the
mineralization which was trenched on surface as well as a feldspar porphyry
which is argillic altered. The drill core has also intersected sections of (i)
quartz-pyrite-chalcopyrite mineralization; (ii) pyrite-galena-sphalerite
mineralization and (iii) semi-massive pyrite chalcocite-covellite-bornite
mineralization.
Assay results are scheduled to be published in Q3-2014 along with further
description of the drill core from the holes.
Chuprene License Acquisition
Chuprene is an underexplored area by modern exploration methods with the
potential for discovery of high sulphidation copper-gold, sediment hosted gold
and intrusion related gold-silver deposits.
In consideration for the transfer of Chuprene, the Company has made an
upfront payment to the seller of 350,000 common shares of Mundoro at a deemed
price of C$0.30 per share. The shares will be subject to a four month hold
period expiring November 15, 2014. In the future, in the event that the
Company files a NI 43-101 compliant resource with respect to Chuprene,
identifying at least 1,000,000 ounces of gold-equivalent in the Measured and
Indicated resource categories, the Company will have the option to either (i)
issue an additional 3,500,000 common shares of Mundoro or (ii) pay C$1 million
to the seller. The seller also retains a 10% Net Profit Interest royalty in
Chuprene which can be purchased by the Company for C$1 million at any time.
"Chuprene is located in an underexplored portion of the prolific Tethyan
Gold Belt which the Company believes has potential to host further new
discoveries. Mundoro will be initiating an exploration program in Q3-2014 to
build upon the prior stream sediment and rock sampling program conducted by
the prior operator, to cover geochemical sampling, prospecting, mapping and
ground geophysics to delineate drill targets" stated Teo Dechev, President and
CEO of Mundoro.
Chuprene is located in the Late Palaeozoic Belt of north-west Bulgaria
which is host to numerous copper-gold, lead-zinc-silver and poly-metallic
gold-silver deposits mined underground in the early twentieth century. The
exploration area contains several Cu-Au mineral occurrences which have been
exploited since ancient times.
Most significant of the historical mineral occurrences in the Chuprene
license is the Chuprene Cu-Au occurrence which was explored in the late 1940's
and which had historical production of 30,000 tonnes of ore at grades of 6-8%
Cu.
The geology of Chuprene is made up of green schist metamorphic rocks and
meta-volcanics cut by granitoids. Structural network is complex with numerous
faults - normal, thrust and reverse. Recent exploration work undertaken by the
prior operator is:
--  Data compilation, general prospecting and rock grab sampling of
known mineral occurrences.
--  Stream sediment sampling over an area of 87km² within the
central part of the license consisted of two parts: regional
and detailed. The regional sampling was done at 1km² grid with
1km between two neighboring samples along the same stream. The
detailed sampling covered 12km² at a grid 0.17km² and distance
between two neighboring samples less than 300m.
--  Limited follow up of anomalous stream sediment catchments.
Prospecting work has covered the known mineral occurrences and partly the
anomalous stream sediment catchments. A total of 279 rock samples were
collected from hydrothermally altered and mineralized rocks over five areas
totaling 18.7km² deemed to be prospective for discovery of Au and Cu-Au
mineralization. Rock grab sampling has returned encouraging high grade gold
results such as: 2.64 g/tonne Au, 2.91 g/tonne Au and up to 16.7 g/tonne Au.
Quartz vein sample returned 3m (at) 2.41 g/tonne Au, 110 g/tonne Ag and 0.56% 
Cu.
Technical information contained in this Press Release has been reviewed
and approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by
National Instrument 43-101.
On behalf of the Company, Teo Dechev, Chief Executive Officer, President
and Director
About Mundoro Capital Inc.
Mundoro is a well-funded, Canadian based, company focused on mineral
acquisition, exploration, and development. Our primary focus is advancing our
properties on the Tethyan Belt in Southeastern Europe. Mundoro has
methodically acquired a district-scale land position on this prolific mineral
belt which hosts significant Gold-Copper porphyry and related epithermal
deposits. Our strong project pipeline, which also includes assets in Mexico
and China, is positioned to drive long-term, sustainable growth in order to
attain production and shareholder return.
Sampling, Analysis and Quality Assurance and Control (QAQC)
The Company uses the ALS Romania and Bor Serbia managed laboratories to
assay all samples from Serbian and Bulgarian properties. Soil and stream
sediment samples are assayed in ALS Romania using ultra-trace level methods
combination of ICP-AES and ICP-MS acid digest, 51 elements; whereas gold is
assayed by low level detection fire assay method 50g, AAS finish. Preparation
of samples includes drying, screening to -80(number sign), fine crushing, split 
and
pulverizing to 75 µm. Rock samples are assayed in ALS Romania using ME-ICP61M
four acid digest 35 elements; gold fire assay 50 g, AAS finish.
Stream sediment samples were collected from optimum trap sites for heavy
minerals, wet or dry sieved approximately 2kg -1mm silt in the field. Samples
were taken at regular intervals of approximately 1.5km along stream, designed
to represent catchment areas of approximately 3-4km². Soil sampling was
carried out along grid profiles oriented perpendicular to controlling
structures of the mineralisation. Samples were collected at regular 50m
intervals. Rock sampling was carried out as chip-channels in outcrops on 1 to
3m intervals collecting minimum 1kg material per meter.
In addition to laboratory's internal quality assurance quality control
(QAQC) procedures the Company implements its own QAQC with systematic
insertion into sample streams of certified reference materials, field
duplicates and blanks. Field duplicate samples are taken every 25 samples and
known standards and blanks are inserted after every 20th sample. All data
collected in the field and assay results from the laboratories are routinely
entered into a data base.
Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference into this
News Release may contain forward-looking statements. All statements, other
than statements of historical fact, included or incorporated by reference in
this News Release are forward-looking statements, including, without
limitation, statements regarding activities, events or developments that the
Board expects or anticipates may occur in the future. These forward-looking
statements can be identified by the use of forward-looking words such as
"will", "expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material assumptions
that were applied in making the forward looking statements in this News
Release include expectations as to the Company's future strategy and business
plan and execution of the Company's existing plans. There can be no assurance
that the plans, intentions or expectations upon which these forward-looking
statements are based will occur. We caution readers of this News Release not
to place undue reliance on forward looking statements contained in this News
Release, which are not a guarantee of performance and are subject to a number
of uncertainties and other factors that could cause actual results to differ
materially from those expressed or implied by such forward-looking statements.
These factors include general economic and market conditions, changes in law,
regulatory processes, the status of Mundoro's assets and financial condition,
actions of competitors and the ability to implement business strategies and
pursue business opportunities. The forward-looking statements contained in
this News Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release are
made as of the date of this News Release and the Board undertakes no
obligation to publicly update such forward-looking statements to reflect new
information, subsequent events or otherwise, except as required by law.
Shareholders are cautioned that all forward-looking statements involve risks
and uncertainties and for a more detailed discussion of such risks and other
factors that could cause actual results to differ materially from those
expressed or implied by such forward-looking statements, refer to the
Company's filings with the Canadian securities regulators available on
www.sedar.com.
Neither TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mundoro Capital Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2014/14/c7666.html

-0-                           07/14/2014
/For further information:
For further information please contact Teo Dechev, CEO, President and
Director of Mundoro Capital Inc. at +1-604-669-8055 or Michelle Roth, Roth
Investor Relations at +1-732-792-2200.
/
(MUN.)

CO:  Mundoro Capital Inc.
ST:  British Columbia
IN:  MNG
SU:  TNM

-30-