Source	MARKET NEWS
Date	07/15/2014
Time	06:44:50 AM

Company	 Rockhaven Resources Ltd.
Title	Drills 
56.4 G/t Gold And 318 G/t Silver (62.76 G





    CDNX Symbol: RK











Press Release	





ROCKHAVEN RESOURCES LTD ("RK-V")
- Drills 56.4 G/t Gold And 318 G/t Silver (62.76 G/t Gold Eq)
- Over 1.31 M And 28.9 G/t Gold And 669 G/t Silver (42.28 G/t
- Gold Eq) Over 1.65 M At Klaza Project, Yukon

Rockhaven Resources Ltd. ("Rockhaven") is pleased to announce
results for the first eight drill holes from the 2014 program at its
100%-owned Klaza property located in the Dawson Gold Belt of southern
Yukon. The 12,000 m diamond drill program is focused on delineating and
expanding areas of high-grade gold and silver mineralization within
multiple structural zones that have been identified on the property.

Highlights from the new drill holes testing the Western BRX Zone
are as follows:

--  56.4 g/t gold and 318 g/t silver (62.76 g/t gold EQ(i)) over 1.31 m and
10.6 g/t gold and 32.2 g/t silver (11.24 g/t gold EQ) over 1.41 m -
Hole
137 --  40.5 g/t gold and 536 g/t silver (51.22 g/t gold EQ) over
0.63 m - Hole
138 --  29.9 g/t gold and 660 g/t silver (43.10 g/t gold EQ) over
1.10 m - Hole
141 --  6.38 g/t gold and 83.8 g/t silver (8.06 g/t gold EQ) over
2.39 m - Hole
142 --  28.9 g/t gold and 669 g/t silver (42.28 g/t gold EQ) over
1.65 m - Hole
143



"We are very excited to release some of the best results from the
property to date, with six intercepts from the first eight drill holes
assaying greater than 40 g/t gold equivalent," stated Matt Turner, CEO
of Rockhaven Resources. "These high-grade results continue to increase
our confidence in the continuity and potential of the Western BRX Zone,
which was only broadly outlined by previous trenching and drilling
programs. Drilling is proceeding ahead of schedule and on budget with
35 holes having been successfully completed at the Western BRX and
Western Klaza Zones to further evaluate these exceptional targets."

Western BRX Zone

The Western BRX Zone is the main target of the 2014 diamond drill
program. It is a 750 m long, linear structure hosting high-grade gold
and silver veins emplaced alongside or in close proximity to a feldspar
porphyry dyke. Systematic infill and step-out diamond drilling in 2014
at the Western BRX Zone has further confirmed the continuity of the
structure while delineating areas of high-grade gold and silver
mineralization. The eight holes reported in this release have tested a
275 m section of this 750 m long zone and demonstrate the potential of
this target.

Significant results including mineralized secondary structures are
shown in the table below.

//st

---------------------------------------------------------------------------
-
Drill Hole      Zone ID                   From             To       Interval
(m)            (m)           (m)+
---------------------------------------------------------------------------
-
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-136       BRX                      58.30          58.80           0.50
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-137       secondary                24.42          27.41           2.99
---------------------------------------------------------------------------
-
and             BRX                     110.87         112.28           1.41
----------------
---------------------------------------------
incl.                                   111.40         111.71           0.31
----------------
---------------------------------------------
and                                     125.15         128.10           2.95
----------------
---------------------------------------------
incl.                                   125.15         126.46           1.31
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-138       BRX                     131.80         132.43           0.63
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-139       secondary                98.05          98.81           0.76
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-141       secondary               109.40         110.35           0.95
---------------------------------------------------------------------------
-
and             BRX                     137.21         138.31           1.10
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-142       BRX                     155.13         157.52           2.39
----------------
---------------------------------------------
incl.                                   157.16         157.52           0.36
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-143       BRX                     118.92         120.20           1.28
----------------
---------------------------------------------
and                                     123.40         125.05           1.65
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
Drill Hole      Zone ID                   Gold         Silver        Gold EQ
(g/t)          (g/t)       (g/t)(i)
---------------------------------------------------------------------------
-
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-136       BRX                       2.98           12.5           3.23
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-137       secondary                 1.92           29.8           2.52
---------------------------------------------------------------------------
-
and             BRX                       10.6           32.2          11.24
----------------
---------------------------------------------
incl.                                     38.9            107          41.04
----------------
---------------------------------------------
and                                       26.9            181          30.52
----------------
---------------------------------------------
incl.                                     56.4            318          62.76
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-138       BRX                       40.5            536          51.22
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-139       secondary                 1.98           13.0           2.24
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-141       secondary                 1.84           13.0           2.10
---------------------------------------------------------------------------
-
and             BRX                       29.9            660          43.10
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-142       BRX                       6.38           83.8           8.06
----------------
---------------------------------------------
incl.                                     39.0            498          48.96
---------------------------------------------------------------------------
-

---------------------------------------------------------------------------
-
KL-14-143       BRX                       2.23           47.0           3.17
----------------
---------------------------------------------
and                                       28.9            669          42.28
---------------------------------------------------------------------------
-
+ Represents the diamond drill hole length. True widths are estimated to be
approximately 80-90% of the interval.
*Gold equivalence (EQ) has been calculated using metal prices of $1300 per
ounce gold & $26.00 per ounce silver, to be consistent with earlier
calculations & assumes 100% recoveries of both metals.
KL-14-136 returned poor core recovery from the BRX structural zone,
KL-14-139 appears to have intersected an unmineralized cross-fault that
off-sets the BRX structural zone, & KL-14-140 did not return significant
results but check samples are pending.

//et

Drilling and trenching at the road-accessible Klaza property since
2010 have identified nine main mineralized structural zones and
numerous subsidiary structures within a 2,000 by 4,000 m corridor.
Individually, the main zones range from 1 to 75 m in width and are
continuously mineralized over strike lengths of 250 to 2,400 m. The
zones have been traced over a cumulative strike length of 9,400 m and
all remain open for expansion along strike and to depth.

Maps, sections and an expanded assay list which includes copper,
lead and zinc values for the significant intervals can be viewed at the
Company's website at www.rockhavenresources.com. Additional results
from the 2014 exploration program at Klaza will be released once assays
are received, compiled and evaluated.

All analyses for rock and core samples from the 2014 program were
performed by ALS Minerals with sample preparation in Whitehorse and
assays and geochemical analyses in North Vancouver. Core samples are
routinely analyzed for gold by fire assay followed by atomic absorption
(Au-AA24) and 48 other elements by inductively coupled plasma-mass
spectrometry (ME-MS61). Samples that exceed the detection limits of the
routine methods are assayed for silver, copper, lead and zinc by
inductively coupled plasma-atomic emission spectroscopy (Ag/Cu/Pb/Zn -
OG62) and gold by gravimetric analysis (Au-GRA22). Rigorous procedures
are in place regarding sample collection, chain of custody and data
entry. Certified assay standards, coarse reject duplicates, field
duplicates and blanks are routinely inserted into the sample stream to
ensure integrity of the assay process. All of the results reported have
passed the QAQC screening.

The 2014 program is managed by Archer, Cathro & Associates (1981)
Limited (Archer Cathro). Technical information in this news release has
been approved by Matthew R. Dumala, P.Eng., a geological engineer with
Archer Cathro and qualified person for the purpose of National
Instrument 43-101.

Rockhaven Resources Ltd. is a well-funded company focused on
growth through exploration of its wholly-owned projects. For additional
information concerning Rockhaven Resources Ltd. or its various
exploration projects please visit Rockhaven's website at
www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

TSX Venture closing price for RK-V
Date: 2014/07/14
Closing Price: 0.28

TEL:  604-688-2568  Rockhaven Resources Ltd.
Matthew Turner, CEO and Director
E-mail: mturner@rockhavenresources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1419500015TS11419501157-06441420140715