Source	CANADA NEWSWIRE
Date	07/18/2014
Time	06:03:51 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol reports high-grade gold and silver assays associated with
geophysical anomalies at the Atlas project, Chile





    CDNX Symbol: MRZ











Press Release	




" BC-Mirasol-Atlas-Project   07-18 1300
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Mirasol reports high-grade gold and silver assays associated with
geophysical anomalies at the Atlas project, Chile@

VANCOUVER, July 18, 2014 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
Frankfurt: M8R)
--  AGZ prospect - Rock chip samples from this gold-enriched zone
outline an 800 by 500 m area hosting multiple vuggy silica
structures with up to 50.3 g/t Au and 56.9 g/t Ag.

--  ASZ prospect - Rock chip samples from this silver-enriched zone
outline 700 m long trend with hydrothermal breccia and
silicified tuffs returning new silver results up to 215.0 g/t
Ag and anomalous gold from recent sampling.

--  Atlas Pampa prospect - Float and subcrop rock chip samples have
outlined this new gold-silver prospect.

--  An IP electrical geophysical survey over the central part of
the Atlas alteration system outlined a series of large highly
resistive anomalies spatially associated with gold-silver
bearing surface rock chips.
Mirasol closed the southern hemisphere 2013-14 summer exploration season
in early June. At season's end approximately 80% of the +25 sq. km Atlas
alteration system had been systematically reconnaissance sampled with over
2,479 surface rock chip (Figure 1) and 334 stream sediment samples collected
this season (also see news release of February 26, 2014). These results have
expanded the dimensions and upgraded the potential of the Atlas Gold Zone
(AGZ) and the Atlas Silver Zone (ASZ) prospects as well as defining a large
gold-silver anomaly at the new Pampa prospect.
At the Atlas Gold Zone new assay results from detailed surface
prospecting have outlined a series of northwest-oriented mineralized trends in
float and subcrop (thought to be very near its source outcrop), extending away
from last season's trenches (see news release of September 16, 2013). Rock
chip sampling of the trends has returned multi-gram gold and silver assays
over an 800 by 500 m area, including best assays of 30.70 g/t Au with 42.3 g/t
Ag and 50.30 g/t Au with 5.24 g/t Ag. Higher grades are associated with
subcrop of vuggy silica structures and hydrothermal breccias, typical of
high-sulphidation epithermal systems. Some of these trends correlated to
mineralization exposed in last season's trenches. However the recently
identified higher-grade trends have not yet been trenched, suggesting the
potential for significant new zones of mineralization underlying the rock chip
anomalies and surrounding soil cover.
At the Atlas Silver Zone systematic prospecting and mapping has outlined
a 700 m long zone of anomalous silver-gold mineralization in rock chip float
and subcrop samples, surrounded by widespread soil and alluvium. This cover
may conceal additional mineralization. At the ASZ high-grade silver assays in
the range 112.0 to 639.0 g/t Ag (with anomalous gold to 0.15 g/t), are
associated with silicified tuffs and high-level upward flaring breccia bodies.
The breccia hosts clasts of mineralization containing silver sulphide
minerals, which are interpreted to be fragments of mineralized rock
transported from depth during hydrothermal eruption that also formed the
breccia. Where exposed in last season's trenches, the ASZ mineralization is
associated with prominent native sulphur and highly anomalous epithermal
pathfinder elements. The funnel- shaped form of the breccia combined with the
element association suggest that the current outcrop level of the ASZ is near
the top of the mineralized interval in a typical epithermal system, and may
suggest potential for more extensive mineralization at depth.
The new Pampa prospect is less well understood due to limited outcrop,
however assay results from surface rock chip sampling, suggest further
exploration is warranted. Here rock chip float and subcrop samples have
returned anomalous gold and silver assays over an area of approximately 500 by
500 m. To date, assays from this prospect correspond to narrow (< 30 cm wide)
quartz-alunite altered breccias and pervasively altered tuffs. Assay results
fall into two groups. Those with similar amounts of gold and silver, with
assays up to 2.91 g/t Au and 5.70 g/t Ag; and those where silver is dominant
over gold, with highest silver assays in the range 248.0 to 421.0 g/t and gold
up to 0.08 g/t. This may suggest two distinct sources of mineralization in the
area or overprinting phases of mineralization.
A 5.4 sq. km, 100 to 200 m line-spacing IP electrical geophysical survey
(Figure 2) has been completed over the centre of the alteration system,
identifying a series of resistivity anomalies associated with surface
alteration and rock chip/trench gold-silver assays. These anomalies have
locally returned very high resistivity readings in the range 5,000 to 15,400
Ohm/m and in some cases form part of large, open-ended resistive zones in
excess of 1 km in strike length. In epithermal systems such as Atlas,
resistive anomalies of this nature can map the distribution of hydrothermal
silica accumulations that can be associated with precious metal
mineralization. At Atlas the resistivity anomalies associated with the AGZ,
Pampa prospect and a larger, high intensity covered resistive anomaly in the
northeast of the survey area are considered by Mirasol to represent priority
drill targets.
The previously mentioned resistive anomalies show only weak associated
chargeable anomalies in this survey, suggesting low sulphide content in these
areas, possibly a result of deep supergene oxidation. This is consistent with
the 100 to 150 m depth of oxidation encountered by Mirasol whilst drilling the
adjacent Titan project, and highlights the potential for oxide-gold
mineralization at the Atlas project.
Mirasol is very encouraged by the results received this season from the
Atlas project where exploration has to date has identified anomalous gold and
silver mineralization in multiple centres over a 6.7 sq. km area, in what is
emerging as a large precious metal system with potential to develop multiple
drill targets.
Atlas is a 100% Mirasol-owned, newly discovered gold-silver system in the
prolifically mineralized Miocene-age volcanic arc of northern Chile. This arc
hosts a number of world-class gold and copper mines. Atlas and the adjacent
Titan project are the most advanced projects of Mirasol's nine 100%-owned
properties in its Gorbea Belt portfolio. In keeping with Mirasol's project
generator Joint Venture business model, the company is actively seeking a
strong JV partner to advance the Gorbea Belt properties to drill testing.
Stephen Nano is the Qualified Person under NI 43-101 who has prepared and
approves the technical content of this news release.
Quality Assurance/Quality Control: Exploration at the Atlas Project is
supervised by Stephen C. Nano, who is the Qualified Person under NI 43-101 and
Timothy Heenan, Exploration Manager. All technical information for the
Company's projects is obtained and reported under a formal quality assurance
and quality control (QA/QC) program. All drill, rock chip and stream sediment
samples are collected under the supervision of Company geologists in
accordance with standard industry practice. Samples are dispatched via
transport to an ISO 9001:2000-accredited laboratory in Chile for analysis. All
drill, and rock chip samples are submitted to the Laboratory with
independently sourced, accredited standards and blanks and where appropriate
duplicate samples to facilitate monitoring of laboratory performance.
Certified Results are examined by an independent qualified consultant to
ensure laboratory performance meets required standards.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2014/18/c8175.html

-0-                           07/18/2014
/For further information:

Stephen Nano President and CEO
Tel: (604) 602-9989: Fax:(604) 609-9946
Email: contact(at)mirasolresources.com Website: www.mirasolresources.com
/
(MRZ.)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG PCS
SU:

-30-