Source	Marketwire
Date	07/21/2014
Time	07:33:58 AM

Company	 MAX RESOURCE CORP.
Title	MAX Commences Drilling at East Manhattan Wash Gold Project, Nye County, 
Nevada





    CDNX Symbol: MXR











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: MAX Resource Corp

TSX VENTURE SYMBOL: MXR
OTCBB SYMBOL: MXROF
FRANKFURT SYMBOL: M1D

July 21, 2014

MAX Commences Drilling at East Manhattan Wash Gold Project, Nye County, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 21, 2014) - MAX Resource Corp. 
(TSX VENTURE:MXR)(OTCBB:MXROF)(FRANKFURT:M1D) has commenced drilling at its 
East Manhattan Wash gold project in Nevada. This eight hole (720 m) drill 
program will be the first known drilling to be conducted at East Manhattan 
Wash, where surface sampling by MAX has identified a soil anomaly exposed over 
a surface area in excess of 1,650 m by 450 m that returned values ranging from 
0.05 ppm to 1.5 ppm (1.5 g/t) Au in soils. During an initial bulk sample 
conducted in 2009, MAX recovered 4.9 g/t Au and 1.2 g/t Ag from a 793 pound 
sample taken at surface. Mineralization appears to be free gold in a volcanic 
lithic welded tuff that will be drill tested to determine the overall depth of 
the gold mineralization, extend the known mineralization below the overburden 
and/or alluvium cover, and determine the overall grade.

The EMW property is comprised of 78 claims (1,560 acres) located in the 
Manhattan Mining District 40 miles north of the town of Tonopah and eight miles 
south of the Round Mountain Mine (jointly owned by Kinross and Barrick), a 
conventional open pit operation that has produced more than 12 Moz of gold to 
date. For 2013, Kinross Gold reported a proven and probable gold resource at 
Round Mountain (net to its 50% interest) of 42.147 million tonnes at 0.68 g/t 
Au.

This news release has been reviewed by Mr. Clancy J. Wendt, P. Geo, a 
"qualified person" as that term is defined under National Instrument 43-101.

About MAX Resource Corp.

MAX Resource Corp. is a Canadian exploration company focused on gold and silver 
exploration in Nevada. For more information, please visit our web site at 
www.maxresource.com.

On behalf of the Board of Directors of MAX Resource Corp.

Stuart Rogers, President

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This News Release includes certain "forward looking statements". Without 
limitation, statements regarding potential mineralization and resources, 
exploration results, and future plans and objectives of the Company are forward 
looking statements that involve various degrees of risk. The following are 
important factors that could cause MAX's actual results to differ materially 
from those expressed or implied by such forward looking statements: changes in 
the world wide price of mineral commodities, general market conditions, risks 
inherent in mineral exploration, risks associated with development, 
construction and mining operations, the uncertainty of future profitability and 
the uncertainty of access to additional capital.

- 30 -

CONTACT INFO:

MAX Resource Corp.
Leonard MacMillan
Corporate Communication
604-637-2140 or Toll Free: 1-866-331-5088
info@maxresource.com

or

Paradox Public Relations
514-341-0408 or Toll Free: 1-866-460-0408
info@paradox-pr.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=491629580