Source	Marketwire
Date	07/22/2014
Time	05:45:10 AM

Company	 ROCKHAVEN RESOURCES LTD.
Title	Rockhaven Resources Ltd. Continues to Intersect High-Grade Gold and Silver 
Mineralization at the Western BRX Zone, Klaza Project, Yukon





    CDNX Symbol: RK











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Rockhaven Resources Ltd.

TSX VENTURE SYMBOL: RK

July 22, 2014

Rockhaven Resources Ltd. Continues to Intersect High-Grade Gold and Silver 
Mineralization at the Western BRX Zone, Klaza Project, Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 22, 2014) - Rockhaven 
Resources Ltd. (TSX VENTURE:RK) ("Rockhaven") is pleased to announce results 
for five additional drill holes from the 2014 program at its 100%-owned Klaza 
property located in the Dawson Range Gold Belt of southern Yukon.

The 12,000 m diamond drill program is focused on delineating and expanding 
areas of high-grade gold and silver mineralization within multiple structural 
zones that have been identified on the property.

Highlights from the new drill holes testing the Western BRX Zone are as follows:

/T/

--  26.80 g/t gold and 705 g/t silver (40.90 g/t gold EQ(i)) over 0.84 m and
29.30 g/t gold and 36.8 g/t silver (30.04 g/t gold EQ) over 1.01 m -
Hole 144
--  10.79 g/t gold and 121 g/t silver (13.21 g/t gold EQ) over 2.90 m - Hole
145
--  15.95 g/t gold and 123 g/t silver (18.41 g/t gold EQ) over 1.89 m - Hole
147

/T/

"These new high-grade intercepts provide further confirmation of the excellent 
continuity and size potential of the Western BRX Zone," stated Matt Turner, CEO 
of Rockhaven Resources. "Systematic drilling continues within the Western BRX 
and Western Klaza Zones, with a total of 46 holes successfully completed to 
date."

Western BRX Zone

The Western BRX Zone is the main target of the 2014 diamond drill program. It 
is a 750 m long, linear structure hosting high-grade gold and silver veins 
emplaced alongside or in close proximity to a feldspar porphyry dyke. 
Systematic infill and step-out diamond drilling in 2014 at the Western BRX Zone 
has further confirmed the continuity of the structure while delineating areas 
of high-grade gold and silver mineralization. Twelve of the thirteen holes 
reported from 2014 drilling have tested a 400 m section of this 750 m long 
zone. The other hole (KL-14-146) appears to have entered an offset fault that 
post-dates mineralization, before reaching the targeted Western BRX Zone.

Significant new results, including some from mineralized secondary structures, 
are shown in the table below.

/T/

----------------------------------------------------------------------------
From      To   Interval    Gold    Silver   Gold EQ
Drill Hole  Zone ID       (m)     (m)       (m)+   (g/t)     (g/t)  (g/t)(i)
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-144   BRX        102.27  104.67       2.40   10.25       259     15.43
------------         -------------------------------------------------------
incl.                  102.92  103.76       0.84   26.80       705     40.90
------------         -------------------------------------------------------
and                    108.34  112.10       3.76   10.99      21.0     11.41
------------         -------------------------------------------------------
incl.                  111.09  112.10       1.01   29.30      36.8     30.04
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-145   BRX         96.99   99.89       2.90   10.79       121     13.21
------------         -------------------------------------------------------
incl.                   96.99   97.76       0.77   13.05       310     19.25
------------         -------------------------------------------------------
and incl.               99.59   99.89       0.30   67.40       320     73.80
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-146   secondary   63.36   64.36       1.00    3.62      24.9      4.12
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-147   BRX        145.81  150.40       4.59    7.36       225     11.86
------------         -------------------------------------------------------
incl.                  145.81  147.70       1.89   15.95       123     18.41
------------         -------------------------------------------------------
and incl.              149.56  150.40       0.84    4.06       946     22.98
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-148   BRX        190.95  194.97       4.02    1.35      10.5      1.56
----------------------------------------------------------------------------
secondary  210.20  210.47       0.27    4.31       148      7.27
----------------------------------------------------------------------------
+ Represents the diamond drill hole length. True widths are estimated to be
approximately 80-90% of the interval.
(i)Gold equivalence (EQ) has been calculated using metal prices of $1300 per
ounce gold and $26.00 per ounce silver, to be consistent with earlier
calculations and assumes 100% recoveries of both metals.

/T/

Drilling and trenching at the road-accessible Klaza property since 2010 have 
identified nine main mineralized structural zones and numerous subsidiary 
structures within a 2,000 by 4,000 m corridor. Individually, the main zones 
range from 1 to 75 m in width and are continuously mineralized over strike 
lengths of 250 to 2,400 m. The zones have been traced over a cumulative strike 
length of 9,400 m and all remain open for expansion along strike and to depth.

Maps, sections and an expanded assay list which includes copper, lead and zinc 
values for the significant intervals can be viewed at the Company's website at 
www.rockhavenresources.com. Additional results from the 2014 exploration 
program at Klaza will be released once assays are received, compiled and 
evaluated.

All analyses for rock and core samples from the 2014 program were performed by 
ALS Minerals with sample preparation in Whitehorse and assays and geochemical 
analyses in North Vancouver. Core samples are routinely analyzed for gold by 
fire assay followed by atomic absorption (Au-AA24) and 48 other elements by 
inductively coupled plasma-mass spectrometry (ME-MS61). Samples that exceed the 
detection limits of the routine methods are assayed for silver, copper, lead 
and zinc by inductively coupled plasma-atomic emission spectroscopy 
(Ag/Cu/Pb/Zn - OG62) and gold by gravimetric analysis (Au-GRA22). Rigorous 
procedures are in place regarding sample collection, chain of custody and data 
entry. Certified assay standards, coarse reject duplicates, field duplicates 
and blanks are routinely inserted into the sample stream to ensure integrity of 
the assay process. All of the results reported have passed the QAQC screening.

The 2014 program is managed by Archer, Cathro & Associates (1981) Limited 
(Archer Cathro). Technical information in this news release has been approved 
by Matthew R. Dumala, P.Eng., a geological engineer with Archer Cathro and 
qualified person for the purpose of National Instrument 43-101.

Rockhaven Resources Ltd. is a well-funded company focused on growth through 
exploration of its wholly-owned projects. For additional information concerning 
Rockhaven Resources Ltd. or its various exploration projects please visit 
Rockhaven's website at www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

- 30 -

CONTACT INFO:

Rockhaven Resources Ltd.
Matthew Turner
CEO and Director
604-688-2568
mturner@rockhavenresources.com
www.rockhavenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=491718477