Source	Marketwire
Date	07/23/2014
Time	04:30:16 AM

Company	 ATAC RESOURCES LTD.
Title	ATAC Announces Positive PEA Results for the High-Grade Oxide Gold Tiger 
Deposit, Rackla Gold Project-Yukon





    CDNX Symbol: ATC











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: ATAC Resources Ltd.

TSX VENTURE SYMBOL: ATC

July 23, 2014

ATAC Announces Positive PEA Results for the High-Grade Oxide Gold Tiger 
Deposit, Rackla Gold Project-Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 23, 2014) - ATAC Resources 
Ltd. (TSX VENTURE:ATC) is pleased to announce the completion of a positive 
Preliminary Economic Assessment ("PEA") for the oxide portion of the Tiger 
Deposit located at the western end of the Company's 100% owned Rackla Gold 
Project, Yukon. The Tiger Deposit was discovered in 2007 and is distinct from 
the more recent larger scale Carlin-type discoveries located 100 km to the 
east, which remain the exploration focus of the Company.

The lead engineering firm for the PEA was Kappes Cassiday & Associates ("KCA") 
(metallurgy, processing, infrastructure, financial analysis) in cooperation 
with Tetra Tech, Inc. ("Tetra Tech") (mining), Giroux Consultants Ltd. (mineral 
resource), Resource Strategies (environmental and permitting) and Gerald G. 
Carlson, Ph.D., P.Eng. (history, geology, drilling). Unless specified 
otherwise, all values are shown in Canadian dollars, where 1 CAD = 0.92 USD.

PEA HIGHLIGHTS (using US$1,250 per ounce gold price):

/T/

--  Conventional open-pit mining with single-stage, low intensity crushing
followed by size classification - no grinding or agglomeration needed;
--  Life of mine ("LOM") production of 2.06 million tonnes of oxide material
at an average diluted grade of 3.72 g/t gold;
--  Overall gold recoveries of 89.8% from hybrid heap-leach (87.8% recovery)
and agitated tank (91.0% recovery) carbon-in-leach ("CIL") process;
--  Four year, seasonal operation with LOM production of 221,558 ounces of
gold;
--  Pre-tax net present value ("NPV") of $52.1 million at a 5% discount rate
and internal rate of return ("IRR") of 30% with an all-in sustaining
cash cost of $626(i);
--  At a US$1,350 per ounce gold price the pre-tax NPV increases to $72.6
million at a 5% discount rate and IRR of 39.5%; and,
--  Pit slope engineering, Tiger Deposit infill drilling and exploration of
numerous untested nearby oxide targets have the potential to enhance the
value of the project economics.
(i)All-in sustaining costs are presented as defined by the World Gold
Council less corporate G&A.

/T/

"Although we remain focused on the Carlin-type gold targets 100 km to the east, 
we are very pleased with the results of the comprehensive Tiger Deposit PEA. It 
gives the Company a clear understanding of the potential viability and value of 
our first Rackla Gold Project discovery, and highlights the advantages of a 
rare high-grade, at surface, oxide gold deposit that is located in one of the 
most favourable mining jurisdictions in the world," states Graham Downs, CEO of 
ATAC. "The simplicity of the mining and processing combined with the approach 
of modular design and construction for the on-site facilities has resulted in 
an optimized development scenario for this size of deposit. Additional 
geotechnical and resource drilling at the Tiger Deposit combined with 
exploration drilling at over six untested satellite oxide targets has the 
potential to significantly enhance the PEA and the district potential of the 
Rackla Gold Project."

Economic Results and Sensitivities

The following table demonstrates the sensitivity of the Tiger Deposit economics 
to the price of gold. US$1,250 per ounce gold price was used as the base case 
and is highlighted in the table.

Summary of gold price sensitivity

/T/

----------------------------------------------------------------------------
Gold Price US$/oz                             $1,100  $1,250  $1,350  $1,500
----------------------------------------------------------------------------
Pre-Tax Cumulative Net Cash Flow $M            $36.7   $72.7   $96.6  $132.6
----------------------------------------------------------------------------
Pre-Tax NPV (5% discount rate) $M              $21.4   $52.1   $72.6  $103.3
----------------------------------------------------------------------------
Pre-Tax IRR                                    15.5%   30.0%   39.5%   53.5%
----------------------------------------------------------------------------
Pre-Tax Payback (years)                          2.9     2.2     1.8     1.3
----------------------------------------------------------------------------

----------------------------------------------------------------------------
After-Tax Cumulative Net Cash Flow             $10.4   $51.0   $67.3   $91.5
----------------------------------------------------------------------------
After-Tax NPV (5% discount rate) $M            $12.6   $33.7   $47.5   $68.0
----------------------------------------------------------------------------
After-Tax IRR                                  11.2%   21.5%   27.9%   37.2%
----------------------------------------------------------------------------
After-Tax Payback (years)                        3.2     2.6     2.3     1.9
----------------------------------------------------------------------------

/T/

Mining and Processing

The Tiger Deposit has been modeled as an open-pit mining operation with a 
hybrid heap leach and CIL gold recovery process. A summary of: (i) gold 
production and processing metrics; (ii) pre-production costs; and (iii) 
operating costs are presented in the following tables.

Projected Production and Processing Summary

/T/

----------------------------------------------------------------------------
Total Process Feed                          2.06 million tonnes
----------------------------------------------------------------------------
Processing Rate
(158 days per year)                           3,300 tonnes/day
----------------------------------------------------------------------------
LOM Strip Ratio                                    5.6:1
----------------------------------------------------------------------------
Combined
Heap Leach                    Average or
Proportional Processing Feed             (42%)      CIL (58%)          Total
----------------------------------------------------------------------------
Average Process Feed Grade         3.45 g/t Au    3.91 g/t Au    3.72 g/t Au
----------------------------------------------------------------------------
Average Recovery                         87.8%          91.0%          89.8%
----------------------------------------------------------------------------
Average Annual Production LOM
(oz)                                   21,132         34,257         55,389
----------------------------------------------------------------------------
Total Production (oz)                   84,528        137,029        221,558
----------------------------------------------------------------------------
Silver is a minor by-product of gold production with an assumed recovery of
19% and process feed grade of 5 g/t. Total recovered silver ounces over LOM
is 63,057 oz.

/T/

Pre-Production and Sustaining Capital Costs (Millions)

/T/

----------------------------------------------------------------------------
Pre-     Sustaining
Capital Costs                       Production        capital            LOM
----------------------------------------------------------------------------
Site Infrastructure                       $1.7                          $1.7
----------------------------------------------------------------------------
Heap Leach/Tailings(i)                    $5.7          $20.4          $26.1
----------------------------------------------------------------------------
Mining Equipment                         $10.1           $1.7          $11.8
----------------------------------------------------------------------------
Pre-Stripping & Stockpiling              $10.5                         $10.5
----------------------------------------------------------------------------
Process Plant                            $40.3                         $40.3
----------------------------------------------------------------------------
Contingency (20%)                        $11.6           $4.4          $16.0
----------------------------------------------------------------------------
Indirect costs                           $12.3                         $12.3
----------------------------------------------------------------------------
Total(ii)                                $92.3          $26.5         $118.8
----------------------------------------------------------------------------
(i) Pre-production and annual heap leach cell and tailings development
(ii) Totals may not add exactly due to rounding

/T/

Operating Costs

/T/

----------------------------------------------------------------------------
Operating Costs                                                  LOM Average
----------------------------------------------------------------------------
Mining Costs(i) ($/tonne mined)                                        $4.46
----------------------------------------------------------------------------
Processing ($/tonne processed)                                        $20.10
----------------------------------------------------------------------------
G & A ($/tonne processed)                                              $7.11
----------------------------------------------------------------------------
(i) Not including capitalized pre-production mining costs

/T/

Project Description

The Tiger Deposit is located approximately 55 km northeast of Keno City, Yukon. 
Access to the Tiger Deposit would be by a proposed 51.6 km winter road that 
utilizes 24.6 km of the existing and permitted Wind River Winter Trail. The 
deposit is currently accessed by air via a 2,500 foot airstrip located 8 km 
from the deposit.

An owner-operated open-pit mine, with one year of pre-stripping followed by 
four years of production is envisioned in the PEA. Average annual production 
would be approximately 55,389 oz gold with year one production projected to be 
78,500 oz gold. A total of 2.06 million tonnes of oxide material at an average 
diluted grade of 3.72 g/t would be extracted by hydraulic excavator. Based on a 
geotechnical study, no blasting of mineralized material would be necessary due 
to its highly weathered and sandy nature. Mining and stockpiling would take 
place year-round, while processing of mineralized material would occur during 
May through September (158 days annually) at a rate of 3,300 tonnes per day.

Processing has been designed to begin near the open-pit where material would be 
fed into a single skid-mounted low-intensity mineral sizer. Material would then 
be transported downhill by overland conveyor to a modular processing facility 
to be scrubbed and sized into two size fractions. The study proposes a hybrid 
approach where approximately 42% of the material (+0.212 mm) would be sent to 
the heap leach facility. The remaining 58% (finer material) would be sent to 
the CIL plant. A 50 day heap leach cycle has an estimated gold recovery of 
87.8% while the retention time for the CIL plant is 24 hours with an estimated 
gold recovery of 91.0%.

All major project components for the Tiger Deposit would be engineered and 
constructed to achieve efficient closure. Heap leach cells would be built 
annually and progressively reclaimed, while the tailings facilities would be 
expanded annually and fully reclaimed at closure.

Opportunities to Enhance the Project

ATAC is very pleased with the base case results from the detailed PEA and 
believes that opportunities exist that could greatly enhance the economics of 
the project. Some key opportunities include:

/T/

--  Future geotechnical studies may permit steeper pit slopes, which could
potentially capture a greater percentage of the presently known resource
and/or reduce the strip ratio;
--  Trade-off studies between owner-operator and contract mining or mining
fleet leasing could decrease pre-production capital;
--  Resource expansion and upgrading inferred resources to the indicated
category may be achieved with a modest drill program; and,
--  Significant potential exists to increase the resource base and life
expectancy of the project with the exploration of more than six untested
satellite oxide gold targets and geochemical anomalies.

/T/

Environment and Community Engagement

Since 2007, the Company has completed comprehensive environmental, water, 
heritage, geotechnical and metallurgical studies which have resulted in a 
highly advanced project at the PEA stage. Due to the nature of the geology of 
the deposit and environmental studies completed to date, permitting would 
likely be without significant problems.

Community and First Nation engagement began in 2008 with the first Exploration 
Cooperation Agreement with the First Nation of Na Cho Nyak Dun ("NND") signed 
in 2010. This Exploration Cooperation Agreement with the NND was recently 
renewed and provides a framework within which exploration activities and 
environmental regulatory processes on ATAC's Rackla Gold Project have been and 
will continue to be carried out. The Rackla Gold Project lies exclusively 
within the Traditional Territory of the NND.

Going forward

The Company will continue with environmental baseline work and ongoing studies 
while it explores opportunities to advance or monetize the Tiger Deposit 
through sole development, joint venture or outright sale.

Project Mineral Resources

Gold occurs in both sulphide and oxide mineralization within the Tiger Deposit. 
The PEA considers the oxide portion of the deposit. The following two tables 
show the oxide only resource used for the PEA and the oxide plus sulphide 
resources for reference only.

Tiger Deposit Oxide Only Resource

/T/

----------------------------------------------------------------------------
Cut-off grade                         Grade         Ounces
Category             (g/t) (Au)         Tonnes     (g/t) (Au)           (Au)
----------------------------------------------------------------------------
Indicated                  1.60      2,470,000           4.25        337,500
----------------------------------------------------------------------------
Inferred                   1.60        180,000           3.00         17,400
----------------------------------------------------------------------------

/T/

Tiger Deposit Oxide Plus Sulphide Resource

/T/

----------------------------------------------------------------------------
Cut-off grade                         Grade         OuncesCategory             
(g/t) (Au)         Tonnes     (g/t) (Au)           (Au)
----------------------------------------------------------------------------
Indicated                  1.60      3,260,000           3.85        403,500
----------------------------------------------------------------------------
Inferred                   1.60      1,570,000           2.44        123,200
----------------------------------------------------------------------------

/T/

The PEA is based on a 43-101 compliant mineral resource estimate completed by 
Gary Giroux, P.Eng., M.A.Sc. (Giroux Consultants Ltd.) who is a qualified 
person and independent of ATAC, based on the criteria defined by National 
Instrument 43-101. Quality control data generated during the various drill 
programs conducted at the Tiger Deposit were independently reviewed by Giroux 
Consultants Ltd. as part of the resource study. The full report dated effective 
November 15, 2011 and titled "Preparation of the Tiger Zone Mineral Resource 
Estimate" was filed on SEDAR (http://www.sedar.com/) December 1, 2011.

It should be noted that this PEA is preliminary in nature and includes inferred 
mineral resources that are considered too speculative geologically to have the 
economic considerations applied to them that would enable them to be 
categorized as mineral reserves. There is no certainty that the PEA forecast 
will be realized or that any of the resources will ever be upgraded to 
reserves. Mineral Resources that are not Mineral Reserves do not have 
demonstrated economic viability. A NI 43-101 technical report for the Tiger 
Deposit PEA will be filed on SEDAR (www.sedar.com) and ATAC's website 
(www.atacresources.com) within 45 days.

Qualified Persons

The independent qualified persons responsible for preparing the Tiger Deposit 
Preliminary Economic Assessment are Dan Kappes, P.Eng., of KCA, Sabry Abdel 
Hafez, Ph.D., P.Eng., of Tetra Tech, Gary Giroux, M.A.Sc., P.Eng., of Giroux 
Consultants Ltd., Rob McIntyre, R.E.T. of Resource Strategies and Gerald G. 
Carlson, Ph.D., P.Eng., an independent consultant. All of the aforementioned 
qualified persons have reviewed and approved the contents of this news release.

Robert C. Carne, M.Sc., P.Geo., the President and a Director of ATAC Resources 
Ltd., is the company's designated QP for this news release within the meaning 
of NI 43-101 and has reviewed and validated that the information contained in 
the release is consistent with that provided by the QPs responsible for the PEA.

About ATAC

ATAC Resources Ltd. is a Yukon-based exploration company focused on developing 
Canada's only Carlin-type gold district at its 100% owned Rackla Gold Project. 
Recent work on the 1,700 sq/km project has resulted in a positive Preliminary 
Economic Assessment for the Tiger Deposit, drilling of multiple high-grade 
Carlin-type gold zones and the identification of numerous early-stage gold 
exploration targets. The Rackla Gold Project has no underlying royalties or 
third-party interests. ATAC is well financed with approximately $23 million in 
its treasury.

On behalf of Management and the Board of Directors of ATAC Resources Ltd.,

Graham Downs, CEO

ATAC Resources Ltd.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS NEWS RELEASE.

This news release contains forward-looking information. Forward-looking 
information contained in this news release includes, but is not limited to, 
statements with respect to: (i) the estimation of inferred and indicated 
mineral resources; (ii) the success of exploration activities; (iii) the 
results of the PEA including statements about future production, future 
operating and capital costs, the projected IRR, NPV, payback period, and 
production timelines for the Tiger Deposit.

These statements are based on information currently available to the Company 
and the Company provides no assurance that actual results will meet 
management's expectations. In certain cases, forward-looking information may be 
identified by such terms as "anticipates", "believes", "could", "estimates", 
"expects", "may", "shall", "will", or "would". Forward-looking information 
contained in this news release is based on certain factors and assumptions 
regarding, among other things, the estimation of mineral resources, the 
realization of resource estimate, gold metal prices, the timing and amount of 
future exploration and development expenditures, the estimation of initial and 
sustaining capital requirements, the estimation of labour and operating costs, 
the availability of necessary financing and materials to continue to explore 
and develop the Tiger Deposit in the short and long-term, the progress of 
exploration and development activities, the receipt of necessary regulatory 
approvals, the completion of the environmental assessment process, and 
assumptions with respect to currency fluctuations, environmental risks, title 
disputes or claims, and other similar matters. While the Company considers 
these assumptions to be reasonable based on information currently available to 
it, they may prove to be incorrect.

Forward-looking information involves known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company to be materially different from any future results, performance 
or achievements expressed or implied by the forward-looking information. Such 
factors include risks inherent in the exploration and development of mineral 
deposits, including risks relating to changes in project parameters as plans 
continue to be redefined including the possibility that mining operations may 
not commence at the Tiger Deposit, risks relating to variations in mineral 
resources, grade or recovery rates resulting from current exploration and 
development activities, risks relating to changes in gold prices and the 
worldwide demand for and supply of gold, risks related to increased competition 
in the mining industry generally, risks related to current global financial 
conditions, uncertainties inherent in the estimation of mineral resources, 
access and supply risks, reliance on key personnel, operational risks inherent 
in the conduct of mining activities, including the risk of accidents, labour 
disputes, increases in capital and operating costs and the risk of delays or 
increased costs that might be encountered during the development process, 
regulatory risks, including risks relating to the acquisition of the necessary 
licenses and permits, financing, capitalization and liquidity risks, including 
the risk that the financing necessary to fund the exploration and development 
activities at the Tiger Deposit may not be available on satisfactory terms, or 
at all, risks related to disputes concerning property titles and interest, and 
environmental risks. This list is not exhaustive of the factors that may affect 
any of the Company's forward-looking information. These and other factors 
should be considered carefully and readers should not place undue reliance on 
the Company's forward-looking information. The Company does not undertake to 
update any forward-looking information that may be made from time to time by 
the Company or on its behalf, except in accordance with applicable securities 
laws.

- 30 -

CONTACT INFO:

Vanessa Pickering, Manager, Corporate Communications
ATAC Resources Ltd.
T: 604-687-2522 ext. 260
vpickering@atacresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=491825567