Source	CANADA NEWSWIRE
Date	07/23/2014
Time	05:32:40 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol advances Atlas AGZ prospect in the Miocene belt of Chile with
new rock chip and trench gold - silver results





    CDNX Symbol: MRZ











Press Release	




" BC-MirasolMiningResults   07-23 1000
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Mirasol advances Atlas AGZ prospect in the Miocene belt of Chile with
new rock chip and trench gold - silver results@

VANCOUVER, July 23, 2014 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
Frankfurt: M8R)
--  At the AGZ (Atlas Gold Zone) prospect surface rock chip
sampling has outlined an 800 by 500 m area hosting multiple
gold-anomalous quartz-alunite alteration trends, with 55 of 473
rock chips assaying between 1.0 and 50.3 g/t gold.

--  Detailed re-sampling of existing AGZ trenches which lie within
the area of the rock chip gold anomaly returned best
length-weighted average channel samples of:

o 8.4 m at 1.85 g/t Au and 0.5 g/t Ag
o 11.3 m at 1.32 g/t Au and 7.3 g/t Ag
o 14.9 m at 1.67 g/t Au and 0.6 g/t Ag

--  Highest individual channel samples from the re-sampled trenches
include 1.2 m at 8.85 g/t Au and 45.8 g/t Ag, and 1.0 m at 5.63
g/t Au and 5.13 g/t Ag.
Mirasol Resources recently reported that it had outlined an 800 by 500 m
zone of anomalous gold and silver mineralization in rock chip float and
subcrop samples at its 100%-owned Atlas AGZ prospect (Figure 1; and see news
release of July 18, 2014). Of the 473 rock chip samples collected here, 55
have assayed between 1.0 to 50.3 g/t Au. These higher-grade samples are
interpreted to define a series of northwest-trending quartz-alunite alteration
zones with vuggy silica and hydrothermal breccias, hosted by andesitic lava
flows, or an andesitic flow dome.
The gold - silver trends are spatially associated with a 1 km long,
opened-ended highly resistive geophysical anomaly defined in Mirasol's recent
IP survey at Atlas. These resistive anomalies may represent hydrothermal
feeder zones or buried flow domes. Anomalous rock chip samples with assays in
the range 0.1 to 30.7 g/t Au and with Ag assays up to 56.9 g/t occur on the
margin, or over the top, of the buried resistive anomalies potentially
representing geochemical leakage from the covered geophysical features.
Mirasol also recently completed a detailed re-mapping and channel
re-sampling program (Figure 2) over the existing trenches at the AGZ prospect
to better understand the mineralization in the trenches and its relationship
to the Au and Ag-bearing quartz-alunite zones at surface. The best
length-weighted average trench channel results (Table 1) from this season's
sampling include 11.3 m at 1.32 g/t Au and 7.3 g/t Ag, and 14.9 m at 1.67 g/t
Au and 0.6 g/t Ag (at a 0.1 g/t Au equivalent cut-off). Higher-grade channel
intervals (at a 0.5 g/t Au equivalent cut-off) include 2 m at 4.91 g/t Au and
3.0 g/t Ag, and 2.2 m at 5.08 g/t Au and 26.0 g/t Ag.
The gold - silver mineralization in the AGZ trenches correlates to a
series of vuggy silica structures (Photo Gallery A, B, C) and alunite matrix
hydrothermal breccias (Photo Gallery D, E, F) with quartz-alunite alteration
halos. These structures and breccias are best developed over a 70 m section of
Trench 2, with individual vuggy silica structures ranging up to 4 m wide,
while the hydrothermal alunite matrix breccias are exposed for intervals of up
to 23 m along the trench wall (true width unknown at this stage). Mineralized
zones in the trenches show a strong correlation with the surface
quartz-alunite trends. The higher-grade surface rock chip trends, including
areas with rock chip assays up to 30.7 g/t Au and 42.3 g/t Ag identified this
season have not yet been trenched. This presents an excellent opportunity to
extend the mineralized zones.
The presence of abundant primary hypogene alunite and vuggy silica
alteration of the gold - silver host rock is consistent with a
high-sulphidation epithermal character to the AGZ mineralization. This type of
mineralization has produced both high-grade structurally-controlled and
open-pit bulk mineable gold-silver mines elsewhere in the Miocene belt of
Chile. All trench and surface rock chip samples at the AGZ are strongly
oxidized with no preserved sulphide recorded. This suggests the potential for
oxide-gold mineralization at the project.
Mirasol's geologists are processing results from surface sampling,
re-mapping and channel re-sampling of the Atlas Silver Zone (ASZ) trenches.
These results will be reported once complete.
Mirasol's management are very pleased with the exploration outcomes of
the 2014 summer program and the Atlas project where three prospects; the AGZ,
ASZ and Pampa zone have now been identified and new quality drill targets are
beginning to emerge at the AGZ prospect.
Stephen Nano, President and CEO is the Qualified Person under NI 43-101
who has prepared and approves the technical content of this news release.
Quality Assurance/Quality Control: Exploration at the Atlas Project is
supervised by Stephen C. Nano, who is the Qualified Person under NI 43-101 and
Timothy Heenan, Exploration Manager. All technical information for the
Company's projects is obtained and reported under a formal quality assurance
and quality control (QA/QC) program. All drill, rock chip and stream sediment
samples are collected under the supervision of Company geologists in
accordance with standard industry practice. Samples are dispatched via
transport to an ISO 9001:2000-accredited laboratory in Chile for analysis. All
drill, and rock chip samples are submitted to the Laboratory with
independently sourced, accredited standards and blanks and where appropriate
duplicate samples to facilitate monitoring of laboratory performance.
Certified Results are examined by an independent qualified consultant to
ensure laboratory performance meets required standards.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2014/23/c8491.html

-0-                           07/23/2014
/For further information:
Stephen Nano President and CEO
Tel : (604) 602-9989 Fax : (604) 609-9946
Email : contact(at)mirasolresources.com Website: www.mirasolresources.com
/
(MRZ.)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG PCS
SU:

-30-