Source	MARKET NEWS
Date	07/23/2014
Time	06:03:30 AM

Company	 Mirasol Resources Ltd.
Title	Advances 
Atlas AGZ Prospect In The Miocene Belt





    CDNX Symbol: MRZ











Press Release	





MIRASOL RESOURCES LTD ("MRZ-V;MRZLF-0")
- Advances Atlas AGZ Prospect In The Miocene Belt Of Chile With
- New Rock Chip And Trench Gold - Silver Results

At the AGZ (Atlas Gold Zone) prospect surface rock chip sampling
has outlined an 800 by 500 m area hosting multiple gold-anomalous
quartz-alunite alteration trends, with 55 of 473 rock chips assaying
between 1.0 and 50.3 g/t gold.

Detailed re-sampling of existing AGZ trenches which lie within the
area of the rock chip gold anomaly returned best length-weighted
average channel samples of:

8.4 m at 1.85 g/t Au and 0.5 g/t Ag
11.3 m at 1.32 g/t Au and 7.3 g/t Ag
14.9 m at 1.67 g/t Au and 0.6 g/t Ag

Highest individual channel samples from the re-sampled trenches
include 1.2 m at 8.85 g/t Au and 45.8 g/t Ag, and 1.0 m at 5.63 g/t Au
and 5.13 g/t Ag.

Mirasol Resources recently reported that it had outlined an 800 by
500 m zone of anomalous gold and silver mineralization in rock chip
float and subcrop samples at its 100%-owned Atlas AGZ prospect (Figure
1; and see news release of July 18, 2014). Of the 473 rock chip samples
collected here, 55 have assayed between 1.0 to 50.3 g/t Au.  These
higher-grade samples are interpreted to define a series of
northwest-trending quartz-alunite alteration zones with vuggy silica
and hydrothermal breccias, hosted by andesitic lava flows, or an
andesitic flow dome.

The gold - silver trends are spatially associated with a 1 km
long, opened-ended highly resistive geophysical anomaly defined in
Mirasol's recent IP survey at Atlas. These resistive anomalies may
represent hydrothermal feeder zones or buried flow domes.  Anomalous
rock chip samples with assays in the range 0.1 to 30.7 g/t Au and with
Ag assays up to 56.9 g/t occur on the margin, or over the top, of the
buried resistive anomalies potentially representing geochemical leakage
from the covered geophysical features.

Mirasol also recently completed a detailed re-mapping and channel
re-sampling program (Figure 2) over the existing trenches at the AGZ
prospect to better understand the mineralization in the trenches and
its relationship to the Au and Ag-bearing quartz-alunite zones at
surface. The best length-weighted average trench channel results (Table
1) from this season's sampling include 11.3 m at 1.32 g/t Au and 7.3
g/t Ag, and 14.9 m at 1.67 g/t Au and 0.6 g/t Ag (at a 0.1 g/t Au
equivalent cut-off). Higher-grade channel intervals (at a 0.5 g/t Au
equivalent cut-off) include 2 m at 4.91 g/t Au and 3.0 g/t Ag, and 2.2
m at 5.08 g/t Au and 26.0 g/t Ag.

The gold - silver mineralization in the AGZ trenches correlates to
a series of vuggy silica structures (Photo Gallery A, B, C) and alunite
matrix hydrothermal breccias (Photo Gallery D, E, F) with
quartz-alunite alteration halos. These structures and breccias are best
developed over a 70 m section of Trench 2, with individual vuggy silica
structures ranging up to 4 m wide, while the hydrothermal alunite
matrix breccias are exposed for intervals of up to 23 m along the
trench wall (true width unknown at this stage). Mineralized zones in
the trenches show a strong correlation with the surface quartz-alunite
trends. The higher-grade surface rock chip trends, including areas with
rock chip assays up to 30.7 g/t Au and 42.3 g/t Ag identified this
season have not yet been trenched. This presents an excellent
opportunity to extend the mineralized zones.

The presence of abundant primary hypogene alunite and vuggy silica
alteration of the gold - silver host rock is consistent with a
high-sulphidation epithermal character to the AGZ mineralization.  This
type of mineralization has produced both high-grade
structurally-controlled and open-pit bulk mineable gold-silver mines
elsewhere in the Miocene belt of Chile.  All trench and surface rock
chip samples at the AGZ are strongly oxidized with no preserved
sulphide recorded.  This suggests the potential for oxide-gold
mineralization at the project.

Mirasol's geologists are processing results from surface sampling,
re-mapping and channel re-sampling of the Atlas Silver Zone (ASZ)
trenches. These results will be reported once complete.

Mirasol's management are very pleased with the exploration
outcomes of the 2014 summer program and the Atlas project where three
prospects; the AGZ, ASZ and Pampa zone have now been identified and new
quality drill targets are beginning to emerge at the AGZ prospect.

Stephen Nano, President and CEO is the Qualified Person under NI
43-101 who has prepared and approves the technical content of this news
release.

Quality Assurance/Quality Control:

Exploration at the Atlas Project is supervised by Stephen C. Nano,
who is the Qualified Person under NI 43-101 and Timothy Heenan,
Exploration Manager.  All technical information for the Company's
projects is obtained and reported under a formal quality assurance and
quality control (QA/QC) program.  All drill, rock chip and stream
sediment samples are collected under the supervision of Company
geologists in accordance with standard industry practice.  Samples are
dispatched via transport to an ISO 9001:2000-accredited laboratory in
Chile for analysis.  All drill, and rock chip samples are submitted to
the Laboratory with independently sourced, accredited standards and
blanks and where appropriate duplicate samples to facilitate monitoring
of laboratory performance.  Certified Results are examined by an
independent qualified consultant to ensure laboratory performance meets
required standards.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release

SOURCE  Mirasol Resources Ltd.
TSX Venture closing price for MRZ-V
Date: 2014/07/22
Closing Price: 1.20

TEL:  (604) 602-9989  Stephen Nano, President and CEO
FAX:  (604) 609-9946
EMAIL:  contact@mirasolresources.com
INTERNET:  www.mirasolresources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1420300006TS11420300709-06010620140723