Source	CANADA NEWSWIRE
Date	07/23/2014
Time	11:09:25 AM

Company	 Search Minerals Inc.
Title	Search Minerals Announces Metallurgical Breakthrough for Rare Earth
Recovery





    CDNX Symbol: SMY











Press Release	




" BC-SearchRareEarthDscvry   07-23 2100
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business  Editors:
^Search Minerals Announces Metallurgical Breakthrough for Rare Earth
Recovery@

TORONTO, July 23, 2014 /CNW/ - Search Minerals Inc. ("Search" or the
"Company") (TSXV: SMY) and its wholly-owned subsidiary, Alterra Resources
Inc., are pleased to announce the development of a simplified metallurgical
process tested on a bulk sample from the Company's Foxtrot Project ("Foxtrot"
or the "Project"), located in the Port Hope Simpson Rare Earth Element
District in SE Labrador, to produce a high grade rare earth elements ("REE")
product for refining. A patent application has been lodged with the United
States Patent Office to protect the Company's ownership of this technology.
Support was received from the Research & Development Corporation ("RDC") of
Newfoundland and Labrador and from the Atlantic Canada Opportunities Agency
("ACOA") for this development. Testing was completed by SGS Canada Inc.
("SGS").
HIGHLIGHTS
--  A simple metallurgical treatment of coarse-crushed Foxtrot ore
has been demonstrated to give high overall extractions of rare
earths (73.1 to 78.9% for La-Er).  There is no longer any need
for grinding, flotation, gravity or magnetic separation to
treat the Foxtrot ore.
--  A crushed sample of Foxtrot ore (6 mesh, 3.35 mm) was treated
by acid (200 °C) and water leaching to extract rare earths.
Extraction from the ore ranged from 73.8 to 80% for La-Er and
55.9 to 69.9% for Tm-Lu.
--  The leachate was purified by pH adjustment, and then
precipitated to give a mixed carbonate precipitate.
--  The mixed carbonate was further refined by acid leaching,
oxalate re-precipitation and calcination to produce a high
grade rare earth oxide ("REO") containing low levels of key
impurities (including thorium) for refining to separate rare
earth products.
--  A larger demonstration test of the Company's technology is
scheduled for Q3 2014 at SGS.
--  Search is expected to enter into discussions with interested
parties for the refining of the high grade rare earth oxide
product starting in Q3 2014.
--  A United States Provisional Patent has been filed to protect
the new rare earth recovery process.

Stephen Keith, President and CEO of Search, commented on the findings,
"We are very pleased with these developments, as they are expected to
significantly lower the Foxtrot operating and capital costs. This innovative
technology should also allow the Company to move the Foxtrot Project more
quickly to development, resulting in long-term value growth for the Company."
A metallurgical sample of the Foxtrot ore (channel sample) was subjected
to a simple process of crushing and treatment with concentrated sulfuric acid.
The acid treated ore was water leached to extract REEs into the solution. The
leached solids were filtered and washed. The leachate containing REEs was
purified by a series of steps to produce a purified REO. The key steps
included purification by pH adjustment with magnesium carbonate, precipitation
of REEs with sodium carbonate, selective re-extraction of the REEs with
hydrochloric acid, re-precipitation of REEs with oxalic acid and, finally,
calcination of the rare earth oxalate to produce a REO for refining.
The results of the acid treatment/water leach are shown in Table 1. A
sample of Foxtrot ore was crushed to 6 mesh (approximately 3 mm in size) and
treated with 100 kg of H2So4 per tonne of ore at 200 °C for two hours. The
acid treated ore was then leached with water at 90 °C for 24 hours, followed
by filtration and washing to recover a filtrate. The extraction of impurity
elements like iron (Fe) and aluminum (Al) were controlled to 5.5 and 4.6%
respectfully.

________________________________________________________________________________
________________________
|   La |   Ce |   Pr |   Nd |   Sm |   Eu |   Gd |   Tb |   Dy |   Ho |   Y  
|   Er |   Tm |   Yb |   Lu |
|______|______|______|______|______|______|______|______|______|______|______|__
____|______|______|______|
| 76.7 | 78.1 | 79.6 | 80.0 | 79.6 | 79.1 | 78.4 | 79.3 | 77.5 | 76.0 | 77.0 | 
73.8 | 69.9 | 64.9 | 55.9 |
|______|______|______|______|______|______|______|______|______|______|______|__
____|______|______|______|
Table 1. REE Extractions (%) from Foxtrot Ore using Search's Simplified
Process
The water leachate was treated with magnesium carbonate to precipitate
impurities as a solid residue. The purified solution was then treated with
sodium carbonate to precipitate a mixed rare earth carbonate. The loss of REEs
in the purification process was low and the precipitation efficiency was high.
Table 2 summarizes the overall recoveries of REEs using the simplified
process.

________________________________________________________________________________
________________________
|   La |   Ce |   Pr |   Nd |   Sm |   Eu |   Gd |   Tb |   Dy |   Ho |   Y  
|   Er |   Tm |   Yb |   Lu |
|______|______|______|______|______|______|______|______|______|______|______|__
____|______|______|______|
| 75.9 | 77.3 | 78.9 | 79.3 | 78.9 | 78.4 | 77.6 | 78.4 | 78.7 | 75.3 | 76.3 | 
73.1 | 69.2 | 64.3 | 55.4 |
|______|______|______|______|______|______|______|______|______|______|______|__
____|______|______|______|
Table 2. Overall REE Recovery (%) from Foxtrot Ore to Mixed Carbonate
Precipitate using Search's Simplified Process
The rare earth carbonate precipitate was purified by selective releaching
in hydrochloric acid, precipitation with oxalic acid and calcination (to
convert the precipitate to a REO). The provisional analysis for the mixed REO
is shown in Table 3 (Chemical Analysis) and Table 4 (Impurity Analysis).

________________________
|    REO  | Analysis (%) |
|_________|______________|
|   La2O3 |      14.66   |
|_________|______________|
|   CeO2  |      34.89   |
|_________|______________|
|  Pr6O11 |       3.90   |
|_________|______________|
|   Nd2O3 |      15.28   |
|_________|______________|
|   Sm2O3 |       2.19   |
|_________|______________|
|   Eu2O3 |       0.12   |
|_________|______________|
|   Gd2O3 |       2.11   |
|_________|______________|
|   Tb4O7 |       0.33   |
|_________|______________|
|   Dy2O3 |       1.85   |
|_________|______________|
|   Ho2O3 |       0.36   |
|_________|______________|
|   Y2O3  |      10.02   |
|_________|______________|
|   Er2O3 |       0.98   |
|_________|______________|
|   Tm2O3 |       0.12   |
|_________|______________|
|   Yb2O3 |       0.61   |
|_________|______________|
|   Lu2O3 |       0.07   |
|_________|______________|
|         |              |
|_________|______________|
|   TREO(x) |       87.5   |
|_________|______________|
|  LREO(x)(x) |       68.7   |
|_________|______________|
| HREO(x)(x)(x) |       18.8   |
|_________|______________|
Table 3. Chemical Analysis (%) of the REO using ICP and XRF (Inductively
Coupled Plasma and X-Ray Fluorescence)
(x)TREO refers to the sum of all REs and Y as oxides (x)(x)LREO refers to the
sum of La, Ce, Pr, Nd oxides (x)(x)(x)HREO refers to the sum of Sm, Eu, Gd, Tb, 
Dy,
Ho, Er, Tm, Yb, Lu and Y oxides

__________________________
| Element | Analysis (g/t) |
|_________|________________|
|     Th  |         6.5    |
|_________|________________|
|      U  |         48.5   |
|_________|________________|
|     Si  |          <5    |
|_________|________________|
|     Al  |        <2000   |
|_________|________________|
|     Fe  |         744    |
|_________|________________|
|     Mg  |         316    |
|_________|________________|
|     Ca  |        <2000   |
|_________|________________|
|     Na  |        <1000   |
|_________|________________|
|      K  |        <1000   |
|_________|________________|
|     Ti  |         <40    |
|_________|________________|
|      P  |         <40    |
|_________|________________|
|     Mn  |          64    |
|_________|________________|
|     Zn  |         1490   |
|_________|________________|
|   F (%) |         0.15   |
|_________|________________|
|   C (%) |         0.02   |
|_________|________________|
Table 4. Impurity Analysis of the REO Note that fluoride (F) and carbon
(C) are reported as (%)
This process is a significant improvement over the earlier Foxtrot work
reported on May 9, 2012 (see "Search Minerals Announces Successful
Metallurgical Testing of Foxtrot Project Sample to Recover a 55.48% TREO +
Y2O3 Product (46.99% TREE+Y) with Overall Average Recovery of 78.8%"). The
steps of grinding, flotation, gravity and magnetic separation to produce an
ore concentrate are no longer required to process the Foxtrot ore. The coarse
crushed ore is directly treated with small amounts of acid in a heated pug
mill, a conventional mixing device, prior to water leaching.
A larger scale demonstration test will be performed at SGS in the Q3
2014. The test will provide data for engineering scale-up, optimization of
process parameters and production of a multi-kilogram REO product for sampling
to potential refining partners for evaluation. Search is now engaging with
potential refining partners to assess the technical and commercial
requirements for refining the high grade REO product from the Foxtrot ore.
Following completion of the demonstration of the Search's process, it is
expected that the revised economics of the Project will be developed by an
independent engineering contractor.
Search Minerals would like to recognize the support, totalling C$225,000,
made available equally from RDC and ACOA to assist in the development of
innovative technologies for the recovery and refining of REEs from ore mined
at the Project.
Qualified Person Dr. David Dreisinger, Ph.D., P.Eng., is the Company's
Vice President, Metallurgy and Qualified Person for the purposes of NI 43-101.
Dr. Dreisinger has reviewed and approved the technical disclosure contained in
this news release as applicable. The company will endeavour to meet high
standards of integrity, transparency, and consistency in reporting technical
content, including geological and assay (e.g., REE) data.
About The Foxtrot Project The Foxtrot Project in the Port Hope Simpson
Rare Earth Element District in southeastern Labrador has a positive
Preliminary Economic Assessment indicating a Life-of-Mine plan with indicated
mineral resources of 5.3 Mt, at an average grade of 0.89% Total Rare Earth
Elements ("TREE"), could be mined over 10 years, including open pit mining
TREE for the first 3.5 years and underground mining thereafter. Production at
the Project is anticipated to total 38 million kg of payable rare earth
material. Indicated mineral resources are estimated to total 9.23 Mt at 0.88%
TREE (or 1.07% Total Rare Earth Oxides ("TREO")), and inferred mineral
resources are estimated to total 5.17 Mt at 0.77% TREE (or 0.93% TREO).
Pending successful completion of a financing, Search is planning an
exploration program to further map and sample Foxtrot-like mineralization
throughout the Fox Harbour volcanic belt (see "Search Minerals Announces Ten
New Foxtrot-like REE Prospects in 64 km-long Mineralized Belt in SE Labrador",
October, 30, 2013) and to prioritize targets for a small exploration drilling
program. The aim of this program is to discover/document additional
Foxtrot-like deposits in close proximity to the Foxtrot Deposit, and to add to
the Foxtrot resource (currently 9.3 million tonnes Indicated at 189 ppm Dy,
and 5.2 million tonnes Inferred at 176 ppm Dy (see "Search Minerals Phase III
Drilling Increases Foxtrot REE Project Resource Estimate by 55% of Similar
Grade," November 1, 2012).
About Search Minerals Search Minerals Inc. (TSXV: SMY) is a TSX Venture
Exchange listed company focused on creating value through finding and
developing mineral assets with growing demand and constrained or restricted
supply, and with increasing use in innovative technologies. The Company is
actively pursuing opportunities and partnerships in critical metals,
including, but not limited to, tin, tungsten, dysprosium and neodymium,
prioritizing projects that can be partnered, funded and developed in a
relatively short period of time, in strategic, friendly jurisdictions.
Search is the discoverer of the Port Hope Simpson REE District, a highly
prospective light and heavy REE belt located in southeast Labrador, where the
Company controls a dominant land position in a belt 70 km long and up to 8 km
wide. In addition, Search holds a number of additional mineral prospects in
Newfoundland and Labrador in its portfolio, including claims in the Strange
Lake Complex (where Quest Rare Minerals has a Joint Venture with Search); and
at the Red Wine Complex (where Great Western Minerals Group has a Joint
Venture with Search).
All material information on the Company may be found on its website at
www.searchminerals.ca and on SEDAR at sedar.com.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility of the adequacy or accuracy of this release.
Cautionary Statement Regarding Forward-Looking Information: This news
release includes certain "forward-looking statements" under applicable
Canadian securities legislation that are not historical facts. Forward-looking
statements involve risks, uncertainties, and other factors that could cause
actual results, performance, prospects, and opportunities to differ materially
from those expressed or implied by such forward-looking statements. The
preliminary economic assessment is preliminary in nature, it includes inferred
mineral resources that are considered too speculative geologically to have the
economic considerations applied to them that would enable them to be
categorized as mineral reserves and there is no certainty that the preliminary
economic assessment will be realized. Mineral resources that are not mineral
reserves do not have demonstrated economic viability. Forward-looking
statements are necessarily based on a number of estimates and assumptions
that, while considered reasonable, are subject to known and unknown risks,
uncertainties and other factors which may cause actual results and future
events to differ materially from those expressed or implied by 
suchforward-looking statements. Such factors include, but are not limited to:
general business, economic and social uncertainties; litigation, legislative,
environmental and other judicial, regulatory, political and competitive
developments; and those additional risks set out in Search's public documents
filed on SEDAR at www.sedar.com. Although Search believes that the assumptions
and factors used in preparing the forward-looking statements are reasonable,
undue reliance should not be placed on these statements, which only apply as
of the date this news release and no assurance can be given that such events
will occur in the disclosed time frames or at all. Except where required by
law, Search disclaim any intention or obligation to update or revise any
forward-looking statement, whether as a result of new information, future
events, or otherwise.
SOURCE Search Minerals Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2014/23/c8533.html

-0-                           07/23/2014
/For further information:

Stephen Keith T: 416-368-8288 President & Chief Executive Officer
E: info(at)searchminerals.ca
/
(SMY.)

CO:  Search Minerals Inc.
ST:  Ontario
IN:  MNG
SU:

-30-