Source	MARKET NEWS
Date	07/23/2014
Time	11:09:52 AM

Company	 Search Minerals Inc.
Title	Metallurgical Breakthrough for Rare Earth Recove





    CDNX Symbol: SMY











Press Release	





Metallurgical Breakthrough for Rare Earth Recovery --->@NEWS RELEASE
SEARCH MINERALS INC ("SMY-V;SHCMF-0")
- Metallurgical Breakthrough for Rare Earth Recovery

Search Minerals Inc. ("Search" or the "Company") and its
wholly-owned subsidiary, Alterra Resources Inc., are pleased to
announce the development of a simplified metallurgical process tested
on a bulk sample from the Company's Foxtrot Project ("Foxtrot" or the
"Project"), located in the Port Hope Simpson Rare Earth Element
District in SE Labrador, to produce a high grade rare earth elements
("REE") product for refining. A patent application has been lodged with
the United States Patent Office to protect the Company's ownership of
this technology. Support was received from the Research & Development
Corporation ("RDC") of Newfoundland and Labrador and from the Atlantic
Canada Opportunities Agency ("ACOA") for this development. Testing was
completed by SGS Canada Inc. ("SGS").

HIGHLIGHTS

//st

A simple metallurgical treatment of coarse-crushed Foxtrot ore has been
demonstrated to give high overall extractions of rare earths (73.1 to
78.9% for La-Er).  There is no longer any need for grinding, flotation,
gravity or magnetic separation to treat the Foxtrot ore.
A crushed sample of Foxtrot ore (6 mesh, 3.35 mm) was treated by acid
(200 C) and water leaching to extract rare earths.  Extraction from  the
ore ranged from 73.8 to 80% for La-Er and 55.9 to 69.9% for Tm-Lu.
The leachate was purified by pH adjustment, and then precipitated to
give a mixed carbonate precipitate.
The mixed carbonate was further refined by acid leaching, oxalate
re-precipitation and calcination to produce a high grade rare earth  oxide
("REO") containing low levels of key impurities (including  thorium) for
refining to separate rare earth products.
A larger demonstration test of the Company's technology is scheduled
for  Q3 2014 at SGS.
Search is expected to enter into discussions with interested parties
for  the refining of the high grade rare earth oxide product starting in Q3
2014.
A United States Provisional Patent has been filed to protect the new
rare earth recovery process.

//et

Stephen Keith, President and CEO of Search, commented on the
findings, "We are very pleased with these developments, as they are
expected to significantly lower the Foxtrot operating and capital
costs. This innovative technology should also allow the Company to move
the Foxtrot Project more quickly to development, resulting in long-term
value growth for the Company."

A metallurgical sample of the Foxtrot ore (channel sample) was
subjected to a simple process of crushing and treatment with
concentrated sulfuric acid. The acid treated ore was water leached to
extract REEs into the solution. The leached solids were filtered and
washed. The leachate containing REEs was purified by a series of steps
to produce a purified REO. The key steps included purification by pH
adjustment with magnesium carbonate, precipitation of REEs with sodium
carbonate, selective re-extraction of the REEs with hydrochloric acid,
re-precipitation of REEs with oxalic acid and, finally, calcination of
the rare earth oxalate to produce a REO for refining.

The results of the acid treatment/water leach are shown in Table
1. A sample of Foxtrot ore was crushed to 6 mesh (approximately 3 mm in
size) and treated with 100 kg of H2So4 per tonne of ore at 200 C for
two hours. The acid treated ore was then leached with water at 90 C for
24 hours, followed by filtration and washing to recover a filtrate. The
extraction of impurity elements like iron (Fe) and aluminum (Al) were
controlled to 5.5 and 4.6% respectfully.

//st
La     Ce   Pr   Nd   Sm   Eu   Gd   Tb   Dy   Ho    Y   Er   Tm   Yb   Lu
76.7 78.1 79.6 80.0 79.6 79.1 78.4 79.3 77.5 76.0 77.0 73.8 69.9 64.9 55.9

//et

Table 1. REE Extractions (%) from Foxtrot Ore using Search's Simplified
Process

The water leachate was treated with magnesium carbonate to
precipitate impurities as a solid residue. The purified solution was
then treated with sodium carbonate to precipitate a mixed rare earth
carbonate. The loss of REEs in the purification process was low and the
precipitation efficiency was high. Table 2 summarizes the overall
recoveries of REEs using the simplified process.

//st
La     Ce   Pr   Nd   Sm   Eu   Gd   Tb   Dy   Ho    Y   Er   Tm   Yb   Lu
75.9 77.3 78.9 79.3 78.9 78.4 77.6 78.4 78.7 75.3 76.3 73.1 69.2 64.3 55.4

//et

Table 2. Overall REE Recovery (%) from Foxtrot Ore to Mixed Carbonate
Precipitate using Search's Simplified Process

The rare earth carbonate precipitate was purified by selective
releaching in hydrochloric acid, precipitation with oxalic acid and
calcination (to convert the precipitate to a REO). The provisional
analysis for the mixed REO is shown in Table 3 (Chemical Analysis) and
Table 4 (Impurity Analysis).

//st
REO                                         Analysis (%)
La2O3                                       14.66
CeO2                                        34.89
Pr6O11                                      3.90
Nd2O3                                       15.28
Sm2O3                                       2.19
Eu2O3                                       0.12
Gd2O3                                       2.11
Tb4O7                                       0.33
Dy2O3                                       1.85
Ho2O3                                       0.36
Y2O3                                        10.02
Er2O3                                       0.98
Tm2O3                                       0.12
Yb2O3                                       0.61
Lu2O3                                       0.07

TREO*                                       87.5
LREO**                                      68.7
HREO***                                     18.8

//et

Table 3. Chemical Analysis (%) of the REO using ICP and XRF (Inductively
Coupled Plasma and X-Ray Fluorescence)

*TREO refers to the sum of all REs and Y as oxides

**LREO refers to the sum of La, Ce, Pr, Nd oxides

***HREO refers to the sum of Sm, Eu, Gd, Tb, Dy, Ho, Er, Tm, Yb,
Lu and Y oxides

//st
Element                                     Analysis (g/t)
Th                                          6.5
U                                           48.5
Si                                          (5
Al                                          (2000
Fe                                          744
Mg                                          316
Ca                                          (2000
Na                                          (1000
K                                           (1000
Ti                                          (40
P                                           (40
Mn                                          64
Zn                                          1490
F (%)                                       0.15
C (%)                                       0.02

//et

Table 4. Impurity Analysis of the REO
Note that fluoride (F) and carbon (C) are reported as (%)

This process is a significant improvement over the earlier Foxtrot
work reported on May 9, 2012 (see "Search Minerals Announces Successful
Metallurgical Testing of Foxtrot Project Sample to Recover a 55.48%
TREO + Y2O3 Product (46.99% TREE+Y) with Overall Average Recovery of
78.8%"). The steps of grinding, flotation, gravity and magnetic
separation to produce an ore concentrate are no longer required to
process the Foxtrot ore. The coarse crushed ore is directly treated
with small amounts of acid in a heated pug mill, a conventional mixing
device, prior to water leaching.

A larger scale demonstration test will be performed at SGS in the
Q3 2014. The test will provide data for engineering scale-up,
optimization of process parameters and production of a multi-kilogram
REO product for sampling to potential refining partners for evaluation.
Search is now engaging with potential refining partners to assess the
technical and commercial requirements for refining the high grade REO
product from the Foxtrot ore. Following completion of the demonstration
of the Search's process, it is expected that the revised economics of
the Project will be developed by an independent engineering contractor.


Search Minerals would like to recognize the support, totalling
C$225,000, made available equally from RDC and ACOA to assist in the
development of innovative technologies for the recovery and refining of
REEs from ore mined at the Project.

Qualified Person

Dr. David Dreisinger, Ph.D., P.Eng., is the Company's Vice
President, Metallurgy and Qualified Person for the purposes of NI
43-101. Dr. Dreisinger has reviewed and approved the technical
disclosure contained in this news release as applicable. The company
will endeavour to meet high standards of integrity, transparency, and
consistency in reporting technical content, including geological and
assay (e.g., REE) data.

About The Foxtrot Project

The Foxtrot Project in the Port Hope Simpson Rare Earth Element
District in southeastern Labrador has a positive Preliminary Economic
Assessment indicating a Life-of-Mine plan with indicated mineral
resources of 5.3 Mt, at an average grade of 0.89% Total Rare Earth
Elements ("TREE"), could be mined over 10 years, including open pit
mining TREE for the first 3.5 years and underground mining thereafter.
Production at the Project is anticipated to total 38 million kg of
payable rare earth material. Indicated mineral resources are estimated
to total 9.23 Mt at 0.88% TREE (or 1.07% Total Rare Earth Oxides
("TREO")), and inferred mineral resources are estimated to total 5.17
Mt at 0.77% TREE (or 0.93% TREO).

Pending successful completion of a financing, Search is planning
an exploration program to further map and sample Foxtrot-like
mineralization throughout the Fox Harbour volcanic belt (see "Search
Minerals Announces Ten New Foxtrot-like REE Prospects in 64 km-long
Mineralized Belt in SE Labrador", October, 30, 2013) and to prioritize
targets for a small exploration drilling program. The aim of this
program is to discover/document additional Foxtrot-like deposits in
close proximity to the Foxtrot Deposit, and to add to the Foxtrot
resource (currently 9.3 million tonnes Indicated at 189 ppm Dy, and 5.2
million tonnes Inferred at 176 ppm Dy (see "Search Minerals Phase III
Drilling Increases Foxtrot REE Project Resource Estimate by 55% of
Similar Grade," November 1, 2012).

About Search Minerals

Search Minerals Inc. (TSXV: SMY) is a TSX Venture Exchange listed
company focused on creating value through finding and developing
mineral assets with growing demand and constrained or restricted
supply, and with increasing use in innovative technologies. The Company
is actively pursuing opportunities and partnerships in critical metals,
including, but not limited to, tin, tungsten, dysprosium and neodymium,
prioritizing projects that can be partnered, funded and developed in a
relatively short period of time, in strategic, friendly jurisdictions.

Search is the discoverer of the Port Hope Simpson REE District, a
highly prospective light and heavy REE belt located in southeast
Labrador, where the Company controls a dominant land position in a belt
70 km long and up to 8 km wide. In addition, Search holds a number of
additional mineral prospects in Newfoundland and Labrador in its
portfolio, including claims in the Strange Lake Complex (where Quest
Rare Minerals has a Joint Venture with Search); and at the Red Wine
Complex (where Great Western Minerals Group has a Joint Venture with
Search).

All material information on the Company may be found on its
website at www.searchminerals.ca and on SEDAR at sedar.com.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility of the adequacy or accuracy of this
release.

Cautionary Statement Regarding Forward-Looking Information:

This news release includes certain "forward-looking statements"
under applicable Canadian securities legislation that are not
historical facts. Forward-looking statements involve risks,
uncertainties, and other factors that could cause actual results,
performance, prospects, and opportunities to differ materially from
those expressed or implied by such forward-looking statements. The
preliminary economic assessment is preliminary in nature, it includes
inferred mineral resources that are considered too speculative
geologically to have the economic considerations applied to them that
would enable them to be categorized as mineral reserves and there is no
certainty that the preliminary economic assessment will be realized.
Mineral resources that are not mineral reserves do not have
demonstrated economic viability. Forward-looking statements are
necessarily based on a number of estimates and assumptions that, while
considered reasonable, are subject to known and unknown risks,
uncertainties and other factors which may cause actual results and
future events to differ materially from those expressed or implied by
such forward-looking statements. Such factors include, but are not
limited to: general business, economic and social uncertainties;
litigation, legislative, environmental and other judicial, regulatory,
political and competitive developments; and those additional risks set
out in Search's public documents filed on SEDAR at www.sedar.com.
Although Search believes that the assumptions and factors used in
preparing the forward-looking statements are reasonable, undue reliance
should not be placed on these statements, which only apply as of the
date this news release and no assurance can be given that such events
will occur in the disclosed time frames or at all. Except where
required by law, Search disclaim any intention or obligation to update
or revise any forward-looking statement, whether as a result of new
information, future events, or otherwise.

TSX Venture closing price for SMY-V
Date: 2014/07/22
Closing Price: 0.03

TEL:      416-368-8288 Stephen Keith, President & CEO
E-mail:   info@searchminerals.ca
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1420300031TS11420301826-11084720140723