Source	MARKET NEWS
Date	07/28/2014
Time	04:31:30 AM

Company	 Victoria Gold Corp.
Title	Continues to 
Receive High Grade Results at Olive





    CDNX Symbol: VIT











Press Release	





VICTORIA GOLD CORP ("VIT-V")
- Continues to Receive High Grade Results at Olive; $3 million
- Phase 2 Development Program Approved

Victoria Gold Corp. "Victoria" or the "Company" is pleased to
announce commencement of the 2014 Phase 2 Olive exploration program
following receipt of additional high grade gold intercepts from the
2014 Phase 1 program at the Olive Zone, adjacent to Victoria's Eagle
Gold deposit, Yukon Canada.

Mr. John McConnell, President and CEO of Victoria commented "Our
confidence continues to increase that the Olive Zone will have a
meaningful economic impact on the proposed Eagle Gold Mine. We intend
to demonstrate this through a maiden Olive Resource Estimate followed
by an update to the Eagle Feasibility Study and economic model with the
incorporation of Olive."

Phase 1 Program

Drilling

Victoria's 2014 Phase 1 Olive Exploration program included 20
diamond drill holes, 3 of which were used solely for metallurgical
testing. The first 5 diamond drill holes from the Phase 1 program
yielded highly encouraging results including 69.7m of 2.29 g/t gold and
96.1m of 1.22 g/t gold (see News Release dated June 24, 2014).

Victoria has received assay results for an additional 6, Phase 1
holes including 31.5 m of 2.19 g/t gold and 35.3 m of 1.67 g/t gold. A
summary of mineralized intervals from assay results from the latest 6
holes is presented below.

//st

-----------------------------------------------
|Table 1 -                                    |
|Summary of                                   |
|the Olive                                    |
|Zone Phase                                   |
|1 Diamond                                    |
|Drilling                                     |
|Results                                      |
|for                                          |
|DG14-587C                                    |
|through                                      |
|DG14-594C                                    |
|---------------------------------------------|
|Hole ID  |From (m)|To (m)|Length (m)|Au (g/t)|
|---------------------------------------------|
|DG14-587C|metallurgical test hole            |
|---------------------------------------------|

|---------------------------------------------|
|DG14-588C|46.2    |146.0 |99.9      |1.02    |
|---------------------------------------------|
|including|46.2    |77.7  |31.5      |2.19    |
|---------------------------------------------|

|---------------------------------------------|
|DG14-589C|metallurgical test hole            |
|---------------------------------------------|

|---------------------------------------------|
|DG14-590C|36.6    |131.1 |94.5      |0.99    |
|---------------------------------------------|
|including|74.4    |109.7 |35.3      |1.67    |
|---------------------------------------------|

|---------------------------------------------|
|DG14-591C|metallurgical test hole            |
|---------------------------------------------|

|---------------------------------------------|
|DG14-592C|15.2    |47.8  |32.6      |0.97    |
|---------------------------------------------|

|---------------------------------------------|
|DG14-593C|165.1   |175.9 |10.8      |0.91    |
|---------------------------------------------|

|---------------------------------------------|
|DG14-594C|145.1   |150.2 |5.1       |1.38    |
|---------------------------------------------|

|---------------------------------------------|
|DG14-595C|40.9    |52.5  |11.6      |0.71    |
-----------------------------------------------

//et

Note: Reported intersections are drilled intersections, as true
widths have not yet been determined.

Assays are pending for 6 additional Phase 1 exploration diamond
drill holes targeting the North-East extent of the mineralized Olive
Shear Zone. An updated plan map and drill sections relating to the
assay results presented above will be available on the Company's
website.

Metallurgy

As part of the Phase 1 program, Victoria engaged Kappes Cassidy &
Associates of Reno, NV ('KCA') to conduct additional metallurgical
testing on Olive samples. Initial tests to support moving forward on a
Phase 2 program included 96-hour bottle roll tests on 3 composite oxide
and 3 composite sulphide samples. Importantly, all samples were tested
using a crush size to match the proposed crushing facility at Eagle
(P80 6.3 mm). Gold recovery exceeded management expectations and
averaged 61% on the oxide samples at a P80 6.3mm crush size or 93% at a
grind size of 75 microns. While the average oxide recovery is less than
Eagle, the higher grade targeted at Olive is anticipated to result in
materially higher recovered grade than the average recovered grade at
Eagle.

With results from 11 of 17 diamond drill holes and metallurgy now
in hand, Victoria has confidence the Phase 1 exploration objectives
were achieved, namely:

1)The identification of near surface mineralization with gold
grades in excess of 1 g/t over significant intervals;

2)Definition of significant tonnage (in excess of 10 million
tonnes) to materially influence the mine plan at Eagle; and

3)Confirmed near surface oxide material is amenable to heap
leaching and would add to the total recovered gold at Eagle.

Phase 2 Program

Victoria's Board of Directors have approved the 2014 Phase 2 Olive
Exploration program. The Phase 2 program is underway and entails
continued delineation of the high grade Olive Zone as well as
exploration drilling along strike to the North-East and South-West of
the Phase 1 drilling.

Objectives

The objectives of the Phase 2 exploration program include:

1)Completion of sufficient step out and in-fill drilling to
prepare a NI 43-101 Resource Estimate including an Indicated Resource;

2)Completion of sufficient metallurgical testing, including bulk
column testing, to enable a Qualified Person ('QP') to sign off on
feasibility study level engineering for gold recovery;

3)Completion of sufficient geotechnical drilling to enable a QP to
develop a feasibility study level mine plan;

4)Update of the 2012 Eagle Feasibility Study to include:

A mine plan with additional ore from Olive;

An update to the capital estimate and operating expense estimate;
and

Incorporation of potential capital cost savings while preserving
the currently permitted project scope pursuant to the positive YESAA
decision document issued for Eagle (see News Release dated February 19,
2013).

Analytical Method

All drill core from the Olive 2014 drilling program was analyzed
at ALS Laboratories of Vancouver, B.C. utilizing the ME-ICP61
33-element analytical package with AuAA-24 Fire Assay finish for gold
on all samples. All core samples were split on-site at Victoria's Eagle
camp and shipped to ALS Laboratories preparation facility in Whitehorse
where samples were sorted and crushed to appropriate particle size
(pulp) and representatively split to a smaller size for shipment to
ALS' Vancouver analysis facility. A comprehensive system of standards,
blanks and field duplicates was implemented in the 2014 exploration
program and is monitored as chemical assay data become available.

Qualified Person

The technical content of this news release has been reviewed and
approved by Paul D. Gray, P.Geo., as the Qualified Person.

About Olive

The Olive Zone target is defined by a broad gold/arsenic in-soils
geochemical anomaly and lies on the intrusive-sediment contact of the
Potato Hills Trend (as does the Eagle Deposit) and is punctuated by
several historically exploited high-grade sulphide veins. The Olive
area was mined on a small scale from shallow shafts and adits in the
early 1900's and via placer mining in creeks draining the area. The
Olive vein system is located near the top of Olive Gulch and consists
of gold-bearing quartz-scorodite-arsenopyrite vein material centralized
in a shear zone structure.

About the Dublin Gulch Project

Victoria Gold's 100%-owned Dublin Gulch gold property is situated
in the central Yukon Territory, Canada, approximately 375 kilometers
north of the capital city of Whitehorse, and approximately 85
kilometers from the town of Mayo. The Property is accessible by road
year-round, and is located within Yukon Energy's electrical grid. The
Company has constructed and maintains a 100 person all-season camp at
the project site.

The Property covers an area of approximately 555 square
kilometers, and is the site of the Company's Eagle Gold Deposit. The
Eagle Gold Deposit is expected to be Yukon's next operating gold mine
and includes Probable Reserves of 2.3 million ozs of gold from 92
million tonnes of ore with a grade of 0.78 grams of gold per tonne, as
outlined in a National Instrument 43-101 feasibility study. The NI
43-101 Mineral Resource has been estimated to host 222 million tonnes
averaging 0.68 grams of gold per tonne, containing 4.9 million ounces
of gold in the "Indicated" category, inclusive of Probable Reserves,
and a further 78 million tonnes averaging 0.60 grams of gold per tonne,
containing 1.5 million ounces of gold in the "Inferred" category.

Cautionary Language and Forward-Looking Statements
Neither the TSX Venture Exchange, nor its Regulation Services
Provider accepts responsibility for the adequacy or accuracy of this
release. This press release includes certain statements that may be
deemed "forward-looking statements". All statements in this discussion,
other than statements of historical facts, that address future
exploration drilling, exploration activities, anticipated metal
production, internal rate of return, estimated ore grades, commencement
of production estimates and projected exploration and capital
expenditures (including costs and other estimates upon which such
projections are based) and events or developments that the Company
expects, are forward looking statements. Although the Company believes
the expectations expressed in such forward looking statements are based
on reasonable assumptions, such statements are not guarantees of future
performance and actual results or developments may differ materially
from those in forward-looking statements. Factors that could cause
actual results to differ materially from those in forward-looking
statements include metal prices, exploration successes, continued
availability of capital and financing, and general economic, market or
business conditions. Accordingly, readers should not place undue
reliance on forward-looking statements.

TSX Venture closing price for VIT-V
Date: 2014/07/25
Closing Price: 0.14

TEL: 416-866-8800     John McConnell
FAX: 416-866-8801     President & CEO
www.vitgoldcorp.com   Victoria Gold Corp
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1420800001TS11420800272-04300320140728