Source	Marketwire
Date	07/29/2014
Time	05:45:09 AM

Company	 ROCKHAVEN RESOURCES LTD.
Title	Rockhaven Resources Ltd. Drills 66.20 g/t Gold and 403 g/t Silver (74.26 
g/t Gold EQ) over 1.00 m and 26.71 g/t Gold and 172 g/t Silver (30.15 g/t Gold 
EQ) over 2.98 m at the Klaza Project, Yukon





    CDNX Symbol: RK











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Rockhaven Resources Ltd.

TSX VENTURE SYMBOL: RK

July 29, 2014

Rockhaven Resources Ltd. Drills 66.20 g/t Gold and 403 g/t Silver (74.26 g/t 
Gold EQ) over 1.00 m and 26.71 g/t Gold and 172 g/t Silver (30.15 g/t Gold EQ) 
over 2.98 m at the Klaza Project, Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 29, 2014) - Rockhaven 
Resources Ltd. (TSX VENTURE:RK) ("Rockhaven") is pleased to announce results 
for twelve additional drill holes from the Western BRX Zone at its 100%-owned 
and road-accessible Klaza property, located in the Dawson Range Gold Belt of 
southern Yukon. The most recent results continue to delineate areas of 
high-grade gold and silver mineralization within the Western BRX Zone (See News 
Release dated July 15th 2014 and July 22nd 2014). The current 12,000 m diamond 
drill program is focusing on the BRX and Klaza Zones which are two of the nine 
well-mineralized structural zones that have been identified on the property.

Highlights from the new drill holes testing the Western BRX Zone are as follows:

/T/

--  26.71 g/t gold and 172 g/t silver (30.15 g/t gold EQ(i)) over 2.98 m
including 38.20 g/t gold and 333 g/t silver (44.86 g/t gold EQ) over
1.16 m - Hole 150
--  22.43 g/t gold and 245 g/t silver (27.33 g/t gold EQ) over 3.21 m
including 64.90 g/t gold and 725 g/t silver (79.40 g/t gold EQ) over
0.72 m - Hole 151
--  11.10 g/t gold and 86.8 g/t silver (12.84 g/t gold EQ) over 2.10 m -
Hole 152
--  14.30 g/t gold and 142 g/t silver (17.14 g/t gold EQ) over 2.06 m
including 32.20 g/t gold and 252 g/t silver (37.24 g/t gold EQ) over
0.76 m - Hole 153
--  66.20 g/t gold and 403 g/t silver (74.26 g/t gold EQ) over 1.00 m - Hole
154
--  14.30 g/t gold and 513 g/t silver (24.56 g/t gold EQ) over 0.97 m - Hole
156
--  9.65 g/t gold and 240 g/t silver (14.45 g/t gold EQ) over 1.74 m - Hole
157
--  12.28 g/t gold and 123 g/t silver (14.74 g/t gold EQ) over 1.39 m and
42.00 g/t gold and 432 g/t silver (50.64 g/t gold EQ) over 0.50 m - Hole
158

/T/

"The current drill program is proving to be highly successful and is validating 
that the Western BRX Zone is a significant gold-silver discovery," stated Matt 
Turner, CEO of Rockhaven Resources. "The new holes continue to indicate 
exceptional continuity and size potential and are encouraging Rockhaven to test 
this target further along strike and at depth."

Western BRX Zone

The Western BRX Zone is the main target of the 2014 diamond drill program. The 
zone consists of three linear vein structures which have been traced over a 750 
m strike length and from surface to a maximum down-dip depth of 400 m. The 
highest grade veins are emplaced directly adjacent to or in close proximity to 
the hanging wall (BRXh) and footwall (BRXf) contacts of a feldspar porphyry 
dyke that can be traced along the length of the zone. A secondary vein (BRXb), 
located 20 to 70 m into the hanging wall of the dyke, is oriented slightly 
oblique to the main veins. This vein appears to be unaffected by cross-cut 
faults that off-set the main veins and may represent a later-stage mineralizing 
event.

A total of 23 of the 25 holes reported from 2014 drilling at the Western BRX 
Zone have tested a 580 m section of this 750 m long zone. The other two holes 
have defined a post-mineralization cross-fault that off-sets the zone.

Significant new results are shown in the table below.

/T/

----------------------------------------------------------------------------
From       To Interval     Gold   Silver  Gold EQ
Drill Hole     Zone ID      (m)      (m)     (m)+    (g/t)    (g/t) (g/t)(i)
----------------------------------------------------------------------------
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-149       Fault^    67.68    71.35     3.67     1.39     4.58     1.48
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-150         BRXh    46.49    49.47     2.98    26.71      172    30.15
-------------         ------------------------------------------------------
incl.                     46.49    47.17     0.68    51.50      181    55.12
-------------         ------------------------------------------------------
and incl.                 48.31    49.47     1.16    38.20      333    44.86
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-151         BRXb   142.95   144.20     1.25     1.50     77.8     3.06
----------------------------------------------------------------------------
and             BRXh+f   183.95   187.16     3.21    22.43      245    27.33
----------------------------------------------------------------------------
incl.             BRXh   183.95   184.75     0.80    31.00      310    37.20
----------------------------------------------------------------------------
and incl.         BRXf   186.44   187.16     0.72    64.90      725    79.40
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-152         BRXb     6.24     9.66     3.42     1.63     5.54     1.74
----------------------------------------------------------------------------
and               BRXf    62.14    64.24     2.10    11.10     86.8    12.84
-------------         ------------------------------------------------------
incl.                     62.14    62.83     0.69    25.20      163    28.46
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-153         BRXb    17.37    18.09     0.72     8.74     71.2    10.16
----------------------------------------------------------------------------
and               BRXh    63.30    67.10     3.80     4.47     23.8     4.95
-------------         ------------------------------------------------------
incl.                     66.70    67.10     0.40    19.10      112    21.34
----------------------------------------------------------------------------
and               BRXf    71.45    73.51     2.06    14.30      142    17.14
-------------         ------------------------------------------------------
incl.                     72.75    73.51     0.76    32.20      252    37.24
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-154         BRXh    46.70    47.70     1.00    66.20      403    74.26
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-155         BRXh   105.60   106.02     0.42     6.14      369    13.52
----------------------------------------------------------------------------
and               BRXf   116.70   117.02     0.32     3.09     18.8     3.47
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-156         BRXb   114.03   114.50     0.47     6.05      101     8.07
----------------------------------------------------------------------------
and               BRXh   196.32   198.81     2.49     5.68      253    10.74
-------------         ------------------------------------------------------
incl.                    197.84   198.81     0.97    14.30      513    24.56
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-157         BRXh    69.59    71.33     1.74     9.65      240    14.45
-------------         ------------------------------------------------------
incl.                     69.59    70.24     0.65    18.55      334    25.23
----------------------------------------------------------------------------
and               BRXf    79.52    79.93     0.41     1.58      777    17.12
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-158         BRXh   144.65   146.04     1.39    12.28      123    14.74
-------------         ------------------------------------------------------
incl.                    144.65   145.57     0.92    17.27      175    20.77
----------------------------------------------------------------------------
and               BRXf   163.12   163.88     0.76    27.84      291    33.66
-------------         ------------------------------------------------------
incl.                    163.12   163.62     0.50    42.00      432    50.64
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-160         BRXh    74.20    76.14     1.94     2.15     88.4     3.92
----------------------------------------------------------------------------

----------------------------------------------------------------------------
KL-14-161         BRXh    36.91    37.37     0.46     0.47      110     2.67
----------------------------------------------------------------------------

+ Represents the diamond drill hole length. True widths are estimated to be
approximately 80-90% of the interval.
(i) Gold equivalence (EQ) has been calculated using metal prices of $1300
per ounce gold and $26.00 per ounce silver, to be consistent with earlier
calculations and assumes 100% recoveries of both metals.
^ KL-14-149 appears to have entered an offset fault that post-dates
mineralization before testing the Western BRX Zone structure.
KL-14-159 is an exploration hole from elsewhere on the property. Results
from this hole are pending.

/T/

Drilling and trenching at the road-accessible Klaza property since 2010 have 
identified nine main mineralized structural zones and numerous subsidiary 
structures within a 2,000 by 4,000 m corridor. Individually, the main zones 
range from 1 to 75 m in width and are continuously mineralized over strike 
lengths of 250 to 2,400 m. The zones have been traced over a cumulative strike 
length of 9,400 m and all remain open for expansion along strike and to depth.

In 2014, a total of 9,500 m of diamond drilling has been completed in 54 holes 
at the Klaza property. Maps, sections and an expanded assay list which includes 
copper, lead and zinc values for the significant intervals can be viewed at the 
Company's website at www.rockhavenresources.com. Additional results will be 
released once assays are received, compiled and evaluated.

All analyses for rock and core samples from the 2014 program were performed by 
ALS Minerals with sample preparation in Whitehorse and assays and geochemical 
analyses in North Vancouver. Core samples are routinely analyzed for gold by 
fire assay followed by atomic absorption (Au-AA24) and 48 other elements by 
inductively coupled plasma-mass spectrometry (ME-MS61). Samples that exceed the 
detection limits of the routine methods are assayed for silver, copper, lead 
and zinc by inductively coupled plasma-atomic emission spectroscopy 
(Ag/Cu/Pb/Zn - OG62) and gold by gravimetric analysis (Au-GRA22). Rigorous 
procedures are in place regarding sample collection, chain of custody and data 
entry. Certified assay standards, coarse reject duplicates, field duplicates 
and blanks are routinely inserted into the sample stream to ensure integrity of 
the assay process. All of the results reported have passed the QAQC screening.

The 2014 program is managed by Archer, Cathro & Associates (1981) Limited 
(Archer Cathro). Technical information in this news release has been approved 
by Matthew R. Dumala, P.Eng., a geological engineer with Archer Cathro and 
qualified person for the purpose of National Instrument 43-101.

Rockhaven Resources Ltd. is a well-funded company focused on growth through 
exploration of its wholly-owned projects. For additional information concerning 
Rockhaven Resources Ltd. or its various exploration projects please visit 
Rockhaven's website at www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

- 30 -

CONTACT INFO:

Rockhaven Resources Ltd.
Matthew Turner
CEO and Director
604-688-2568
mturner@rockhavenresources.com
www.rockhavenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=492453343