Source	Marketwire
Date	07/31/2014
Time	05:00:34 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Results from 2014 Expansion Drilling at the Brodie 
Satellite Deposit, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

July 31, 2014

Scorpio Gold Reports Results from 2014 Expansion Drilling at the Brodie 
Satellite Deposit, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 31, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports 
additional results from its 2014 satellite deposit drilling program at the 70% 
owned Mineral Ridge project, located in Nevada. The Brodie deposit lies 
southwest of the currently producing Drinkwater and Mary/LC pits and is 
immediately adjacent to the leach pad.

On July 21, 2014, the Company reported an updated Life of Mine Plan ("LOM") for 
the Mineral Ridge Operation, which includes the currently producing Drinkwater 
and Mary/LC pits and five adjacent satellite deposits, including the Brodie 
deposit. The cut-off date for the LOM was March 31, 2014. Continued drilling 
since the March 31, 2014 cut-off date is designed to potentially upgrade and 
increase the reported mineral reserve and resource estimate and potentially 
extend life of mine. Drilling on the Brodie deposit continues to meet with 
success, returning significant intercepts both within and extending outside of 
the pit shell outlines modelled in the updated LOM.

Highlights from this latest phase of RC drilling on the Brodie deposit include:

/T/

--  MR14838: 10.34 grams per tonne ("g/t") gold over 6.10 meters
--  MR14839: 4.49 g/t gold over 3.05 meters
--  MR14847: 2.52 g/t gold over 7.62 meters
--  MR14942: 2.75 g/t gold over 21.34 meters
--  MR14943: 2.02 g/t gold over 6.10 meters

/T/

A drill hole location map is available at: 
www.scorpiogold.com/i/maps/mr/Brodie_DHplan.jpg.

Table 1. Brodie Deposit - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole         Azm    Dip From   To Width    From      To  Width   Gold   Gold
No.        (deg)  (deg) (ft) (ft)  (ft)     (m)     (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR14837        0    -90   10   15     5    3.05    4.57   1.52  0.012   0.41
----------------------------------------------------------------------------
MR14838      200    -61   80   85     5   24.38   25.91   1.52  0.011   0.38
----------------------------------------------------------------------------
115  135    20   35.05   41.15   6.10  0.302  10.34
----------------------------------------------------------------------------
incl.                    120  125     5   36.58   38.10   1.52   1.12  38.40
----------------------------------------------------------------------------
MR14839       78    -52   10   20    10    3.05    6.10   3.05  0.027   0.91
----------------------------------------------------------------------------
45   55    10   13.72   16.76   3.05  0.131   4.49
----------------------------------------------------------------------------
110  115     5   33.53   35.05   1.52  0.013   0.45
----------------------------------------------------------------------------
MR14840        0    -90   75   80     5   22.86   24.38   1.52  0.011   0.38
----------------------------------------------------------------------------
MR14841        0    -90   15   20     5    4.57    6.10   1.52  0.017   0.58
----------------------------------------------------------------------------
65   75    10   19.81   22.86   3.05  0.016   0.53
----------------------------------------------------------------------------
MR14842      351    -67    0   10    10    0.00    3.05   3.05  0.024   0.81
----------------------------------------------------------------------------
50   75    25   15.24   22.86   7.62  0.016   0.55
----------------------------------------------------------------------------
140  155    15   42.67   47.24   4.57  0.013   0.43
----------------------------------------------------------------------------
MR14843        0    -90   20   40    20    6.10   12.19   6.10  0.018   0.62
----------------------------------------------------------------------------
50   55     5   15.24   16.76   1.52  0.024   0.82
----------------------------------------------------------------------------
75   80     5   22.86   24.38   1.52  0.012   0.41
----------------------------------------------------------------------------
MR14847      336    -61   10   20    10    3.05    6.10   3.05  0.083   2.83
----------------------------------------------------------------------------
30   35     5    9.14   10.67   1.52  0.022   0.75
----------------------------------------------------------------------------
45   70    25   13.72   21.34   7.62  0.074   2.52
----------------------------------------------------------------------------
MR14848        0    -90                No Significant Results
----------------------------------------------------------------------------
MR14849        0    -90   50   55     5   15.24   16.76   1.52  0.033   1.13
----------------------------------------------------------------------------
70   75     5   21.34   22.86   1.52  0.015   0.51
----------------------------------------------------------------------------
MR14942        0    -90  140  175    35   42.67   53.34  10.67  0.017   0.60
----------------------------------------------------------------------------
195  205    10   59.44   62.48   3.05  0.015   0.50
----------------------------------------------------------------------------
215  240    25   65.53   73.15   7.62  0.011   0.39
----------------------------------------------------------------------------
265  335    70   80.77  102.11  21.34  0.080   2.75
----------------------------------------------------------------------------
365  390    25  111.25  118.87   7.62  0.012   0.43
----------------------------------------------------------------------------
445  450     5  135.64  137.16   1.52  0.020   0.70
----------------------------------------------------------------------------
460  470    10  140.21  143.26   3.05  0.016   0.55
----------------------------------------------------------------------------
MR14943        0    -90  190  195     5   57.91   59.44   1.52  0.022   0.75
----------------------------------------------------------------------------
245  270    25   74.68   82.30   7.62  0.028   0.96
----------------------------------------------------------------------------
280  295    15   85.34   89.92   4.57  0.010   0.34
----------------------------------------------------------------------------
335  355    20  102.11  108.20   6.10  0.059   2.02
----------------------------------------------------------------------------
375  400    25  114.30  121.92   7.62  0.019   0.64
----------------------------------------------------------------------------
MR14944        0    -90  255  270    15   77.72   82.30   4.57  0.025   0.86
----------------------------------------------------------------------------
390  415    25  118.87  126.49   7.62  0.030   1.03
----------------------------------------------------------------------------
435  455    20  132.59  138.68   6.10  0.018   0.60
----------------------------------------------------------------------------
MR14945        0    -90  205  210     5   62.48   64.01   1.52  0.021   0.73
----------------------------------------------------------------------------
220  230    10   67.06   70.10   3.05  0.015   0.50
----------------------------------------------------------------------------
260  265     5   79.25   80.77   1.52  0.012   0.42
----------------------------------------------------------------------------
280  310    30   85.34   94.49   9.14  0.016   0.56
----------------------------------------------------------------------------
320  330    10   97.54  100.58   3.05  0.026   0.90
----------------------------------------------------------------------------
385  455    70  117.35  138.68  21.34  0.016   0.55
----------------------------------------------------------------------------
MR141021       0    -90    0    5     5    0.00    1.52   1.52  0.051   1.76
----------------------------------------------------------------------------
20   25     5    6.10    7.62   1.52  0.011   0.37
----------------------------------------------------------------------------
MR141022       0    -90   20   25     5    6.10    7.62   1.52  0.056   1.91
----------------------------------------------------------------------------
130  135     5   39.62   41.15   1.52  0.038   1.31
----------------------------------------------------------------------------
205  210     5   62.48   64.01   1.52  0.018   0.60
----------------------------------------------------------------------------
230  235     5   70.10   71.63   1.52  0.019   0.65
----------------------------------------------------------------------------
435  440     5  132.59  134.11   1.52  0.021   0.72
----------------------------------------------------------------------------
MR141023       0    -90  170  180    10   51.82   54.86   3.05  0.031   1.06
----------------------------------------------------------------------------
MR141024       0    -90  215  225    10   65.53   68.58   3.05  0.048   1.65
----------------------------------------------------------------------------
MR141025       0    -90  285  290     5   86.87   88.39   1.52  0.014   0.48
----------------------------------------------------------------------------
MR141026       0    -90  300  305     5   91.44   92.96   1.52  0.014   0.48
----------------------------------------------------------------------------
MR141027       0    -90  150  155     5   45.72   47.24   1.52  0.032   1.10
----------------------------------------------------------------------------
170  175     5   51.82   53.34   1.52  0.012   0.41
----------------------------------------------------------------------------
185  190     5   56.39   57.91   1.52  0.016   0.55
----------------------------------------------------------------------------
MR141028       0    -90  220  225     5   67.06   68.58   1.52  0.016   0.55
----------------------------------------------------------------------------
235  240     5   71.63   73.15   1.52  0.011   0.38
----------------------------------------------------------------------------
MR141029       0    -90  115  120     5   35.05   36.58   1.52  0.039   1.34
----------------------------------------------------------------------------
140  150    10   42.67   45.72   3.05  0.050   1.71
----------------------------------------------------------------------------
215  220     5   65.53   67.06   1.52  0.014   0.48
----------------------------------------------------------------------------
MR141030       0    -90  150  175    25   45.72   53.34   7.62  0.037   1.25
----------------------------------------------------------------------------
205  230    25   62.48   70.10   7.62  0.031   1.06
----------------------------------------------------------------------------
245  250     5   74.68   76.20   1.52  0.014   0.48
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: www.scorpiogold.com/i/pdf/reports/QAQC-MR.pdf.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%), and Scorpio Gold is currently entitled to 
receive 80% of cash flow generated. Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's President, Steve Roebuck, PGeo, is a Qualified Person as defined 
by National Instrument 43-101 and has reviewed and approved the content of this 
release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.
The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including potential further exploration or development 
of the Brodie deposit, any potential expansion of the current pit shell 
outlines thereof, and any potential increase in the mineral reserve and 
resource estimate in respect thereof. Such forward-looking statements involve 
known and unknown risks, uncertainties and other factors that could cause 
actual events or results to differ materially from estimated or anticipated 
events or results implied or expressed in such forward-looking statements, 
including risks involved in mineral exploration and development programs and 
those risk factors outlined in the Company's Management Discussion and Analysis 
as filed on SEDAR. Any forward-looking statement speaks only as of the date on 
which it is made and, except as may be required by applicable securities laws, 
the Company disclaims any intent or obligation to update any forward-looking 
statement, whether as a result of new information, future events or results or 
otherwise. Forward-looking statements are not guarantees of future performance 
and accordingly undue reliance should not be put on such statements due to the 
inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Steve Roebuck
President
(819) 825-7618
sroebuck@scorpiogold.com
www.scorpiogold.com

or

Investor Relations:
Jim Macdonald
Torrey Hills Capital
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=492925477