Source	Marketwire
Date	07/06/2015
Time	05:30:28 AM

Company	 ANGEL GOLD CORP.
Title	Stream Sediment Sampling Results Identify 5 New Anomalous Gold Areas on 
Angel Gold's El Porvenir Project in Colombia





    CDNX Symbol: ANG











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Angel Gold Corp.

TSX VENTURE SYMBOL: ANG

July 6, 2015

Stream Sediment Sampling Results Identify 5 New Anomalous Gold Areas on Angel 
Gold's El Porvenir Project in Colombia


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 6, 2015) - Angel Gold Corp. 
(TSX VENTURE:ANG) ("Angel" or the "Company") is pleased to announce results 
from our recently completed stream geochemical sampling program. These results 
highlight five new priority gold targets. Individual assays ranged to 1480 ppb 
Au. In addition, analysis of the multi-element data has identified 
multi-element patterns and provide geochemical evidence for three large 
distinct, multi-element mineralized zones.

Results:

/T/

--  For the 80 sites sampled within the 60km2 property, individual gold
assays range from 0.1 ppb (parts per billion ) to a high of 1480 ppb. Of
these 80 assays, 42 are greater than 1.4ppb, of which 21 are greater
than  5ppb, 18 greater than 10ppb, and 5 greater than 100ppb - with a
peak value of 1480ppb Au. Specific gold anomalies become evident at 5ppb
but are generally greater than 10ppb Au. (For the discussion that
follows, values of 1.4 - 5.0 ppb Au are considered to be geochemically
anomalous, greater than 5.0 & less than 20 ppb as modestly anomalous,
greater than 20 & less than 100 ppb as strongly anomalous and greater
than  100 ppb as very strongly anomalous.)
--  3 large, weak yet distinct, multi-element anomalous areas have been
identified. Puna, located in the northeast sector of the property,
measures 6 km x 2.2 km, and overlies metamorphic rock units. Corales-
Guayabales is approximately 6.8 km x 5.2 km,strikes NNE, and overlies
predominantly Cretaceous aged black sediment units in the central area
of the property. Bagrecito is centred upon the southern portion of the
Bagre fault within the property limits, strikes N-S, and measures
approximately 6 km E-W x 5.3 km N-S. These areas possibly represent
buried intrusive/mineralizing centres.
--  Two completely different gold-silver multi-element anomaly patterns are
recognized: Au-Ag-Hg-Se-Te (represented by the Puna), and Au-Ag-Pb-Bi-As
(as seen for Corales-Guayabales). Bagrecito perhaps reflects the one
system locally overprinted by the other. These same multi-element
correlations were identified earlier during the re-assay of the historic
core samples. Thus they are extremely useful screening areas not only to
add confidence to areas with high Au values, but also ensure that areas
with low Au values are not overlooked.
--  The Puna Gold anomaly forms a core to the Puna multi-element area,
measures 2.6 km x 1.3 km, and is very strongly anomalous. Gold value for
samples from 3 adjacent drainages are 1,480 ppb, 91.2 ppb and 59.9 ppb.
The area is located to the NE of the Abejero Au occurrence and SE of the
Bominas Au occurrence, but there are no known artisanal mine workings
within the area.
--  The Nus-Corales gold anomaly comprises 5 contiguous drainages, is
modestly anomalous with a peak value of 23.6 ppb Au. Gold values for
other drainages were 4.6, 4.0, 3.0 and 2.2 ppb Au. The anomaly is
situated at the SW extent of the Corales-Guayabales multi-element
anomaly, lies between the Nus fault and the new discovered "Corales"
intrusive and is some 1.8 km in strike length. This anomalous area is
further enhanced by the fact that the Nus Fault at one point in this
area was observed to be a 2m wide quartz-veined and pyritic
shear/breccia, with at least six 3 to 5m wide quartz-veined and sulfide-
bearing silicified zones that occur on both sides of the fault over a
minimum width of 60m. There were no previously known artisanal mines in
this area, though one has since been discovered on the Nus Fault itself.
--  The Segovia Batholith gold anomaly is strong to very strongly anomalous,
extends northward from the Iguana gold occurrence to the property
boundary and is approximately 2 km wide. Stream sediment sample results
include 460ppb, 44.9 ppb, 30.4 ppb, 16.6 ppb, 14.2 ppb, 12.3 ppb, 3.1
ppb, 2.6 ppb, 1.9 ppb, and 0.7 ppb Au. Factors that heighten the
attractiveness of this area include a) evidence of widespread quartz
veining, b) signs of former artisanal mechanized alluvial mining in the
larger drainage channels and c) ongoing panning operations in smaller
channels. In addition, panning of the creeks during the stream sampling
program indicated the presence of widespread small gold nuggets of sugar
crystal size.
--  The modestly anomalous Southeast Metamorphic anomaly occurs in the SE
corner of the property. It comprises two adjacent drainages from which
gold values for stream sediment samples were 21.7 ppb Au and 5.9 ppb Au.
A value for a third sample with a drainage area mainly to the east of
the property was 51.2 ppb Au. There are no known artisanal mines in this
general area.
--  As its name implies, the Black Sediment Gold anomaly overlies black
sediment rock units. It is a single drainage anomaly of about 1 km2, the
sample from which had a very strongly anomalous value of 160 ppb Au. It
occurs in the north central part of the property in an area with no
known artisanal workings.
--  Samples were taken in the vicinity of the known Au occurrences Abejero,
Bominas and Guayabales. The value for the sample upstream from Abejero
assayed a modest 21.2 ppb Au, whereas values for samples upstream from
Bominas were geochemically anomalous. Values for three samples taken in
the vicinity of the Guayabales occurrence were modestly anomalous.

/T/

Maps of the results, and location of the anomalies referred to above, and an 
updated provisional geology map are posted on the Angel Gold website 
http://www.angelgoldcorp.com/index.php/projects/el-porvenir-project, as are 
photos of the porphyryitic Corales intrusive and jasperoid.

"We are extremely pleased with the results of our stream sampling program in 
that we have identified 5 new priority target areas in addition to our 
pre-existing targets." stated Stella Frias, President and CEO of Angel Gold 
Corp. "Our exploration efforts continue to confirm the potential of this 
under-explored property for gold mineralization, not only for additional 
structurally-hosted mineralization but also for other styles of mineralization 
as well."

Survey and Analytical Methodology

Sampling was of generally between 2 to 4 kg of active stream sediment, dried 
and sieved at ALS Medellin to -80# (180 micron). Assaying was carried out by 
ALS Peru, using method ST43-PKG with Au by 25g aqua regia digestion and ICP-MS 
finish, and 51 element ICP-MS (method ME-MS41). Quality control included the 
duplicating of 3 samples at the identical initial sample location, while 3 
other sites had replicate samples collected from 2 to 5 metres away. 
Additionally another 2 samples were each screened and split at the laboratory 
and each split assayed as consecutive samples. Two blanks and two standards 
were inserted. The laboratory splits, blanks and standards all repeated 
excellently. Of the repeat samples 4 repeated surprisingly well, but one 
duplicate and one replicate which repeated excellently for the multi-element 
suite showed large disparities with the original samples in gold assay. This 
variability in gold for separate samplings is as to be expected, as the 
presence or absence of a single flake of gold in the sample can produce highly 
variable assay results. For exactly this reason emphasis during anomaly 
interpretation has been placed on multiple-sample anomalies and multi-element 
anomalism and zonations rather than on individual absolute gold values.

There are 2 completely different gold-silver anomaly patterns: Au-Ag-Hg-Se-Te, 
and Au-Ag-Pb-Bi-As. Both stream anomaly associations correspond to observations 
from earlier multi-element correlations carried out over re-assayed historic 
drill samples. Aqua regia, rather than 4 acid digest, was specifically selected 
for use on the stream sediments, so it is expected that much of the metals 
anomalism - notably Sn, W, Co, Cu, Mo, Hg, Se, Te, Bi, As - would actually 
reflect contained values released from impure pyrites, and thus reflect a 
combination of impurity zonation patterns in weak pyritic haloes, as well as of 
different generations of pyrite mineralization.

Quality Person

Mr. James G. Burns, P.Eng, a Qualified Person under NI 43-101 and a technical 
advisor to the Company has reviewed and approved the technical information 
contained in this news release.

About Angel Gold Corp.:

Angel is a Canada-based gold exploration company focused on responsible 
development of mineral resources in Colombia, host to some of the world's 
largest gold deposits. Angel has been working in Colombia for over five years. 
The Company continues its strategy to acquire strategic opportunities in 
Colombia's best mining districts.

On Behalf of the Board of Directors of Angel Gold Corp.

Blanca Stella Frias, Director, President and Chief Executive Officer

Neither the TSX Venture Exchange nor the Investment Industry Regulatory 
Organization of Canada accepts responsibility for the adequacy or accuracy of 
this news release.

The TSX Venture Exchange has not reviewed the content of this News Release and 
therefore does not accept responsibility or liability for the adequacy or 
accuracy of the contents of this News Release. This news release contains 
certain "forward- looking statements" within the meaning of Section 21E of the 
United States Securities and Exchange Act of 1934, as amended. Except for 
statements of historical fact relating to the Company, certain information 
contained herein constitutes forward- looking statements. Forward-looking 
statements are based upon opinions and estimates of management at the date the 
statements are made, and are subject to a variety of risks and uncertainties 
and other factors which could cause actual results to differ materially from 
those projected in the forward looking statements. The reader is cautioned not 
to place undue reliance on forward-looking statements. The transaction 
described in this News Release is subject to a variety of conditions and risks 
which include but are not limited to: regulatory approval, shareholder 
approval, market conditions, legal due diligence for claim validity, financing, 
political risk, security risks at the property locations and other risks. As 
such, the reader is cautioned that there can be no guarantee that this 
transaction will complete as described in this News Release. We seek safe 
harbour.

- 30 -

CONTACT INFO:

For investor relations please contact:
Stella Frias
+57 321 427 6977
+1 (360) 650-1440
info@angelgoldcorp.com

or

Angel Gold Corp.
604-684-6264
Fax: 604-684-6242
info@angelgoldcorp.com
www.angelgoldcorp.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=534964305