Source	Marketwire
Date	07/07/2015
Time	05:36:42 PM

Company	 NICOLA MINING INC.
Title	Nicola Mining Inc. Completes Preliminary Exploration Program That Includes 
+0.9% Cu Sample on its Thule Copper Project, British Columbia





    CDNX Symbol: NIM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Nicola Mining Inc.

TSX VENTURE SYMBOL: NIM

July 7, 2015

Nicola Mining Inc. Completes Preliminary Exploration Program That Includes 
+0.9% Cu Sample on its Thule Copper Project, British Columbia


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 7, 2015) - Nicola Mining Inc. 
(the "Company" or "Nicola Mining") (TSX VENTURE:NIM) is pleased to announce 
that it has successfully completed a preliminary (Spring 2015) mineral 
exploration program on its Thule Project, which covers an area of 8,272 
hectares in the Nicola Mining Division, located 14 kilometres northwest of 
Merritt in southern British Columbia.

A total of 48 rock samples were collected over the property from 14 known 
mineral tenures (MINFILES) located within the Company's mineral tenure. 
(http://minfile.gov.bc.ca/default.aspx?page=searchresults&d=150706062917&10=50&1
1=10&12=9&13=50&14=15&15=60&16=120&17=52&18=39&19=121&20=1&21=33&22=NAD+83&t=0).

The rock samples consisted of grab samples from road-cut, outcrop and historic 
trench and shaft dumps. Copper values ranged from trace to 9080 ppm copper. The 
highest value, 9080 ppm copper sample (0.9% copper), was collected from trench 
dump material located at the TITAN QUEEN (092ISE034) historic showing. Surface 
copper mineralization above 2000 ppm was also verified at the MARB (092ISE033), 
ERIC (092ISE036) and the MARB 72 (092ISW037) mineral showings (MINFILES). 
Mineralization is primarily hosted 1) as malachite-mineralization along 
fracture zones within quartz diorite and potasically altered volcanics, 2) in 
quartz veins with finely disseminated chalcopyrite within quartz diorite, and 
3) within magnetite + epidote skarn-altered limy tuffs with malachite +/- 
azurite +/- chalcopyrite mineralization.

The 2015 Thule exploration program (the "Initial Program") consisted of five 
main objectives:

1. Examine known historical porphyry and skarn mineral showings (MINFILES).

2. Follow-up on geophysical trends defined in the 2012 helicopter aeromagnetic 
gradient and spectrometer survey, as highlighted on the Company's website. 
http://nicolamining.com/wp-content/uploads/2015/03/Geophysical_Interpretation_Me
mo.pdf.

3. Examine road cut and outcrop exposure along new logging roads.

4. Photo catalogue and re-log diamond drill core from Christopher James Gold 
Corp's 2005 drilling program on the Craigmont property.

5. To compile and digitize historical geochemical, geophysical, drilling and 
geological data. Nicola Mining has nine banker boxes worth of "hard copy" data, 
which includes historical air photos, internal memos, geological maps, more 
than 1000 underground drill logs, 100 surface drill logs, and over 100,000 
line-metres of ground geophysical data. Data and maps from over 100 BC 
Assessment Reports and property files available electronically are also being 
included in the electronic data compilation.

Future exploration work will consist of: 1) building upon the initial database 
compilation with the goal of generating a geological and mineralogical block 
model for the Craigmont mine site area and 2) further ground exploration work 
proximal to the MARB 72 and WP showings, with the goal of identifying 
additional porphyry-style targets.

Property Geology

An east-northeast trending, steeply dipping, volcanic pile of Upper Triassic 
Nicola Group rocks, bound to the north by the Early Jurassic-Late Triassic 
Guichon Creek Batholith and unconformably overlain by the Middle and Upper 
Cretaceous Spences Bridge Group underlies the Thule Property. Thick gravel 
overburden caps most of the Property.

The Thule Property hosts at least two types of mineralization described as 
copper-iron skarn and copper porphyry. Carbonate-rich, silicate-rich or 
intrusive rocks along the southern flanks of the Guichon Batholith host the two 
types of mineralization.

Several major faults cut through the property including the north-trending 
Lornex Fault on the west, responsible for controlling large-tonnage porphyry 
copper deposits to the north, including Valley, Lornex, Bethlehem and Highmont. 
Faults controlling mineralization around the mine include the northwest 
trending Embayment Faults, the Mine East Fault and the East-West fault.

Property History

The Property covers a large area along the southern extents of the Guichon 
Batholith where many of the copper prospects on the Property have been 
intermittently explored since as early as the 1930's. The most important 
discovery to date has been the past producing Craigmont Copper-Iron mine 
located in the central part of the claim holdings.

Craigmont was operated as an open-pit mine by Craigmont Mines Ltd. from 1961 to 
1967 and as an underground sub-level block cave mine from 1967 to 1982. Over 
its operating life, the mine produced 34,000,000 metric tonnes of ore averaging 
1.28% copper from Body No.1 and Body No. 2 
(http://nicolamining.com/wp-content/uploads/2015/03/Technical_Report_on_the_Thul
e_Copper_Iron_Property.pdf). A policy decision was made by the board of 
Craigmont to shut the mine down in 1982, at a time when the copper price was 
approximately $0.60 per pound.

From 1982 to 1992, Craigmont shipped up to 60,000 tonnes of clean metallurgical 
magnetite per year from its stockpile to coal producers in North America for 
use in the coal flotation process. After 1992, Craigmont continued to produce a 
limited amount of products for the coal industry from re-worked iron fines in 
the tailings pond.

On March 3, 2011, Nicola Mining (formerly Huldra Silver Inc.) agreed to buy all 
of the outstanding shares of Craigmont Holdings Ltd. in consideration for 
certain cash and share payments. Nicola Mining and the previous owners of the 
property are the shareholders of Thule Property, which is managed by Nicola 
Mining.

Historical Estimates

There are currently no mineral resource estimates on the Thule Property. 
Historical resource calculations are recorded in internal memos and geological 
reports for Placer Development. An internal memo written by J.F. Bristow on 
October 30, 1985 to Craigmont Mines Ltd. reported a zone known as "Body No. 3" 
contains a historical estimate of 1,290,000 tons of copper grading 1.53%(i). 
The estimate assumes a 0.7% cut-off and a 20 foot mining width between drill 
sections 6565E and 8015E. The material in Body No. 3 contains mineralization 
primarily in silicate-rich rocks.

Additionally, J.F. Bristow reported in an internal memo on July 22, 1985 to 
Craigmont Mines Limited a rough calculation of 27,754,000 tonnes of copper 
grading 1.79% copper left behind in the sub-level cave(i). The material is from 
the previously mined out No.1 Body and No.2 Body.

The Company is currently in the process of inputting historic drill holes and 
underground workings to assess the historical estimate of Body No. 3.

(i)These are historical resource estimates that do not comply with the current 
CIM Definition Standards on Mineral Resources and Mineral Reserves as required 
by NI 43-101. A Qualified Person has not done sufficient work to upgrade or 
classify these historical resources estimates to current mineral resources 
prepared in accordance with NI 43-101. The issuer is not treating the 
historical estimate as current mineral resources and the historical estimate 
should not be relied on.

Quality Assurance & Quality Control

Samples were described and sampled bagged, tagged, photographed, catalogued, 
sealed and sent to Activation Laboratories Ltd. in Kamloops (an ISO 17025 
certified lab which is independent of the company) for analysis using aqua 
regia partial extraction and ICP analysis for 24 elements with fire assay for 
gold. Due to the preliminary nature of the program, the company relied on 
internal laboratory standards, blanks and duplicates. A library sample from 
each sample location site was collected and is currently stored at the Merritt 
Mill facility.

The foregoing geological disclosure has been reviewed and verified by Brian 
May, P.Geo., a qualified person for the purpose of National Instrument 43-101, 
Standards of Disclosure for Mineral Projects.

Stock Option Grants

The Company also announces that it will grant investor relations and consulting 
firms an aggregate of 530,000 options, each exercisable into one common share 
of the Company at a price of $0.06 per share until June 19, 2019, pursuant to 
the conditions of the Company's Stock Option Plan.

Peter Espig, Chief Executive Officer, commented, "Nicola Mining continues to 
explore the potential of Thule Copper both internally and with third parties in 
order to better understand the asset and its potential. We are also excited 
about the Company's momentum and will place greater investor relations emphasis 
and efforts on explaining the Nicola Mining story in the future."

On behalf of the Board of Directors

Peter Espig, CEO & Director

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Disclaimer for Forward-Looking Information

This press release contains projections and forward-looking information that 
involve various risks and uncertainties regarding future events related to the 
Company's proposed exploration plans at its Thule property. Such 
forward-looking information includes statements based on current expectations 
involving a number of risks and uncertainties and are not guarantees of future 
performance of the Company, such as the Company's ability to finance its 
planned exploration; the Company's ability to source the necessary 
infrastructure to effect its exploration plans; current economic conditions and 
the state of mineral exploration and mineral prices in general. These risks and 
uncertainties could cause actual results, and the Company's plans and 
objectives, to differ materially from those expressed in the forward-looking 
information. The Company can offer no assurance that its exploration and 
development plans will be completed in the time expected or at all. These and 
all subsequent written and oral forward-looking information are based on 
estimates and opinions of management on the dates they are made and expressly 
qualified in their entirety by this notice. Except as required by law, the 
Company assumes no obligation to update forward-looking information should 
circumstances or management's estimates or opinions change.

- 30 -

CONTACT INFO:

Nicola Mining Inc.
Peter Espig
(604) 647-0142
peter@huldrasilver.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=535302814