Source	MARKET NEWS
Date	07/09/2015
Time	01:42:18 PM

Company	 Happy Creek Minerals Ltd.
Title	Identifies New Targets on the Rateria property,





    CDNX Symbol: HPY











Press Release	





Identifies New Targets on the Rateria property, Highland Valley B.C.Drill data 
from 1965 reports 60 metres of 0.40% copper at End of theHole --->@NEWS 
RELEASE
HAPPY CREEK MINERALS LTD ("HPY-V;HPYCF-0")
- Identifies New Targets on the Rateria property, Highland Valley
- B.C. Drill data from 1965 reports 60 metres of 0.40% copper at
- End of the Hole

Happy Creek Minerals Ltd. (the "Company) is pleased to provide an
update on its 100% owned Rateria copper property located in the
Highland Valley area of British Columbia. The property is over 180
square kilometres in area and adjoins Teck's Highland Valley Copper
mine property.

The Company has received and reviewed certain private exploration
data obtained during 1965, which contains information thought to be
pertinent to further exploration of the property. The data consists of
rough location maps, written drill logs, assays, and cross sections for
a number of relatively short diamond drill holes from several
prospects, including the Sho and Corridor area that is between Zone 1
and 2. Although the work was performed by qualified geologists, results
cannot be verified and as such they are considered to be historical in
nature and cannot be relied upon under NI43-101.

Historical results have been converted from imperial (feet) to
metric (metres) and difficult drilling is evident with holes having
frequent poor core recovery. A number of drill core sections where
malachite, chalcopyrite, bornite or chalcocite (copper minerals) was
noted in drill logs were not sampled.

The drill holes at the Sho prospect contain positive copper values
and include a drill hole returning 6.0 metres of 0.65% copper, 3.0
metres of 1.85% copper, and 18.39 metres of 0.30% copper with
un-sampled sections in-between and beyond these samples. For a drill
hole between Zone 1 and 2, core recovery was apparently so poor that
samples of the ground-up rock material (sludge) returned from the
bottom 60 metres were collected and averaged 0.40% copper. None of the
samples appear to have been analyzed for gold or molybdenum, however
several samples were analyzed for silver such as 0.60 m of 4.5% copper
100 g/t silver.

The historical drill data are from areas where positive and
sizeable modern three dimensional induced polarization (IP) geophysical
responses were obtained by the Company. They are thought to improve the
opportunity for new copper deposits to occur.

In June, these and other prospective areas of the Rateria property
were reviewed in the field. With the property 95% covered by glacial
till, outcrops are rare, however in a recently logged area several new,
small outcrop exposures occur about three kilometres south of the
Company's Zone 1. These outcrops (West Sho prospect) are adjacent a
strong north-south trending structure and a positive IP geophysical
response approximately one km by one km in dimension that extends over
500 metres in depth. The outcrops consist of strongly fractured Skeena
or Bethlehem phase rocks variably altered and veined with quartz,
sericite-muscovite and kaolin and locally malachite and iron oxide
staining.

David Blann, P.Eng., President of Happy Creek states: "The
historical drill data from the Sho prospect indicates more widespread
copper occurs than previously thought. The Sho is part of a sizable
geophysical target extending over 500 metres below surface and possibly
over one kilometre in length. In addition, the geology of new outcrops
at the West Sho along with a substantial geophysical target is very
positive. We are also encouraged with historical drilling results of 60
metres of 0.40% copper between Zone 1 and 2, which are both open in
extent. The new information increases confidence in two new large-scale
targets, and increases potential to expand Zone 1 and 2 further."

Summary of the 100% owned Rateria and West Valley property

Copper, molybdenum deposits of the Highland Valley district are
calc-alkaline porphyry systems hosted within the Guichon Batholith. The
Company has discovered two new copper zones on the Rateria property 6.5
km from a currently producing open pit. Drill results include 95.0
metres of 0.67% copper, 250.0 metres of 0.25% copper and 152.5 metres
of 0.35% copper, 0.06 g/t gold and 0.57 g/t rhenium in Zone 1 and 2,
respectively. Both Zone 1 and 2 are open in extent and have clear
resource potential with excellent metallurgical qualities. The Company
is also developing several prospective target areas on the
under-explored portions of the Rateria and West Valley property.

On behalf of the Board of Directors,

"David E Blann"

____________________
_______________________________________________
TSX Venture closing price for HPY-V
Date: 2015/07/08
Closing Price: 0.10
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1518900053TS11518902194-13405020150709