Source	MARKET NEWS
Date	07/22/2015
Time	07:17:38 AM

Company	 Westminster Resources Ltd.
Title	Multiple Gold and Silver Targets Discovered at G





    CDNX Symbol: WMR











Press Release	




[200/News Release]WMRVWESTMINSTER RESOURCES LTDJUL 22 2015  07:14 AM
Multiple Gold and Silver Targets Discovered at Guyacan Project --->@NEWS 
RELEASE
WESTMINSTER RESOURCES LTD. ("WMR-V")
- Multiple Gold and Silver Targets Discovered at Guyacan Project

Westminster Resources Ltd. ("the Company") reports 2015 results from
Guyacan targets located in the NW portion of the 100% owned 21,228 hectare
EL COBRE Property, Sonora Mexico.

Highlights from the rock sampling program are:

* North Guyacan : 12.1 g/t gold and 16.8 g/t silver

* Red Soil and SGH soil geochemical target : 11.3 g/t gold and 212.0 g/t
silver

* Middle Guyacan : 9.2 g/t gold and 9.9 g/t silver

* South Guyacan : 675 ppb gold and 126 g/t silver and 2.5 % copper

* South Guyacan-Far east : 18.0 g/t gold and 400 g/t silver

At this early stage, most samples are composite rock chip or selected grab
samples.

The 2015 work program to date has consisted of prospecting and field
geology. Previous exploration by the Company at Guyacan has included a
helicopter airborne VTEM-MAG geophysical survey, an extensive soil
geochemical survey (710 samples), a soil gas hydrocarbon geochemical survey
(1074 SGH samples), and geological mapping and prospecting, all
systematically completed during the 2011 - 2014 seasons. The exploration
programs have followed-up on anomalous circular and linear magnetic low
features obtained from the airborne VTEM-MAG geophysical helicopter survey.
The recent positive results have expanded the number, and defined in more
detail, zones of alteration and surface mineralization in subcrop-outcrop
across the 3.5 kilometer wide expression of the airborne circular magnetic
geophysical anomalous patterns. New discoveries included zones peripheral
to precious metal bearing porphyry systems, skarns, unroofed porphyry
system veins, stockworks and breccia vein mineralization.

The Guyacan target is situated in flat lying Sonora ranch lands with thin
young volcanic cover rocks or sand and gravel material overlying much of
the bedrock geophysical anomalies expression. The significant ASTER IMAGERY
patterns coincident with the disrupted airborne magnetic survey response of
circular features and super-imposed linear magnetic lows have been mapped
as epithermal and porphyry ?style alteration. This is interpreted by the
Company as the expression of multiple phase intrusive events related to
this largely unroofed mineralized porphyry system.

NORTH GUYACAN Target
A 500 m long target area designated "North Guyacan" is exposed as a zone of
intense clay and sericite intrusive alteration with red ochre iron oxides
on fractures , and in quartz veinlets and breccia zones. Several historic
hand dug workings are present in the partially exposed altered granite and
granodiorite and on local structures. Free gold grains were panned from
well developed, red, iron oxide, boxwork- textured material . The
geochemical results and textures observed in these iron rich,
oxidized-weathered rocks collected from numerous pits and their sorting
dumps suggest derivation from copper sulphides such as chalcocite.

An example of results from a composite grab sample of this type of dump
oxide material from one North Guyacan zone graded 15.4% iron, 12.1g/t gold,
16.8 g/t silver , 0.26 % lead and 675 ppm copper. Other composite quartz+
iron oxide- rich grab samples from scattered pits across the North Guyacan
zone graded 17.9 g/t, 16.9g/t , 16.3g/t and 12.1 g/t gold. Some of the red
iron oxide material hosts secondary copper minerals (chrysocolla) which
enrich the copper contents to over 1% Cu. When accompanied with elevated
precious metal pathfinder elements like bismuth, tellurium and mercury, the
samples graded up to 22.3g/t silver.

The Company interprets these NORTH GUYACAN historic diggings as being at
high levels in the peripheral halo of the main mineralizing system and
considers this exposed precious metal high grade zone to be a high
priority, drill -ready target.

At a site starting about 300 meters south from the North Guyacan historic
workings area, a well -developed granular, glassy quartz breccia with a
hematite ?specularite matrix is intermittently exposed for about 100
meters. This breccia trends to the south adjacent to and parallel with the
N-S strike of the granite ?granodiorite intrusive bodies' contact before
dipping under gravel overburden. Variations of this same type of grey
quartz breccia are found adjacent to and in sericite alteration zones
scattered across Guyacan's 3.5 kilometer wide geophysically anomalous
magnetic target pattern. A typical occurrence in the magnetic lows is
present at the South-South Guyacan target located 3.5 kilometers to the
south on the southern edge of the main circular magnetic feature. At the
North Guyacan target, these quartz breccia example samples graded 11.6 g/t,
7.0 g/t, 2.4 g/t silver with low levels of gold contents.

RED SOIL + SGH GEOCHEMICAL ANOMALIES TARGET

About 800 meters SE from NORTH GUYACAN historic diggings a 50 meter by 200
meter area of intensely altered sericite-iron oxide bearing granite is
exposed. Rusty hematite quartz veinlets and iron oxides in fractures are
exposed in creek banks and flat areas. Intensely red coloured soils are
found with sericite bordering quartz veinlets and iron oxide veins. Most of
this area, underlain by anomalous SGH soil geochemistry, is flat lying and
covered by debris. Results from a composite sample of float (iron oxide+
quartz stockwork and veinlets with strong sericitic borders) returned 105
ppm molybdenum, 10.1 g/t silver and 127 ppb gold. The Company interprets
this mineralization as part of the porphyry systems stockwork development.

Importantly, the highest grade mineralization found at this RED SOIL +SGH
target appears to be overprinted on the main alteration zone .This is
interpreted to be intermediate sulphidation epithermal vein material from
massive quartz-hematite-malachite vein-brecciation. The best composite grab
sample graded 80.0 g/t silver, 13.5 g/t gold with a polymetallic content of
1.1 % lead, 0.14 % molybdenum, 0.3 % zinc, 0.9 % copper and 6.6% iron. The
sample was well leached, contained secondary copper mineralization
(malachite) and is strongly anomalous in content of the precious-metal
pathfinder suite of elements mercury, bismuth, tellurium, tungsten, arsenic
and antimony.

Another sample from the RED SOIL+ SGH target area was not totally weathered
and leached of sulphur as it contained 0.19 % sulphur. This vein sample
graded 6.5 % iron, 10.68 % lead, 1.7 % copper and again contained high
grades of precious metals with gold at 11.3 g/t and silver at 212 g/t. This
sample of intermediate sulphidation vein material again had a distinctive
epithermal pathfinder element signature with high contents of mercury (7927
ppb), tellurium (11 g/t), bismuth (245 ppm) , arsenic (224 ppm) and barium
(859 ppm).

The Company considers this exposed zone to be a high priority, drill -ready
target.

MIDDLE GUYACAN SKARN ? HORNFELS and Felsic unit zone

Approximately 1600 meters SE from the NORTH GUYACAN old hand dug workings,
the Company has made important discoveries during follow-up of precious
metal soil survey geochemical anomalies. Several small exposures of
mineralized underlying bedrock were located on a ridge as windows through a
thin veneer of Tertiary andesitic volcanic rocks. This ridge area is
adjacent to an extensive SGH soil anomaly target. The newly discovered
MIDDLE GUYACAN SKARN-HORNFELS-FELSIC UNIT target is 400 meters SE from the
high grade intermediate sulphidation epithermal veins in the RED SOIL
target previously described. The newly located zone consists of secondary
copper mineralization in magnetite-epidote bearing skarn rocks and
silicified, altered intrusive rocks (Hornfels?) found in bedrock windows in
the ridge and talus cover at anomalous soil survey sample sites.

Examples of precious metal results from composite rock material collected
from sample sites in the MIDDLE GUYACAN anomalous soil zone are 3.7 g/t
gold + 5.0 g/t silver; 2.1 g/t gold + 4.0 g/t silver; 5.7 g/t gold + 15.0
g/t silver; 1.2g/t gold + 1.3 g/t silver and 9.2 g/t gold + 9.9 g/t silver.
The samples are generally low in base metals and pathfinder elements.
However , a site with minor malachite staining contained very anomalous
contents of tellurium (17.6 ppm Te ).

About 100 meters south of the above MIDDLE GYUACAN gold in soil target ,
malachite stained magnetite and epidote bearing skarnoid bedrock material
is found as a window in an historic hand dug shallow pit. Copper stained
dump composites from two samples graded 0.5% and 1.86% copper, 10.0 % and
13.0% iron, 189 ppb and 1127 ppb gold , and 490 ppb + 1127 ppb silver.

The Company interprets these SKARN-HORNFELS -FELSIC zones as halo styles of
mineralization typically found peripheral to porphyry systems. The Company
plans additional work to determine the extent of these as-yet undefined
precious metal targets, in preparation for drill testing.

MIDDLE GUYACAN COPPER SOIL + OLD HAND DUG PIT ZONES

Approximately one kilometer west of the MIDDLE GUYACAN SKARN ridge zone in
a flat area, some old shallow hand diggings in intensely altered sericitic
and red ochre stained iron oxide rich rock debris were discovered .

This new 50 m by 300 m subcropping malachite and chrysocollla secondary
copper mineral bearing zone lies about 300 m further west from the
intermittent low ridge of altered granitic subcrop (dyke) which runs north
to south joining the NORTH GUYACAN and SOUTH GUYACAN-COPPER SHAFT
mineralized zones. The soil geochemical survey has coincident anomalous
base and precious metals and an elevated content pathfinder element suite
approximating the area where iron-rich to red ochre bearing boxwork-
textured , chrysocolla -quartz rich samples have been collected. Assays are
pending but previously, a single quartz vein, prospector -collected float
rock sample in the area contained 73 g/t silver and 238 ppb gold.

The Company considers this area to be a high priority target. This MIDDLE
GUYACAN COPPER SOIL and OLD PIT ZONE surficial expression confirms the
large scale of the mineralized porphyry system extending 3.5 kilometers
north-south across the entire airborne geophysical anomaly.

SOUTH GUYACAN TARGET

This prospect area lies on a north to south linear trend of the altered
granitic dyke which bisects the 3.5 kilometer wide magnetic low comprising
the Guyacan airborne target anomaly .The variably sericitic- altered ,low
granitic ridge and adjacent flats contain anomalous geochemical soil survey
multi element sample sites. Two east to west granite dykes and related
structures cross cut the ridge.

The SOUTH GUYACAN - COPPER SHAFT zone is located in the granitic dyke ridge
about 2.7 kilometers directly south of the old NORTH GUYACAN diggings. It
is characterized by an E-W crosscutting structure hosting quartz and iron
oxides on fractures and in sericitic altered granite. The 20 meter deep,
hand-dug, shaft-dump material is generally comprised of quartz breccia vein
and hematitic-sericite granite with abundant secondary copper (chrysocolla
and malachite) staining similar to that exposed in bedrock at the SOUTH
COPPER SHAFT crosscutting structure.

A composite grab sample from the hand dug, shaft - dump rock material
graded 2.5 % copper, 126 g/t silver and 675 ppb gold with elevated content
of the pathfinder elements tellurium and bismuth. About 175 meters further
to the south from the COPPER SHAFT along the altered main GUYACAN granitic
N-S ridge(dyke) quartz veins and a crosscutting south dyke structure host
chrysocolla in altered biotite to argillic altered granite. A quartz rich
composite sample from this structure with chrysocolla staining graded 0.4%
copper, 22.7g/t silver , 244 ppb gold, with high contents of the
pathfinders tellurium ( 24 ppm) and bismuth (714 ppm).

The Company considers the SOUTH GUYACAN- COPPER SHAFT area ready for drill
testing.

The FAR SOUTH - SOUTH GUYACAN zone is about a kilometer further south from
the historic SOUTH GUYACAN SHAFT. This target lies in a flat lying area on
the southern edge of the entire GUYACAN circular pattern airborne magnetic
anomaly. Precious metal soil survey geochemical anomalous sample sites are
present in an 200 meter area where sericite altered granite occurring as
subcrop is intruded by various styles and intensities of quartz breccia
bodies and veins. These showings are similar to the quartz breccia found
3.5 kilometers north at the NORTH GUYACAN zone and at other zones scattered
across the GUYACAN target. At the FAR SOUTH -SOUTH GUYACAN zone, the
breccias are grey, glassy quartz and quartz-hematite matrix filled breccias
containing low levels of base metals and minor elevated mercury, bismuth
and tellurium contents. Quartz-hematite breccia samples from various
locations along the 200 meters of the N to S strike graded : 1.4 g/t, 1.7
g/t , 4.6 g/t , 4.8 g/t, 3.1 g/t and 10.0 g/t silver with the two best gold
content breccia rock composites grading 111 ppb and 306 ppb gold.

SOUTH GUYACAN - FAR EAST EPITHERMAL TARGET

In 2015 during follow-up of anomalous geochemical gold-in soil sample sites
located about 1000 to 1200 meters directly east from the SOUTH GUYACAN -
COPPER SHAFT Target, some old surface prospect diggings were located on an
east facing Tertiary volcanic cover ridge and slope. These diggings are
adjacent to flat land to the east where an area of some hundreds of meters
of clay-sericite and red soil altered material is exposed. The diggings and
this area of intense alteration are positioned on the flank of the more
intense low magnetic patterns present on the far eastern side of the 3.5
kilometer wide circular magnetic anomaly outlining the entire GUYACAN
mineralized system.
The Company has designated the zone epithermal (perhaps intermediate
sulphidation?) because of the presence of grey-blue silica and classic
chalcedony plus an unusual suite of epithermal pathfinder and base metal
elements contained in dominantly iron oxide material. Gold, silver and
polymetallic mineralization are scattered over a 100-150 meter area in
windows through the Tertiary andesite volcanic cover rocks on the ridge.

Highest values in composite and grab samples of leached iron oxide -rich
(7.2 % to 8.7 % iron )with epithermal silica material assayed : 4.87 % ,
10.15 % , and 9.35 % lead ; 0.24 % to 0.39 % copper ; 0.17 % to 0.26 % zinc
and up to 690 ppm molybdenum. Respectively to the lead content listed above
, these samples assayed 7.2 g/t gold, 18.3 g/t gold and 4.6 g/t gold and
respectively 310 g/t silver, 400 g/t silver ,and 413 g/t silver.

Compared to the many other occurrences of enriched precious metals with
epithermal pathfinder element anomalies found across the entire magnetic
pattern GUYACAN TARGET, the SOUTH GUYACAN -FAR EAST EPITHERMAL TARGET is
unique. Geochemical pathfinder element epithermal signatures such as high
vanadium (as high as 4373 ppm V ), high mercury ( as high as 2272 ppb Hg),high 
arsenic (as high as 1409 ppm As) and enriched tellurium (1.9 ppm Te)
accompanied by the high content of gold plus silver and base metals is
interpreted by the Company to indicate that a well developed , episodic ,
overprinting hydrothermal system was active during the emplacement of the
epithermal to porphyry style portions of the GUYACAN TARGET system.

The Company considers the SOUTH GUYACAN-FAR EAST EPITHERMAL TARTGET as a
drill ready zone of possible intermediate epithermal style mineralization,
perhaps overprinted and structurally controlled. This target is emplaced
near the far eastern edge of the over burden covered 3.5 kilometer wide
semi-circular GUYACAN porphyry system magnetic signature.

Westminster Resources President Glen Indra stated " The grades reported in
this Press Release from the several new 2015 surface precious ?metal and
copper discoveries at the Guyacan Project have demonstrated and brought
into focus the outstanding exploration potential of this large mineralizing
system. The Company will continue its 2015 exploration campaign at the
gold-silver ?copper Guyacan Project."

This news release has been reviewed and approved by Glen Macdonald, P.GEO (
a Qualified Person for the purpose of National Instrument 43-101, Standards
for Disclosure for Mineral Projects).

Glen Macdonald, P.Geo.
DIRECTOR

About Westminster:

Managed by an experienced team, the Company is focused on exploring and
developing projects on its 28,632 hectare El Cobre and 13,398 hectare
Navojoa properties in Sonora, Mexico. The El Cobre property contains among
other prospects, the 100% owned Guyacan project and the Cumbral-San Bartolo
project. On the Navojoa property the Company is exploring
gold-silver-copper targets.

For further information regarding Westminster Resources Ltd., please
contact Bill Conlin at 604-608-0400, Toll Free: 1-877-608-0007 or visit our
website at www.westminsterres.com.

Quality Assurance and Quality Control

In the field, the sample location and detailed sample description note
taking is followed by systematic sample numbering and tagging at the field
sample site and in the plastic sealed rock sample numbered bag. The up to 2
kilogram prospecting rock samples are submitted by the Company directly to
the sample preparation laboratory located in Hermosillo Mexico or they are
picked up by the Prep Lab at the Company's secure warehouse and office
facility in Obregon completing secure chain of custody. At the PREP LAB the
samples are dried -crushed -pulverized and then sample pulp splits are
created so that each rock powder split of 100-200g can be sent via secure
courier to the ACME analytical laboratory in Vancouver Canada.

ACME Laboratory is now known as BVML , the globally certified ,Bureau
Veritas Minerals Laboratories where the samples were geochemically analyzed
with all over limit samples assayed by ore grade methods. The laboratory
QA-QC program included blanks, duplicates and certified control reference
standards inserted randomly into the sample stream. Cautionary Note:
Geochemical results and the assay data derived from these subcrop to
outcrop rock samples discussed in this press release cannot be relied upon
to be representative of the grade of mineralization found at surface or at
depth in drill core. The rocks are weathered samples generally leached of
their primary sulphides and may contain secondary minerals. The single
"grab" hand- sized samples, "composite-grab"samples from numerous similar
rocks, or "composite -chip" rock samples from outcrops are collected in an
irregular to randomly spaced manner over an area based upon the geologists'
and/or technicians' judgement and experience .The data is used by the
Company to guide further exploration and evaluation of the mineral
potential of the target prospects.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking information which is not
comprised of historical facts. Forward-looking information involves risks,
uncertainties and other factors that could cause actual events, results,
performance, prospects and opportunities to differ materially from those
expressed or implied by such forward-looking information. Forward looking
information in this news release may include, but is not limited to, the
Company's objectives, goals or future plans. Factors that could cause
actual results to differ materially from such forward-looking information
include, but are not limited to, those risks set out in the Company's
public documents filed on SEDAR. Although the Company believes that the
assumptions and factors used in preparing the forward-looking information
in this news release are reasonable, undue reliance should not be placed on
such information, which only applies as of the date of this news release,
and no assurance can be given that such events will occur in the disclosed
time frames or at all. The Company disclaims any intention or obligation to
update or revise any forward-looking information, whether as a result of
new information, future events or otherwise, other than as required by law.
______________________________________
_______________________________________________
TSX Venture closing price for WMR-V
Date: 2015/07/21
Closing Price: 0.04
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1520200020TS11520201139-07145320150722