Source	MARKET NEWS
Date	07/20/2015
Time	07:27:34 AM

Company	 Codrington Resource Corporation
Title	Tests 
Up To 95.3% Graphite Purity At L.A.B.





    CDNX Symbol: CA











Press Release	





CODRINGTON RESOURCE CORP ("CA-V")
- Tests Up To 95.3% Graphite Purity At L.A.B.

LAB Project Produces Large Flake Graphite with 95% Purity
Highlights:

1. Test F1 returns 94.7% graphite (Cg) in the + 48 mesh
concentrate (jumbo flake)

2. Test F2 returns 95.3% graphite in the + 48 mesh concentrate
(jumbo flake)

Codrington Resource Corporation (the "Company") is pleased to
announce results from beneficiation testing on graphite samples from
it's L.A.B. Project , located in Quebec, Canada.

The test-work was performed by SGS Canada Inc., of Burnaby B.C.
Canada, an I.S.O. Certified Laboratory. The results for two separate
tests are:

Test F1 produced the three sized concentrates with grades of 94.7%
C(g) in the +48 mesh concentrate (jumbo flake), 95.3% C(g) (large
flake) in the +100 mesh concentrate and 86% C(g) in the -100 mesh
concentrate (small flake). The combined concentrate had an overall
graphite recovery of 89.6% at grade of 91.0% C(g).

Test F2 was performed to improve the graphite grade by increasing
the regrind times in all three regrind stages. The three sized
concentrates had grades of 95.3% C(g) (jumbo flake) in the +48 mesh
concentrate, 94% C(g) in the +100 mesh concentrate (large flake) and
81.2% C(g) in the -100 mesh concentrate. The combined concentrate had
an overall graphite recovery of 96.2% at grade of 88.3% C(g).

In both tests, 30% of the total graphite was recovered in the +48
mesh concentrate (jumbo flake) and 21 to 24% recovered in the +100 mesh
concentrates (large flake) for a combined over 50% jumbo and large
flake concentrate. Both large and jumbo flake graphite is targeted for
the premium market.

A total of 68 kilograms of rock samples were obtained from the
project, including graphite grab samples and country rock. The coarse
rocks were received as 10 separate samples. Each sample was weighed and
crushed to -6 mesh and submitted for head assays. Six of the graphite
mineralized samples were blended to make a 42 kg Master Composite for
testing. The main objective of this testing was to produce a
concentrates with a graphitic carbon grade of 95% or greater. The
flotation testing consisted of several stages of grinding, screening
and flotation producing three concentrates at +48 mesh, +100 mesh and
-100 mesh, with the overall combined concentration a sum of all three.

A mineralogical study was conducted by SGS on a master composite
sample with optical microscopy and quantitative X-ray diffraction (XRD)
to determine the occurrence and liberation of graphite and associated
gangue minerals. The sample was examined at -6 mesh. Graphite particles
range in size from ~ 5 [im to ~2 mm generally most of the graphite
grains are comprised of coarse grained () 400 [im) particles. The
particles occur mainly as polycrystalline, tabular, platy and prismatic
grains. The graphite occurs as liberated (~33%) and exposed particles
(~61%) with minor amounts of locked grains (~6%). These results show
high recovery potential of graphite (94%) through floatation which was
confirmed in the metallurgical test-work.

Further test-work is now underway at SGS Canada Inc. , to
determine the optimal grind size to maximize the purity of the graphite
concentrate.

All sampling was completed by and under the supervision of Mr.
Martin Ethier, geo (#1520) who is a Member of the Order of Geologists
of Quebec and a "Qualified Person" under NI 43-101.

"We are highly encouraged by the initial results, which returned
large flake high graphite concentrate in 50% of the samples, from
simple grind and float recovery methods. The Company has tasked the
labs to optimize graphite recovery through further grinding and
floatation, and carry out hydrometallurgical testing to produce battery
grade spherical graphite in the next round of test work", Company
President Adrian F.C. Hobkirk is quoted.

The Property is located in a very active graphite exploration and
production area, and is adjacent and contiguous to the south of the
TIMCAL (Imerys Graphite & Carbon Mine) formally known as the Stratmin
Lac des lles Graphite Mine in Quebec. A total of 25,000 tonnes of
graphite were produced in North America in 2013, with the majority of
this production coming from the TIMCAL Mine (source: United Sates
Geological Survey "Graphite "by Donald W. Olson). Location of TIMCAL's
mine adjacent to the north of the L.A.B. Graphite Project was confirmed
during the due diligence property visit of May 2015. The claims are
road accessed, with water, power and technical support available
locally.

The contents of this press release, and the preparation of this
press release, was supervised by Mr. Martin Ethier, geo (#1520) who is
a Member of the Order of Geologists of Quebec (OGQ) and a "Qualified
Person" under NI 43-101.

On behalf of the Board of Directors,
Adrian Hobkirk, President and CEO
Ph 714-316-3272
Toll Free: 1-855-894-4524
E: ahobkirk@resourceexploration.com
W: www.resourceexploration.com

The TSX Venture Exchange has not reviewed the content of this news
release and therefore does not accept responsibility or liability for
the adequacy or accuracy of the contents of this news release.This news
release contains certain "forward- looking statements" within the
meaning of Section 21E of the United States Securities and Exchange Act
of 1934, as amended. Except for statements of historical fact relating
to the Company, certain information contained herein constitutes
forward- looking statements. Forward-looking statements are based upon
opinions and estimates of management at the date the statements are
made, and are subject to a variety of risks and uncertainties and other
factors which could cause actual results to differ materially from
those projected in the forward looking statements. The reader is
cautioned not to place undue reliance on forward-looking statements.
The transaction described in this news release is subject to a variety
of conditions and risks which include but are not limited to:
regulatory approval, shareholder approval, market conditions, legal due
diligence for claim validity, financing, political risk, security risks
at the property locations and other risks. As such, the reader is
cautioned that there can be no guarantee that this transaction will
complete as described in this news release. We seek safe harbour.


TEL:  714-316-3272  Adrian Hobkirk, President and CEO
TSX Venture closing price for CA-V
Date: 2015/07/14
Closing Price: 0.07

TEL:  1-855-894-4524
EMAIL:  ahobkirk@resourceexploration.com
INTERNET:  www.resourceexploration.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1520000024TS11520001072-07260220150720