Source	Marketwire
Date	07/16/2015
Time	05:00:43 AM

Company	 MUNDORO CAPITAL INC.
Title	Mundoro Announces Drilling Commences at Serbian Properties





    CDNX Symbol: MUN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Mundoro Capital Inc.

TSX VENTURE SYMBOL: MUN
FRANKFURT SYMBOL: NGU:GR

July 16, 2015

Mundoro Announces Drilling Commences at Serbian Properties


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 15, 2015) - Mundoro Capital 
Inc. (TSX VENTURE:MUN)(FRANKFURT:NGU), (www.mundoro.com) ("Mundoro" or the 
"Company") is pleased to report drilling has commenced on the Company's 
100%-owned exploration licenses, Savinac, Sumrakovac, Bacevica and Osnic (the 
"Southern Timok Properties") which are located at the southern end of the Timok 
Magmatic Complex ("TMC") in northeastern Serbia (see Location Map of Drilling).

Drilling commenced on July 14, 2015 under the Option Agreement between Mundoro 
and First Quantum Minerals Inc. ("FQM") announced June 8, 2014. FQM has 
committed to drill a minimum of 5,000 meters on the Southern Timok Properties 
by October 31, 2015. This drill program will be focused on testing various 
copper-gold porphyry systems within the four properties. FQM is sole funding 
the drilling program which comprises reverse circulation drilling and diamond 
drilling. The final number of holes drilled will be dependent on results 
obtained through the course of the drilling program.

Teo Dechev, CEO and President of Mundoro, commented "We believe this drilling 
program is a good step towards testing various copper-gold porphyry targets 
over the Southern Timok Properties in the TMC which is a prolific portion of 
the Tethyan belt with potential to host further discoveries. For Mundoro 
shareholders, the funds FQM will spend on drilling and geophysics will allow 
for more aggressive exploration of the Southern Timok Properties. The work FQM 
is conducting will meet near term exploration objectives as well as the 
required expenditures for each of these licenses. Mundoro has completed the 
required expenditures for calendar 2015 for the remaining four licenses 
available for option. We continue to have ongoing discussions regarding 
potential joint ventures for the remaining licenses. As we are operating in a 
time of difficult capital markets for mineral explorers, working under this 
form of partnership enables us to conserve the Company's treasury while at the 
same time advance this large suite of projects. Mundoro ended Q1-2015 with a 
treasury of $7 million and no debt."

This drilling program is designed to test various copper-gold targets over the 
Southern Timok Properties. The targets have been identified through a 
systematic program completed by the Company comprising detailed mapping, 
geochemistry, alteration mapping, ground magnetics, regional geophysics and 
interpretation of limited historical drilling. The properties and targets to be 
tested are:

The Sumrakovac license:

/T/

--   A 103 sq.km area located 5km southwest of the Bor Mine Complex and is
adjacent on the west side to the Freeport/Reservoir Brestocac-Metovnica
license which hosts the Cukaru Peki discoverty.
--  The Skorusa Cu-Au porphyry is known from creek exposures of AB-vein
quartz stockworks and from historical exploration drill holes completed
in the vicinity of the outcrop. Ground magnetic geophysical results
highlighted additional anomalous centers east of the known Skorusa Cu-Au
porphyry. The initial target area at Skorusa is the northern edge of a
domain covering 900m x 500m defined by a molybdenum anomaly in soils,
outward from which anomalies of pathfinder elements appear to define a
halo. The western margin of the anomaly may reflect cover by post-
mineral units, in which case the target could be open to the west.
--  The target area is further broken down into two identified targets:
Skorusa East and Skorusa North, which were identified through mapping,
geochemistry and ground magnetics.
--  Skorusa East is a soil molybdenum anomaly with a radius of 800 m located
immediately east of Skrousa porphyry, and Skorusa North is a molybdenum
anomaly with an elongate footprint of 700m x 300 m at the northern limit
of detailed sampling. These anomalies are also surrounded by elevated
concentrations of volatile metalloid elements (As, Sb, Te, Bi) in the
soil.

/T/

The Savinac license:

/T/

--  A 90 sq.km area that is located 15km southwest of the Bor Mine Complex.
--  The property contains a significant area of strong alteration in an
approximately 14 sq.km elongated belt which hosts several epithermal Cu-
Au prospects marked by Cu-Mo-Ag-Pb-Zn geochemical anomalies.
--  During 2014, the Company discovered the Tilva Rosh zone where drilling
intersected 7m @ 7.9 g/t Au; 5m @ 2.54 g/t Au, 0.59 % Cu and 9.1m @1.24
g/t Au, 0.33% Cu. Approximately 3 km to the north is the Savinac North
target which will be drilled tested during this drilling program.
--  Savinac North is an intensely developed bleached zone that includes
phyllic and relict advanced argillic assemblages. Spectral mineralogy on
a few scattered outcrop samples yielded consistent high-Aluminium
illites and pyrophyllite.
--  The target is highlighted by strong molybdenum soil anomalism which
grades southward (and weakly northward) to zones characterised by strong
coincident anomalies of Au, As, Sb, Bi, and Te.
--  The discovery opportunity at Savinac is likely for north-striking
tabular geometry of blind porphyry mineralisation. This geometry could
generate appreciable volumes of mineralised rock and the coarse
scattered historic drill pattern does not adequately test for this
possibility.

/T/

The Bacevica license

/T/

--  A 148 sq.km area located directly south of the Savinac license.
--  In the current field season the Company has been engaged in additional
detailed mapping, rock and soil sampling. In addition, on June 15, 2015
the Company began a ground magnetics program, which is funded by FQM,
and is budgeted for 138 line-km over a 8 km long alteration trend.
--  The drill holes planned for this license area are aimed to test the
Bacevica West and Bacevica East targets.
--  Bacevica West is defined by a broad surface geochemical anomaly that
accurately maps out the surface bleaching alteration envelope. It
consists of two sub-areas: (i) a southern area characterised by advanced
argillic alteration that was unsuccessfully drill-tested two decades
ago, and a northern area that has no prior drill testing. The target in
this section of Bacevica West is defined by surface anomalies of
normalised Cu, Mo, coincident with areas depleted of Pb, Zn and Mn, and
around which these elements and other volatiles are concentrated.
--  The Bacevica East target is defined by a NNW-elongate alteration zone
developed at the western extent of latite intercalation in the TMC. The
prospect exhibits a coarse S to N zonation defined by Mn and Zn
depletion and Mo enrichment in the central and southern parts, grading
to progressively greater enrichment in volatile elements (As, Sb, Te,
Bi) in the north.

/T/

The Osnic license

/T/

--  A 74 sq.km area located directly to the east of Sumrakovac and Savinace
and approximately 20km south of the Bor Mine Complex.
--  In preparation for the drilling in the second half of 2015, the work
program at Osnic will consist of interpretation of geochemical sampling
completed to date, followed by ground magnetics in August 2015, and
thereafter drill testing.

/T/

Technical information contained in this Press Release has been reviewed and 
approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by National 
Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian based public company which is focused on generating value 
for its shareholders through utilizing the collective expertise of our 
directors, management and technical staff to invest in mineral projects that 
have the potential to generate future cash.

Caution Concerning Forward-Looking Statements

Information included, attached to or incorporated by reference into this News 
Release may contain forward-looking statements. All statements, other than 
statements of historical fact, included or incorporated by reference in this 
News Release are forward-looking statements, including, without limitation, 
statements regarding activities, events or developments that the Board expects 
or anticipates may occur in the future. These forward-looking statements can be 
identified by the use of forward-looking words such as "will", "expect", 
"intend", "plan", "estimate", "anticipate", "believe" or "continue" or similar 
words or the negative thereof. The material assumptions that were applied in 
making the forward looking statements in this News Release include expectations 
as to the Company's future strategy and business plan and execution of the 
Company's existing plans. There can be no assurance that the plans, intentions 
or expectations upon which these forward-looking statements are based will 
occur. We caution readers of this News Release not to place undue reliance on 
forward looking statements contained in this News Release, which are not a 
guarantee of performance and are subject to a number of uncertainties and other 
factors that could cause actual results to differ materially from those 
expressed or implied by such forward-looking statements. These factors include 
general economic and market conditions, changes in law, regulatory processes, 
the status of Mundoro's assets and financial condition, actions of competitors 
and the ability to implement business strategies and pursue business 
opportunities. The forward-looking statements contained in this News Release 
are expressly qualified in their entirety by this cautionary statement. The 
forward-looking statements included in this News Release are made as of the 
date of this News Release and the Board undertakes no obligation to publicly 
update such forward-looking statements to reflect new information, subsequent 
events or otherwise, except as required by law. Shareholders are cautioned that 
all forward-looking statements involve risks and uncertainties and for a more 
detailed discussion of such risks and other factors that could cause actual 
results to differ materially from those expressed or implied by such 
forward-looking statements, refer to the Company's filings with the Canadian 
securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Mundoro Capital Inc.
Teo Dechev
CEO, President and Director
+1-604-669-8055 x101

or

Roth Investor Relations
Michelle Roth
+1-732-792-2200

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=536251561