Source	MARKET NEWS
Date	07/28/2015
Time	06:42:07 AM

Company	 Excelsior Mining Corp.
Title	Hydrology 
Pump Tests Confirm Favourable Conditio





    CDNX Symbol: MIN











Press Release	





EXCELSIOR MINING CORP ("MIN-V;EXMGF-0")
- Hydrology Pump Tests Confirm Favourable Conditions For In-situ
- Operations

Excelsior Mining Corp. ("Excelsior" or the "Company")is pleased to
announce comprehensive hydrological results for the Gunnison Copper
Project in Arizona ("Gunnison Project"). The results generated
hydrological conductivities in the range expected for typical fracture
controlled deposits and show the deposit is suitable for in-situ
recovery ("ISR") operations. These results will be incorporated into a
full Feasibility Study scheduled for completion in 2016.

Commenting on these results, President and CEO Stephen Twyerould
said, "The successful completion of the hydrology test program is a
major milestone in the advancement of our Gunnison Copper Project. The
favourable results once again demonstrate the potential to extract this
significant deposit using economically superior and environmentally
friendly in-situ mining."

A total of 32 hydrology wells were laid out over the North Star
deposit of the Gunnison Project and its surroundings. These wells
targeted a variety of fractured zones, rock types and mineralized
areas. Twenty-seven of the 32 wells were hydraulically tested and the
remaining five served as observation wells. An additional 21 core holes
from previous drilling programs were used as water level observations
to provide a radial distribution of observation bores to each of the
tested wells.

Pump Rates

Hydraulic properties and sustainable pumping rates for individual
formations and structures were quantified by assessing the connectivity
between pumping wells and observation wells. A pump rate is considered
sustainable when at least 50% of the available drawdown is achieved at
the end of the total test duration, which typically lasts for five
days. Available drawdown is defined as the well bore interval between
pump intake and the pre-test level of the water table. Sustainable pump
rates of up to 170 gallons per minute (gpm) were observed; these
results demonstrate favourable flow rates for potential in-situ copper
recovery operations.

Hydraulic Conductivity

Drawdown response analysis is the quantification of the hydraulic
conductivity and is a measure of the efficiency with which water moves
through the rock. Hydraulic conductivity (K) is measured in units of
length over time, and is represented as feet per day (ft/d). Previous
pump tests (pre-2014) conducted by Excelsior produced hydraulic
conductivities that ranged from 0.17 ft/day to 4.9 ft/day. These test
results were incorporated into the 2014 Prefeasibility Study. Table 1
shows the combined data from all tests, together with the tested depth
and span of the hydraulic interval (D).

Table 1 Summary of Hydraulic Testing Results

//st
---------------------------------------------------------------
Hydrology Well  K (feet / day)  Hydraulic Interval (ft)  D (ft)
---------------------------------------------------------------
NSH -001                   0.3               702 - 1096     394
---------------------------------------------------------------
NSH -002                   4.5               608 - 1264     656
---------------------------------------------------------------
NSH -003                   0.2              1216 - 1400     184
---------------------------------------------------------------
NSH -004B                  0.5               695 - 1031     336
---------------------------------------------------------------
NSH -005                   5.0               647 - 1020     373
---------------------------------------------------------------
NSH -006(1)               45.0                640 - 681      41
---------------------------------------------------------------
NSH -007                   0.4                469 - 620     151
---------------------------------------------------------------
NSH -008                   0.4                700 - 847     147
---------------------------------------------------------------
NSH -009                  0.01               785 - 1018     233
---------------------------------------------------------------
NSH -010                   0.1                555 - 720     165
---------------------------------------------------------------
NSH -011                   0.2                470 - 545      75
---------------------------------------------------------------
NSH -013                   0.9               656 - 1070     414
---------------------------------------------------------------
NSH -014B(2)              0.02              1160 - 1274     114
---------------------------------------------------------------
NSH -015                   4.6                600 - 820     220
---------------------------------------------------------------
NSH -016                   3.1                580 - 820     240
---------------------------------------------------------------
NSH -017                   5.8               919 - 1200     281
---------------------------------------------------------------
NSH -018                   9.3                591 - 992     401
---------------------------------------------------------------
NSH -019                   4.8               638 - 1300     662
---------------------------------------------------------------
NSH -020                   2.0              1110 - 1582     472
---------------------------------------------------------------
NSH -021C                  0.5               624 - 1372     748
---------------------------------------------------------------
NSH -022                   0.1               919 - 1131     212
---------------------------------------------------------------
NSH -023                   0.4               645 - 1442     792
---------------------------------------------------------------
NSH -024                   0.2               625 - 1440     815
---------------------------------------------------------------
NSH -025                  0.05              1461 - 1590     129
---------------------------------------------------------------
NSH -026                   0.3                625 - 900     275
---------------------------------------------------------------
NSH -027                   0.6               840 - 1010     170
---------------------------------------------------------------
NSH -028                   0.2                572 - 800     228
---------------------------------------------------------------



//et

1 Alluvium

2 NSH -014B tested the non-mineralized zone beneath the deposit.

Drawdown analyses from the majority of the wells indicate confined
flow conditions and rapid initial response, which are characteristic of
fractured bedrock aquifers. When fracture flow was identified,
appropriate analysis verified that fracturing was sufficiently frequent
such that modeling with an equivalent porous medium model was
justified.

Hydrology Model

A regional groundwater model has been constructed that is capable
of modeling and predicting local and regional groundwater flow during
simulations of various in-situ recovery scenarios sufficient to support
production modeling at the feasibility level. The model has been
successfully calibrated by comparison of measured and predicted
groundwater levels. Results validate that the deposit is amenable to
in-situ mining.

The model is necessary in the permitting phase to demonstrate
understanding and control of groundwater flow at the site and to
quantify the potential volumes of mine-affected water. It is also being
used to develop preliminary designs of the hydraulic interaction
between extraction and delivery wells for different configurations and
well spacing. In-situ recovery mining relies on flow between a delivery
well and the neighboring extraction wells. This flow is controlled by
the hydraulic conductivity between the delivery and the extraction
point, and by the hydraulic gradient. The gradient can be controlled by
means of delivery and extraction rates which create a pressure head
("mounding") in the delivery well and a cone of depression at the
recovery well. Modelling has shown that flow rates necessary for
in-situ mining and hydraulic control are fully supported by the
hydraulic conductivities shown in Table 1.
About Excelsior

Excelsior is a mineral exploration and development company that is
advancing the Gunnison Copper Project. The Excelsior management team
consists of experienced professionals with proven track records of
advancing mining projects into production. Further information about
the Gunnison Copper Project can be found in the technical report filed
on SEDAR at www.sedar.com entitled: "Gunnison Copper Project, NI 43-101
Technical Report, Prefeasibility Study" dated February 14, 2014.

For more information on Excelsior, please visit our website at
www.excelsiormining.com.

Mr. R. Douglas Bartlett, RG, CPG, CHG, a Principal Hydrogeologist
with Clear Creek Associates and a Qualified Person as defined by NI
43-101, has reviewed and approved the technical information disclosed
in this news release. Mr. Bartlett has verified the data underlying the
test results by approving the test procedure, obtaining all the
analytical data over the life of the experiment, and performing the
calculations presented above.

ON BEHALF OF THE EXCELSIOR BOARD

Mark J. Morabito, Executive Chairman

Cautionary Note Regarding Forward-Looking Information

This news release contains "forward-looking information"
concerning anticipated developments and events that may occur in the
future. Forward looking information contained in this news release
includes, but is not limited to, statements with respect to (i) the
details of the mineral resource estimate; (i) the use of in-situ
recovery to mine the Gunnison Project; (ii) in-situ recovery mining
being economically superior and environmentally friendly; (iii)
expected future hydrological conditions of the Gunnison Project based
on the test results; (iv) the completion of a Feasibility Study; and
(v) the advancement of the Gunnison Project.

Such forward-looking information can be identified by the use of
the word "will". Forward-looking information contained in this news
release is based on certain factors and assumptions regarding, among
other things, the estimation of mineral resources and mineral reserves,
the realization of resource and reserve estimates, copper and other
metal prices, the timing and amount of future exploration and
development expenditures, the accuracy of the test results and that
they are indicative of full scale mining at the Gunnison Project, the
estimation of initial and sustaining capital requirements, the
estimation of labour and operating costs, the availability of necessary
financing and materials to continue to explore and develop the Gunnison
Project in the short and long-term, the progress of exploration and
development activities, the receipt of necessary regulatory approvals,
the completion of the permitting process, the estimation of insurance
coverage, and assumptions with respect to currency fluctuations,
environmental risks, title disputes or claims, and other similar
matters. While the Company considers these assumptions to be reasonable
based on information currently available to it, they may prove to be
incorrect.

Forward looking information involves known and unknown risks,
uncertainties and other factors which may cause the actual results,
performance or achievements of the Company to be materially different
from any future results, performance or achievements expressed or
implied by the forward-looking information. Such factors include risks
inherent in the exploration and development of mineral deposits,
including risks relating to changes in project parameters as plans
continue to be redefined including the possibility that mining
operations may not commence at the Gunnison Project, risks relating to
variations in mineral resources and reserves, grade or recovery rates
resulting from current exploration and development activities, risks
relating to the ability to access infrastructure, risks relating to
changes in copper and other commodity prices and the worldwide demand
for and supply of copper and related products, risks related to
increased competition in the market for copper and related products and
in the mining industry generally, risks related to current global
financial conditions, uncertainties inherent in the estimation of
mineral resources, access and supply risks, reliance on key personnel,
operational risks inherent in the conduct of mining activities,
including the risk of accidents, labour disputes, increases in capital
and operating costs and the risk of delays or increased costs that
might be encountered during the development process, regulatory risks,
including risks relating to the acquisition of the necessary licenses
and permits, financing, capitalization and liquidity risks, including
the risk that the financing necessary to fund the exploration and
development activities at the Gunnison Project may not be available on
satisfactory terms, or at all, risks related to disputes concerning
property titles and interest, environmental risks and the additional
risks identified in the "Risk Factors" section of the Company's reports
and filings with applicable Canadian securities regulators.

Although the Company has attempted to identify important factors
that could cause actual actions, events or results to differ materially
from those described in forward-looking information, there may be other
factors that cause actions, events or results not to be as anticipated,
estimated or intended. Accordingly, readers should not place undue
reliance on forward-looking information. The forward-looking
information is made as of the date of this news release. Except as
required by applicable securities laws, the Company does not undertake
any obligation to publicly update or revise any forward-looking
information.
Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release, and no securities regulatory authority has either approved or
disapproved of the contents of this release.

JJ Jennex
Vice President, Corporate Affairs
604-681-8030 x240
info@excelsiormining.com
www.excelsiormining.com
______________________________________
_______________________________________________
TSX Venture closing price for MIN-V
Date: 2015/07/27
Closing Price: 0.26
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106
1520800011TS11520801023-06392820150728