Source	CANADA NEWSWIRE
Date	07/28/2015
Time	05:32:51 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol Provides Exploration Update on the Gorbea Belt JV and New IP
Geophysical Program at Atlas





    CDNX Symbol: MRZ











Press Release	




" BC-MRZ-GorbeaUpdate   07-28 1030
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol Provides Exploration Update on the Gorbea Belt JV and New IP
Geophysical Program at Atlas@

VANCOUVER, July 28, 2015 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
Frankfurt: M8R) Mirasol Resources is pleased to provide an exploration update
on its Gorbea Belt projects where the Company has recently announced a joint
venture (see news release March 26, 2015).
<<

--  The mild winter conditions have led Mirasol's JV partner to complete a
65 line-km, deep-penetrating IP geophysical survey over a portion of the
Atlas high-sulphidation epithermal gold-silver system.
--  Preliminary analysis of the IP data highlights large resistivity
anomalies coincident with known gold-silver prospects, and outlines new
anomalies that represent new exploration targets.
--  The capacity of the Gorbea exploration camp has been doubled ahead of
the planned southern hemisphere spring / summer aggressive exploration
program.
--  The Gorbea exploration camp is now secured for the winter months, with a
planned restart during September - October 2015.
>>
The new IP survey completed by the JV partner covers approximately 24 sq.
km of the Atlas gold system (Figure 1), and is comprised of 3 to 7 km long,
400 m spaced lines with dipoles on 150 m spacing. The configuration of this IP
survey effectively maps a large part of the Atlas mineral system and
penetrates to depths exceeding 400 m, deeper than previous Mirasol IP,
providing a system scale overview for drill hole targeting. This geophysical
survey will be further extended and infilled over key target areas in the
springtime (September-October 2015). The expanded survey is planned to cover
mineralization previously identified by Mirasol (see news releases December
10, July 18 and 23, and February 26, 2014), including the northern extension
of the Atlas Gold Zone, the Escondida high grade silver target area, and the
southern flanks of the Dos Hermanas (syn and post mineral) flow domes which
may conceal additional exploration targets.
Final processing and interpretation of this new data by the JV partner is
in progress. Review of preliminary processed data by Mirasol in cross section
and plan reveals a set of large geophysical anomalies which are in a number of
cases spatially coincident with priority prospects defined by Mirasol, and in
other cases outline new potential targets. This includes resistivity anomalies
(+1000 ohm/m) over 2 km in length which extend the Oculto and Pampa Zone
targets. Resistivity anomalies in high-sulphidation epithermal systems
elsewhere in the Miocene-aged mineral belt of Chile have indicated the
presence of hydrothermal silica that can be associated with precious metal
mineralization. Large chargeable features were also noted to underlie the main
prospect areas in the Atlas IP survey, suggesting that sulphide bearing
mineralization may be present at depth.
The IP survey data can also be used to estimate the potential depth of
oxidation at Atlas that in some areas is interpreted to be in excess of 150 to
200 m. This relatively deep oxidation profile is an encouraging
characteristic, suggesting the potential for discovery of oxide gold
mineralization which may be amenable to cost-effective bulk-minable dump-leach
methods.
Over the July to September winter months the recent geophysical data will
be integrated with Mirasol's previous exploration data by the JV partner to
plan the 2015 spring and summer exploration program. This program will include
drilling at Atlas and Titan, as prescribed under the terms of the Gorbea JV,
which requires a minimum combined total of 3,000 m drilling at the Atlas and
Titan projects by the 1st year anniversary of the JV (May 9, 2016).
Mirasol's management is pleased with the progress and the results to date
from the Gorbea JV; further updates will be made as key exploration milestones
are reached on the nine Mirasol projects included in the JV.
Stephen Nano, President and CEO of Mirasol Resources has approved the
technical content of this news release and is a Qualified Person under NI 43
-101.
Quality Assurance/Quality Control of the exploration program:
The JV Partner operates the Gorbea Joint Venture and generated the
geophysical and information reported to Mirasol Resources. Industry accepted
procedures have been used for the collection and analysis of this information.
Mirasol has performed an independent analysis of the information provided.
Stephen Nano has reviewed the data and prepared this news release, and is a
qualified person as defined by National Instrument 43-101.
Mirasol's previous exploration at the Project was supervised by Stephen
C. Nano, President and CEO, who is the Qualified Person under NI 43-101; and
Leandro Echavarria, Mirasol's Principal Geologist. All technical information
for the Atlas project was obtained and reported under a formal quality
assurance and quality control (QA/QC) program. Rock chip and trench channel
samples were collected under the supervision of Company geologists in
accordance with standard industry practice. Samples were dispatched via
commercial transport to an ISO 9001:2000-accredited laboratory in Chile for
analysis. Results of this exploration program have been audited by an
independent geochemist to confirm the Company's QA/QC process/procedures and
laboratory performance met required standards.
Assay results from drill samples may be higher, lower or similar to
results obtained from surface samples due to surficial oxidation and
enrichment processes or due to natural geological grade variations in the
primary mineralization.
Forward Looking Statements: The above contains forward looking statements
that are subject to a number of known and unknown risks, uncertainties and
other factors that may cause actual results to differ materially from those
anticipated in our forward looking statements. Factors that could cause such
differences include: changes in world commodity markets, equity markets, costs
and supply of materials relevant to the mining industry, change in government
and changes to regulations affecting the mining industry. Forward-looking
statements in this release include statements regarding future exploration
programs, operation plans, geological interpretations, mineral tenure issues
and mineral recovery processes. Although we believe the expectations reflected
in our forward looking statements are reasonable, results may vary, and we
cannot guarantee future results, levels of activity, performance or
achievements
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2015/28/c8245.html

-0-                           07/28/2015
/For further information: Stephen Nano, President and CEO or; John
Toporowski, Manager of Investor Relations, Tel: (604) 602-9989; Email:
contact(at)mirasolresources.com, Website: www.mirasolresources.com/
(MRZ.)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MIN MNG
SU:  JVN

-30-