Source	CANADA NEWSWIRE
Date	07/28/2015
Time	06:03:51 AM

Company	 Tinka Resources Limited
Title	Tinka commences 10,000 metre drill program at Ayawilca zinc project,
announces new IP results & targets





    CDNX Symbol: TK











Press Release	




" BC-Tinka-AyawilcaProject   07-28 1114
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Tinka commences 10,000 metre drill program at Ayawilca zinc project,
announces new IP results & targets@

Large IP anomaly modelled immediately below surface zinc anomalies
VANCOUVER, July 28, 2015 /CNW/ - Tinka Resources Limited ("Tinka" or the
"Company") (TSXV: TK) (OTCPK: TKRFF) is pleased to announce that the Company
has mobilized two drill rigs to commence up to 10,000 metres of diamond
drilling at the Company's 100%-owned Ayawilca zinc project, Peru. The key
objective of the drill program is to expand the existing Inferred Mineral
Resource of 13.3 million tonnes grading 7.7% zinc equivalent (see PR February
26, 2015). In addition, the results of a new Induced Polarization (IP)
geophysical survey highlight a number of exciting new zinc targets.
Highlights include:
<<

--  Up to 10,000 metre fully funded drill program to commence immediately:
o Two rig drill program;
o Objective to expand existing NI 43-101 Zinc Mineral Resource areas;
>>

<<

--  Significant new IP survey anomalies defined:
o Previously unmapped and untested; and
o Directly coincident to surface zinc soil anomalies and gossans.
>>

Dr. Graham Carman, Tinka's President and CEO, stated: "We are excited to
recommence drilling at Ayawilca following our successful drill campaign of
2014, which resulted in our Inferred Mineral Resource of 13.3 million tonnes
grading 7.7% Zinc equivalent containing 1.7 billion pounds zinc, 909 tonnes
indium, 5.8 million ounces silver, and 55 million pounds lead. Our key
objective for this year is to substantially increase our zinc-rich Inferred
Mineral Resource. Known sulphide bodies at Ayawilca occur as carbonate
replacement deposits or "mantos" which are constrained in size and shape only
by lack of drilling. The expanded IP has provided us with additional drill
targets which could significantly increase the mineralization footprint. I
look forward to updating the market on the drill results."
2015 Ayawilca Drill ProgramThe 2015 program will focus on drill testing
extensions of the Inferred Mineral Resource at East, Central and West Ayawilca
as well as testing some new targets (Figure 1 and Figure 2). Up to 24 step-out
holes are planned commencing with two rigs drilling concurrently. The program
is expected to take around 4 months to complete, with results to be released
once assays become available and interpreted.
The drill program will commence at East Ayawilca where zinc
mineralization is open in all directions. East Ayawilca has zinc intercepts
which were not included in the resource calculation due to the sparsity of
past drilling (including 19.6 metres at 5.7% zinc and 81 g/t indium from 164
metres depth: hole A14-21). Drill holes are also planned at West and Central
Ayawilca where zinc mineralization is open in two directions along strike and
where tin-copper mineralization was discovered at depth (Figure 3).
IP Geophysical Survey ResultsAn IP geophysical survey was recently
completed covering 9 km2 of prospective ground at Ayawilca / Colquipucro, with
the data modelled from surface to a maximum depth of 500 metres below
surface(x). Results show a number of strong, coherent chargeability anomalies in
the depth range of 150 to 450+ metres, interpreted as zones of disseminated
sulphides believed to be highly prospective for zinc. Many of these IP
anomalies occur beyond the extents of the Inferred Mineral ZnEq Resource. The
most significant IP chargeability anomaly, covering approximately 1 km2 at
Chaucha, is open to the north. The anomaly is adjacent to the current silver
oxide resource at Colquipucro (Mineral Resource of 14.3 Moz (at) 60 g/t Ag
Indicated and 13.3 Moz (at) 48 g/t Ag Inferred), is coincident with a
zinc-in-soil anomaly, and has no previous drilling (Figure 1). The Chaucha IP
anomaly will be drill tested once permits in that area are renewed.
(x)A conventional pole-dipole IP survey was carried out on eleven 300
metre-spaced lines each orientated 060 degrees azimuth, using electrode
spacing of 120 metres. The data was modelled with a high degree of confidence
from surface to maximum depths of between 400 and 500 metres.
Other NewsMariana Resources Limited has terminated the option agreement
on the Company's 100%-owned Rurimarac Properties with no drilling completed.
The qualified person, Dr. Graham Carman, Tinka's President and CEO, and a
Fellow of the Australasian Institute of Mining and Metallurgy, has reviewed
and verified the technical contents of this release.
About Tinka Resources LimitedTinka is an exploration and development
company with projects in Peru. Tinka's focus is on its 100%-owned Ayawilca and
Colquipucro projects in the highly mineralized zinc-lead-silver belt of
central Peru, 200 kilometres north of Lima. The Ayawilca project (Inferred
Mineral Resource of 13.3 Mt (at) 7.7% Zn equiv., Feb 2015) has the potential to
be a major zinc sulphide discovery located 40 kilometres from Peru's largest
historic zinc mine, Cerro de Pasco. The adjacent Colquipucro silver oxide
project (Indicated Mineral Resource of 7.4 Mt (at) 60g/t Ag for 14.3 Moz Ag and
Inferred Mineral Resource of 8.5 Mt (at) 48 g/t Ag for 13.2 Moz Ag, Feb 2015) is
a near-surface, sandstone-hosted, silver oxide deposit.
On behalf of the Board,
"Graham Carman"Dr. Graham Carman, President & CEO
Forward Looking Statements. Certain information in this news release
contains forward-looking statements and forward-looking information within the
meaning of applicable securities laws (collectively "forward-looking
statements"). All statements, other than statements of historical fact, are
forward-looking statements. Forward-looking statements are based on the
beliefs and expectations of Tinka as well as assumptions made by and
information currently available to Tinka's management. Such statements reflect
the current risks, uncertainties and assumptions related to certain factors
including, without limitations, the proposed drill program, the Company's
expectations regarding mineral resources, capital and other costs varying
significantly from estimates, production rates varying from estimates, changes
in world metal markets, changes in equity markets, availability and costs of
financing needed in the future, equipment failure, unexpected geological
conditions, imprecision in resource estimates or metal recoveries, success of
future development initiatives, competition, operating performance,
environmental and safety risks, delays in obtaining or failure to obtain
necessary permits and approvals from local authorities, community relations,
and other development and operating risks. Should any one or more of these
risks or uncertainties materialize, or should any underlying assumptions prove
incorrect, actual results may vary materially from those described herein.
Although Tinka believes that assumptions inherent in the forward-looking
statements are reasonable, forward-looking statements are not guarantees of
future performance and accordingly undue reliance should not be put on such
statements due to the inherent uncertainty therein. Except as may be required
by applicable securities laws, Tinka disclaims any intent or obligation to
update any forward-looking statement.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this news release.
SOURCE Tinka Resources Limited



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2015/28/c5491.html

PDF available at:
http://stream1.newswire.ca/media/2015/07/28/20150728_C5491_PDF_EN_460428.pdf

PDF available at:
http://stream1.newswire.ca/media/2015/07/28/20150728_C5491_PDF_EN_460430.pdf

PDF available at:
http://stream1.newswire.ca/media/2015/07/28/20150728_C5491_PDF_EN_460432.pdf

-0-                           07/28/2015
/For further information: Investor Information: www.tinkaresources.com,
1305 - 1090 West Georgia St., Vancouver, BC, V6E 3V7, Mariana Bermudez,
1.604.699.0202, info(at)tinkaresources.com/
/Web Site: http://www.tinkaresources.com /
(TK. TKRFF)

CO:  Tinka Resources Limited
ST:  British Columbia
IN:  MNG
SU:

-30-