Source	Marketwire
Date	07/30/2015
Time	05:32:24 AM

Company	 KAMINAK GOLD CORPORATION
Title	Kaminak Reports Up to 85% Gold Recovery from Transitional Mineralization 
at Coffee Gold Project





    CDNX Symbol: KAM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

July 30, 2015

Kaminak Reports Up to 85% Gold Recovery from Transitional Mineralization at 
Coffee Gold Project


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 30, 2015) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) today announced results of the comprehensive 
metallurgical test work program conducted on transitional facies mineralization 
collected from the Coffee Gold Project, Yukon. The metallurgical results from 
bottle rolls, column testing and extensive cyanide (CN) soluble assaying will 
be used to better define the different facies of mineralization in the updated 
2015 resource block model, which will be included in the feasibility study 
("FS"), currently underway and scheduled for completion in Q1, 2016.

In 2014, Kaminak undertook a preliminary economic assessment ("PEA") at Coffee, 
which focused on oxide mineralization (mineralized zones containing in excess 
of 90% oxidized material) as there was little data available at that time to 
characterize gold recoveries from deeper transitional facies material. Later in 
the year, Kaminak collected additional metallurgical samples from both upper 
transitional mineralization (defined as nominal 80% cyanide recoverable gold 
between 70% and 90% oxide) and middle transitional (defined as nominal 60% 
cyanide recoverable gold between 50% and 70% oxide) with the aim of potentially 
qualifying additional recoverable gold resources for inclusion in the FS. A 
complete table of results from the 2014-2015 program is included below with 
highlights as follows:

Highlights

/T/

--  Column leach test results for transitional material at the 0.5 inch and
2.0 inch crush sizes collected from the Latte, Supremo and Kona deposits
yielded the following recoveries:

--  Latte upper transition core composite recovered 82.5% (2 tests)
--  Latte middle transition core composite recovered 58.5% (2 tests)
--  Supremo upper transition core composite recovered 84% (2 tests)
--  Kona upper transition core composite recovered 74% (2 tests)

--  Agglomeration was not required for any of the column tests and low
reagent consumption was reported.

--  All of the column leach tests at the 0.5 inch size were performed at a
temperature of 4 degrees Centigrade to simulate cold climate leaching.
Column leach test work was conducted by Kappes, Cassiday and Associates
("KCA"), industry leading experts in heap leach processing.

/T/

Supporting images associated with this metallurgical test work program may be 
viewed by clicking the following link:  
http://kaminak.com/_resources/images/NR_FinalMetSamplesTransitional.pdf

Kaminak cautions that these new metallurgical recoveries should not be applied 
to the 2014 block model for the purposes of estimating a potential contribution 
of transitional ounces to the existing PEA mine plan, as the mineralized 
oxidization facies were defined differently in 2013 and 2014 and are not 
comparable. Further, the final FS will incorporate a revised block model (based 
on infill drilling completed in 2014/2015) together with detailed geotechnical 
information, which was unavailable for the PEA.

Fred Lightner, Director of Mine Development to Kaminak stated: "The most recent 
test results from the KCA testing program will provide the basis for a much 
better quantification of gold recoveries from transitional material of the 
Coffee deposits for inclusion in the FS. When all of the revised block models 
for each deposit area have been completed and the final mine plan has been 
established, we will then have the basis for the determination of gold 
production for the FS."

2014-2015 Coffee Gold Project Metallurgical Test Work Program

Results of the column leach tests conducted by KCA are detailed below in Table 
1, 2 and 3. It should be noted that two different crush sizes were tested on 
the core composited transitional samples: 2 inch refers to a sample 100% 
passing 62.5 mm or approximately 80% passing 50 mm and 0.5 inch refers to a 
sample 100% passing 16 mm or approximately 80% passing 12.5 mm.

/T/


Table 1      Column Leach Test Results
Core Composites Transitional Samples (180 samples collected from 54 drill
holes)
----------------------------------------------------------------------------
Calculated
Crush          Head     Extracted
Column Sample Description       Temp       Size         Grade         Grade
and Location             degrees C      inches        g/t Au        g/t Au
----------------------------------------------------------------------------
Latte Upper Transition            22        2.0         1.458         1.197
----------------------------------------------------------------------------
Latte Upper Transition             4        0.5         1.928         1.597
----------------------------------------------------------------------------
Latte Middle Transition           22        2.0         1.473         0.924
----------------------------------------------------------------------------
Latte Middle Transition            4        0.5         1.061         0.578
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Supremo Upper Transition          22        2.0         1.041         0.890
----------------------------------------------------------------------------
Supremo Upper Transition           4        0.5         0.932         0.753
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Kona Upper Transition             22        2.0         1.358         0.979
----------------------------------------------------------------------------
Kona Upper Transition              4        0.5         1.351         1.022
----------------------------------------------------------------------------



Table 1      Column Leach Test Results
Core Composites Transitional Samples (180 samples collected from 54 drill
holes)
----------------------------------------------------------------------------
Addition
Gold              Consumption      Hydrated
Column Sample Description    Recovery       Days          NaCN          Lime
and Location                       %   of Leach          kg/t          kg/t
----------------------------------------------------------------------------
Latte Upper Transition             82%        81          0.79          1.49
----------------------------------------------------------------------------
Latte Upper Transition             83%        81          0.44          1.51
----------------------------------------------------------------------------
Latte Middle Transition            63%        81          0.76          1.52
----------------------------------------------------------------------------
Latte Middle Transition            54%        81          0.30          1.50
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Supremo Upper Transition           85%        67          0.61          1.50
----------------------------------------------------------------------------
Supremo Upper Transition           81%        67          0.43          1.20
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Kona Upper Transition              72%        81          0.76          1.53
----------------------------------------------------------------------------
Kona Upper Transition              76%        81          0.50          2.01
----------------------------------------------------------------------------

/T/

No percolation problems were reported in any of the column leach tests; 
therefore, the use of cement agglomeration was not required. All of the column 
leach tests at the 0.5 inch size were performed at a temperature of 4 degrees 
Centigrade to simulate cold climate leaching. The 2 inch crush size columns 
were too large to be contained in the refrigerator and were leached at ambient 
lab temperature (22 degrees C). Previous work has shown only a minor (-1%) gold 
recovery difference between ambient and simulated cold climate leaching.

Comparative Bottle Roll Test Work

Results from bottle roll test work undertaken on splits of the same composites 
utilized for column leaching are detailed below in Table 2. By using a fine 
grind, recoveries were not substantially increased over the column leach tests, 
indicating that heap leaching is the preferred method of gold extraction over 
agitation leaching (given the lower capital and operating costs typically 
associated with heap leaching).

/T/


Table 2      Results of Bottle Roll Leach Tests
----------------------------------------------------------------------------
Addition
Calculated Extracted    Avg.     Gold  Consumption    Hydrated
Head Grade     Grade   Tails Recovery        NaCN,        Lime
Description       g/t Au    g/t Au  g/t Au        %         kg/t        kg/t
----------------------------------------------------------------------------
Latte Upper
Transition        2.003     1.733   0.271       86%        0.15        2.50
----------------------------------------------------------------------------
Latte Middle
Transition        1.117     0.712   0.465       61%        0.16        2.50
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Supremo
Upper
Transition        0.994     0.859   0.135       86%        0.12        2.00
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Kona Upper
Transition        1.310     1.060   0.250       81%        1.33        2.75
----------------------------------------------------------------------------

/T/

2014-2015 Core Transitional Sample Selection and Classification Criteria

In order to better evaluate the amenability and variability of transitional 
material to metallurgical cyanide leach recovery, approximately 14,000 samples 
representing 82% of all samples above a fire assay value of 0.3g/t Au within 
mineralized intercepts drilled from the initial drilling year of 2010 up to and 
including 2015 have been subjected to a cyanide shake flask extraction test 
completed on assay pulps (cyanide soluble assay). The cyanide soluble assays 
were performed by ALS Laboratories (Au-AA13 method).

The difference between the cyanide soluble assay and the original fire assay, 
on an individual assay by assay basis, or across composites made up of 
equivalent samples, may be utilized to provide an indication of the gold within 
the sample that is amenable to cyanide leach. This may be referred to as (the 
percentage of total gold recoverable by CN solution or the CN solubility). By 
extension, CN solubility also indicates the amount of oxidation of the sample.

/T/


Classification criteria for mineralization facies:
Oxide: 90 - 100% CN soluble
Upper transition: 70 - 90% CN soluble
Middle transition: 50 - 70% CN soluble

/T/

To date, column test results, such as reported in Table 1 & 2, demonstrate the 
strong correlation of the cyanide soluble gold recovery to the actual column 
leach test recovery indicating that cyanide soluble gold recovery is a reliable 
method (or 'proxy') to map the metallurgical recovery throughout the oxide, 
transitional and sulphide zones of the Coffee deposits.

All of the samples used for the column leach tests were composited from drill 
core consisting of a wide distribution of different drill holes and individual 
intervals to give a representative sample of each deposit area. Furthermore, 
transitional samples for the 2014-2015 column testing were collected using the 
gold cyanide soluble database whereas in previous years transitional material 
was collected using visual estimations of the proportion of oxide and sulphide 
in drill samples. Details of the metallurgical test work composite selection 
are provided in Table 3.

/T/


Table 3      Metallurgical Core Composite Selection
----------------------------------------------------------------------------
No. of Core Drill    No. of Individual
Sample Description                                Holes      Drill Intervals
----------------------------------------------------------------------------
Latte Upper Transition                               13                   48
----------------------------------------------------------------------------
Latte Middle Transition                              11                   38
----------------------------------------------------------------------------
Supremo Upper Transition                             20                   45
----------------------------------------------------------------------------
Kona Upper Transition                                10                   
49----------------------------------------------------------------------------

/T/

QA / QC

Kaminak's disclosure of metallurgical data in this press release has been 
reviewed and approved by Fred Lightner, P.E., Director or Mine Development to 
Kaminak Gold Corporation, who serves as a Qualified Person under the definition 
of National Instrument 43-101. Disclosure of additional technical or scientific 
information in this press release has been reviewed and approved by Tim Smith, 
P.Geo., Vice President Exploration of Kaminak Gold Corporation, who serves as a 
Qualified Person under the definition of National Instrument 43-101.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO, Kaminak Gold Corporation

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of the 
future potential of the Coffee Project, costs and timings for completion of the 
Coffee Project feasibliity study and future exploration programs, constitute 
forward-looking statements that are subject to numerous risks, uncertainties 
and other factors relating to Kaminak's operations as a mineral exploration 
company that may cause future results to differ materially from those expressed 
or implied in such forward-looking statements, including risks as to the 
completion of the plans and projects. Readers are cautioned not to place undue 
reliance on forward-looking statements. Except as required by law, Kaminak 
expressly disclaims any intention or obligation to update or revise any 
forward-looking statements, whether as a result of new information, future 
event or otherwise.

The Company has not made a production decision, and the Company's strategic 
plan to develop a stand-alone heap leach operation is subject to the results of 
its Feasibility Study. Further, if and when the Company makes any production 
decision, it will disclose the basis of such decision in accordance with the 
requirements of National Instrument 43-101 Standards of Disclosure for Mineral 
Projects ("NI 43-101").

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice President of Corporate Development
604.646.4534 or toll free 1.844.646.4520
info@kaminak.com
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=537851841