Source	MARKET NEWS
Date	07/21/2016
Time	06:10:54 AM

Company	 Independence Gold Corp.
Title	Commences Drilling, Yukon





    CDNX Symbol: IGO











Press Release





Commences Drilling, Yukon --->@NEWS RELEASE
INDEPENDENCE GOLD CORP ("IGO-V;IEGCF-0")
- Commences Drilling, Yukon

Independence Gold Corp. ("the Company") is pleased to announce the
commencement of a reverse circulation (RC) drill program at its 100%
owned Boulevard Project, located 135 kilometres ("km") south of Dawson
City, 35 km south of Kinross Gold Corporation's Golden Saddle Deposit,
and contiguous to Goldcorp Inc's Coffee Deposit. The Company will also
be undertaking a rotary air blast (RAB) drill program on its recently
optioned Rosebute Property situated 58 km south of Dawson City. These
drill programs form Phase Two of the Company's $1.5 million Yukon
Exploration program in the White Gold District.

Approximately 2,000 metres ("m") of RC drilling is planned on the
Boulevard Project to test the Denali and Sunrise-Sunset Zones. The
Coffee Creek Fault system is an important structure that controlled the
emplacement of the 2.16 Million ounce Coffee Deposit (Kaminak Gold
press release Jan 6, 2016). This structure continues to the west and is
interpreted to extend into the Denali area, where soil sampling has
identified a 1.2 km long multi-element geochemical anomaly. RC drilling
will follow-up drill hole YCS15-03 which intersected 4.25 grams per
tonne ("g/t") gold across 6.10 m within the centre of this robust soil
anomaly. A similar structure, oriented subparallel with the Coffee
Creek Fault, is interpreted to control the 2.3 kilometre ("km") long
Sunrise-Sunset multi-element soil anomaly. For a map showing the
location of these two target areas and their proximity to the Coffee
Deposit please visit the Company's website www.ingold.ca.

Additionally, up to 1,500 m of RAB drilling is planned for the
Hudbay Zone on the Rosebute Property (July 5, 2016 news release). The
Hudbay Zone hosts three, north trending gold-in-soil anomalies, each
greater than 1.0 km in length and 150 m in width. In 2012, Taku
intersected 6.2 g/t gold over 5.0 m (Trench 2), 1.2 g/t gold over 10.0
m (trench 5) and 1.5 g/t gold over 20.0 m (Trench 4) (Taku news release
September 12, 2012) all located within the Hudbay Zone.

Independence Gold Corp. (TSX VENTURE:IGO) is a well-financed
mineral exploration company listed on the TSX Venture Exchange, with a
portfolio of projects in the Yukon and the 3Ts Project located in
British Columbia. The Company's holdings range from early stage
grassroots exploration to advanced-stage resource expansion. For
additional information please visit the Company's website
www.ingold.ca.

David Gale, P.Geo., the Company's Qualified Person as defined by
National Instrument 43-101 for the White Gold District projects, has
reviewed the technical information in this news release.

INDEPENDENCE GOLD CORP.
Randy Turner, President & CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.



Independence Gold Corp.
Corporate Development
604-687-3959
info@ingold.ca
______________________________
_______________________________________________
TSX Venture closing price for IGO-V
Date: 2016/07/20
Closing Price: 0.36
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1620200013TS11620200832-06085920160721