Source	Marketwire
Date	07/21/2016
Time	06:03:34 AM

Company	 MIDLAND EXPLORATION INC.
Title	Midland Completes Phase I Prospecting Program on the Willbob Gold Project, 
Labrador Trough, and Identifies Several New High-Grade Gold Showings Up to 15 
g/t Au





    CDNX Symbol: MD











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Midland Exploration Inc.

TSX VENTURE SYMBOL: MD

July 21, 2016

Midland Completes Phase I Prospecting Program on the Willbob Gold Project, 
Labrador Trough, and Identifies Several New High-Grade Gold Showings Up to 15 
g/t Au


MONTREAL, QUEBEC--(Marketwired - July 21, 2016) - Midland Exploration Inc. 
("Midland") (TSX VENTURE:MD) is pleased to report the latest results of its 
reconnaissance campaign conducted this summer on its Willbob Project (wholly 
owned by Midland) including the discovery of several new significant gold 
showings with values up to 15.05 grams per tonne gold ("g/t Au") on the PBN 
showing ("PBN"). These new gold occurrences are located along a high-grade 
gold-bearing corridor that includes also several other historical occurrences 
such as showing 31, which graded up to 31.0 g/t Au, as well as the Kuni (up to 
19.8 g/t Au), Lafrance (up to 21.9 g/t Au), Dupuis East (up to 15.0 g/t Au), 
and Polar Bear (up to 6.4 g/t Au) showings.

The PBN showing is located 700 metres north of the Polar Bear showing (6.4 g/t 
Au) and returned values of 15.05 g/t Au, 0.68 g/t Au, and 0.16 g/t Au. These 
grab samples were collected in quartz veins with pyrite and galena 
mineralization and in a carbonate-facies iron formation. Another significant 
alteration zone with ankerite-albite-chlorite, named the Sunshine showing 
("Sunshine"), returned gold grades up to 7.27 g/t Au. The Sunshine zone was 
traced over more than 150 metres strike length and also returned values of 3.18 
g/t Au, 2.72 g/t Au, 1.72 g/t Au, 1.27 g/t Au, and six other gold values 
between 0.20 g/t Au and 0.65 g/t Au. (Note that gold values from selected grab 
samples may not be representative of the mineralized zones).

Over a short period of 28 days, a total of 619 grab samples were collected, 
mainly in the north part of the property between the Dessureault and Kuni South 
showings. The first phase of the 2016 summer program also included systematic 
mapping of quartz-ankerite-albite-chlorite alteration halos surrounding 
gold-bearing systems on the Willbob property. Only 212 samples have been 
analyzed to date, out of the 619 samples collected in the field. The remaining 
assay results are expected in the coming weeks.

An airborne magnetic survey was successfully completed and covered the entire 
Willbob property, which extends over more than 30 kilometres along a NNW-SSE 
axis by more than 7 km in width. The survey covered the property with flight 
lines spaced every 100 metres, for a total of 2,164 line kilometres.

Results of the 2015 work program included the discovery of two new showings 
with grades of 1.2 g/t Au and 77.6 g/t Au, respectively located 500 metres and 
850 metres south of the Kuni showing. Closer and located between the two 
high-grade gold occurrences, a new polymetallic grab sample also yielded values 
of 1.2 g/t Au, 132 g/t Ag, 8.5% Pb and 7.1% Zn (see Midland press release dated 
August 26, 2015). Also in 2015, the new Golden Tooth discovery, including 
nearly 30 samples collected along a newly identified shear zone with 
quartz-albite alteration, revealed the presence of gold with ten samples 
grading more than 3.0 g/t Au and reaching up to 25.2 g/t Au (see Midland press 
release dated October 6, 2015). None of these new occurrences had been 
previously tested by channel sampling or drilling.

Similar to orogenic gold deposits, these showings are characterized by strong 
iron carbonate, fuchsite (chrome-rich mica) and quartz alteration as well as 
the presence of disseminated arsenopyrite, chalcopyrite, pyrrhotite and pyrite, 
observed over thicknesses ranging from 10 to 100 metres and traced 
discontinuously over more than 10 kilometres strike length.

Midland has great hopes for this project and intends to resume its exploration 
efforts in the fall, with prospecting, mapping, channel sampling, as well as a 
diamond drilling campaign totalling about 1,500 to 2,000 metres. The Willbob 
property consists of 318 mining claims covering a surface area of about 140 
square kilometres and is located about 70 kilometres west of the town of 
Kuujjuaq, in Nunavik. The claim block is underlain by a volcano-sedimentary 
complex that exhibits complex folding and is injected with several gabbroic and 
ultramafic sills.

Figures showing the location of the new gold occurrences on the Willbob Project 
may be consulted using the following link: 
http://media3.marketwire.com/docs/Willbob_July_21_2016.pdf

Quality Control

All analysis were performed by ALS Minerals in Val d'Or. All samples were 
analyzed for gold by fire assay with an atomic absorption finish (AA23) on a 
fraction of 30 grams and a gravimetric finish for values greater than 3.0 g / t 
Au. For the quality control, in each transmission, certified standards and 
blanks were inserted at regular intervals throughout the sequence of samples. 
The data was reviewed by Mario Masson, VP Exploration for Midland, certified 
geologist and Qualified Person as defined by NI 43-101.

About Midland

Midland targets the excellent mineral potential of Quebec to make the discovery 
of new world-class deposits of gold, platinum group elements, base metals and 
rare earth elements. Midland is proud to count on reputable partners such as 
Agnico Eagle Mines Limited, Teck Resources Limited, SOQUEM INC., Osisko 
Exploration James Bay Inc., Japan Oil and Gas and Metals National Corporation 
and Abcourt Mines Inc. Midland prefers to work in partnership and intends to 
quickly conclude additional agreements in regard to newly acquired properties. 
Management is currently reviewing other opportunities and projects to build up 
the Company portfolio and generate shareholder value.

This press release was prepared by Richard D. St-Cyr, project geologist, 
certified geologist and Qualified Person as defined by NI 43-101. For further 
information, please consult Midland's website www.midlandexploration.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This press release may contain forward-looking statements that are subject to 
known and unknown risks and uncertainties that could cause actual results to 
vary materially from targeted results. Such risks and uncertainties include 
those described in Midland's periodic reports including the annual report or in 
the filings made by Midland from time to time with securities regulatory 
authorities.

- 30 -

CONTACT INFO:

Gino Roger
President and Chief Executive Officer
450 420-5977
Fax: 450 420-5978
info@midlandexploration.com
www.midlandexploration.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=573060256