Source	MARKET NEWS
Date	07/21/2016
Time	06:47:14 AM

Company	 Midland Exploration Inc.
Title	Completes Phase I Prospecting Program On The Wil





    CDNX Symbol: MD











Press Release





Completes Phase I Prospecting Program On The Willbob Gold Project,Labrador 
Trough, And Identifies Several New High Grade Gold ShowingsUp To 15 G/t Au 
--->@NEWS RELEASE
MIDLAND EXPLORATION INC ("MD-V")
- Completes Phase I Prospecting Program On The Willbob Gold
- Project, Labrador Trough, And Identifies Several New High-Grade
- Gold Showings Up To 15 G/t Au

Midland Exploration Inc. ("Midland") is pleased to report the
latest results of its reconnaissance campaign conducted this summer on
its Willbob Project (wholly owned by Midland) including the discovery
of several new significant gold showings with values up to 15.05 grams
per tonne gold ("g/t Au") on the PBN showing ("PBN").These new gold
occurrences are located along a high-grade gold-bearing corridor that
includes also several other historical occurrences such as showing 31,
which graded up to 31.0 g/t Au, as well as the Kuni (up to 19.8 g/t
Au), Lafrance (up to 21.9 g/t Au), Dupuis East (up to 15.0 g/t Au), and
Polar Bear (up to 6.4 g/t Au) showings.

The PBN showing is located 700 metres north of the Polar Bear
showing (6.4 g/t Au) and returned values of 15.05 g/t Au, 0.68 g/t Au,
and 0.16 g/t Au.These grab samples were collected in quartz veins with
pyrite and galena mineralization and in a carbonate-facies iron
formation. Another significant alteration zone with
ankerite-albite-chlorite, named the Sunshine showing
("Sunshine"),returned gold grades up to 7.27 g/t Au.The Sunshine zone
was traced over more than 150 metres strike length and also returned
values of 3.18 g/t Au, 2.72 g/t Au, 1.72 g/t Au, 1.27 g/t Au, and six
other gold values between 0.20 g/t Au and 0.65 g/t Au.(Note that gold
values from selected grab samples may not be representative of the
mineralized zones).

Over a short period of 28 days, a total of 619 grab samples were
collected, mainly in the north part of the property between the
Dessureault and Kuni South showings. The first phase of the 2016 summer
program also included systematic mapping of
quartz-ankerite-albite-chlorite alteration halos surrounding
gold-bearing systems on the Willbob property. Only 212 samples have
been analyzed to date, out of the 619 samples collected in the field.
The remaining assay results are expected in the coming weeks.

An airborne magnetic survey was successfully completed and covered
the entire Willbob property, which extends over more than 30 kilometres
along a NNW-SSE axis by more than 7 km in width. The survey covered the
property with flight lines spaced every 100 metres, for a total of
2,164 line kilometres.

Results of the 2015 work program included the discovery of two new
showings with grades of 1.2 g/t Au and 77.6 g/t Au, respectively
located 500 metres and 850 metres south of the Kuni showing. Closer and
located between the two high-grade gold occurrences, a new polymetallic
grab sample also yielded values of 1.2 g/t Au, 132 g/t Ag, 8.5% Pb and
7.1% Zn (see Midland press release dated August 26, 2015). Also in
2015, the new Golden Tooth discovery, including nearly 30 samples
collected along a newly identified shear zone with quartz-albite
alteration, revealed the presence of gold with ten samples grading more
than 3.0 g/t Au and reaching up to 25.2 g/t Au (see Midland press
release dated October 6, 2015). None of these new occurrences had been
previously tested by channel sampling or drilling.

Similar to orogenic gold deposits, these showings are
characterized by strong iron carbonate, fuchsite (chrome-rich mica) and
quartz alteration as well as the presence of disseminated arsenopyrite,
chalcopyrite, pyrrhotite and pyrite, observed over thicknesses ranging
from 10 to 100 metres and traced discontinuously over more than 10
kilometres strike length.

Midland has great hopes for this project and intends to resume its
exploration efforts in the fall, with prospecting, mapping, channel
sampling, as well as a diamond drilling campaign totalling about 1,500
to 2,000 metres. The Willbob property consists of 318 mining claims
covering a surface area of about 140 square kilometres and is located
about 70 kilometres west of the town of Kuujjuaq, in Nunavik. The claim
block is underlain by a volcano-sedimentary complex that exhibits
complex folding and is injected with several gabbroic and ultramafic
sills.

Figures showing the location of the new gold occurrences on the
Willbob Project may be consulted using the following link:
http://media3.marketwire.com/docs/Willbob_July_21_2016.pdf

Quality Control

All analysis were performed by ALS Minerals in Val d'Or. All
samples were analyzed for gold by fire assay with an atomic absorption
finish (AA23) on a fraction of 30 grams and a gravimetric finish for
values greater than 3.0 g / t Au. For the quality control, in each
transmission, certified standards and blanks were inserted at regular
intervals throughout the sequence of samples. The data was reviewed by
Mario Masson, VP Exploration for Midland, certified geologist and
Qualified Person as defined by NI 43-101.

About Midland

Midland targets the excellent mineral potential of Quebec to make
the discovery of new world-class deposits of gold, platinum group
elements, base metals and rare earth elements. Midland is proud to
count on reputable partners such as Agnico Eagle Mines Limited, Teck
Resources Limited, SOQUEM INC., Osisko Exploration James Bay Inc.,
Japan Oil and Gas and Metals National Corporation and Abcourt Mines
Inc. Midland prefers to work in partnership and intends to quickly
conclude additional agreements in regard to newly acquired properties.
Management is currently reviewing other opportunities and projects to
build up the Company portfolio and generate shareholder value.

This press release was prepared by Richard D. St-Cyr, project
geologist, certified geologist and Qualified Person as defined by NI
43-101. For further information, please consult Midland's website
www.midlandexploration.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

This press release may contain forward-looking statements that are
subject to known and unknown risks and uncertainties that could cause
actual results to vary materially from targeted results. Such risks and
uncertainties include those described in Midland's periodic reports
including the annual report or in the filings made by Midland from time
to time with securities regulatory authorities.

TSX Venture closing price for MD-V
Date: 2016/07/20
Closing Price: 1.00

TEL:  450 420-5977  Gino Roger
President and Chief Executive Officer
FAX:  450 420-5978
EMAIL:  info@midlandexploration.com
INTERNET:  www.midlandexploration.com
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1620200018TS11620200943-06462820160721