Source	Marketwire
Date	07/05/2016
Time	06:13:32 AM

Company	 KHALKOS EXPLORATION INC.
Title	Khalkos Drills on the Malartic Property, Révillard Part/Resignation of a 
Director





    CDNX Symbol: KAS











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Khalkos Exploration Inc.

TSX VENTURE SYMBOL: KAS

July 5, 2016

Khalkos Drills on the Malartic Property, Révillard Part/Resignation of a 
Director


MONTREAL, QUEBEC--(Marketwired - July 5, 2016) - Khalkos (TSX VENTURE:KAS) 
announces that more than 1,000 metres of diamond drilling will be undertaken in 
upcoming days on the Malartic property, Revillard part. This first drilling 
campaign aims to investigate the auriferous potential under the main stripping 
zone of Revillard showing. No drilling was executed under this stripping zone 
with an area of around 3,000 square metres on which around one hundred 
twenty-five linear metres of channel sampling were undertaken in 2006. Samples 
collected during these fieldworks yielded the following results: 200 samples 
ranging 0.01 g/t Au to 1 g/t Au, 70 samples of 1 to 3 g/t Au, 35 samples of 3 
to 6 g/t Au, 19 samples of 6 to 10 g/t Au and 10 samples of more than 10 g/t Au 
(reference press release of Britannica Resources of 18 July, 2006).

Ten short drill holes will be undertaken directly under the stripping zone in 
two different directions. The first direction aims to validate the grade and 
the thickness of the principal shear zone while the second will allow to 
validate the presence of high-grade gold, sulphide veinlets oriented in an 
another direction than the shear zone itself. The main shear zone is located at 
the contact of mafic volcanic rocks of Blake River Group and sedimentary rocks 
of Kewagama Group.

The president of the Company, Robert Gagnon, states that it is exceptional that 
a junior company is able to survey a gold surface showing of this amplitude 
which still has not been tested by drilling in one of the most important mining 
camps in Canada. The Malartic property is constituted of 3 different, 
contiguous parts for a total of 82 claims located in between the Marban East 
and Marban West properties of the Osisko Mining company.

Resignation of a Director

The Company wishes to announces the resignation of Mr. Andre Proulx from its 
Board of Directors. The board of Khalkos would like to thank M. Proulx for its 
two terms as director of the Company.

This press release was prepared by Robert Gagnon, President of Khalkos, 
Qualified Person pursuant to National Instrument 43-101.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Robert Gagnon
President
(819) 825-2303
rgagnon@khalkos.com

or

Christian Guilbaud
Corporate Development
(514) 813-7862
cguilbaud@videotron.ca
www.khalkos.com
Fax: (514) 510-7964

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=571536151