Source	Marketwire
Date	07/05/2016
Time	10:01:33 AM

Company	 MUNDORO CAPITAL INC.
Title	Mundoro Commences Drill Program on Jogmec-Mundoro JV Serbian Properties





    CDNX Symbol: MUN











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Mundoro Capital Inc.

TSX VENTURE SYMBOL: MUN

July 5, 2016

Mundoro Commences Drill Program on Jogmec-Mundoro JV Serbian Properties


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 5, 2016) - Mundoro Capital 
Inc. (TSX VENTURE:MUN) (www.mundoro.com) ("Mundoro" or the "Company") is 
pleased to report drilling has commenced on the Company's 100% owned 
exploration licenses, Dubrava and Zeleznik which are located at the central and 
northern end of the Timok Magmatic Complex ("TMC") in northeastern Serbia (see 
Figure 1: Location Map - Timok North Projects).

HIGHLIGHTS

/T/

--  3000 m drill program began July 1 on Timok North Projects
--  Timok North Project work programs sole funded by JV partner JOGMEC
--  Previous drilling and geophysics programs provided high priority targets
including:
--  25.8 m of 0.47% CuEq interval in the West Zone (ZELDD01 from 29.2 m
to 55.0 m)
--  4.9 m of 1.40% CuEq interval in the East Zone (ZELDD06 from 137.4 m
to 142.3 m EOH)
--  2.8 m of 2.98% CuEq interval in the East Zone (ZELDD05 from 26.6 m
to 29.4 m)
--  Mundoro maintains a strong treasury and is debt free

/T/

Teo Dechev, CEO and President of Mundoro commented, "This program will focus on 
testing three copper-gold porphyry and epithermal systems within the two 
properties. We believe the drilling program at Zeleznik will further delineate 
the extent of the copper-gold porphyry identified in the West Zone from the 
first round of drilling results in January 2015 as well as the massive 
sulphides identified in the East Zone. For Mundoro shareholders, the JOGMEC 
funded exploration activity including drilling and geophysics will allow for 
more aggressive exploration of the Timok North Projects and bring us closer to 
identify a resource on the discovery at Zeleznik. At the end of Q1-2016, 
Mundoro had a treasury of $5.1 million and no debt."

Drilling commenced on July 1, 2016 under the Option Agreement between Mundoro 
and Japan Oil, Gas and Metals National Corporation. ("JOGMEC") announced March 
7, 2016. Under the terms of the agreement JOGMEC may earn a 51% interest in the 
Timok North Projects by making US$3 million in expenditures by March 7, 2018. 
JOGMEC is under a firm commitment to expend US$1 million of this amount by 
March 7, 2017. Stage Two Earn-in: Following the Stage One Earn-in, JOGMEC has a 
right to acquire an additional 24% interest in the Timok North Projects, for a 
total of 75% interest, by funding the completion of a Feasibility Study by the 
eighth anniversary of the Agreement (March 7, 2024). The current drill program, 
which is a part of the Stage One Earn-in and the US$1 million commited 
expenditure, is being sole funded by JOGMEC and includes this 3000 m diamond 
drilling program.

JOGMEC-Mundoro Drill Program

This drilling program is designed to test various copper-gold targets over two 
of the Timok North Projects. The final number of holes drilled will be 
dependent on results obtained through the course of the drilling program. The 
targets have been identified through a systematic program completed by the 
Company comprising of detailed mapping, geochemistry, alteration mapping, 
ground geophysics, regional geophysics and initial drilling testing. The 
properties and targets to be tested are described below.

Zeleznik Property

The Zeleznik license is a 60 sq.km area located at the northern end of the TMC 
in northeastern Serbia, 160 km southeast of Belgrade. Zeleznik directly borders 
the Majdanpek mining complex to north and is 45 km northwest of the Bor 
smelter-refinery. The southern end of the property has several areas of 
anomalous Cu-Mo-Au geochemical results related to andesite-diorite porphyry 
intrusions. The western anomaly ("West Zone") is 600 m x 450 m and is open 
along strike to the north and south, while the eastern anomaly ("East Zone") is 
300 m x 300 m in outcrop and dips under a limestone cap to the northeast and 
remains open along strike.

Initial drilling at these two target areas has intersected mineralization 
throughout the drill holes and indicated the systems remain open at depth and 
along strike at both the West Zone and East Zone.

An initial ground magnetic survey was completed over the West Zone and East 
Zone during the 2015 field season. Additional geophysics surveys consisting of 
IP-Resistivity and CSAMT-AMT were completed in Q1-2016. The follow-up surveys 
comprised 8 profiles lines, each 3200 m long and totalling 25.6 line-km. Both 
surveys successfully identified drill targets and were used to focus the 
current drilling program (see Figure 2: Zeleznik Drillhole Location Map).

At the West Zone, the phase 1 drilling intersected several porphyry dikes 
cutting basement gneiss. The intersected porphyries are potassic altered and 
the host gneiss is cut by A-type quartz veins and veinlets containing 
pyrite-chalcopyrite mineralisation. A 25.8 m intercept centred on the early 
porphyry dyke averages 0.47% copper-equivalent ("CuEq"). At the West Zone Cu-Au 
porphyry system, geophysics results show that the strongest IP chargeability 
anomalies remain untested at depth as well as highlighting an additional 
interpreted porphyry target at the northern end of the system. Three drillholes 
(PH07, PH09 and PH12) totalling 1070 m are planned for the West Zone:

/T/

--  PH07 is designed to test the continuation of the stockwork
mineralisation and diorite porphyry intersected in ZELDD01, the strong
IP anomaly, and the interpreted mineralised structure. The planned depth
of 350 m will penetrate through a resistivity high and test the
resistivity low anomaly coincident with the strongest IP anomaly in the
West Zone.
--  PH09 is planned to a depth of 370 m and designed to test the strong IP
anomaly coinciding with moderate resistivity anomaly and the
continuation of mineralisation and potassic alteration intersected in
ZELDD02.
--  PH12 is designed to test the high resistivity with strong IP near
surface phyllic alteration with quartz (overprint) while the IP high
with resistivity low anomaly at depth suggests primary mineralisation
related to a structure or possibly porphyry stock projected to 700 to
800 m depth in magneto-telluric sections.

/T/

At the East Zone, all three drillholes from phase 1 drilling intersected 
andesite porphyry containing massive sulphide blocks with typically 0.3-0.5% Cu 
and 0.3-0.6 g/t Au; however, one 4.9 m interval at the end of drill hole 
ZELDD06 (137-142 m) averaged 1.4% CuEq (approx. 1% Cu and 1 g/t Au). A block of 
gossan after massive sulphide intersected in drill hole ZELDD05 (26-29 m) 
reported even higher grades of 2.8 m @ 2.98% CuEq (approx. 2% Cu and 2 g/t Au) 
and is similar to the gossan sampled in proximal road cuts (7.57 g/t Au; 2.65% 
Cu).

The Company believes the drilling and surface sampling work and geophysical 
interpretations to-date suggest the potential for discovery of bulk porphyry 
mineralisation containing high grade sulphide blocks formed by carbonate 
replacement along porphyry-host limestone contact. The existence of these 
sulphide blocks is significant in that close analogues to this style of 
mineralisation demonstrate that the blocks can boost the overall grade of the 
related porphyry system.

Prior drilling on the East Zone has bottomed in mineralisation and requires 
further testing to depth and along strike. The strongest Cu-Au soil and trench 
anomalies in the area also remain untested. The IP-resistivity survey 
highlighted new targets and fault zones which appear to be related to a newly 
inferred and larger mineralisation center. The regional stratigraphy, preserved 
limestone cap and epithermal geochemical signature all suggest that little 
erosion has taken place and the presence of a potentially preserved copper-gold 
mineralised system beneath. This geological model requires further exploration 
drilling along strike and at depth. Three drillholes (PH08, PH10 and PH11) 
totalling 1100 m are planned for the East Zone:

/T/

--  PH08 is located at the strongest Cu-Au soil anomaly at the East Zone
which remained untested from the previous drilling. It is believed that
drill hole ZELDD06 tested the margin of the anomaly at a depth of 142.3
m where it intersected brecciated and faulted diorite containing quartz-
carbonate-pyrite-chalcopyrite veinlets at upper levels and a brecciated
fault zone bearing massive and disseminated pyrite-chalcopyrite
mineralization at lower levels. Results from geophysical surveys also
show significant low resistivity and moderate IP chargeability related
to the surface Cu-Au anomaly capped by highly resistive limestone. The
drillhole is projected to a depth of 500 m aiming to intersect the low
resistivity anomaly and reach the moderate to high chargeability
anomaly.
--  PH10 is designed to test the strongest IP anomaly at the East Zone which
is located under the limestone cap. This area is characterized by Sb-As
pervasive soil anomaly and spotty Au anomalies which penetrate through
the recrystallized limestone. The IP anomaly coincides with a
resistivity low and both start at 200 m depth. To date, PH10 will be the
northern most drillhole testing the northern extension of the
mineralised system under the limestone cap.
--  PH11 is designed to test a strong surface Au-in-soil anomaly and
anomalous trench samples which coincide with a prominent resistivity low
at depth that extends to 1500 m depth. The resistivity low was
determined by the AMT and IP resistivity surveys. There is no detectable
IP anomaly at this area however elevated chargeability is directly
related to the surface soil anomaly.

/T/

Dubrava Property

The Dubrava license totals 51 sq.km and wraps around the eastern side of the 
Bor Mine Complex and the Veliki Krivelj open pit mine, and is 3.5 km north from 
the Cukaru Peki deposit discovered by the Freeport-Reservoir JV. Mundoro's 
exploration work on the Dubrava license has demonstrated very encouraging 
results of 28 m @ 0.2% Cu, 0.25 g/t Au (0.36% CuEq) in drillhole BJ-04 
including 7 m @ 0.5% Cu, 0.69 g/t Au (0.94% CuEq).

Since the Dubrava license has no outcrop and is mostly covered by post-mineral 
Miocene and Cretaceous sediments, the Company has relied on geophysical 
exploration methods and has completed AMT, CSAMT, IP and gravity surveys over 
prospective parts of the licence area. In proximity of drillhole BJ04, four 
closely spaced (approx. 50 m apart) IP lines have been carried out in order to 
delineate the massive sulfide mineralisation intersected at depth as well as to 
try to locate the controlling hydrothermal breccia structure (see Figure 3: 
Dubrava Drillhole Location Map). IP Resistivity and CSAMT surveys at Dubrava 
have identified two IP/Resistivity anomalies located west of drill hole BJ04. 
As such, the following two drill holes are planned to test these targets:

/T/

--  PDUB01 is located 180 m northwest of BJ04 and is designed to test the
IP/Resistivity anomaly which starts at 50 m depth and is well defined up
to 300 m. This anomaly also encompasses the area of drill hole BJ04 and
the intersected sulphide mineralisation. The drillhole aims to test for
lateral and depth continuation of this previously intersected
mineralisation.
--  PDUB02 is located 430 m west of BJ04 and 270 m southeast of PDUB01. It
is projected to test the well expressed IP/Resistivity anomaly. It is
open at depth and laterally links with the anomalies to the north at
shallower levels. The IP chargeability anomaly overlaps with the
resistivity anomaly which makes the target promising for possible
relation to a massive sulphide body.

/T/

Technical information contained in this Press Release has been reviewed and 
approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by National 
Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian based public company which is focused on generating value 
for its shareholders through utilizing the collective expertise of our 
directors, management and technical staff to invest in mineral projects that 
have the potential to generate future cash.

About JOGMEC

JOGMEC was established in February, 2004, following the integration of the 
former Japan National Oil Corporation (JNOC) and Metal Mining Agency of Japan 
(MMAJ). It is a state corporation administrated by the Ministry of Economics, 
Trade and Industry of Japan (METI), with a mandate of developing minerals 
projects worldwide to help secure a stable supply of natural resources for 
Japanese industry.

Caution Concerning Forward-Looking Statements
Information included, attached to or incorporated by reference into this News 
Release may contain forward-looking statements. All statements, other than 
statements of historical fact, included or incorporated by reference in this 
News Release are forward-looking statements, including, without limitation, 
statements regarding activities, events or developments that the Board expects 
or anticipates may occur in the future. These forward-looking statements can be 
identified by the use of forward-looking words such as "will", "expect", 
"intend", "plan", "estimate", "anticipate", "believe", "promising", "encouring" 
or "continue" or similar words or the negative thereof. The material 
assumptions that were applied in making the forward looking statements in this 
News Release include expectations as to the Company's future strategy and 
business plan and execution of the Company's existing plans. There can be no 
assurance that the plans, intentions or expectations upon which these 
forward-looking statements are based will occur. We caution readers of this 
News Release not to place undue reliance on forward looking statements 
contained in this News Release, which are not a guarantee of performance and 
are subject to a number of uncertainties and other factors that could cause 
actual results to differ materially from those expressed or implied by such 
forward-looking statements. These factors include general economic and market 
conditions, changes in law, regulatory processes, the status of Mundoro's 
assets and financial condition, actions of competitors and the ability to 
implement business strategies and pursue business opportunities. The 
forward-looking statements contained in this News Release are expressly 
qualified in their entirety by this cautionary statement. The forward-looking 
statements included in this News Release are made as of the date of this News 
Release and the Board undertakes no obligation to publicly update such 
forward-looking statements to reflect new information, subsequent events or 
otherwise, except as required by law. Shareholders are cautioned that all 
forward-looking statements involve risks and uncertainties and for a more 
detailed discussion of such risks and other factors that could cause actual 
results to differ materially from those expressed or implied by such 
forward-looking statements, refer to the Company's filings with the Canadian 
securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Mundoro Capital Inc.
Teo Dechev
CEO, President and Director
+1-604-669-8055

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=571565223