Source	MARKET NEWS
Date	07/06/2016
Time	06:05:40 AM

Company	 Great Thunder Gold Corp.
Title	Commissions Technical Report For Chubb And Bouvi





    CDNX Symbol: GTG











Press Release





Commissions Technical Report For Chubb And Bouvier LithiumProspects; Pegmatite 
Target Zones Already Identified On BothProperties --->@NEWS RELEASE
GREAT THUNDER GOLD CORP ("GTG-V")
- Commissions Technical Report For Chubb And Bouvier Lithium
- Prospects; Pegmatite Target Zones Already Identified On Both
- Properties

Great Thunder Gold Corp. is pleased to announce that it has
commissioned Dr. Michel Boily to prepare a National Instrument 43-101
technical report on its recently optioned Chubb and Bouvier lithium
properties located in the Preissac-Lacorne plutonic complex of the
Abitibi Greenstone Belt near Val d?Or, Quebec. Dr. Boily expects to
conduct a site inspection July 13 and 14.

Pegmatite target zones are already identified on both properties
from previous IP/Resistivity surveys. Great Thunder expects to carry
out drilling campaigns on the Chubb and Bouvier properties once the
technical report is complete and identifies new possible targets.

The Chubb Property

The Chubb lithium property is situated within the Preissac-Lacorne
plutonic complex of the Abitibi Greenstone Belt - the complex forming
one of the best prospective areas for lithium mineralization. The
plutonic complex generated the Quebec Lithium mine for which Canada
Lithium reported measured and indicated resources of 29.3 Mt grading
1.19% Li2O and 20.9 Mt of inferred resources grading 1.15% Li2O,
respectively, according to a technical report by Canada Lithium filed
on SEDAR June 8, 2011.

The Chubb property lies 32 kilometres north of Val d?Or and
consists of 35 contiguous recorded mineral claims with a total area of
1,509 hectares. The property's geology is dominated by quartz
monzodiorite and metasomatized quartz diorite (tonalite). A swarm of
spodumene-rich granitic pegmatite dykes intrude fractures and small
faults within the plutonic rocks. The pegmatite dykes are 1 to 6 m
thick, oriented 345 - 350 and vary in length from 25 to 250 m. They are
crudely zoned, some having quartz cores and border zones of aplite. The
granitic pegmatites are composed of quartz, albite and/or
cleavelandite, K-feldspar, muscovite, with 5 to 25% spodumene. There
are three important granitic pegmatite dykes containing spodumene
mineralization (Dyke #1, #2 and Main Dyke).

Exploration of the Chubb property persists since the early 1950s
and has consisted mainly of mapping, trenching, geophysical surveys and
diamond drilling. The best drilling intersections were obtained in 1994
by Abitibi Lithium Corp., producing intervals of 3.72 m @1.78 wt. %
Li2O, 2.75 m @1.00 wt. % Li2O and 2.38 m @1.25 wt. % Li2O. In 2010,
Mineral Hill Industries Ltd. carried out magnetic and IP geophysical
surveys, mapping, channel sampling and grab sampling in the area
surrounding the three principal spodumene-bearing dykes. The main dyke
- which is 300 m long - was shown to have Li2O concentration of 1.00
wt. % (n=41).

The Bouvier Property

The Bouvier property is located within the Preissac-Lacorne
plutonic complex of the Abitibi Greenstone Belt, in the Saint-Mathieu
Municipality of Figuery Township. The geological setting and structure
of the volcano-sedimentary assemblages form an ideal host for
lithium-rich pegmatites being located between the Northern Manneville
Deformation Zone and the northern edge of the fertile Lacorne
monzogranite pluton.

The Bouvier property consists of 16 contiguous recorded mineral
claims for a total area of 692 hectares. The southern Bouvier property
contains several exposures of biotitemuscovite monzogranitic plutonic
rocks intruding metasediments and injected by granitic pegmatite and
aplite dykes that constitute nearly 20% of the rock. Many granitic
pegmatites contain beryl and tantalite, but very few have spodumene.

To the north, the metasediments are in structural contact with the
metavolcanic rocks of the Malartic and Harricana groups, with the
Manneville Deformation Zone marking the contact between the
metasedimentary and metavolcanic formations. Spodumene-bearing granitic
pegmatite dykes occur only south of the Manneville Fault and were
emplaced principally in metasediments. The dykes are oriented parallel
to the Manneville Fault and can reach 100 m in length and 10 m in
apparent thickness. Most granitic pegmatites are zoned, some having
quartz cores and border zones of aplite. They are composed of quartz,
albite and/or cleavelandite, K-feldspar, muscovite, with 5 to 25%
spodumene. Accessory minerals are beryl, tantalite, garnet, bismuthine
and molybdenite.

The Bouvier property was submitted to sporadic mining exploration
from the early 1950s to 1979 that included geological mapping, rock
sampling, trenching and diamond drilling. A bulk sample taken by Teck
Corporation and reported in their 1979 Annual Report, returned an
average grade of 1.39% Li2O and an estimated "possible" historical
resource of 907,000 tons. In 2010, Mineral Hill Industries Ltd. carried
out an exploration program involving line cutting, a magnetic and
IP/Resistivity survey, trenching, and panel and grab rock sampling. The
work unearthed east-west oriented spodumene-bearing granitic pegmatite
dykes parallel to the Manneville Deformation Zone. The main dyke
displayed an average lithium concentration of 1.51 Li2O wt. % (n=20).

The estimates presented are treated as historic information and
have not been verified or relied upon for economic evaluation by the
Company. These historical mineral resources do not refer to any
category of sections 1.2 and 1.3 of National Instrument 43-101, such as
mineral resources or mineral reserves as stated in the 2010 CIM
Definition Standards on Mineral Resources and Mineral Reserves. The
Company is unable to verify the data acquired by the various historical
drilling campaigns, and must undertake additional sampling and drilling
to verify historical estimates. A Qualified Person has not done
sufficient work to classify the historical estimates as current mineral
resources or mineral reserves. The Company is not treating the
historical estimates as current mineral resources or mineral reserves.

Technical Reports

The Chubb and Bouvier properties were the subject of a National
Instrument 43-101 report written in 2010 by Dr. Boily for Mineral Hill
Industries Ltd. entitled, "Technical Report and Recommendations for
Three Li-Mo Properties Associated With the Preissac-Lacorne Batholith
in the Abitibi Subprovince, Quebec, Canada: The Chubb, International
and Athona Properties."

The technical contents of this release were approved by Michel
Boily, PhD, geo, an independent Qualified Person as defined by National
Instrument 43-101.

The company also reports that it has cancelled its proposed sale
of a 50% interest in one of its Valentine Mountain mineral claims as
originally announced April 6, 2016.

ON BEHALF OF THE BOARD
Signed "Kevin C. Whelan"
Kevin C. Whelan, President
Direct line: (250) 474-6640

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Source: Great Thunder Gold Corp.
TSX Venture closing price for GTG-V
Date: 2016/07/04
Closing Price: 0.10

INTERNET:  http://www.greatthundergold.com/
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1618700015TS11618700826-06035820160706