Source	MARKET NEWS
Date	07/06/2016
Time	09:18:03 AM

Company	 Merrex Gold Inc.
Title	Diakha RC Drill 
Results Including 70 Metres Aver





    CDNX Symbol: MXI











Press Release




[200/News Release]MXIVMERREX GOLD INCJUL 06 2016  09:15 AMDiakha RC Drill 
Results Including 70 Metres Averaging 1.55g/t Aufrom the Siribaya Gold 
Project, Mali --->@NEWS RELEASE
MERREX GOLD INC ("MXI-V;MXGIF-0")
IAMGOLD CORP ("IMG-T")
- Diakha RC Drill Results Including 70 Metres Averaging 1.55g/t Au
- from the Siribaya Gold Project, Mali

Greg Isenor, President and CEO of Merrex Gold Inc., ("Merrex"
or the "Company") announces:

Highlights



-41 holes totaling 6,623 metres completed

-Over 80% of drill holes with significant mineralization

-Hole 644 - 70 metres of 1.55g/t Au





RC Drill Results

During March and April, 2016 the Merrex-IAMGOLD joint venture
completed 41 reverse circulation ("RC") drill holes totaling 6,623
metres within the northern extension of the Diakha deposit area of
Siribaya gold project in Mali. Holes were drilled in a heel-to-toe
pattern with depth ranging from 80 to 204m along drill fences
approximately 100 to 150m apart with the objective of testing the gold
mineralization in the projected strike extension of the Diakha deposit.


The results of this 'first pass' reconnaissance RC drill program
returned significant gold mineralization in 34 of 41 holes and extended
the mineralized strike length of the Diakha deposit area by
approximately 600m from 800 metres to approximately 1.4 km.

These initial drill results in the northern extension area are
comparable with the initial drill results from the 2014 'first pass'
drill program in the southern Diakha deposit area. In both cases over
80% of the RC holes drilled returned significant gold mineralization.
(see historical news release July 2, 2014)

See Map 1 below for locations of drill holes in the northern
Diakha extension area reported here.

See Map 2 for a compilation of selected assay results from the
2014 and 2015 drilling programs in the Diakha southern deposit area.

See Table of Significant Assays below for a complete listing of
significant assay results. The Table of Significant Assays was provided
by the project operator.

Additional Program Updates

Diamond drilling is continuing with two rigs active within the
southern Diakha resource area. Air core drilling is continuing on
termite mound geochemical targets within a second structural trend to
the northeast of the Diakha resource area.

Assays are pending and will be released when available.

Commentary

"We are pleased to report that the drilling program on the newly
granted northern extension to the Diakha permit area has returned
positive results and confirmed the extension of gold mineralization
northward for approximately 600m along strike of the Diakha Deposit"
said Merrex president Greg Isenor. "Of particular note hole SRC16-644
located near the centre of the extension area returned 70 metres with
an average grade 1.55g/t Au. Additional drilling, both RC and core,
will be required to better understand this extension to the Diakha
deposit."

Map 1  RC drill hole locations - Diakha northern extension

(img src='https://www.thenewswire.com/client_files/tnwTTRqGs_.png'
/) @ https://www.thenewswire.com/client_files/tnwTTRqGs.png
Click Image To View Full Size

Note: The red dotted line in the south (bottom) of the map
represents the old boundary of the Kambaya permit. Both the southern
Diakha deposit area (see Map 2) and the newly granted Diakha extension
area are now encompassed in a new single amended Kambaya permit.

Map 2  Compilation of 2014 and 2015 drilling - Diakha southern
deposit area

(img src='https://www.thenewswire.com/client_files/tnwYvW7kg_.png'
/) @ https://www.thenewswire.com/client_files/tnwYvW7kg.png
Click Image To View Full Size

Note: The grey line labelled 'Permit Boundary' is the old permit
boundary. The new permit boundary is approximately 1km north.

Table of Significant Assays

http://www.thenewswire.ca/archives?tnwcatalyst2=release_id%3D19477




Technical Information and Quality Control Notes

The drilling results contained in this release have been prepared
in accordance with National Instrument 43-101 Standards of Disclosure
for Mineral Projects. The sampling of, and assay data from, rock chips
is monitored through the implementation of a quality assurance -
quality control program designed to follow industry best practice.

Rock chips from Reverse Circulation (RC) drilling are collected at
the rig site, at one meter intervals, under the direct supervision of
IAMGOLD geologists. Samples are immediately weighted and later split to
retain two samples of 3kg each. An air compressor is used to blow clean
the splitter (riffles) between each sample. One sample is retained at
the project site for reference purposes and the other is used to
prepare 2-meter composite samples. Composite samples are prepared at
the project site, by trained technician supervised by IAMGOLD
geologists; two (2) consecutives samples of 3 kg are further split and
mixed to get two (2) composite samples for each 2 meter interval. One
is retained for reference purposes and the other is sent to the assay
laboratory for analysis.

Samples were analyzed at the SGS Minerals Analytical Laboratory in
Bamako, Mali, using a standard fire assay with a 50-gram charge and an
Atomic Absorption finish.

Gold Intercept Interval - Computation of Composite Interval

Grade composite intervals were computed as follow: the minimum
reported interval grade is 0.5g/t, with a cut-off of 0.3 g/t and a
maximum interval dilution of 4m. No external dilution is included.
Intervals with no samples were set to grade zero but were included in
the composite if it occurred within the 4m internal dilution.

About Merrex's Siribaya Gold Project

The Siribaya Gold Project is a 50/50 joint Merrex-IAMGOLD
advanced-stage gold exploration project in West Mali which consists of
11 contiguous exploration permits which cover a total area of 876.5
square kilometres and is located in the Kedougou-Kenieba inlier of the
West African Craton region of western Mali along the borders with
Senegal and Guinea.

The Diakha, Siribaya 1B, and Taya Ko deposits are hosted within
highly prospective, Birimian-aged metasedimentary, volcanic and
intrusive rocks proximal to the Senegal-Mali Shear Zone. At Diakha,
gold mineralization occurs within an albitized sandstone similar to
IAMGOLD's Boto gold deposit located approximately 10 kilometres to the
north along strike. Zone 1B and Taya Ko occur within the
north-northeast trending Siribaya structural trend, which extends over
10 kilometres along strike, and gold mineralization occurs within
breccia-hosted stockworks or fault related silicified zones.

During 2014 and 2015 exploration was focussed primarily on the 1.2
km Diakha deposit area which is located along the Fekola-Boto trend in
the western-most portion of land package approximately 10 kilometres
south along strike of IAMGOLD's Boto gold deposit (scoping and
pre-feasibility studies in progress) and approximately 20 kilometres
south along strike from B2Gold's Fekola deposit (mine construction
commenced).

The 2015 drilling program enabled geological 3D-modeling and
completion of an initial NI 43-101 compliant resource estimate. The
initial resource (table below) was released February 9, 2016.

//st
-------------------------------------------------------
|                                                     |
|                                                     |
|                                                     |
|                                                     |
|                                                     |
|                                                     |
|                                                     |
|                                                     |
|                                                     |
|                                                     |
| siribaya                                            |
|Project                                              |
|-                                                    |
|Mineral                                              |
|Resource                                             |
|Estimate*                                            |
|                                                     |
|-----------------------------------------------------|
| |Classification|Zone   |Tonnage|Gold    |Contained  |
| |              |       |(000s) |Grade   |Ounces     |
| |              |       |       |(g/t Au)|(Au) (000s)|
|-----------------------------------------------------|
| |Indicated     |Zone 1B|2,102  |1.90    |129        |
|-----------------------------------------------------|
| |Total         |       |2,102  |1.90    |129        |
| |Indicated     |       |       |        |           |
|-----------------------------------------------------|
| |Inferred      |Zone 1B|4,094  |1.52    |200        |
|-----------------------------------------------------|
| |Inferred      |Taya Ko|882    |1.02    |29         |
|-----------------------------------------------------|
| |Inferred      |Diakha |14,840 |1.81    |863        |
|-----------------------------------------------------|
| |Total Inferred|       |19,816 |1.71    |1,092      |
-------------------------------------------------------
//et

Notes:

(ol style='list-style-type:none')

1.CIM definitions were followed for classification of Mineral
Resources.

2.Cut-off grades range from 0.45 to 0.60 g/t Au and vary by
weathering material type.

3.Mineral Resources are estimated using a gold price of US$1,500
per ounce.

4.Bulk density varies from 1.55 g/cm3 to 2.63 g/cm3 based on
deposit and weathering code.

5.The resources are constrained by a Whittle optimized pit shell.

6.Numbers may not add due to rounding.

7.Assays are capped prior to compositing. Capping levels reduced
the resource estimate gold grade




of Diakha by approximately 12%, and of Zone 1B and Taya Ko by
approximately 4%.

*The resource estimate was prepared by RPA Inc. and is as at
December 31, 2015. Readers are referred to Merrex news release of
February 9, 2016 and the complete NI43-101 Technical Report filed on
SEDAR January 25, 2016.

The 2016 drill program of approximately 17,500 metres includes
7000m of Diamond Drilling ("DD"), 6500m of Reverse Circulation ("RC")
drilling, 3000m of Air Core ("AC") drilling and 1000m of Auger
drilling. The 2016 drilling program is focusing on deeper DD core
drilling to test high-grade ()6 g/t Au targets) near the bottom of the
optimized pit shell of the Diakha resource area and a combination of DD
and RC drilling to extend the Diakha mineralized zone within the
interpreted northern extension of the Diakha deposit along the 800
metre strike length of newly permitted area. (See also news release May
4, 2016.)

Financial Advisory

Further to the Company's news release of June 21, 2016 the parties
have modified the financial advisory compensation payable to Haywood
Securities Ltd. No share purchase warrants will be issued.

Qualified Person

Greg Isenor, P.Geo., President of Merrex Gold and a Qualified
Person as defined by NI 43-101, has reviewed and approved the contents
of this release.

The mineral resource estimate referred to above, including
verification of the data disclosed, is at December 31, 2015, was
prepared by RPA Inc. and reported in accordance with National
Instrument 43-101 (NI43-101) requirements and CIM Estimation Best
Practice Guidelines. The supporting NI 43-101 Technical Report is
available on SEDAR at www.sedar.com and on the Company's website at
www.merrexgold.com.

Merrex is primarily a West African focused gold exploration
company with experienced management, a solid exploration team, a
prominent gold-producer as a JV partner and an expanding gold resource.


For further details about the Company's exploration activities
visit Merrex's website at www.merrexgold.com. To be added to Merrex's
email contact list please email your request to info@merrexgold.com.

On Behalf of the Board

Gregory Isenor

Gregory Isenor, P.Geo.
President & CEO



MERREXGOLD
Suite 802, 1550 Bedford Highway,

Bedford, NS B4A 1E6

Tel.: (902) 832-5555  Fax: (902) 832-2223

Forward Looking Statement

This news release contains forward-looking statements. All
statements, other than of historical fact, that address activities,
events or developments that the Company believes, expects or
anticipates will or may occur in the future (including, without
limitation, statements regarding expected, estimated or planned gold
and niobium production, cash costs, margin expansion, capital
expenditures and exploration expenditures and statements regarding the
estimation of mineral resources, exploration results, potential
mineralization, potential mineral resources and mineral reserves) are
forward-looking statements. Forward-looking statements are generally
identifiable by use of the words "may", "will", "should", "continue",
"expect", "anticipate", "outlook", "guidance", "estimate", "believe",
"intend", "plan" or "project" or the negative of these words or other
variations on these words or comparable terminology. Forward-looking
statements are subject to a number of risks and uncertainties, many of
which are beyond the Company's ability to control or predict, that may
cause the actual results of the Company to differ materially from those
discussed in the forward-looking statements. Factors that could cause
actual results or events to differ materially from current expectations
include, among other things, without limitation: changes in the global
prices for gold, niobium, copper, silver or certain other commodities
(such as diesel, aluminum and electricity); changes in U.S. dollar and
other currency exchange rates, interest rates or gold lease rates;
risks arising from holding derivative instruments; the level of
liquidity and capital resources; access to capital markets, financing
and interest rates; mining tax regimes; ability to successfully
integrate acquired assets; legislative, political or economic
developments in the jurisdictions in which the Company carries on
business; operating or technical difficulties in connection with mining
or development activities; laws and regulations governing the
protection of the environment; employee relations; availability and
increasing costs associated with mining inputs and labour; the
speculative nature of exploration and development; contests over title
to properties, particularly title to undeveloped properties; and the
risks involved in the exploration, development and mining business.Risks and 
unknowns inherent in all projects include the inaccuracy of
estimated reserves and resources, metallurgical recoveries, capital and
operating costs of such projects, and the future prices for the
relevant minerals. Development projects have no operating history upon
which to base estimates of future cash flows. The capital expenditures
and time required to develop new mines or other projects are
considerable, and changes in costs or construction schedules can affect
project economics. Actual costs and economic returns may differ
materially from estimates and the Company could fail to obtain the
governmental approvals necessary for the operation of a project; in
either case, the project may not proceed, either on its original timing
or at all.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.






__________________________________________________
_______________________________________________
TSX Venture closing price for MXI-V
Date: 2016/07/05
Closing Price: 0.24
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1618700042TS11618701512-09153920160706