Source	Marketwire
Date	07/11/2016
Time	02:30:49 AM

Company	 AQM COPPER INC.
Title	AQM Copper Files Technical Report for Preliminary Feasibility Study of the 
Zafranal Copper Project in Peru





    CDNX Symbol: AQM











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: AQM Copper Inc.

TSX VENTURE, BVL SYMBOL: AQM

July 11, 2016

AQM Copper Files Technical Report for Preliminary Feasibility Study of the 
Zafranal Copper Project in Peru


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 11, 2016) - AQM Copper Inc. 
(TSX VENTURE:AQM)(BVL:AQM) ("AQM Copper" or the "Company") is pleased to 
announce that it has filed a NI 43-101 compliant technical report on SEDAR on 
July 8, 2016 in connection with the Preliminary Feasibility Study ("PFS") of 
the Company's Zafranal Project ("Project") previously announced on May 24, 2016.

The Zafranal Copper Project is owned by Compania Minera Zafranal S.A.C. 
("CMZ"), a joint venture company that is beneficially owned by AQM, Teck 
Resources Limited, and Mitsubishi Materials Corporation. AQM, through Minera 
AQM Copper Peru S.A.C. ("MAQM"), has been the operator of the Project since 
2009.

The Zafranal PFS was independently prepared by Ausenco Peru S.A.C., 
("Ausenco"), Amec Foster Wheeler PLC ("AmecFW") and NCL Ingenieria y 
Construccion SpA ("NCL"), with the support from other specialist consultants. 
The PFS report reflects the design of an open pit mine, conventional flotation 
concentrator processing facility and associated infrastructure.

PFS Highlights:

/T/

--  The reported mineral reserve totals 401 million tonnes ("Mt") grading
0.40 % total copper ("Cu") and 0.07 g/t gold ("Au"), and the mine-
concentrator as designed is expected to produce 3.1 billion pounds of
copper and 484,000 ounces of gold over the 19-year life of the
operation.
--  Initial capital cost is US$ 1.16 billion and the base case after-tax
valuation yields an expected net cash flow of US$ 1.6 billion with a net
present value ("NPV") of US$ 496 million at an 8 % discount rate.
--  After-tax internal rate of return ("IRR") is 15.9 % and the Project has
a 5.1-year payback period from the start of operations.
--  Production averages 120,000 tonnes per annum ("tpa") of copper in
concentrate over the first 5-year period and 75,000 tpa over the life of
the operations.
--  A total of 4.4 million dry metric tons ("dmt") of concentrate will be
produced over a 19-year period with an average grade of 32.5 % copper
and 3.4 grams per tonne gold.
--  No deleterious elements in any significant concentration were found in
the copper concentrate produced from the flotation testwork, and all the
impurity elements were found to be below smelter penalty limits.
--  A brackish-water aquifer located within 35 kilometres ("km") of the
proposed process plant site has the potential to satisfy the project's
process water requirements. Testwork has indicated this water is
suitable for concentrator processing,
--  Thickened tailings disposal will be in a natural basin approximately 1
km downhill from the plant site.

/T/

On Behalf of the Board

AQM COPPER INC.

Bruce L. Turner, President and Chief Executive Officer

About AQM Copper

AQM Copper Inc. is a Canadian mineral exploration company exploring and 
developing copper deposits in South America. Through its Peruvian subsidiary, 
Minera AQM Copper Peru S.A.C. (MAQM), the Company is developing the Zafranal 
Copper-Gold Porphyry Project located in Southern Peru. MAQM is the operator of 
a 50/50 Joint Venture with Teck Resources Limited through a sole purpose 
Peruvian company, Compania Minera Zafranal. MAQM is owned 60 % by AQM Copper 
Inc. and 40 % by Mitsubishi Materials Corporation.

The Company's management and directors have extensive experience working for 
the world's largest mining copper producers and investment banking backgrounds. 
Please refer to the Company's website at www.aqmcopper.com, for further 
information regarding the Company and the Zafranal Project.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE

CAUTIONARY STATEMENT REGARDING FORWARD-LOOKING INFORMATION

Except for statements of historical fact relating to AQM Copper Inc., certain 
information contained herein constitutes "forward-looking statements". 
Forward-looking statements include statements that are predictive in nature, 
depend upon or refer to future events or conditions, or include words such as 
"expects", "anticipates", "plans", "believes", "considers", "intends", 
"targets", or negative versions thereof and other similar expressions, or 
future or conditional verbs such as "may", "will", "should", "would" and 
"could". We provide forward-looking statements for the purpose of conveying 
information about our current expectations and plans relating to the future and 
readers are cautioned that such statements may not be appropriate for other 
purposes. By its nature, this information is subject to inherent risks and 
uncertainties that may be general or specific and which give rise to the 
possibility that expectations, forecasts, predictions, projections or 
conclusions will not prove to be accurate, that assumptions may not be correct 
and that objectives, strategic goals and priorities will not be achieved. These 
risks and uncertainties include but are not limited to those identified and 
reported in AQM Copper Inc's public filings, which may be accessed at 
www.sedar.com. Other than as specifically required by law, we undertake no 
obligation to update any forward-looking statement to reflect events or 
circumstances after the date on which such statement is made, or to reflect the 
occurrence of unanticipated events, whether as a result of new information, 
future events, results or otherwise.

- 30 -

CONTACT INFO:

Investor Relations
Pinnacle Capital Markets LTD.
Spyros P. Karellas
(416) 433-5696
(416) 800-8921
spyros@pinnaclecapitalmarkets.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=571927030