Source	Marketwire
Date	07/11/2016
Time	07:12:45 AM

Company	 MONUMENT MINING LIMITED
Title	Monument Announces Significant Intercepts Assay Results at NOA7 8 in 
Burnakura





    CDNX Symbol: MMY











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Monument Mining Limited

TSX VENTURE SYMBOL: MMY
FRANKFURT SYMBOL: D7Q1

July 11, 2016

Monument Announces Significant Intercepts Assay Results at NOA7_8 in Burnakura


VANCOUVER, BRITISH COLUMBIA--(Marketwired - July 11, 2016) - Monument Mining 
Limited (TSX VENTURE:MMY)(FRANKFURT:D7Q1) "Monument" or the "Company" is 
pleased to announce that significant intercepts assay results have been 
received for the North of Alliance ("NOA") 7_8 deposit at the Burnakura Gold 
Project driven by Monument's fiscal 2016 exploration programs ("FY2016 
Exploration Program"). The FY2016 Exploration Program includes infill and 
extensional drilling to update a resource statement that may potentially 
increase the life of mine for Burnakura Gold Project.

Highlight of the best intercepts and exploration progress at NOA7_8

/T/

----------------------------------------------------------------------------
HOLE ID              From (m)     To (m)     Au g/t   Interval Length /Grade
----------------------------------------------------------------------------
16MRC014                  118        124       8.35         6.00m @ 8.35 g/t
16MRC023                   82         94       7.16        12.00m @ 7.16 g/t
16MRC024                  112        120       5.54         8.00m @ 5.54 g/t
16MRC027                  104        110       5.32         6.00m @ 5.32 g/t
16MRC043                    9         13       6.97         4.00m @ 6.97 g/t
----------------------------------------------------------------------------

/T/

The 2016 drilling at NOA was designed to extend the life of mine at the 
existing optimized pits at Alliance and New Alliance ("ANA") and Federal City 
deposits, and de-risk the early stage of gold production under heap leach and 
CIL processes at the Burnakura Gold Project. It included confirmation drilling 
to NOA North, encompassing NOA 7_8, NOA 6 and NOA 4, and to NOA South deposits 
NOA1 and NOA2 (Figure 1). The FY2016 Exploration Program also aimed to verify 
the continuity of mineralization under open pits down dip to connect infill 
data points for potential super pits or underground mining in the second stage 
of production that was carried out previously by the previous owner.

The FY2016 Exploration Program at NOA7_8 deposit was completed by June 2016 and 
comprised of 64 exploration holes for 8,532 meters RC drilling, plus one 
metallurgical hole for 129.4 meters DD drilling (Figure 2). As a result 6,746 
assay results have been received to date (including QAQC samples), confirming 
the good continuity of the known mineralization envelopes and their extensions 
down-dip. A follow up economic study is ongoing to optimize the early stage 
mine plan. In the meantime, the Company is planning a deep drilling program to 
extend resources and investigate underground production potential to confirm 
the economics for longer term production.

To view Figure 1 - Drill hole Location Plan for FY2016 Exploration Program in 
NOA deposits, please visit the following link: 
http://media3.marketwire.com/docs/NOA_deposits.jpg.

Preliminary Interpretation Results and Deep Drilling Follow-up

Table 1 "Significant Drill Intercepts greater than 1.0g/t - DD holes" is 
included in this news release, showing a breakdown of fire assay best intercept 
results completed by SGS Lab for intervals of mineralization greater than 1.0 
g/t Au along with collar information for the RC drill holes (Table 2). The 
infill and extensional drilling was angled at around 60 degrees towards the 
west, and has confirmed and allowed the Company to refine the understanding on 
the existing oxide and sulphide mineralized zones. Most of the significant 
intercepts come from infill drilling located in regions modeled previously as 
lower grade mineralization. This indicates that an upcoming resource model 
update should increase significantly the total Resource, while increasing the 
confidence in the geometry and grade continuity.

Table 2 in this news release shows the collar coordinates of highlighted 
exploration RC drilling in corresponding intercepts listed in the Table 1.

FY2016 drill holes, including the mineralized assay results greater than 1.0g/t 
Au at NOA7_8 highlighted at Figure 2 below, together with historical holes 
prior to FY2016, are being used as input data for the ongoing Resource 
estimation. The drill hole orientation for exploration drilling was designed to 
target perpendicular to mineralization for true thickness. The drill hole 
intercepts reported in this statement represent composited sample intervals 
obtained from drilling.

To view Figure 2 - Drill hole Collar Location Plan for NOA7_8 in FY2016, 
highlighting holes with composited assays greater than 1.0g/t, please visit the 
following link: http://media3.marketwire.com/docs/FY2016.jpg.

The available hard data information composed of historical drilling 
(1991-2013), BMGS Resource block model 2012, Rock Team Underground Mining Study 
2012 and Monument drilling within FY2016 (highlighting significant assay 
results) were compiled and visualized in an integrated way, aiming to verify 
more closely the potential for underground mining mineralization at NOA7_8. The 
recent Monument drilling, even being predominantly shallower, provides 
important information evidencing the trends for gold spatial continuity.

Figure 3 presents a cross-section showing some of the significant intercepts 
listed in Table 1, together with the grade shell interpretation for the ongoing 
modelling. It could be observed that the recent Monument infill drilling has 
filled some information gaps, indicating in some cases a mineralization 
approximately matching the previously interpreted ore geometry however with 
much higher grade. In this and other sections it is clear that the 
mineralization is still open at depth. The mineralization is locally much 
thicker and consistently higher grade than modelled previously with the 
information then available.

Fault offsets may have displaced the mineralization, and or new pods may have 
been identified and should be investigated further. This is being better 
studied in the ongoing modelling. It is also clearly confirmed that the deposit 
mineralization is structurally controlled and there is a plunging of the high 
grades to north. The BMGS 2012 previous model is shown in 3D in Figure 4, 
indicating these gold high grade trends.

To view Figure 3 - Cross-section 7011330mN (+/- 10m), showing significant 
intercepts for Monument (in green label) and historical holes, in relation to 
the current interpretation and pits (section trace shown in plan view), please 
visit the following link: http://media3.marketwire.com/docs/NOA-7_8.jpg.

To view Figure 4 - Oblique view for block model and drilling in relation to 
actual (brown) and optimised (blue) pits, please visit the following link: 
http://media3.marketwire.com/docs/oblique.jpg.

The study of the available information and ongoing resource modeling update 
based on the new drilling information has evidenced positive indications for 
the increase of mineralized volume and gold grade/ounces for a good part of NOA 
7_8, in particular coming from the significant intercepts observed. It has also 
enhanced the strong potential for the continuity of deep mineralization in the 
central and north portions of NOA 7_8 deposit.

The completion of the resource modelling will provide the mining department 
with an indication of possible CIL addition to the earlier phases of the LOM, 
while providing more updated model indication of the underground potential for 
designing a further deep drilling program. This will bring a more accurate 
picture of the potential for both expansion of the optimized pit for CIL high 
grade purpose, and opportunities for deep drilling and underground development 
in the near future.

Roger Stangler, Chief Managing Geologist of the Company, MEng, MAusIMM, MAIG, 
has prepared, reviewed, supervised the preparation and approved the scientific 
and technical disclosure in the news release as a Qualified Person under 
NI43-101 standards.

About Monument

Monument Mining Limited (TSX VENTURE:MMY)(FRANKFURT:D7Q1) is an established 
Canadian gold producer that owns and operates the Selinsing Gold Mine in 
Malaysia. Its experienced management team is committed to growth and is 
advancing several exploration and development projects including the Mengapur 
Polymetallic Project, in Pahang State of Malaysia, and the Murchison Gold 
Projects comprising Burnakura, Gabanintha and Tuckanarra in the Murchison area 
of Western Australia. The Company employs approximately 240 people in both 
regions and is committed to the highest standards of environmental management, 
social responsibility, and health and safety for its employees and neighboring 
communities.

/T/

Robert F. Baldock, President and CEO
Monument Mining Limited
Suite 1580 - 1100 Melville Street
Vancouver, BC V6E 4A6

/T/

FOR FURTHER INFORMATION visit the company web site at www.monumentmining.com.

"Neither TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release."

Forward-Looking Statement

This news release includes statements containing forward-looking information 
about Monument, its business and future plans ("forward-looking statements"). 
Forward-looking statements are statements that involve expectations, plans, 
objectives or future events that are not historical facts and include the 
Company's plans with respect to its mineral projects and the timing and results 
of proposed programs and events referred to in this news release. Generally, 
forward-looking information can be identified by the use of forward-looking 
terminology such as "plans", "expects" or "does not expect", "is expected", 
"budget", "scheduled", "estimates", "forecasts", "intends", "anticipates" or 
"does not anticipate", or "believes", or variations of such words and phrases 
or state that certain actions, events or results "may", "could", "would", 
"might" or "will be taken", "occur" or "be achieved". The forward-looking 
statements in this news release are subject to various risks, uncertainties and 
other factors that could cause actual results or achievements to differ 
materially from those expressed or implied by the forward-looking statements. 
These risks and certain other factors include, without limitation: risks 
related to general business, economic, competitive, geopolitical and social 
uncertainties; uncertainties regarding the results of current exploration 
activities; uncertainties in the progress and timing of development activities; 
foreign operations risks; other risks inherent in the mining industry and other 
risks described in the management discussion and analysis of the Company and 
the technical reports on the Company's projects, all of which are available 
under the profile of the Company on SEDAR at www.sedar.com.
Material factors and assumptions used to develop forward-looking statements in 
this news release include: expectations regarding the estimated cash cost per 
ounce of gold production and the estimated cash flows which may be generated 
from the operations, general economic factors and other factors that may be 
beyond the control of Monument; assumptions and expectations regarding the 
results of exploration on the Company's projects; assumptions regarding the 
future price of gold of other minerals; the timing and amount of estimated 
future production; the expected timing and results of development and 
exploration activities; costs of future activities; capital and operating 
expenditures; success of exploration activities; mining or processing issues; 
exchange rates; and all of the factors and assumptions described in the 
management discussion and analysis of the Company and the technical reports on 
the Company's projects, all of which are available under the profile of the 
Company on SEDAR at www.sedar.com. Although the Company has attempted to 
identify important factors that could cause actual results to differ materially 
from those contained in forward-looking statements, there may be other factors 
that cause results not to be as anticipated, estimated or intended. There can 
be no assurance that such statements will prove to be accurate, as actual 
results and future events could differ materially from those anticipated in 
such statements. Accordingly, readers should not place undue reliance on 
forward-looking statements. The Company does not undertake to update any 
forward-looking statements, except in accordance with applicable securities 
laws.

To view Table 1: Significant Drill Intercepts greater than 1.0g/t - RC holes 
for 2015-2016 drilling programs in NOA 7_8, please visit the following link: 
http://media3.marketwire.com/docs/MONUMENT_Table1.pdf.

MONUMENT MINING LIMITED

Table 2: Significant Drill Intercepts: Collar coordinates in MGA94, Zone 50 grid

/T/

----------------------------------------------------------------------------
Hole
No.  Project   Hole ID Type             RTK DGPS                Dip Azimuth
---------------------------------
East       North       RL
----------------------------------------------------------------------------
1      NOA7_8  15MRC151   RC   645658.16  7011393.15   457.52  -59.2   271.3
----------------------------------------------------------------------------
2      NOA7_8  15MRC157   RC   645528.18  7011567.59   456.61  -59.7   273.3
----------------------------------------------------------------------------
3      NOA7_8  15MRC170   RC   645574.12  7011072.35   458.43  -60.5   271.3
----------------------------------------------------------------------------
4      NOA7_8  16MRC005   RC   645588.49  7011083.66   458.59    -56   269.4
----------------------------------------------------------------------------
5      NOA7_8  16MRC008   RC   645566.39  7011148.85   458.09  -59.1   270.8
----------------------------------------------------------------------------
6      NOA7_8  16MRC009   RC   645590.55  7011148.36   458.24  -59.5   268.2
----------------------------------------------------------------------------
7      NOA7_8  16MRC014   RC   645590.94  7011222.75   457.92  -59.9   271.9
----------------------------------------------------------------------------
8      NOA7_8  16MRC016   RC    645573.9  7011241.73   457.83  -56.1   270.2
----------------------------------------------------------------------------
9      NOA7_8  16MRC018   RC   645531.46  7011283.01   457.55  -60.4     271
----------------------------------------------------------------------------
10     NOA7_8  16MRC019   RC   645567.79  7011284.16   457.71  -60.3   270.9
----------------------------------------------------------------------------11  
   NOA7_8  16MRC023   RC   645577.05  7011324.95   457.61  -59.5   269.8
----------------------------------------------------------------------------
12     NOA7_8  16MRC024   RC   645621.77  7011323.96   457.68  -60.5   269.8
----------------------------------------------------------------------------
13     NOA7_8  16MRC027   RC   645550.82   7011364.9   457.43    -59   270.1
----------------------------------------------------------------------------
14     NOA7_8  16MRC028   RC   645588.99  7011362.73   457.53  -59.8   269.9
----------------------------------------------------------------------------
15     NOA7_8  16MRC031   RC   645592.64  7011405.08   457.29  -58.9     269
----------------------------------------------------------------------------
16     NOA7_8  16MRC034   RC    645597.8  7011444.74   457.24  -60.2   269.2
----------------------------------------------------------------------------
17     NOA7_8  16MRC036   RC   645603.95  7011464.72   457.22  -59.2   270.1
----------------------------------------------------------------------------
18     NOA7_8  16MRC037   RC   645576.07  7011484.87   457.15  -59.3   269.5
----------------------------------------------------------------------------
19     NOA7_8  16MRC040   RC   645568.87  7011510.03   456.92    -53     270
----------------------------------------------------------------------------
20     NOA7_8  16MRC043   RC   645513.11     7011555   452.84  -55.6   269.6
----------------------------------------------------------------------------
21     NOA7_8  16MRC047   RC    645552.9  7011390.67   457.35  -58.6   269.7
----------------------------------------------------------------------------

/T/

- 30 -

CONTACT INFO:

Richard Cushing
MMY Vancouver
+1-604-638-1661 x102
rcushing@monumentmining.com

or

Wolfgang Seybold
Axino GmbH
+49 711-82-09-7211
wolfgang.seybold@axino.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=571875736