Source	MARKET NEWS
Date	07/12/2016
Time	06:28:08 AM

Company	 Silver Range Resources Ltd.
Title	Commences Work at Up Town Gold Near Yellowknife





    CDNX Symbol: SNG











Press Release





Commences Work at Up Town Gold Near Yellowknife --->@NEWS RELEASE
SILVER RANGE RESOURCES LTD ("SNG-V")
- Commences Work at Up Town Gold Near Yellowknife

Silver Range Resources Ltd. ("Silver Range") has begun an
exploration program at the Up Town Gold Project near Yellowknife, NWT.

The Up Town Gold Project consists of 6 claims (3,267 hectares)
approximately 5 km from downtown Yellowknife.  The property covers
eight gold prospects in granitoid rocks, adjacent to the Giant Mine
which produced 7.1 million ounces of gold at an average grade of 15.5
g/t Au from 1948 to 1999.  Mineralization at Up Town Gold was
discovered and briefly explored during the early 1960's.   Three
showings were drilled to shallow depths ((60 m) but no deeper drilling
was completed despite favourable results.  At two of these showings
(Rod and 22 Vein), small high grade resources greater than 1 ounce per
ton gold were partially mined.  The property was restaked in 2011 and
explored with a few shallow drill holes in 2013 and 2015.  Best recent
drill results were 2.22 m @ 27.47 g/t Au (from 15.6 m) at the Rod
Showing and 4.14 m @ 2.62 g/t Au (from 12.8 m) at the Fox South
Showing.   Exposed mineralization in workings at the Rod Showing
returned promising results including a channel sample of 1.20 m @ 17.27
g/t Au and a selected grab sample of vein material that ran 415 g/t Au.


While the Yellowknife Greenstone Belt has been systematically and
intensely explored for lode gold mineralization, the adjacent granitic
rocks have not received similar attention.   In large part this may be
due to the prevailing view that Archean lode gold mineralization is
confined to metavolcanic and metasedimentary rocks within greenstone
belts.  In the past three decades however, large gold resources have
been discovered and mined in granitoid rocks adjacent to greenstone
belts rocks worldwide. Prominent examples include Woodcutters
Goldfields in Australia and Buzwagi in Tanzania.  In Canada,
granitoid-hosted gold has been mined at Renabie and at several mines in
the Bourlamarque Batholith in Quebec.  In recent years, gold resources
in granitoid rocks have been defined at Hammond Reef and Cote Lake.

Given the large gold endowment of the Yellowknife Greenstone Belt,
Silver Range management considers the adjacent granitic rocks
prospective to host significant gold resources.  The Up Town Gold
showings collectively define several mineralized structural corridors
west of and parallel to the Giant Shear Zone which hosts the Giant
Deposit.   The Giant Shear Zone and the structures on the Up Town Gold
property straddle the surface projection of a regional scale
west-dipping seismic reflector identified in a 1996 Lithoprobe seismic
reflection survey.  This feature has been interpreted to be a deep
crustal fault.  Large gold deposits are localized near such features in
the Yilgarn and Superior Cratons.

Silver Range will conduct geological mapping, prospecting and
geophysical surveys at the Up Town Gold Project during the 2016 field
season.  Geological mapping will be focused on delineating alteration
envelopes and structure within the underlying granodiorite.
Prospecting will be focused on two vein systems which have not been
systematically sampled and on locating new mineralization along the
inferred structural corridors.  Orientation ground geophysical surveys
over two showings and an airborne total magnetic field and radiometric
survey over the entire property are also planned.  Finally, Silver
Range recently acquired proprietary drill data from programs completed
from 1962 to 1964.  This data will be integrated with the surface
sampling and geological data, and used to construct geological models
of the shallow mineralization.

The technical information in this press release has been reviewed
and approved by Mike Power, P.Geo. CPG, CEO of Silver Range Resource
Ltd. and a Qualified Person as defined by Canadian Securities
Administrators National Instrument 43-101.

ON BEHALF OF SILVER RANGE RESOURCES LTD.
"Mike Power"
Chief Executive Officer

For further information concerning Silver Range or its exploration projects
please contact:

Corporate Information
Silver Range Resources Ltd.
Mike Power
President and C.E.O.
Tel: (604) 687-2522

Investor Inquiries
Richard Drechsler
Vice-President, Communications
Tel: (604) 687-2522
NA Toll-Free: (888) 688-2522
rdrechsler@silverrangeresources.com
http://www.silverrangeresources.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of exploration and
other risk factors beyond its control, and actual results may differ
materially from the expected results.

Source: Silver Range Resources Ltd. (TSX Venture:SNG)
http://www.silverrangeresources.com/s/Home.asp
______________________________________
_______________________________________________
TSX Venture closing price for SNG-V
Date: 2016/07/11
Closing Price: 0.21
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1619300019TS11619301024-06264320160712