Source	MARKET NEWS
Date	07/20/2016
Time	08:01:01 AM

Company	 Castle Peak Mining Ltd.
Title	Starts 
Detailed Sampling of Gold Anomalies in Pr





    CDNX Symbol: CAP











Press Release





CASTLE PEAK MINING LTD ("CAP-V")
- Starts Detailed Sampling of Gold Anomalies in Preparation of
- Drilling

Castle Peak Mining Ltd. ("Castle Peak" or the "Company"), is
pleased to announce that in preparation of drilling, a field crew is
being mobilized to our priority prospects at the Akorade Project
located in the southern Ashanti Belt, Ghana to:

1. Complete a more detailed auger sampling survey of the Akoko
Trend prospect to expand and define the two parallel anomalies of
1,000m by an aggregate width of 200m;

2. Complete initial detailed sampling at the Dansuom prospect of a
coincident moderate chargeability (+10ms) and moderate resistivity
(+2550ohm.m) anomaly with dimensions of 600m (open) by 200m immediately
adjacent to 2011 best intercepts of 7m of 1.2 grams per tonne ("g/t")
gold ("Au") and 11m of 2.9 g/t Au (see news release November 15, 2011)
that are characterized by a similar geophysical anomaly;

3. Complete a more detailed auger sampling survey on the
conceptual geological target POW-A1/3 that initial wide spaced auger
sampling partially defined as a 1,000m by 75m anomaly with a core
section of 300m that returned auger soil values ranging from 0.1 g/t to
0.3 g/t Au; and

4. Prospect and sample select additional areas that are considered
to have high potential based on previous field evaluations (DO_New, K4,
POW-B).

These prospects were first identified using 400m x 400m soil
sampling compiled with inferred geology and geophysical information.
Prospecting follow-up included 4m deep auger soil samples on 200m line
spacing and 50m sample spacing. The resulting geochemical anomalies
that define these prospects are trends of coherent samples returning
greater than (")") 50 parts per billion ("ppb") gold which may contain
values ranging from less than 10ppb gold to )1,000ppb gold. The
proposed work program is unique to each target and will sample on 100m
to 200m line spacing and 25m or 50m sample spacing. Each of these
prospects combines geophysical characteristics, geochemical anomalies
and geological settings favourable for the occurrence of gold deposits.
These high potential prospects are within 30km on main roads from the
Nzema, the Iduapriem and the Tarkwa mines.

Maps, descriptions and additional information about of these
prospects and our other prospects and anomalies will be made available
on our website (www.castlepeakmining.com).



Castle Peak continues to evaluate and prioritize targets
immediately adjacent to it's current high grade Apankrah Deposit, a
discovery by Castle Peak consisting of an inferred resource of 76,000
ounces at a grade of 8 g/t gold. Partners are currently being sought in
order to expand and advance this deposit.

Technical Disclosure

Castle Peak's technical disclosure in this news release has been
reviewed and approved by Darren Lindsay, P.Geo., Castle Peak's
President and CEO, who serves as a Qualified Person under the
definition in National Instrument 43-101 ('NI 43-101'). The exploration
activities reported in the release are to be supervised by Henry Sowah,
Castle Peak's Exploration Manager. Auger soil sampling reported herein
was collected as approximately 2kg samples at roughly 4m depth at sites
located using handheld GPS. Soil sampling reported herein was collected
as approximately 2kg samples at roughly 1m depth at sites located using
handheld GPS. Castle Peak inserted control samples every tenth sample
(one of field duplicate or blank standard material). Samples were
analyzed for gold by fire assay and ICP analytical methodologies at SGS
Laboratories in Tarkwa, Ghana. The Akorade Project represents early
stage exploration properties and as such there is no guarantee mineral
resources will be discovered or defined; however, the properties do
include an inferred mineral resource, the Apankrah Deposit with an
effective date of June 1, 2013, as described in the "NI 43-101
Technical Report on The Apankrah Project, Western Region, Ghana" dated
June 1, 2013, prepared by Simon Meadows Smith (IOM3) a Qualified Person
as defined by NI 43-101. A copy of the report is filed under the
Company's profile on SEDAR at www.sedar.com and the Castle Peak
website.

About Castle Peak

Castle Peak Mining Ltd. is a Canadian-based junior exploration
company focused on advancing greenfields and early stage gold projects.
Castle Peak has discovered the high grade Apankrah deposit and believes
there is potential for additional discovery of gold resources. The
Company holds a strategic land package in the Ashanti belt adjacent to
several producing gold mines in Ghana, West Africa. The Ashanti belt is
known as one of the most prolific gold belts in the world.

On behalf of the Board of Castle Peak Mining Ltd.:
"Darren Lindsay"
President and Chief Executive Officer
For additional information please visit www.castlepeakmining.com or
contact:
Darren Lindsay, President and CEO
Tel: 604 345 1926
Email: darrenl@castlepeakmining.com

FORWARD-LOOKING STATEMENTS

Except for statements of historical fact, this news release
contains certain 'forward-looking information' and 'forward-looking
statements' within the meaning of applicable securities laws including
statements regarding the Offering and the proposed use of proceeds.
Such forward-looking statements are based on the opinions and estimates
of management at the date the statements are made, and are subject to
known and unknown risks, uncertainties and assumptions that could cause
actual results to vary materially from the anticipated results or
events predicted in these forward-looking statements, including those
risk factors identified in the Company's Annual MD&A filed under the
Company's SEDAR profile. As a result, readers are cautioned not to
place undue reliance on these forward-looking statements. The
forward-looking statements contained in this news release are made as
of the date of this release. Except as required by applicable law,
Castle Peak disclaims any intention and assumes no obligation to update
or revise any forward-looking statements, whether as a result of new
information, future events or otherwise.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

THIS NEWS RELEASE IS INTENDED FOR DISTRIBUTION IN CANADA ONLY AND
IS NOT FOR DISSEMINATION IN THE UNITED STATES OR FOR DISTRIBUTION TO
UNITED STATES NEWSWIRE SERVICES

Figure 1: Akorade Project prospects.

To view an enhanced version of Figure 1, please visit:
[http://orders.newsfilecorp.com/files/4071/21701_a1469022498867_91.jpg]


Figure 2: Akoko Trend prospect area

*Castle Peak Mining has not independently confirmed or evaluated
the resource reported by Castle Minerals; there is no guarantee similar
mineralization occurs on Castle Peak's land position.

To view an enhanced version of Figure 2, please visit:
[http://orders.newsfilecorp.com/files/4071/21701_a1469022499180_77.jpg]

Figure 3: POW-Dansuom prospect area.
To view an enhanced version of Figure 3, please visit:
[http://orders.newsfilecorp.com/files/4071/21701_a1469022499398_41.jpg]
______________________________________
_______________________________________________
TSX Venture closing price for CAP-V
Date: 2016/07/19
Closing Price: 0.05
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1620100018TS11620101190-07590420160720