Source	CANADA NEWSWIRE
Date	07/26/2016
Time	06:09:10 AM

Company	 Mirasol Resources Ltd.
Title	Mirasol Reports Encouraging Drill Results from Cerro Vanguardia Mines JV
at the Claudia Gold-Silver Project, Santa Cruz Province Argentina





    CDNX Symbol: MRZ











Press Release




" BC-Mirasol-Arg-Drill-Res   07-26 1621
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business Editors:
^Mirasol Reports Encouraging Drill Results from Cerro Vanguardia Mines JV
at the Claudia Gold-Silver Project, Santa Cruz Province Argentina@

VANCOUVER, July 26, 2016 /CNW/ - Mirasol Resources Ltd. (TSX-V: MRZ,
OTCPK: MRZLF "Mirasol") is pleased to announce encouraging intersections of
Au+Ag mineralization in shallow reverse-circulation (RC) drilling at the 100%
owned Claudia project in Santa Cruz Province Argentina. These preliminary
results are from the drilling campaign just completed by Joint Venture partner
Cerro Vanguardia S.A. (CVSA - 92.5 % owned by AngloGold Ashanti, the
controlling shareholder, and 7.5 % by Fomicruz S.E., the Santa Cruz provincial
mining company). Since commencing drilling during May 2016, CVSA has completed
39 shallow RC drill holes totaling 3,543 m across the Curahue prospect,
primarily focused on the "Io" trend (Figure 1).
Assays have been received for 18 of the 26 RC holes that provide a
shallow test of the 2 km long "Io" vein zone in the Curahue prospect. Curahue
is one of five prospect areas identified within the Claudia project (Figure
2), and is defined by a 15 km long Au+Ag bearing epithermal vein corridor
where Mirasol exploration has outlined six large, previously undrilled, vein
trends, including: Io, Europa, Sinope, Calisto, Ganymede and Themisto (see
news release July 27, 2015, Claudia Project Summary).
Gradient array geophysical surveys previously conducted by Mirasol at
Curahue have proved to be a very reliable tool for targeting veins concealed
by gravel on the "Io" trend. The current RC drilling campaign has tested some
of the high-priority "Io" trend targets to depths of between 20 and 120 m
below surface and intersected a series of sizable epithermal veins and
stockworks. Interpretation of preliminary cross-sections suggest the "Io" vein
zone attains estimated maximum true widths ranging up-to approximately 40 m.
RC assay results (Table 1) have defined both narrow zones of higher-grade
and multiple broad zones of lower-grade Au+Ag mineralization including:
Select plus 4 g/t Au down hole intervals,
<<

--  IORC38 13.0 to 13.5m - 0.5 m at 7.35 g/t Au and 448.9 g/t Ag, (14.8 g/t
AuEq60(x))

--  IORC41 80.0 to 81.0m - 1.0 m at 5.15 g/t Au and 580.6 g/t Ag, (14.8 g/t
AuEq60)

--  IORC58 50.0 to 51.0m - 1.0 m at 4.58 g/t Au and 180.5 g/t Ag, (7.6 g/t
AuEq60)
>>
Select lower grade down hole intervals, at 0.3 g/t AuEq60 cut off:
<<

--  IORC27 30.0 to 57.5m - 27.5m at 0.56 g/t Au and 48.33 g/t Ag (1.37 g/t
AuEq60)
Including 2.5 m at 1.16 g/t Au and 165.6 g/t Ag (3.92 g/t AuEq60)

--  IORC41 32.5 to 99.0m - 66.5m at 0.42 g/t Au and 64.74 g/t Ag, (1.50 g/t
AuEq60)
including 13m at 0.81 g/t Au and 105.0 g/t Ag (2.56 g/t AuEq60)

--  IORC58 43.0 to 82.5m 39.5m at 0.70 g/t Au and 74.89 g/t Ag, (1.95 g/t
AuEq60)
including 12.5 m at 1.38 g/t Au and 102.5 g/t Ag (3.08 g/t AuEq60)
>>
The majority of the assay results received to-date are from the
northwest-end of the "Io" trend where the primary vein zone is interpreted to
reach its maximum true width ranging up to approximately 40 m in the RC
drilling. In the southeast area where assays are still pending, drill logs
record narrower but still significant vein development with downhole
intersections suggesting a vein zone of up to 5 to 15 m wide. The assay
results from hole IORC-38, the most southeasterly hole with results to date,
has returned the highest-grade intersection of 0.5 m at 7.35 g/t Au and 448.9
g/t Ag, suggesting there is potential for further mineralized intersections in
this part of the vein zone. The central portion of the "Io" trend remains
largely undrilled at this time.
Preliminary cross section down-hole assay plots (Figure 3) of the "Io" RC
drill results combined with Mirasol trench channel-sample assays suggest that
the Au+Ag grades may be increasing with depth; however deeper drilling will be
required to determine if this Au+Ag grade trend continues. Drill logs show the
"Io" structure and associated Au+Ag mineralization is oxidized, an early
indicator for potentially favourable metallurgical characteristics to the
mineralization.
RC drilling has been used by CVSA to provide a rapid test of the Curahue
prospect. The majority of mineralized intervals from reported RC holes were
collected from below the water table resulting in wet samples. "Wet" RC
drilling under some circumstances can deliver lower sample recoveries and may
produce smearing of samples. Given these possible uncertainties caution in
interpreting these results is advised until confirmation is provided by the
diamond drill core results. None the less Mirasol's management is encouraged
by these assay results that provided an initial near surface test at "Io"
suggesting potential for both mill and near surface heap-leach type Au+Ag
mineralization at Curahue.
This phase of the RC drilling at Curahue was completed on June 29, with
CVSA promptly commencing follow-up diamond core drilling at the prospect.
Diamond core holes will initially target depth extensions of the
mineralization intersected in RC holes at the "Io" trend but will also test
sections of the Europa, Calisto, Sinope and the as yet un-drilled 3 km long
Themisto trend. Assay results are currently pending for a further 8 RC holes
from "Io" and 13 holes for the other trends; 6 holes from Europa, 4 holes from
Calisto and 3 holes from Sinope. These results will be reported as they are
delivered to Mirasol by CVSA.
The Claudia - CVSA Joint Venture is targeting Au+Ag mineralization that
could be mined and processed through CVSA facilities located 28 km over flat
terrain to the north of Curahue, through Claudia project and CVSA lands. The
objective is to identify higher-grade material that could be trucked to the
mill and / or lower-grade ore suitable for an on site heap-leaching, which
could be rapidly brought into production using the established mine
infrastructure.
The Cerro Vanguardia Mine produced 300,000 oz of Au during 2015 and over
1.25 Moz Au in the last five years, mining from a series of open pits, heap
leach and underground operations. The Claudia - CVSA Joint Venture (see new
release March 01, 2016) requires CVSA to drill 12,000 m, spend US$5 million on
exploration and pay US$1 million in staged cash payments over 2 years to earn
51% of the Claudia project. CVSA can earn up to 75% of the project over six
years by delivering a decision to mine with a minimum resource of 350,000 oz
Au and provide funding to production for Mirasol's 25% equity proportion of
the mine. The earn-in timeline can be accelerated at CVSA's discretion by
early delivery on the drill, exploration spend and payments schedule.
Stephen Nano, President and CEO of Mirasol, has approved the technical
content of this news release and is a Qualified Person under NI 43 -101.
Additional Explanatory Notes
(x) AuEq60 Gold Equivalent (AuEq) is calculated using following formula:
assays in g/t Gold + (Silver / 60)
Quality Assurance/Quality Control of the Claudia exploration program:
Under the terms of the Claudia-CVSA Agreement, all exploration is managed
by CVSA. All previous exploration on the projects was supervised by Mirasol
CEO Stephen C. Nano, who is the Qualified Person under NI 43-101. All
information generated from the Claudia-CVSA Joint Venture program is reviewed
by Mirasol prior to release. The technical interpretations presented here are
those of Mirasol Resources Ltd.
CVSA applies industry standard exploration methodologies and techniques.
All geochemical rock and drill samples are collected under the supervision of
CVSA's geologists in accordance with industry practice. Geochemical assays are
obtained and reported under a quality assurance and quality control (QA/QC)
program. Reverse circulation samples are collected at the drill rig either
with a dry or a wet hydraulic splitter. Samples were collected on 0.5, 1 and
2m intervals decided upon by the site geologist. The Reverse circulation
samples are split into two samples at the CVSA mine laboratory where one split
is assayed by the mine laboratory for quick turnaround of results to provide
feedback for the program and the other split dispatched to an ISO
9001:2000-accredited laboratory in Argentina for analysis. CVSA supplied to
Mirasol the independent accredited laboratory analysis results only and these
are reported here. Au is assayed by 50g Fire Assay with an AAS finish. Ag is
assayed by a multi-acid digest with an ICP finish and results > 200 ppm were
reassayed by 50g Gravimetric method. Assay results from reverse circulation
samples may be higher, lower or similar to results obtained from surface
samples due to surficial oxidation and enrichment processes or due to natural
geological grade variations in the primary mineralization.
Forward Looking Statements: The information in this news release contains
forward looking statements that are subject to a number of known and unknown
risks, uncertainties and other factors that may cause actual results to differ
materially from those anticipated in our forward looking statements. Factors
that could cause such differences include: changes in world commodity markets,
equity markets, costs and supply of materials relevant to the mining industry,
change in government and changes to regulations affecting the mining industry.
Forward-looking statements in this release include statements regarding future
exploration programs, operation plans, geological interpretations, mineral
tenure issues and mineral recovery processes. Although we believe the
expectations reflected in our forward looking statements are reasonable,
results may vary, and we cannot guarantee future results, levels of activity,
performance or achievements. Mirasol disclaims any obligations to update or
revise any forward looking statements whether as a result of new information,
future events or otherwise, except as may be required by applicable law.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Mirasol Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/July2016/26/c4101.html

-0-                           07/26/2016
/For further information: Stephen Nano, President and CEO or John
Toporowski, Manager of Investor Relations, Tel: +1 (604) 602-9989, Email:
contact(at)mirasolresources.com, Website: www.mirasolresources.com/
/Web Site: http://www.mirasolresources.com /
(MRZ. MRZLF)

CO:  Mirasol Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:

-30-